## Slide 1: ESE532: System-on-a-Chip Architecture
Day 25: November 28, 2018
Network-on-a-Chip (NoC)

## Slide 2: Today
Ring
2D Mesh Networks
Design Issues
Buffering and deflection
Dynamic and static routing

## Slide 3: Message
Scalable interconnect for locality
  has rich design space
Customize to compute and application
Support real-time with static scheduled communication

## Slide 4: Interconnect
Will need an infrastructure for programmable connections
Rich design space to tune area-bandwidth-locality
  Will explore more later in course
Day 12

## Slide 5: Interconnect Concerns
Avoid being a bottleneck
  Bandwidth
  Latency
Competes for area and energy
  against compute and memory

## Slide 6: Crossbar
Connect any I inputs, O outputs
Area ~ I×O
For N PEs scale as N2

## Slide 7: Today’s SoC Large
At 0.4mm2 small core on Apple A12
  can put 250 on 1cm2 chip
Intel Knight’s Bridge with 76 PEs
120 core MIPS on Stratix V FPGA
  FPGA 2017
1680 core RISC-V on Xilinx Ultrascale
  http://fpga.org/2017/01/12/grvi-phalanx-joins-the-kilocore-club/
Scaling to 100s and 1000s of processing elements (PEs) that need interconnect

## Slide 8: Locality
Delay and energy proportional to distance
Want to keep communications short
  Data near compute
  From compute block to compute block
How build network?
  Scalable (Area ~ N = things connected?)
  Supports locality

## Slide 9: Mesh
Day 12

## Slide 10: Bus to Ring

## Slide 11: Ring

## Slide 12: Preclass 1
Traffic pattern
  Similar bandwidth?
  One has higher bandwidth?

## Slide 13: Bidirectional Ring

## Slide 14: Interleaved Layout
What problem does the bottom layout solve (compared to top)?

## Slide 15: 2D Layout

## Slide 16: Scaling
How does area scale with N?
How does neighbor distance scale with N?
  Unidirectional
  bidirectional
How does worst-case distance in ring scale with N?
  Unidirectional
  bidirectional

## Slide 17: 1D to 2D

## Slide 18: Ring Abstract

## Slide 19: Row and Column Rings

## Slide 20: Mesh as Row & Column Rings

## Slide 21: Directional Mesh (Torus)

## Slide 22: Mesh Datapath

## Slide 23: Bidirectional Mesh

## Slide 24: 2D Mesh Scaling
How does area scale with N?
How does neighbor distance scale with N?
How does worst-case distance in mesh scale with N?

## Slide 25: Specifying Destination
Simple: add destination address
Ring or Mesh wires carry:
  Valid bit + Address + Payload (Data)

## Slide 26: Mesh Routing
Route in Y until reach row
Then route in X until reach column
Consume from PE when arrives

## Slide 27: Mesh Routing
Yout=Yin.valid & row(Yin.address)!=row & Yin + Pin.valid & P
Xout=Xin.valid & column(Xin.address)!=column & Xin + Yin.valid & row(Yin.address==row)
Not deal with congestion
Yin
Xin
Yout
Xout

## Slide 28: Mesh Routing
Yout=Yin.valid & row(Yin.address)!=row & Yin + Pin.valid & P
Xout=Xin.valid & column(Xin.address)!=column & Xin + Yin.valid & row(Yin.address==row)
Complexity of route function can impact
  Area, cycle time, route latency

## Slide 29: Mesh Congestion

## Slide 30: Mesh Congest
What happens when inputs from 2 sides want to travel out same output?
  (here Xin, Yin)

## Slide 31: Dealing with Congestion
Don’t let it happen (offline/static)
  Schedule to avoid
Online/dynamic
  Store in place -- Buffer
  Misroute -- Deflect

## Slide 32: Congestion 1D
For simplicity, we look at congestion in 1D case (Preclass 2)

## Slide 33: Preclass 2ab
Complete table – identify uncongested latencies
Worst-case?

## Slide 34: Preclass 2c
Cycles from simulation?

## Slide 35: Observe
Did have congestion
  Ran slower than the single-link case (2b)
How we make decisions matters
  Who gets to route, which is stalled
Best, global decision can be better than local decisions

## Slide 36: Offline vs. Online
[Kapre et al., FCCM 200]

## Slide 37: Dealing with Congestion
Don’t let it happen (offline/static)
  Schedule to avoid
Online/dynamic
  Store in place -- Buffer
  Misroute -- Deflect

## Slide 38: Congestion: Buffer
Store inputs that must wait until path available
  Typically store in FIFO buffer
  How big do we make the FIFO?
  FIFO Buffers cost space
    Often more than multiplexers

## Slide 39: Congestion: Buffer
Store inputs that must wait until path available
  Typically store in FIFO buffer
  How big do we make the FIFO?
  What if FIFO full?

## Slide 40: Congestion: Buffer
Store inputs that must wait until path available
  Typically store in FIFO buffer
  How big do we make the FIFO?
  What if FIFO full?

## Slide 41: Congestion: Deflect
Misroute: (deflection routing)
  Send in to an available (wrong) direction
  Avoid Buffer
  Requires balance of ins and outs
    Can make work on mesh
  How much more traffic do we create misrouting?

## Slide 42: Static Schedule
Store per-cycle instruction for switch
  Doesn’t need address header on route
  Local memories control destination

## Slide 43: Alternate Static Schedule
Control injection cycle from processor so never have conflict
Simple datapath logic to select available data
  Needs address header on routed data

## Slide 44: Mesh Packet Switched 32b
Bidirectional FIFO
  bidrectional
  1800 LUTs
Deflection (bufferless)
  undirectional
  60 LUTs
[Kapre+Gray, FPL 2015]
Big difference in area costs.
Need to look at area and benefits.

## Slide 45: Deflection Route
What concerns might we have about deflection route?

## Slide 46: Buffer vs. Deflection
[Kapre+Gray, FPL 2015]

## Slide 47: Tuning
How could we increase bandwidth to better handle high throughput?
  Especially when the switches are small
Mesh switch 1800
Deflection Torus 60

## Slide 48: Tune Bandwidth
Add channels to tune bandwidth
  Rings per row, column
  Single deflection channel ~60
    …two around 120 … still << 1800

## Slide 49: Take 2, they are small
[Kapre+Gray, FPL 2015]

## Slide 50: Mesh Area Deflection PS/TM
Hoplite = Deflection
Marathon = Deflection + static schedule at source
[Kapre FCCM 2015]

## Slide 51: Static Schedule vs. Deflection
[Kapre FCCM 2015]
Deflection
Scheduled Deflection

## Slide 52: Static Schedule vs. Deflection
Routing 142K message add20 benchmark
Marathon statically schedule PS
[Kapre FCCM 2015]
Scheduled Deflection
Deflection

## Slide 53: Large VLIW
Natural to use static network with VLIW clusters
  Network routing becomes part of long instruction word
  Schedule with computation
Extreme one operator per mesh PE
Tune bandwidth by clustering

## Slide 54: Mesh Customization

## Slide 55: Tuning Down
What could we do to reduce area if we needed less bandwidth?

## Slide 56: Tuning Down Bandwidth
If need less bandwidth, cluster multiple PEs to share a router.

## Slide 57: Simple Bandwidth/Area Control
Width of channels
  Like SIMD
  All bits going to same destination

## Slide 58: Packets
Simple story is, each “word” routed on mesh is: address+payload
Alternately:
  Multiword packet with single address
  Share “address” across larger payload
  Control width of datapath separate from size of payload
Additional control issues to route packet together and buffer

## Slide 59: Customization
Bandwidth
  Width, clustering, channels
Directional/Bidirectional
Online dynamic/offline static
Buffer/deflect
  Buffer depth
Route function sophistication

## Slide 60: Big Ideas
Scalable interconnect for locality
  Has rich design space
Customize to compute and application
Support real-time with static scheduled communication

## Slide 61: Admin
P4 Due Friday