## Slide 1: ESE532: System-on-a-Chip Architecture
Day 27: December 5, 2018
Representation and Precision

## Slide 2: Today
Fixed Point
Errors from Limited Precision
Precision Analysis / Interval Arithmetic
Floating Point
  If time permits

## Slide 3: Message
We must always calculate with limited precision
Precision costs area (and energy)
  Can economize area (and energy) by judiciously using just the precision we need
    Something can do when building customized accelerator
  Precision-cost tradeoff  design-space axis
Can perform analysis on precision

## Slide 4: Fixed Point
Integer which interpret as a fraction
Fixed-Point N.F
  N bits
  F bits below fraction (typically N>F)
  Equivalently: meaning is Integer-value/2F
    F=0  Integer

## Slide 5: Operator Sizes
Operator | LUTs | LUTs + DSPs
Double FP Add | 712 | 681+3 DSPs
Single FP Add | 370 | 219+2 DSPs
Fixed-Point Add (32) | 16 | 
Fixed-Point Add (n) | n/2 | 
Double FP Multiply | 2229 | 223+10 DSPs
Single FP Multiply | 511 | 461+3 DSPs
Fixed Multiply (32x32) | 1099 | 
Fixed Multiply (16x16) | 283 | 1 DSP
Fixed Multiply (18x25) |  | 1 DSP
Fixed Multiply (n) | ~ n2 | 
FP (Floating Point) sizes from:
https://www.xilinx.com/support/documentation/ip_documentation/ru/floating-point.html

## Slide 6: Observe
Floating-Point operators are large compared to Fixed-Point
  For similar precision
    712 vs. 32 for addition
Double-precision Floating point operators are large
  2229 Multiply, 712 Add
    Can quickly fill 50,000 LUT programmable logic

## Slide 7: Fixed-Point Economy
Can fit more logic (more parallelism) using modest fixed-point
  At 16b: Multiply 283, Add 16
  Vs. Double: 2229, 712
But
  How much precision do we need?
  How do we determine?

## Slide 8: Perfect Representation
Start with Fixed-Point 16.8
What do we need to
  represent the result of an addition? (1a)
  represent the result of a multiplication? (1b)

## Slide 9: Sequence
Across a sequence of operations
  A, B, C start Fixed-Point 16.8
Y=(A+B)*C
Perfect representation for partial results up to Y?

## Slide 10: Looping: Bound loop
res=0;
for(i=0;i<3;i++)
  res=res*x+a[i]
Assume a[i], x start Fixed-Point 16.8
Final precision needed for res?

## Slide 11: Looping: Unbound
res=0;
for(i=0;i<len;i++)
  res=res*x+a[i]
Assume a[i], x start Fixed-Point 16.8, len starts Integer 16
Final precision needed for res?

## Slide 12: Perfect Representation
Start with Fixed-Point 16.8
What do we need to
  represent the result of a division? (1c)
    E.g. 00000001.00000000/00000011.00000000

## Slide 13: Conclude
Cannot generally keep perfect precision
Will typically need to decide how much precision we need and where

## Slide 14: Errors from Limited Precision
Accept errors necessary.
How big are they?
How design to manage them?

## Slide 15: What error introduce?
Absolute Error – what level of error do we have in approximated value or a result
Might be all we care about
  Get answer to 1mV accuracy
  …or 1 pixel accuracy
4.13742 – assume full
4.1374 – 0.00002
  10-5
4.137 – 0.00042
  10-4
4.14 – 0.00256
  10-3
4.1 – 0.03742
  10-2

## Slide 16: What error introduce?
Relative Error – error as percentage of intended result
May be more relevant, particularly if trying to identify small values
4.13742 – 0.0003
  Ideal: 4.13712
  2 decimal frac: 4.14-0.00
    4.14
    (4.14-4.13712)/4.13712
    0.07% error
4.13742-4.13628
  Ideal: 0.00114
  2 decimal fac: 4.14-4.14
    0.00
    (0.00114-0)/0.00114
    100% error

## Slide 17: Preclass 2
Complete Table

## Slide 18: Observe
Add/Multiply relatively well behaved
Must be very careful when
  Division involved
  Divisors can be small
    Get approximated near zero

## Slide 19: Precision Allocation
Full precision can be too expensive
  Non-sensical
Limited precision introduces errors
  May be smaller than we care about
Determine minimal precision needed
  …or where to spend precision…

## Slide 20: Empirical Analysis
Make guess at precisions
Set precisions in calculation
Simulate on data
Evaluate results (absolute, relative error) compared to gold standard
  Unlimited precision…or, at least, higher precision
    Often standard is double-precision float
      …but, as we’ll, even that’s a compromise
Update precision guess and repeat

## Slide 21: Empirical Analysis
Make guess at precisions
Set precisions in calculation
Simulate on data
Evaluate results compared to gold standard
Demands Care
Test coverage
  Adequate set of test data to trigger worst-case errors?
Requires some understanding of calculation
Shouldn’t be entirely black box

## Slide 22: Vivado HLS Support
Has libraries to support
  Arbitrary precision integers
  Arbitrary precision fixed point
For
  Simulation
  Synthesis
UG902 – Vivado HLS User Guide
  Chapter 2: Abritrary Precision Data Type Library

## Slide 23: Precision Analysis

## Slide 24: Precision Analysis
Can analyze worst-case error impacts from limited precision
Give results not sensitive to test set
Give guidance on where to allocate precision
…can be automated

## Slide 25: Limit Precision Inputs
Typically start with limited precision
  A/D only sample to 12b
    Real-world had more precise value, but didn’t capture
  Quantized data stored in representation
    Sound samples, DCT frequency coefficients
We start with error
  What does that mean about values we calculate?

## Slide 26: Interval Analysis
Treat every value as an interval arrange
Model effects of operations on range of results
A=(A.H, A.L) e.g. read 37 (37.49,37.51)
A+B=(A.H+B.H,A.L+B.L)
Assuming Positive A, B and interval not cross 0, what is range for:
  A*B
  A/B

## Slide 27: Interval Analysis
Treat every value as an interval arrange
Model effects of operations on range of results
A=(A.H, A.L)
A+B=(A.H+B.H,A.L+B.L)
Positive A, B and B interval not cross 0
  A*B=(A.H*B.H,A.L*B.L)
  A/B=(A.H/B.L,A.L/B.H)

## Slide 28: Interval Analysis
With ranges that may cross zero…
A*B=(max(A.H*B.H,A.H*B.L,A.L*B.H,A.L*B.L), min(A.H*B.H,A.H*B.L,A.L*B.H,A.L*B.L))
A/B … more complicated
  If B.H positive, B.L negative, can become infinity

## Slide 29: Limited Precision
A=(A.H,A.L)=(A+e,A-e)=A±e
E.g. if rounded to Fixed Point 16.8
  e may be 2-9

## Slide 30: Preclass 2
Complete Table

## Slide 31: Multiplication
(A±e)(B±e)
A*B ± ( (A+B) e + e2 )
A and B can be MAXVAL, MINVAL
  Assume symmetric (MAXVAL=-MINVAL)
A*B ± ( 2*MAXVAL* e + e2 )
  Probably reasonable to drop e2
A*B ± 2*MAXVAL* e

## Slide 32: Multiply Range Example
Recall: Fixed-Point 16.8 multiply
  Full precision result: 32.16 (preclass 1b)
What is error interval for result of 16.8 multiply?

## Slide 33: Range Example
Error Interval for 16.8 fixed-point multiply
For 16.8, e0=1/512, maxval=256
From preclass 3 symbolic answer
  A*B ± 2*MAXVAL* e
  A*B ± 2*256*(1/512)
  Or A*B±1

## Slide 34: Observe
Full precision may keep bits well below the error in the calculation
  E.g. 32.16 result, keeping 16b below 20 term
  Entire fraction is below the error in the calculation
    A*B±1

## Slide 35: Rounding
Rounding introduces an error
Round Nearest A to Fixed-Point N.8
  e=2-9
As does truncation, floor, ceil…
  But asymetric interval

## Slide 36: Compute and Round Error
Error range if round 32.16 result to 18.2?
  (from 16.8 multiply)
  Hint:
    How much from calculation?
    How much additional from rounding?

## Slide 37: Compute and Round Error
Rounding 32.16 to 18.2 introduces a quantization error of 2-3
Our 32.16 multiply result was ±1
  Add an addition ±1/8
  Total error: ±9/8

## Slide 38: Result
Dropping (rounding) bits may not increase error range (much)

## Slide 39: Symbolic
If work through computation symbolically, can generate equation for error
Each rounding (precision drop) adds some ei precision

## Slide 40: Approach
At each step compute interval
Keep track of
  maxval
  e

## Slide 41: Symbolic Example
Start A, B, C with maxval0, e0
Y=(A+B)*C;
A+B maxval1=2maxval0 , e2=2e0+e1
  e1 for round after this operation
(A+B)*C
  maxval2=maxval1*maxval0
  e4=e2*maxval0+e0*maxval1+e3
  e3 for round at this operation

## Slide 42: Result Precision
After series of operations, may have expression like:
  Y±(e3+(e1+4 *e0) *maxval0)
If looking for result with precision ±eres
  eres≥ (e3+(e1+4 *e0 )*maxval0)

## Slide 43: Result Precision
Fixed Precision12.0 = Round(val)
  E.g. A/D output
  Only need to know val to e=1/2
Fixed Precision 12.0 = Round(val/4)
  E.g. Quantized value stored in file
  Only need to know val to e=2
  Start 13.8, maxval0=32
  eres≥ (e3+(e1+4 *e0 )*maxval0)=(e3+(e1+4 *e0 )*32)
    What epsilons might solve?
      Hint: try budget half unit for each e3, e1 term

## Slide 44: Optimize Precision Allocation
  eres≥ (e3+e1+4 *e0 *32)
    Maybe: e0=1/256, e1=1/2, e3=1/64
    1/256 – 7 bit fraction, 1/64 – 5 bit, ½ -- no fraction
More generally
  Combine with area model and look at expense of providing each ei
  Round to 12.7, Fixed 12.7 add, round to 11.5, Fixed 11.5 multiply, round to 12.0
    12/2 add, 12/2 round, 11*11 for multiply ~ 133 LUTs
Try pick ei to meet eres while minimizing area

## Slide 45: Tools
Tools can automate interval calculations to verify precision
  E.g. Gappa++
  https://bitbucket.org/mlinderm/gappa

## Slide 46: Floating Point
(time permit)
Robert Tinney
(Byte circa 1980)

## Slide 47: Floating-Point vs. Fixed-Point
Floating-Point (esp. double-precision) is a big hammer solution
  Trades hardware/energy for programmer attention to needs
  Standards have been well thought out so works over wide range
    One size fits all (…almost)
  Most cases it is more than needed
Cost/energy sensitive designs will ask what’s necessary and tune accordingly

## Slide 48: Floating Point
Leading 0s aren’t that useful
Can represent more compactly by counting them
  Only need log bits to count the zeros
Represent value as v=1.m * 2(exp-offset)
  Mantissa (m)
  Exponent (exp)
Like Scientific Notation

## Slide 49: Floating Point
Floating Point means
  Move the datapath to the interesting/significant part of computation
  Don’t represent leading zeros
  Don’t represent less significant bits
    Even if they are well above 1
      In the integer portion

## Slide 50: Standard Floating Point
Double Precision (64b)
  1 bit sign
  11 bit exponent
    Offset 1023 represents 1023 to -1022
  53 bit mantissa (52b + implicit 1)
Single Precision (32b)
  1 bit sign
  8 bit exponent (offset 127)
  24 bit mantissa (23b + implicit 1)

## Slide 51: Expensive FP Add
Recall
  712 LUTs double
  370 single
Double:
  54b add one stage of 7 in pipeline
  Done in 27 6-LUTs
[Kadric, Arith 2013]

## Slide 52: Floating Point Multiply
Double 2229, Single 461
Don’t need to sort, pre-shift
m=A.m*B.m (53x53 multiply dominates)
e=A.e+B.e
Still have shifting, rounding at end

## Slide 53: Dynamic Range
Floating Point has very wide dynamic range
Can deal with significant piece being anywhere in 1023 to -1022
For fixed-point to cover same range
  Fixed Point 2046.1022
  Add 1024 LUTs
  Multiply ~ 4M LUTs
When need dynamic range, FP economical

## Slide 54: Customization
Can customize Floating Point on FPGA or custom silicon
  Mantissa bits
  Exponent bits
Fewer bits when need less precision or range to save area
More bits if need greater precision or range

## Slide 55: Floating Point
Not free of precision problems
((1+2100)-299)-299=0
1+(2100+(-299-299))=1

## Slide 56: Floating-Point Analysis
Can do similar analysis on floating point
  …and there are tools to help
  Including Gappa++

## Slide 57: Big Ideas
We must always calculate with limited precision
Precision costs area (and energy)
  Can economize area (and energy) by judiciously using just the precision we need
  Precision-cost tradeoff
    Design-space axes
Can perform analysis on precision

## Slide 58: Admin
Project Due Friday
  Report individual
  Elf, bitstream, decoder – one per group
  Code – everyone turn in, but same across group
Return boards Monday in Class
Exam following Friday (12/14)
  Towne 303 (here), 9am