## Slide 1: ESE532: System-on-a-Chip Architecture
Day 28: Dec 10, 2018
Wrapup

## Slide 2: Today
What was course about
Final
Review w/ Simple Models
Other Courses
Questions/Discussion
ZedBoard Return

## Slide 3: Goal
How to design/select/map to SoC to reduce Energy/Area/Delay.

## Slide 4: Outcomes
Design, optimize, and program a modern System-on-a-Chip.
Analyze, identify bottlenecks, design-space
Decompose into parallel components
Characterize and develop real-time solutions
Implement both hardware and software solutions
Formulate hardware/software tradeoffs, and perform hardware/software codesign
Day 1

## Slide 5: Outcomes
Understand the system on a chip from gates to application software, including:
  on-chip memories and communication networks, I/O interfacing, RTL design of accelerators, processors, firmware and OS/infrastructure software.
Understand and estimate key design metrics and requirements including:
  area, latency, throughput, energy, power, predictability, and reliability.
Day 1

## Slide 6: Message for Day
Identify the Bottleneck
  May be in compute, I/O, memory, data movement
Focus and reduce/remove bottleneck
  More efficient use of resources
  More resources
Repeat
Day 2

## Slide 7: Abstract Approach
Identify requirements, bottlenecks
Decompose Parallel Opportunities
  At extreme, how parallel could make it?
  What forms of parallelism exist?
    Thread-level, data parallel, instruction-level
Design space of mapping
  Choices of where to map, area-time tradeoffs
Map, analyze, refine
Day 1

## Slide 8: SoC Designer Hardware Building Blocks
Computational blocks
  Adders, multipliers, dividers, ALUs
Registers
Memory blocks
Busses
Multiplexers, Crossbars
DMA Engines
Processors
I/O blocks
  Ethernet, USB, PCI, DDR, Gigabit serial links

## Slide 9: Final

## Slide 10: Final
Analysis
  Bottleneck
  Amdhal’s Law Speedup
  Computational requirements
  Resource Bounds
  Critical Path
  Latency/throughput/II
Model/estimate speedup, area, energy, yield
From Code
Forms of Parallelism
Dataflow, SIMD, VLIW, hardware pipeline, threads
Map/schedule task graph to (multiple) target substrates
Memory assignment and movement
Area-time points
Real Time

## Slide 11: Final
Like midterm
  Content
  Style
  Closed book, notes
  Calculators allowed (encouraged)
Last term’s final and solutions
  Linked to Fall 2017 syllabus (Spring 2017)
Friday, December 14 9am—11am
  Towne 303 (here)
  2 hours (standard final exam period)

## Slide 12: Review

## Slide 13: Sequential Computation
Computation requires a collection of operations
  Arithmetic
  Logical
  Data storage/retrieval

## Slide 14: Computations in C
Express computations in a programming language, such as C
Can execute computation in many different ways
  Sequential, parallel, spatial hardware
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 15: Memory Characteristics
Small memories
  Fast
  Low energy
  Not dense
    (high area per bit)
Large memories
  Slow
  High energy
  Dense (less area per bit)

## Slide 16: Memory and Compute
Computation involves both arith/logical ops and memory ops

## Slide 17: Memory and Compute
Computation involves both arith/logical ops and memory ops
Either can dominate
  Be bottleneck

## Slide 18: Memory and Compute
Timing
  Tmem=10
  Talu=1
Nmpy=
Nadd=
Nmem=
Total Time, T?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}
(not count loop, indexing costs in this sequence)

## Slide 19: Memory and Compute
Where bottleneck?
  Tmem=10
  Talu=1
Nmpy=16
Nadd=15
Nmem=95
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 20: Data Reuse
Reduce memory operations to large memory by storing in
  Registers
  Small memories

## Slide 21: Memory and Compute
a,b in large mem
y,z in small mem
  Tlem=10
  Tsem=1
  Talu=1
Nmpy=16
Nadd=15
Nlmem=?
Nsmem=?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 22: Memory and Compute
a,b in large mem
y,z in small mem
  Tlem=10
  Tsem=1
  Talu=1
Nmpy=16
Nadd=15
Nlmem=32
Nsmem=63
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}
Performance impact?

## Slide 23: Task Parallel
Can run unrelated tasks concurrently
Ideal: T(p) = T(1)/p

## Slide 24: Data Parallel
Can run same task on independent data in parallel
Ideal: T(p) = T(1)/p

## Slide 25: Data Parallel
What’s data parallel?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 26: Vector/SIMD
Can perform same operation on a set of data items
Ideal: T(VL) = T(1)/VL
(Vector Length)

## Slide 27: Vector/SIMD
Can perform same operation on a set of data items
  Not everything vectorizable

## Slide 28: Vector/SIMD
What’s vectorizable?
Speedup vector piece VL=4
  (assume both memory and compute speedup)
Overall speedup
Amdahl’s Law speedup for VLinfintiy?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 29: Dataflow Pipeline
With no cycles in flowgraph
  (no feedback)
  (no loop carried dependencies)
Producer and consumer can operate concurrently
Prod
Consume

## Slide 30: Data Flow Pipeline
Producer/consumer here?
Time each
  Assuming Tmem=1
Granularity of dataflow pipeline
Size of buffer needed to allow concurrent operation?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 31: Data Flow Pipeline
(note changed second loop)
Granularity of dataflow pipeline
Size of buffer needed to allow concurrent operation?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[16]=y[16];
for (i=15;i>=0;i--)
z[i]=z[i+1]+y[i];
}

## Slide 32: Spatial Pipeline
Can build spatial pipeline of hardware operators to compute a dataflow graph
With no feedback: T=1
With feedback limit II: T=II

## Slide 33: Spatial Pipeline
Pipeline taking one a[i], b[i] per cycle?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 34: Spatial Pipeline
Full pipeline taking all 16 a’s, b’s in cycle?
Latency?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 35: Spatial Pipeline

## Slide 36: Reduce
(note slightly different second loop)
Common pattern is a reduce operation
  Combine a set of data into a single value
When reduce operation is associative, can compute with log depth
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z=0;
for (i=0;i<16;i++)
z+=y[i];
}

## Slide 37: Log-Depth Associative Reduce

## Slide 38: Initiation Interval
What’s II?
  a, b still Tmem=10
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 39: Initiation Interval
What’s II?
  a, b, c Tmem=10
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i]+c[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 40: Initiation Interval
First loop
  II?
  Latency of loop body
while(true) {
g=0;
for (i=0;i<16;i++) {
t=a[i]*b[i]+c[g];
y[i]=t;
g=t%16; }
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 41: VLIW
Can control datapath to perform multiple, heterogeneous operations per cycle
  Tune parallelism
Op types: A, B, C
  Ops NA, NB, NC
  Number of Hardware Units HA, HB, HC
TRB=max(NA/HA, NB/HB, NC/HC,…)≤TVLIW
TCP≤TVLIW

## Slide 42: VLIW
VLIW
  1 load/store (a,b)
    Assume single cycle
  1 mpy
  1 add
RB
CP
Schedule
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 43: VLIW
VLIW
  4 load/store (a,b)
    Assume single cycle
  2 mpy
  2 add
RB
CP
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 44: Memory Bottleneck
Memory can end up being bottleneck
Ideal: T(p) = Tcomp(1)/p+Tmem

## Slide 45: Memory Bottleneck
Pipeline to perform one multiply per cycle
Memory supplies one data item from large memory (a,b) every 10 cycles
Performance?
  (number of cycles)
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 46: Memory Bottleneck
Memory can end up being bottleneck
Ideal: T(p) = Tcomp(1)/p+Tmem/Membw

## Slide 47: Memory Bottleneck
Invest in higher bandwidth
  Wider memory
  More memory banks
Exploit data reuse
  Smaller memories may have more bandwidth
  Smaller memories are additional banks
    More bandwidth

## Slide 48: Communication
Once parallel, communication may be bottleneck
Ideal (like VLIW):
  T≤max(Tcomp/p,Tmem/membw,Tcomm/netbw)

## Slide 49: Area
Can model area of various solutions
  Sum of component areas
  (watch interconnect)
Cost proportional A/Pchip
Without sparing
  Pchip = (Pmm)A
Sparing
  Pmofn

## Slide 50: Multi-Objective Optimization
Many forms of parallelism
Given fixed area (resources, energy)
  Maximize performance
  Select best architecture
Given fixed performance goal
  Find architecture that achieves
  With minimum area (energy, cost)

## Slide 51: Final
Analysis
  Bottleneck
  Amdhal’s Law Speedup
  Computational requirements
  Resource Bounds
  Critical Path
  Latency/throughput
Model/estimate speedup, area, energy, yield
From Code
Forms of Parallelism
Dataflow, SIMD, VLIW, hardware pipeline, threads
Map/schedule task graph to (multiple) target substrates
Memory assignment and movement
Area-time points
Real Time

## Slide 52: Other Courses

## Slide 53: Distinction
CIS240, 501(371)
Best Effort Computing
  Run as fast as you can
Binary compatible
ISA separation
Shared memory parallelism
Caching – automatic memory management
Superscalar
Pipelined processor
ESE532
Hardware-Software codesign
  Willing to recompile, maybe rewrite code
  Define/refine hardware
Real-Time
  Guarantee meet deadline
Non shared-memory models
Explicit memory management
VLIW

## Slide 54: Circuits and Computer Engineering
ESE370
Circuit Level Modeling & Optimization of Dig. Systems
Transistor models, CMOS logic, delay, scaling, energy, interconnects, flip-flops, noise, T-lines, RAM design
ESE578
RF Integrated
Circuits Design
m-wave Eng overview, T-line, Smith-chart, S-parameters, matching, passive devices, small signal amplifier, LNA and PA, mixed signal on chip
ESE319
Electronics
Diode & Transistor Circuits, Single Stage & Diff. Amplifiers, Filters, Oscillators
ESE419 (572)
Analog Integrated Circuits
MOSFET circuits, Ampl. Stages, I-Mirrors, Op-Amps, Feedback, Stability, Root Locus, Cascode Ampl.
or
Digital
Analog
ESE350
Embedded Systems
m-controller architectures, Interfacing, ADC, sensor and actuator control, ROS, network protocols
Embedded
(uP/uC)
ESE570
Digital Integrated Circuits
MOSFET Trans Models, Inverter switching, MOS Logic, Memories, Implementation methods, Layout.
ESE532
SoC Architecture
Hardware/Software
Codesign,
Parallelism, Analysis, Real-Time
ESE672
Integrated Communication Circuits
Receivers, Low-noise amplifiers, mixers, oscillators, phase lock loops, power amplifiers
CIS541
Embedded Cyber Physical Systems
Life-Critical, Real-Time,
Analysis,
Implementations
Validation/verification
ESE568 (Fall)
Mixed-Signal Circuits
A/D, D/A, sampling…
or
ESE519
Real-Time &
Embedded Systems
m-controller architectures, Interfacing, ADC, sensor and actuator control, ROS, network protocols
or
Notes: Simple Story

## Slide 55: Other Courses
Security: CIS331, CIS551
Networking: ESE407, CIS553
GPGPU (graphics focus): CIS565

## Slide 56: Message
Any interesting, challenging computation will require both hardware and software
SoC powerful implementation platform
  Target pre-existing
  Design customized for problem
  Exploit heterogeneous parallelism
Understand and systematically remove bottlenecks
  Compute, memory, communicate, I/O

## Slide 57: Question/Discussion

## Slide 58: Admin
Return Zed Boards
Standard office hours
  Monday 6—8pm
  Tuesday 4:15pm-5:30pm
Final Q&A (office hour)
  Wednesday, Dec. 12th 6-8pm
  Location TBA (watch piazza)
Final: Friday, Dec. 14 9am—11am
  Towne 303 (here)