## Slide 1: ESE532: System-on-a-Chip Architecture
Day 7: September 24, 2018
Pipelining -- Supplement

## Slide 2: Register
On each cycle, the output of the register is the value of the input of the register on the previous cycle.

## Slide 3: Shift Register
Illustrate operation
Data moves through registers
Shifts to right with each cycle
Steady state, output at right is value input 3 cycles prior

## Slide 4: Addition
Combinational Addition
Two Adders
Output is sum of 3 values

## Slide 5: Pipelined Addition
Here we add registers to compute the addition in part of a pipeline
Like the shift register values move through the registers over cycles
The output is the sum of the inputs 3 cycles prior

## Slide 6: Pipelined Addition
Note that the output is all inputs from the same cycle
All the subscripts to A, B, C are the same.

## Slide 7: Retimed Add
Now, we retime the add by applying a lag to the first adder
  Move registers from its inputs to outputs

## Slide 8: Compare Behavior

## Slide 9: Retimed Behavior
To external behavior, the output is unchanged after the lag
  Circuits behave identically

## Slide 10: Retimed Circuit Cycle Time
Original circuit had two adder delays between registers
  Minimum cycle time = 2*Tadd
  Throughput = 1/(2*Tadd)
Retimed circuit has one adder delay between registers
  Minimum cycle time = Tadd
  Throughput = 1/Tadd
By performing the retiming, we doubled the throughput

## Slide 11: What-if just added a register?
Rather than lag, what if we just added a register?

## Slide 12: Just Add Register Behavior
Note how this is different from the original
(and from the retimed)
Here, final output mixes
A1 with B0 and C0

## Slide 13: Just Add Register Function
Output takes the B and C from one
input and adds it to the A that enters
one cycle later.