## Slide 1: ESE532: System-on-a-Chip Architecture
Day 1: August 28, 2019
Introduction and Overview
Everyone grab:
Preclass
Feedback Sheet (1/2 page)

## Slide 2: Today
Case for Programmable SoC
Course Goals
Outcomes
New/evovling Course, Risks, Tools
Sample Optimization
This course (incl. policies, logistics)

## Slide 3: Apple A12 Bionic
84mm2, 7nm
7 Billion Tr.
iPhone XS, XR
  IPad 2019
6 ARM cores
  2 fast
  4 low energy
4 custom GPUs
Neural Engine
  5 Trillion ops/s?

## Slide 4: Questions
Why do today’s SoC look like they do?
How approach programming modern SoCs?
How design a custom SoC?
When building a System-on-a-Chip (SoC)
  How much area should go into:
    Processor cores, GPUs, FPGA logic, memory, interconnect, custom functions (which) …. ?

## Slide 5: FPGA Field-Programmable Gate Array
K-LUT (typical k=4)
Compute block
w/ optional
output Flip-Flop
ESE171, ESE150, CIS371

## Slide 6: Case for Programmable SoC

## Slide 7: The Way things Were
25 years ago
Wanted programmability
  used a processor
Wanted high-throughput
  used a custom IC
Wanted product differentiation
  Got it at the board level
  Select which ICs and how wired
Build a custom IC
  It was about gates and logic

## Slide 8: Today
Microprocessor may not be fast enough
  (but often it is)
  Or low enough energy
Time and Cost of a custom IC is too high
  $100M’s of dollars for development, Years
FPGAs promising
  But build everything from prog. gates?
Premium for small part count
  And avoid chip crossing
  ICs with Billions of Transistors

## Slide 9: Non-Recurring Engineering (NRE) Costs
Costs spent up front on development
  Engineering Design Time
  Prototypes
  Mask costs
Recurring Engineering
  Costs to produce each chip

## Slide 10: NRE Costs

## Slide 11: NRE Cost (continued)
https://semiengineering.com/how-much-will-that-chip-cost/

## Slide 12: Amortize NRE with Volume

## Slide 13: Economics
Economics force fewer, more customizable chips
  Mask costs in the millions of dollars
  Custom IC design NRE 10s—100s of millions of dollars
    Need market of billions of dollars to recoup investment
    With fixed or slowly growing total IC industry revenues
     Number of unique chips must decrease
    Chips must be programmable
Forcing fewer,
more customizable
chips

## Slide 14: Large ICs
Now contain significant software
  Almost all have embedded processors
Must co-design SW and HW
Must solve complete computing task
  Tasks has components with variety of needs
  Some don’t need custom circuit
  90/10 Rule

## Slide 15: Given Demand for Programmable
How do we get higher performance than a processor, while retaining programmability?

## Slide 16: Programmable SoC
Implementation Platform for innovation
  This is what you target (avoid NRE)
  Implementation vehicle

## Slide 17: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 18: Then and Now
25 years ago
Programmability?
  use a processor
High-throughput
  used a custom IC
Wanted product differentiation
  board level
  Select & wired IC
Build a custom IC
  It was about gates and logic
Today
Programmability?
  uP, FPGA, GPU, PSoC
High-throughput
  FPGA, GPU, PSoC, custom
Wanted product differentiation
  Program FPGAs, PSoC
Build a custom IC
  System and software

## Slide 19: Course Goals, Outcomes

## Slide 20: Goals
Create Computer Engineers
  SW/HW divide is wrong, outdated
  Parallelism, data movement, resource management, abstractions
  Cannot build a chip without software
SoC user – know how to exploit
SoC designer – architecture space, hw/sw codesign
Project experience – design and optimization

## Slide 21: Roles
PhD Qualifier
  One broad Computer Engineering
CMPE Concurrency
Hands-on Project course

## Slide 22: Outcomes
Design, optimize, and program a modern System-on-a-Chip.
Analyze, identify bottlenecks, design-space
  Modeling  write equations to estimate
Decompose into parallel components
Characterize and develop real-time solutions
Implement both hardware and software solutions
Formulate hardware/software tradeoffs, and perform hardware/software codesign

## Slide 23: Outcomes
Understand the system on a chip from gates to application software, including:
  on-chip memories and communication networks, I/O interfacing, design of accelerators, processors, firmware and OS/infrastructure software.
Understand and estimate key design metrics and requirements including:
  area, latency, throughput, energy, power, predictability, and reliability.

## Slide 24: New and Evolving Course
Spring 2017 – first offering
  Raw, all assignments new … some buggy
  Assignments too tedious, long
Fall 2017 – second offering
  Refine assignments, project
  Increased explicit modeling emphasis
  Hard, not insane
Fall 2018 – third offering
  Not much different from 2017
  Added real-time ethernet data handling; project groups of 3
  Many students challenged with C and software engineering
  Stream debug and performance challenging
Fall 2019 – now
  Basic structure remains same
  Try front-load more C
  Try better introduce Stream optimization and debug
  Group writeup on projects

## Slide 25: Tools
Are complex
Will be challenging, but good for you to build confidence can understand and master
Tool runtimes can be long
Learning and sharing experience will be part of assignments

## Slide 26: Distinction
CIS240, 371, 501
Best Effort Computing
  Run as fast as you can
Binary compatible
ISA separation
Shared memory parallelism
ESE532
Hardware-Software codesign
  Willing to recompile, maybe rewrite code
  Define/refine hardware
Real-Time
  Guarantee meet deadline
Non shared-memory parallelism models

## Slide 27: Abstraction Stack
Transistors
Devices: ESE521
(ESE218)
Digital:
ESE370/570
Processor Arch:
CIS 371/501
(CIS240)
SoC Arch:
ESE 532
Circuits/VLSI
Gates, Memories
Processors
Systems
Mixed Signal:
ESE 568
ADC, DAC
Switched Capacitors
Analog:
ESE419/572
Amplifier, Compare
Voltage/Current Ref.
Embedded Sys:
ESE350/519
Software

## Slide 28: Approach -- Example

## Slide 29: Abstract Approach
Identify requirements, bottlenecks
Decompose Parallel Opportunities
  At extreme, how parallel could make it?
  What forms of parallelism exist?
    Thread-level, data parallel, instruction-level
Design space of mapping
  Choices of where to map, area-time tradeoffs
Map, analyze, refine
  Write equations to understand, predict

## Slide 30: SPICE Circuit Simulator
Example: Kapre+DeHon, TRCAD 2012
Matrix Solve
Ax=B
A matrix
B vector
x unknown vector
Solve for x
Linear Algebra
solving n eqns
in n unknowns.

## Slide 31: Analyze

## Slide 32: Analyze
T=Tmodeleval+Tmatsolve+Tctrl

## Slide 33: Speedup
T=Tmodeleval+Tmatsolve+Tctrl
What should we speedup first?
What happens if only speedup modeleval?
  T=Tmatsolve+(Tmodeleval)/S+Tctrl

## Slide 34: Analyze
If only accelerated model evaluation only about 2x speedup
If want better than 14x speed, must also attack control

## Slide 35: Model Evaluation: Trivial Hardware Implementation
*
*
-
*
÷
÷
ex
c
d
e
a
b
f
Verilog-AMS as Domain-Specific Language

## Slide 36: Spatial Parallelism
Every operation (*, + /) gets dedicated hardware.
Implement task in space  use additional area for each operator.
Parallel – all operations occur simultaneously.
*
*
-
*
÷
÷
ex
c
d
e
a
b
f

## Slide 37: Parallelism: Model Evaluation Data Parallel
Every device independent
Many of each type of device
Can evaluate in parallel
  T=Tseq/Nproc
Build pipelined circuit for model
  Tseq=Ncomp*Tcycle vs. Tpipe=Tcycle

## Slide 38: Spatial Too Big?
*
*
-
*
÷
÷
ex
c
d
e
a
b
f
*
+
÷
ex
Fully spatial circuit
~100x Speedup
Multiple FPGAs
~10x Speedup
1 FPGA
Custom VLIW
VLIW=Very Long Instruction Word
exploits Instruction-Level Parallelism

## Slide 39: Parallelism: Model Evaluation
Spatial end up bottlenecked by other components
Use custom evaluation engines
…or GPUs

## Slide 40: Parallelism: Matrix Solve
Needed direct solver?
E.g. Gaussian elimination
Data dependence on previous reduce
  Limited data parallelism
Parallelism in subtracts
Some row independence

## Slide 41: Example Matrix

## Slide 42: Example Matrix

## Slide 43: Example Matrix
Reduce to critical path:
from 9 sequential operations
to path of 5 operations.

## Slide 44
Dataflow Processing Element (PE)
*
+
÷
Dataflow trigger
Incoming Messages
Outgoing Messages
Graph
Nodes
Graph
Fanout

## Slide 45: Matrix Solve Only
~2.4x mean

## Slide 46: Parallelism: Matrix Solve
Settled on constructing dataflow graph
Graph can be iteration independent
  Statically scheduled
  (cheaper)
This is bottleneck to further acceleration

## Slide 47: Parallelism Controller?
Could leave sequential
For some designs, becomes the bottleneck once others accelerated
Has internal parallelism in condition evaluation
  T=Tmodeleval/S1+(Tmatsolve)/S2+Tctrl

## Slide 48: Parallelism Controller
Customized datapath controller
Tseqctrl=Nadd+Nmul+10*Ndivide
Tvliwctrl=Max(Nadd/2,Nmul,10*Ndivide)

## Slide 49: Single-Chip Solution

## Slide 50: Area-Time for Each

## Slide 51
Composite Speedup

## Slide 52: Modern SoC

## Slide 53: Class Components

## Slide 54: Class Components
Lecture (incl. preclass exercise)
  Slides on web before class
    (you can print if want a follow-along copy)
  N.B. I will encourage (force) class participation
    Questions (“warm” calls)
Reading [~1 required paper/lecture]
  online: Canvas, IEEE, ACM, also ZynqBook,
  Parallel Programming for FPGAs
Homework
  (1 per week due F5pm)
Project – open-ended (~6 weeks)
Note syllabus, course admin online

## Slide 55: First Half
Quickly cover breadth
Metrics, bottlenecks
Memory
Parallel models
SIMD/Data Parallel
Thread-level parallelism
Spatial, C-to-gates
Real-time
Reactive
Line up with homeworks

## Slide 56: Second Half
Use everything on project
Schedule more tentative
  Adjust as experience and project demands
Going deeper
Memory
Networking
Energy
Scaling
Chip Cost
Verification
Defect + Fault tolerance

## Slide 57: Teaming
HW in Groups of 2
HW: we assign
Individual assignment writeup
Project in Groups of 3
Project: you propose, we review
  Most portions group writeup
  Few components individual writeup

## Slide 58: Office & Lab Hours
Andre: T 4:15pm—5:30pm Levine 270
Yuanlong and Eric:
  Tuesday 10am-12pm in Ketterer
  Tuesday 8pm—10pm in Ketterer
  Thursday 6pm—8pm in Detkin
  Start tomorrow 8/29

## Slide 59: C Review
Course will rely heavily on C
  Program both hardware and software in C
HW1 has some C warmup problems
TA will hold C review
  Ketterer on Sept. 3rd at 8pm
  (before our next class meeting since Monday 9/2 is Labor day)
  Watch piazza for details

## Slide 60: Preclass Exercise
Motivate the topic of the day
  Introduce a problem
  Introduce a design space, tradeoff, transform
Work for ~5 minutes before start lecturing
Do bring calculator class
  Will be numerical examples

## Slide 61: Feedback
Will have anonymous feedback sheets for each lecture
  Clarity?
  Speed?
  Vocabulary?
  General comments

## Slide 62: Policies
Canvas turn-in of assignments
No handwritten work
Due on time
  Individual assignments only
    3 free late days total
Collaboration
  Tools – allowed
  Designs – limited to project teams as specified on assignments
See web page

## Slide 63: Admin
Your action:
  Find course web page
    Read it, including the policies
    Find Syllabus
      Find homework 1
      Find lecture slides
        Will try to post before lecture
      Find reading assignments
  Find reading for lecture 2 on canvas and web
    …for this lecture if you haven’t already
  Find/join piazza group for course
  Signup for Detkin/Ketterer card access
    tiny.cc/detkin-access

## Slide 64: Logistics
Will need SD Card writer for HW2+
  (can get $<10 on amazon.com)

## Slide 65: Coming Soon
Boards not available, yet
  Watch piazza
    Maybe office hours Thursday or Tuesday
SDSoC (Xilinx Software)
  Not available on Linux, yet
  Windows is available
    Ketterer
    Detkin? (fixing some last problems on Tuesday)

## Slide 66: Cautionary Note
Most common board failure was broken USB and power.
New boards will have strain relief.
Don’t unplug USB, power cables from board.

## Slide 67: Cautionary Note
Most common board failure was broken USB and power.
New boards will have strain relief.
Don’t unplug USB, power cables from board.

## Slide 68: Big Ideas
Programmable Platforms
  Key delivery vehicle for innovative computing applications
  Reduce TTM, risk
  More than a microprocessor
  Heterogeneous, parallel
Demand hardware-software codesign
  Soft view of hardware
  Resource-aware view of parallelism