## Slide 1: ESE532: System-on-a-Chip Architecture
Day 10: October 2, 2019
Coding HLS for Accelerators

## Slide 2: Previously
We can describe computational operations in C
    Primitive operations (add, sub, multiply, and, or)
    Dataflow graphs primitives
    To bit level
    Conditionals and loops
    Function abstraction
    Loops, Arrays

## Slide 3: Today
Arrays and Memory Sequentialization (from last time)
Pragmas in Vivado HLS C
Controlling Memories in Vivado HLS C
Time permitting
  malloc, pointers, more dependencies

## Slide 4: Message
Can specify HW computation in C
Vivado HLS gives control over how design mapped (area-time, streaming…)
Code may need some care and stylization to feed data efficiently
Read Design Productivity Guide (UG 1197)
  C-based IP development
Reference Vivado HLS Users Guide (902)
  Design Optimization

## Slide 5: Arrays and Memories

## Slide 6: Loop Interpretations
What does a loop describe?
  Sequential behavior [when execute]
  Spatial construction [when create HW]
  Data Parallelism [sameness of compute]
We will want to use for all 3
C allows expressive loops
  Some expressiveness
    Not compatible with spatial hardware construction

## Slide 7: Arrays as Memory Banks
If single memory has only one port
  Can perform only one memory operation per cycle
  What II if a, b, c all in bigmem?
for (i=0;i<1024;i++)
  c[i]=a[i]*b[i];

## Slide 8: Arrays as Memory Banks
Hardware expression: Sometimes we will want to describe computations with separate memory banks
int a[1024], b[1024], c[1024];
for(i=0;i<1024;i++)
  a[i]=bigmem[offset+i];
for (i=0;i<1024;i++)
  c[i]=a[i]*b[i];

## Slide 9: Physical Memory Port as Limited Shared Resource
Typically single memory port
  Must sequentialize on use of memory port
  Reason for banking
    Put in separate memories, so operations can occur simultaneously
Ultra96 DRAM 1 port
Virtex BRAM 2 ports

## Slide 10: Arrays as things to put in Memory Banks
Computational expression:
  sometimes it is useful to express computation
  then decide how to pack array state into memory banks for different
    Hardware availability
    Area-Time tradeoffs

## Slide 11: Arrays as Local Memory
Hardware/Computational expression: natural way of describing local state
hist(int a[SIZE], out[EVENTS]) {
int local[EVENTS];
for(i=0;i<EVENTS;i++)
local[i]=0;
for(i=0;i<SIZE;i++)
local[a[i]]++;
for(i=0;i<EVENTS;i++)
out[i]=local[i];
}

## Slide 12: Arrays as Inputs and Outputs
Computational Expression: arrays are often a natural way of expression set of inputs and outputs
int c=12;
while(true)
  {
  int aval=astream.read();
  int bval=bstream.read();
  int res=a*b+c;
  resstream.write(res);
    }
void op(int a[BLOCK], int b[BLOCK], int out[BLOCK]) {
for (i=0;i<BLOCK;i++)
  {
  out[i]=a[i]*b[i]+c;
    }
  }

## Slide 13: Array Interpretations
What does an array describe?
  Compact expression [write less code]
  Memory banks [where place data]
    Things put in separate memory banks
  Local memory [not need to be shared]
  I/O [source and sink of data]
We will want to use for all 4
C allows expressive use of arrays/memories
  Some expressiveness will inhibit efficient hardware

## Slide 14: C Memory Model
One big linear address space of locations
Most recent definition to location is value
Sequential flow of statements
000
001
002
005
006
007
008
009
010
011
004
Addr
New value
Current value

## Slide 15: Challenge: C Memory Model
One big linear address space of locations
Assumes all arrays live in same memory
Assumes arrays may overlap?
000
001
002
005
006
007
008
009
010
011
004
Addr
New value
Current value

## Slide 16: Example
Assume a, b live in same memory
Placed in sequence as shown
What happens when
  int a[16];
  int b[16];
  Read from a[17]
  Read from b[-2]
Can inhibit separation into memory banks, parallelism

## Slide 17: Memory Operation Challenge
Memory is just a set of location
But memory expressions in C can refer to variable locations
  Does A[i], B[j] refer to same location?
  A[f(i)], B[g(j)] ?
Can inhibit banking, parallelism
  Or add expensive interconnect

## Slide 18: C Memory/Pointer Sequentialization
Must preserve ordering of memory operations
  A read cannot be moved before write to memory which may redefine the location of the read
    Conservative: any write to memory
    Sophisticated analysis may allow us to prove independence of read and write
  Writes which may redefine the same location cannot be reordered

## Slide 19: C Memory/Pointer Sequentialization
Must preserve ordering of memory operations
  A read cannot be moved before write to memory which may redefine the location of the read
  Writes which may redefine the same location cannot be reordered
True for read/write to single array even if know arrays isolated
  Does A[B[i]] refer to same location as A[C[i]]?
  So expression issue broader than C

## Slide 20: Consequence
Expressions and operations through variables (whose address is never taken) can be executed at any time
  Just preserve the dataflow
Memory assignments must execute in strict order
  Ideally: partial order
  Conservatively: strict sequential order of C

## Slide 21: More at end of lecture
If time permits, more on Sequentialization and Dependencies

## Slide 22: Vivado HLS Mapping Control

## Slide 23: Preclass 2
What dataflow graph does this describe?

## Slide 24: Vivado HLS Pragma DATAFLOW
Enables streaming data between functions and loops
Allows concurrent streaming execution
Requires data be produced/consumed sequentially
  i.e. can connect with FIFO; not need reorder

## Slide 25: Dataflow with Arrays

## Slide 26: Streamable
Processes input and output in order

## Slide 27: Cannot Stream Input
Why?

## Slide 28: Streamable?
Can stream input?
Can stream output?

## Slide 29: Vivado HLS Pragma DATAFLOW
Enables streaming data between functions and loops
Allows concurrent streaming execution
Requires data be produced/consumed sequentially
  i.e. can connect with FIFO; not need reorder
Useful to use stream data type between functions – communicates sequence
  hls::stream<TYPE>

## Slide 30: Streaming Operations
Functions can have stream inputs and outputs
  Must pass a pointers
  hls::stream<Type> &strm
Vivado HLS expressiveness to define hardware streaming operation pipelines

## Slide 32: stream_filter Pipeline

## Slide 33: Dataflow Streaming
Works between loops, as well

## Slide 34: Between Loops

## Slide 35: Vivado HLS Pragma PIPELINE
Direct a function or loop to be pipelined
Ideally start one loop or function body per cycle
  Can control II

## Slide 36
for (i=0;i<N;i++)
yout=0;
#pragma HLS PIPELINE
for (j=0;j<K;j++)
yout+=in[i+j]*w[j];
y[i]=yout;
Which solution
from preclass 3?

## Slide 37: Dataflow and pipelining
Dataflow allows coarse-grained pipelining among loops and functions
Pipeline causes loop bodies to be pipelined

## Slide 38: Dataflow and Pipelining
Cycles for top loop unpipelined?

## Slide 39: Dataflow and Pipelining
Cycles for top loop pipelined?

## Slide 40: Dataflow and Pipelining
Cycles for bottom loop unpipelined?

## Slide 41: Dataflow and Pipelining
Cycles for bottom loop pipelined?

## Slide 42: Dataflow and Pipelining
Composite time, no dataflow, no pipelining?

## Slide 43: Dataflow and Pipelining
Composite time dataflow only?

## Slide 44: Dataflow and Pipelining
Composite time pipelining only?

## Slide 45: Dataflow and Pipelining
Composite time dataflow and pipelining?

## Slide 46: Compare Cases
Unpipe
Pipe
Dataflow
Dataflow
No Dataflow

## Slide 47: Unroll
Vivado HLS has pragmas for unrolling
UG902: Vivado Design Suite HLS User’s Guide
  P139—142 (2018.3)
#pragma HLS UNROLL factor=…
Use to control area-time points
  Use of loop for spatial vs. temporal description
https://www.xilinx.com/support/documentation/sw_manuals/xilinx2018_3/ug902-vivado-high-level-synthesis.pdf

## Slide 48: Vivado HLS Pragma UNROLL
Unroll loop into spatial hardware
  Can control level of unrolling
Any loops inside a pipelined loop gets unrolled by the PIPELINE directive

## Slide 49
for (i=0;i<N;i++)
yout=0;
#pragma HLS UNROLL
for (j=0;j<K;j++)
yout+=in[i+j]*w[j];
y[i]=yout;
Which solution
from preclass 3?

## Slide 50: Dataflow, Unrolling, & Pipelining
Cycles unroll K-loop, dataflow, pipeline?

## Slide 51: Unroll
Can perform partial unrolling
#pragma HLS UNROLL factor=…
Use to control area-time points
  Use of loop for spatial vs. temporal description

## Slide 52: Vivado HLS Pragma INLINE
Collapse function body into caller
  Eliminates interface code
  Allows optimization of inline code
Recursive option to inline a hierarchy
  Maybe useful when explore granularity of accelerator

## Slide 53: Zynq BRAM
36Kb of memory
  Configurable width up to 72b
    512x72 or … 32Kx1
  Dual port
Can be operated as 2x18Kb memory banks
  Configurable width up to 36b
    512x36 or … 16Kx1
  Each memory dual port
Xilinx UGu73, UltraScale Architecture Memory Resources User Guide

## Slide 54: Vivado HLS Pragma ARRAY_PARTITION
Spread out array over multiple BRAMs
  By default placed in single BRAM
    At most 2 ports
  Use to remove memory bottleneck that prevents pipelining (limits II)

## Slide 55: Memory Bottleneck Example
902 example p. 91-92
Xilinx UG1197 (2017.1) p. 50
What problem if put mem
in single BRAM?

## Slide 56: Array Partition
Xilinx UG902 p. 195 (145 in 2017.1 version)

## Slide 57: Array Partition Example
#pragma ARRAY_PARTITION variable=mem cylic factor=4
Xilinx UG902 p. 91

## Slide 58: Vivado HLS Pragma ARRAY_RESHAPE
Pack data into BRAM to improve access (reduce BRAMs)
  May provide similar benefit to partitioning without using more BRAMs

## Slide 59
Xilinx UG902 (2017.1) p. 173

## Slide 60
902 example p. 91-92
Xilinx UG902 p. 91
How fix if dint_t is 16b?
BRAM can be configured
for 72b wide output

## Slide 61: Array Reshape Example
#pragma ARRAY_RESHAPE variable=mem cylic factor=4 dim=1
(if din_t 16b)
Xilinx UG902 p. 91

## Slide 62: HLS Pragma Summary
pragmas allow us to control hardware mapping
  How interpret loops (spatial hw vs. temporal)
  Turn area-time knobs
  Specify how arrays get mapped to memories
Could have rewritten code by hand
  Unroll, separate arrays…
  Pragmas automate; we just need to provide instruction

## Slide 63: Midterm
Analysis
  Bottleneck
  Amdhal’s Law Speedup
  Computational requirements
  Resource Bounds
  Critical Path
  Latency/throughput/II
Will be calculating/estimating runtimes
From Code
Forms of Parallelism
Dataflow, SIMD, hardware pipeline, threads
Pipelining/Retiming
Map/schedule task graph to (multiple) target substrates
Memory assignment and movement
Area-time points

## Slide 64: Midterm
Closed book, notes, etc.
Calculators allowed (encouraged)
Last three midterms, final online
  Both without answers (for practice)
  …and with answers (check yourself)
  Check syllabus for previous terms

## Slide 65: Memory Allocation
Simple answer: “Don’t do it!”

## Slide 66: Demand for malloc()
Data-dependent object (array) size
Data-dependent number of objects

## Slide 67: Hardware Memory
Typically small, fixed, local memory blocks
  E.g. 36Kb BRAMs
Reuse memory blocks
  Not allocate new blocks
  Cannot make data-dependent memory sized blocks
  Cannot hold arbitrary-sized data

## Slide 68: No malloc()
Generally don’t want to use malloc with
  Hardware Accelerated functions
  Real-time computations
Vivado HLS won’t let you use malloc()
  For C running on FPGA array
Instead: statically declare arrays of maximum size data may be

## Slide 69: Pointer Passing
Be careful…

## Slide 70: Pointer Passing
What does it mean to pass a pointer into a function?

## Slide 71: Pointer Passing Interpretations
Multiple uses we may want to express
  Specify which data to work on
    Ok to copy that data to private accelerator memory and work with it
    But, how much data to copy? (length)
  Want to mutate data and have other (parallel) tasks see it OR want to see data mutated by other (parallel tasks)
    Not OK to copy to private accelerator memory
    Force use from large, shared memory
    Forces sequentialization

## Slide 72: Pointer Passing
What if accelerator doesn’t have access to the memory holding the data pointed to by the pointer?

## Slide 73: Pointer Passing
What happens if we give accelerators access to common memory holding data for pointer, but
  There’s only one port into memory
  Memory is 10 cycles away
  And there are 100 accelerators that may need access
  Memory can only handle one memory op per cycle
Maybe only reading data that will not change.

## Slide 74: Avoid Pointer Passing
Tend to copy data into / move data among hardware accelerator memories rather than passing pointers.

## Slide 75: Memory Sequentialization and Data Dependencies
(unlikely to cover in class;
Review on own)

## Slide 76: C Memory Consequence
Expressions and operations through variables (whose address is never taken) can be executed at any time
  Just preserve the dataflow
Memory assignments must execute in strict order
  Ideally: partial order
  Conservatively: strict sequential order of C

## Slide 77: Forcing Sequencing
Demands we introduce some discipline for deciding when operations occur
  Could be a FSM
  Could be an explicit dataflow token
  Callahan (reading) uses control register
Other uses for timing control
  Control
  Variable delay blocks
  Looping

## Slide 78: Scheduled Memory Operations
Source: Callahan

## Slide 79: Hardware/Parallelism Challenge
Can we give enough information to the compiler to
  allow it to reorder?
  allow to put in separate embedded memories (separate banks)?
Is the compiler smart enough to exploit?

## Slide 80: Mux Conversion and Memory
What might go wrong if we mux-converted the following:
if (cond)
  a[i]=0;
else
  b[i]=0;

## Slide 81: Mux Conversion and Memory
What might go wrong if we mux-converted the following:
if (cond)
  a[i]=0;
else
  b[i]=0;
Don’t want memory operations in non-taken branch to occur.

## Slide 82: Mux Conversion and Memory
if (cond)
  a[i]=0;
else
  b[i]=0;
  Don’t want memory operations in non-taken branch to occur.
Conclude: cannot mux-convert blocks with memory operations (without additional care)

## Slide 83: Conditions and Memory
if (cond)
  a[i]=0;
else
  b[i]=0;

## Slide 84: Dependence in Loops
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-1];
If a value needed by one instance of the loop is written by another instance, can create cyclic dependence.
 limit parallelism (pipeline II)

## Slide 85: Dependence in Loops
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-1];
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-2];
Dependence distance same as
# registers in cycle.

## Slide 86: Dependence Fixed/Predictable?
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-1]+Y[i-2];
for(i=0;i<K;i++)
Y[i]=a[i]*Y[b[i]];
If dependence data-dependent, forced to sequentialize.

## Slide 87: Dependence Fixed/Predictable?
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-1]+Y[i-2];
for(i=0;i<K;i++)
Y[i]=a[i]*Y[2*i+3];
If dependence linear, aggressive compliers may be able to resolve.

## Slide 88: Dependence Fixed/Predictable?
for(i=0;i<K;i++)
Y[i]=
a[i]*Y[ceil(sqrt(i)*sin(2i))];
If dependence too complicated, compiler not solve and will force sequential execution.

## Slide 89: Big Ideas
Can specify HW computation in C
Create streaming operations
  Run on processor or FPGA
Vivado HLS gives control over how map to hardware
  Area-time point

## Slide 90: Admin
Reading for Monday
  on web
  and Zynq book
HW5 due Friday
HW6 not out yet
  Hope to have out soon
Midterm on Wednesday, class time
  Review Tuesday office hours