## Slide 1: ESE532: System-on-a-Chip Architecture
Day 13: October 14, 2019
Orchestrating Data in Memories
Midterm:
Average: 55
Std. Dev: 14

## Slide 2: Midterm
Main role is diagnostic
  See where you are
  See what course exams look like
Offer:
  award midterm grade=max(midterm,final)
  Did well on midterm, you have the points
  Didn’t do well … chance to replace with final

## Slide 3: Today
DRAM
DRAM Implications
Tricks for working with DRAM and generally minimizing use of large memories
  Images
  Sort (time permitting)

## Slide 4: Message
How we access data matters
Reuse data to avoid access to large memories
Think about how organize computation and data to minimize
  Use of large memory
  Data movement
…and think about what you expect, so can diagnose unnecessary data bottlenecks

## Slide 5: Day 3: Memory Scaling
Small memories are fast
  Large memories are slow
Small memories low energy
  Large memories high energy
Large memories dense
  Small memories cost more area per bit
Combining:
  Dense memories are slow

## Slide 6: Day 3: Lesson
Cheaper to access wide/contiguous blocks memory
  In hardware
  From the architectures typically build
Can achieve higher bandwidth on large block data transfer
  Than random access of small data items

## Slide 7: DRAM Dynamic Random Access Memory
Usually the largest memory

## Slide 8: Dynamic RAM
Shares even more logic among bits
Share refresh/restoration logic as well
Minimal storage is a capacitor
“Feature” DRAM process is ability to make capacitors efficiently
Denser, but slower

## Slide 9: DRAM
1GB DDR3 SDRAM from Micron
  http://www.micron.com/products/dram/ddr3/
  96 pin pakage
  16b datapath IO
  Operate at 500+MHz
  37.5ns random access latency

## Slide 10: Memory Access Timing
Access:
  Address (RCD)

## Slide 11: Memory Access Timing
Access:
  Address (RCD)
  Row fetch (RP)

## Slide 12: Memory Access Timing
Access:
  Address (RCD)
  Row fetch (RP)
  Column select (CL)

## Slide 13: Memory Access Timing
Access:
  Address (RCD)
  Row fetch (RP)
  Column select (CL)
  writeback/refresh

## Slide 14: Dynamic RAM
Shares even more logic among bits
Share refresh/restoration logic as well
Minimal storage is a capacitor
“Feature” DRAM process is ability to make capacitors efficiently
Denser, but slower

## Slide 15: Memory Access Timing
Access:
  Address (RCD)
  Row fetch (RP)
  Column select (CL)
  writeback/refresh

## Slide 16: Memory Access Timing
Access:
  Address (RCD)
  Row fetch (RP)
  Column select (CL)
  writeback/refresh
Optimization for access within a row

## Slide 17: Memory Access Timing
Access
  Address (RCD)
  Row fetch (RP)
  Column select
    CL: Can repeat
  writeback/refresh
Row 1024b—8192b
Faster to access within row

## Slide 18: Preclass 4
Preclass 4 toy warmup
  Reading n 16b words takes: 10+n cycles
    10 cycles for latency (RCD, RP)
    1 cycle to select each word (CL)
      n cycles for m of them
% time in access latency
  Reading 1 word
  Reading 16 words
  Reading 128 words

## Slide 19: DRAM
1GB DDR3 SDRAM from Micron
  http://www.micron.com/products/dram/ddr3/
  96 pin pakage
  16b datapath IO
  Operate at 500+MHz
  37.5ns random access latency

## Slide 20: DRAM Streaming
Reading row is 2x12.5ns
  (RCD,RP)
16b @ 500MHz
1024b row
1024/16
  64 words per row
How long (ns) to provide full row (64, 16b words) from address?

## Slide 21: DRAM Streaming
Can read from wide memory, but only have 16 pins to bring off chip
But, can clock across those 16 pins at high clock rate compared to memory reference (2ns vs. 12.5ns)
So, can sequentially shift the data out the 16 pins, if grabbing all the data for the row

## Slide 22: DRAM
1GB DDR3 SDRAM from Micron
  http://www.micron.com/products/dram/ddr3/
  96 pin pakage
  16b datapath IO
  Operate at 500+MHz
  37.5ns random access latency

## Slide 23: 1 Gigabit DDR2 SDRAM
[Source: http://www.elpida.com/en/news/2004/11-18.html]

## Slide 24: DIMMS multi-DRAM
DIMMs usually pack multiple DRAM chips, c, in parallel
  Can access c*16b per transfer
  Typically 64, 128, 256b wide
    8 chips = 128b wide
https://commons.wikimedia.org/wiki/File:DIMMs.jpg

## Slide 25: Smart Phone
Will use single DRAM chip
iPhone/iPod – flip chip in package with SoC Processor
Apple APL1W72 A11 Bionic SoC layered over SK Hynix H9HKNNNDBMAUUR 3 GB LPDDR4x RAM
Source:
https://www.ifixit.com/Teardown/iPhone+X+Teardown/98975

## Slide 26: Preclass 1
How many cycles to run loop?
  10 cycle on row change
  3 cycles same row
  128 uint16_b per row (2048b)

## Slide 27: Image Row and DRAM Rows
Address | MSB -- DRAM Row Bytes -- LSB |  |  |  |  |  |  | 
0x027FF0 | [y-1,1023] |  |  |  |  |  |  | 
0x028000 | [y,127] |  |  |  |  |  |  | [y,0]
0x028100 |  |  |  |  |  |  |  | [y,128]
0x028200 |  |  |  |  |  |  |  | 
0x028300 |  |  |  |  |  |  |  | 
0x028400 |  |  |  |  |  |  |  | 
0x028500 |  |  |  |  |  |  |  | 
0x028600 |  |  |  |  |  |  |  | 
0x028700 | [y,1023] |  |  |  |  |  |  | [y,896]
0x028800 |  |  |  |  |  |  |  | [y+1,0]
0x028900 |  |  |  |  |  |  |  | 
0x028a00 |  |  |  |  |  |  |  | 

## Slide 28: Preclass 2
How many cycles to run loop?
  10 cycle on row change
  3 cycles same row
  128 uint16_b per row (2048b)
Note loop
interchange

## Slide 29: Preclass 3
How many cycles to run loop?
  10+n cycles to fetch n<=256 Half-words on row

## Slide 30: DRAM
Latency is large (10s of ns)
Throughput can be high (GB/s)
  If accessed sequentially
  If exploit wide-word block transfers
Throughput low on random accesses
  As we saw for random access on wide-word memory

## Slide 31: Xilinx/SDSoC DMA?
This section focused on what the DRAM can do
  What should happen with an optimized DRAM controller
SDSoC DMA requires setup time
  Which will be in addition to DRAM access time
  High overhead [as you are seeing on HW6]
    Even higher premium for large block transfers

## Slide 32: Maximize Reuse
Minimize need to go to large memory

## Slide 33: Data Management
Large, central memory
  Bottleneck
  High energy
Minimize need to return to it

## Slide 34: Window Filter
Compute based on neighbors
  F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1])
Common idiom
  Image filtering
  Numerical simulation
  Cellular automata
  Search, matching

## Slide 35: Window Filter
Compute based on neighbors
  F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1])
Generalize for different neighborhood sizes
  for (yoff=YMIN; yoff<YMAX;yoff++) for (xoff=XMIN; xoff<XMAX;xoff++) res=fun(res,d[y+yoff][x+xoff]);

## Slide 36: Window Filter
Compute based on neighbors
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++)
  o[y][x]=F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1]);
How work with image in DRAM?
  As written references
  Reads per row

## Slide 37: Window Filter
Compute based on neighbors
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++)
  o[y][x]=F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1]);
Data reused between inner loop invocations when x increments?

## Slide 38: Window Shift x++
 | 23 | 24 | 25 | 26 | 27
17 |  |  |  |  | 
18 |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
19 |  | Y,X-1 | Y,X | Y,X+1 | 
20 |  | Y+1,X-1 | Y+1,X | Y+1,X+1 | 
21 |  |  |  |  | 
 | 23 | 24 | 25 | 26 | 27
17 |  |  |  |  | 
18 |  |  | Y-1,X-1 | Y-1,X | Y-1,X+1
19 |  |  | Y,X-1 | Y,X | Y,X+1
20 |  |  | Y+1,X-1 | Y+1,X | Y+1,X+1
21 |  |  |  |  | 

## Slide 39: Window Filter
Compute based on neighbors
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++)
  o[y][x]=F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1]);
Data reused between y values in outer loop?
  Reuse distance? …assume II=1 pipeline inner loop

## Slide 40: Window Shift y++
 | 23 | 24 | 25 | 26 | 27
17 |  |  |  |  | 
18 |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
19 |  | Y,X-1 | Y,X | Y,X+1 | 
20 |  | Y+1,X-1 | Y+1,X | Y+1,X+1 | 
21 |  |  |  |  | 
 | 23 | 24 | 25 | 26 | 27
17 |  |  |  |  | 
18 |  |  |  |  | 
19 |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
20 |  | Y,X-1 | Y,X | Y,X+1 | 
21 |  | Y+1,X-1 | Y+1,X | Y+1,X+1 | 

## Slide 41: Window Filter
Compute based on neighbors
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++)
  o[y][x]=F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1]);
How much data need to store to hold on to d[y] values that will use again?
Where can we store?

## Slide 42: Line Buffers
Only need to save last 2 (window_height-1) rows (d[y][*])
Store in local buffers
  Type dy[XMAX], dym[XMAX];
    dym for dy minus 1
  Stick value there between uses.

## Slide 43: Variable Naming
 |  | +xm |  | +xp | 
dym |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
dy |  | Y,X-1 | Y,X | Y,X+1 | 
dyp |  | Y+1,X-1 | Y+1,X | Y+1,X+1 | 
 |  | +xm |  | +xp | 
dym |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
dy |  | Y,X-1 | Y,X | Y,X+1 | 
dyp |  | dypxm | dypx | dnew | 

## Slide 44: Window Filter
With line buffers dy, dym
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++) {
  dypxm=dypx; dypx=dnew; dnew=d[y+1][x+1];
  o[y][x]=F(dym[x-1],dym[x],dym[x+1], dy[x-1],dy[x],dy[x+1], dypxm,dypx,dnew);
  dym[x-1]=dy[x-1];
  dy[x-1]=dypxm;
  }

## Slide 45: Lines in Buffers
 |  | +xm |  | +xp | 
dym |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
dy |  | Y,X-1 | Y,X | Y,X+1 | 
dyp |  | Y+1,X-1 | Y+1,X | Y+1,X+1 | 

## Slide 46: Window Filter
With line buffers dy, dym
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++) {
  dypxm=dypx; dypx=dnew; dnew=d[y+1][x+1];
  o[y][x]=F(dym[x-1],dym[x],dym[x+1], dy[x-1],dy[x],dy[x+1], dypxm,dypx,dnew);
  dym[x-1]=dy[x-1];dy[x-1]=dypxm; }
Avoid multiple read dy, dym?
  Save memory ports

## Slide 47: Variable Naming
 |  | +xm |  | +xp | 
dym |  | Y-1,X-1 | Y-1,X | Y-1,X+1 | 
dy |  | Y,X-1 | Y,X | Y,X+1 | 
dyp |  | Y+1,X-1 | Y+1,X | Y+1,X+1 | 
 |  | +xm |  | +xp | 
dym |  | dymxm | dymx | dymxp | 
dy |  | dyxm | dyx | dyxp | 
dyp |  | dypxm | dypx | dnew | 

## Slide 48: Window Filter
Single read and write from dym, dy
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++) {
  dypxm=dypx; dypx=dnew; dnew=d[y+1][x+1];
  dyxm=dyx; dyx=dyxp; dyxp=dy[x+1];
  dymxm=dymx; dymx=dymxp; dymxp=dym[x+1];
  o[y][x]=F(dymxm,dymx,dymxp, dyxm,dyx,dyxp, dypxm,dypx,dnew);
  dym[x-1]=dyxm;dy[x-1]=dypxm; }

## Slide 49: Pipelined Circuit
Single sequential read from big memory (DRAM) per result
Shift registers
Line buffers

## Slide 50: Window Filter
Convert to stream … use Preclass 3 load
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++) {
  dypxm=dypx; dypx=dnew; astream.read(dnew);
  dyxm=dyx; dyx=dyxp; dyxp=dy[x+1];
  dymxm=dymx; dymx=dymxp; dymxp=dym[x+1];
  o[y][x]=F(dymxm,dymx,dymxp, dyxm,dyx,dyxp, dypxm,dypx,dnew);
  dym[x-1]=dyxm;dy[x-1]=dypxm; }

## Slide 51: Window Filter
Convert to stream … use Preclass 3 load
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++) {
  dypxm=dypx; dypx=dnew; astream.read(dnew);
  dyxm=dyx; dyx=dyxp; dyxp=dy[x+1];
  dymxm=dymx; dymx=dymxp; dymxp=dym[x+1];
  ostream.write(F(dymxm,dymx,dymxp, dyxm,dyx,dyxp, dypxm,dypx,dnew));
  dym[x-1]=dyxm;dy[x-1]=dypxm; }

## Slide 52: Multiple Filters
What if want to run multiple filters?
for (f=0;f<FMAX;f++) for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++)
  o[f][y][x]=fun[f](d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1]);
Forces multiple reads through d
Avoidable?

## Slide 53: Take-Away
Can process with a single, streaming read through data in large memory
  Specifically for window filters on images
  General goal to try to achieve
Careful to orchestrate data in small, local buffers
DMA/streaming transfers to achieve near peak DRAM bandwidth

## Slide 54: Sort
Bonus if time permits

## Slide 55: Sort
Order data
  7 3 4 2 1 9 8 0  0 1 2 3 4 7 8 9
Data movement can be challenging
  Last value may become first (vice-versa)
  Especially when not fit in small memories
Many sequential sort solutions access data irregularly
  Want to avoid with DRAM

## Slide 56: Observation: Merge
Merging two sorted list is a streaming operation
Int aptr; int bptr;
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (a[aptr]>b[bptr])
  { o[i]=a[aptr]; aptr++; }
  Else
  { o[i]=b[bptr]; bptr++; }
  Else // copy over remaining from a or b

## Slide 57: Merge using Streams
Merging two sorted list is a streaming operation
Int aptr; int bptr;
astream.read(ain); bstream.read(bin)
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (ain>bin)
  { ostream.write(ain); aptr++; astream.read(ain);}
  Else
  { ostream.write(bin) bptr++; bstream.read(bin);}
  Else // copy over remaining from astream/bstream

## Slide 58: Merge and DRAM
How streaming merge work with DRAM row?
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  if (ain>bin)
  { ostream.write(ain); aptr++; astream.read(ain);}
  else
  { ostream.write(bin) bptr++; bstream.read(bin);}

## Slide 59: Merge and DRAM
First version (repeat below) may alternate between DRAM rows
Int aptr; int bptr;
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (a[aptr]>b[bptr])
  { o[i]=a[aptr]; aptr++; }
  Else
  { o[i]=b[bptr]; bptr++; }
  Else // copy over remaining from a or b

## Slide 60: Merge and DRAM
Want to fetch a as block into local memory, then can do this
Int aptr; int bptr;
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (a[aptr]>b[bptr])
  { o[i]=a[aptr]; aptr++; }
  Else
  { o[i]=b[bptr]; bptr++; }
  Else // copy over remaining from a or b

## Slide 61: Merge using Streams and DRAM
Streaming accomplishes if Streaming is implemented to fetch row into FIFO buffer
Int ptr; int bptr;
astream.read(ain); bstream.read(bin)
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (ain>bin)
  { ostream.write(ain); aptr++; astream.read(ain);}
  Else
  { ostream.write(bin) bptr++; bstream.read(bin);}
  Else // copy over remaining from astream/bstream

## Slide 62: Building from Merge
Know how to get sorted data of length N given two, independently sorted lists of length N/2
If have list of length 1, is it sorted?
Merging two lists of length 1 gives us?
Mergine two lists of length 2 gives us?

## Slide 63: Merge Sort
Strategy
  For i=1 to passes
    Pass over data creating merged sequences of length 2i from pairs of length 2i-1
  What is passes?
Can, at least, limit to passes reads through data from large memory.

## Slide 64: On-chip Merge
As long as can fit sequence (2i) on chip, can stream merge stages without going back to big memory (DRAM)
merge
alternate
2i-1
2i
2i

## Slide 65: On-chip Merge
As long as can fit sequence (2i) on chip, can stream merge stages without going back to big memory (DRAM)
  E.g. with 36Kb BRAMs ~ first 10-12 stages
    Up to ~16 using multiple BRAMs
merge+alt
merge+alt
merge+alt

## Slide 66: On-chip Merge
For sorts up to ~100K elements may be able to cover in one read/write stream to/from DRAM
Larger: ~log2(N)-15 read/writes
merge+alt
merge+alt
merge+alt

## Slide 67: Big Ideas
Must pay attention to orchestrate data movement
  How we access and reuse data
Minimize use of large memories
Regular access to large memories higher performance
  Easier to get bandwidth on wide-word reads

## Slide 68: Admin
Reading for Wednesday on web
HW6 due Friday
  Does include 10 full FPGA builds
    Many can do in parallel
  Plan for that build time
Midterm grade
  Will award midterm grade=max(midterm,final)