## Slide 1: ESE532: System-on-a-Chip Architecture
Day 17: October 28, 2019
Associative Maps, Hash Tables

## Slide 2: Today
Motivation/Reminder
LZW – tree
Associative Memory
  Custom
  FPGA
Software Maps
  Tree
  Hash Tables
Hardware (FPGA) Hash Maps

## Slide 3: Message
Rich design space for Maps
Hash tables are useful tools

## Slide 4: LZW Compression

## Slide 5: Idea
Use data already sent as the dictionary
  Give short names to things in dictionary
  Don’t need to pre-arrange dictionary
  Adapt to common phrases/idioms in a particular document
Day 16 Review
<2,3> short name for “AM ’’
<0,4> short name for “I AM”

## Slide 6: Algorithm Concept
While data to send
  Find largest match in window of data sent
  If length too small (length=1)
    Send character
  Else
    Send <x,y> = <match-pos,length>
  Add data encoded into sent window
Day 16 Review

## Slide 7: Preclass 7
DICT_SIZE comparisons per input character
Day 16 Review

## Slide 8: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
Only check position 0 for “starts with I”

## Slide 9: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
If prefix same, why check redundantly?
  Store things with common prefix together
  Share prefix among substrings
  Represent all strings as prefix tree
Follow prefix trees with fixed work per input character

## Slide 10: Tree Example
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E

## Slide 11: Tree Algorithm
Tree Root for each character
Follow tree according to input until no more match
Send <name of last tree node>
  An <x,y> pair
Extend tree with new character
Start over with this character

## Slide 12: Tree Example
Label with <lastpos,len> pair
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E
<0,1>
<1,2>
<2,3>
<3,4>
<12,4>
<13,5>
<19,4>
<4,5>
<20,5>
T | H | E | N |  | A | N | D |  | T | H | E | R | E | , |  | T | H | E | Y
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
(only showing
Root for ’T’)

## Slide 13: Large Memory Implementation
int encode[SIZE][256];
Name tree node by position in chunk
  lastpos
c is a character
Encode[lastpos][c] holds the next tree node that extends tree node lastpos by c
  Or NONE if there is no such tree node

## Slide 14: Tree Example
Label with <lastpos,len> pair
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E
<0,1>
<1,2>
<2,3>
<3,4>
<12,4>
<13,5>
<19,4>
<4,5>
<20,5>
T | H | E | N |  | A | N | D |  | T | H | E | R | E | , |  | T | H | E | Y
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
encode[2][‘N’]=3
encode[2][‘R’]=12
encode[2][‘Y’]=19
encode[2][‘A’]=NONE
(only showing
Root for ’T’)

## Slide 15: Memory Tree Algorithm
curr – pointer into input chunk
// follow tree
y=0; x=0;
while(encode[x][input[curr+y]]!=NONE)
x=encode[x][input[curr+y]]; y++;
If (y>0)
send <x,y>
else
send input[curr+y]
encode[x][input[curr+y]]=curr+y
curr=curr+y

## Slide 16: Complexity
How much work per character to encode?

## Slide 17: Compact Memory
int encode[SIZE][256];
How many entries in this table are not NONE?

## Slide 18: Compact Memory
int encode[SIZE][256];
Table is very sparse
Store as associative memory
  At most SIZE entries
Look at how to implement associative memories next

## Slide 19: LZW So Far – 4KB chunks
Brute Force
  Needs one byte per byte = 4KB = 1 BRAM
  DICT_SIZE=4096 comparisons per byte
Dense memory encode[SIZE][256]
  Need 2*256B per byte = 512*4KB = 512 BRAMs
  1 comparison and lookup per byte

## Slide 20: Reminder from Last Time

## Slide 21: Associative Memory
Maps from a key to a value
Key not necessarily dense
  Contrast simple RAM
  Cannot afford 2256 word memory
Day 16 Review

## Slide 22: Deduplicate
Compute chunk hash
Use chunk hash to lookup known chunks
  Data already have on disk
  Data already sent to destination, so destination will know
If lookup yields a chunk with same hash
  Check if actually equal (maybe)
If chunks equal
  Send (or save) pointer to existing chunk
Day 16 Review

## Slide 23: Deduplication Architecture
Day 16 Review

## Slide 24: Custom Hardware Associative Memory

## Slide 25: Memory Block Review
Match on address
Select wordline for a row
Reads out a word
Address dense and hardwired
One row for each 2Abits values
width
depth

## Slide 26: Address Blocks
Each address match is AND
width
depth
/A2&/A1&/A0
/A2&/A1&A0

## Slide 27: Address Blocks

## Slide 28: Memory Block Associative
Want address as key
Word is value
Key sparse
Rows<2keybits
Entries<2keybits
Key programmable
width
depth

## Slide 29: Programmable Key
Make row select programmable

## Slide 30: Contrast Assoc. and Dense Memory

## Slide 31: Associative Memory Bank

## Slide 32: Programmable Key
Assoc: 5b key, 8 entries, 8b value
How many memory bits?
Direct: 8 entries, 8b value
How many memory bits?

## Slide 33: Associative Memory Bank
Memory cells = entries*(keybits+valuebits)

## Slide 34: Associative Memory Bank
Will need to be able to write into key
  Another “fixed” decoder to generate key-word line for programming

## Slide 35: Associate Memory Cost
More expensive than equal capacity SRAM memory bank
  Memory cells in decoder
  Need to support write into key

## Slide 36: Associate Memory Cost
Physical associative memory for 4KB LZW Chunk tree encode
  4K entries
  12b output
  12b+8b=20b key
Memory cells assoc.?
Compare direct 4Kx12 memory (cells)?
  How much larger is assoc. for same capacity?
Compare 4096*256 with 12b result for dense LZW case (cells)?
  How much larger to solve same problem

## Slide 37: FPGA
Has BRAMs – normal memories, not associative
36Kb BRAM
  512x72
Can be 9b key  72b value assoc.
  Just using the memory sparsely
Or interpret as programmable decoder with 72 match lines

## Slide 38: Assoc. Mem from BRAM
For wider match
Cover 9b of key with each BRAM
Use 72 output bits to indicate if one of 72 entries match
AND together corresponding entries
Get 72 match bits
Re-encode match bits to lookup value

## Slide 39: BRAM Associative Memory
Previous slide expands match width
How would we expand capacity?

## Slide 40: BRAM Associative Memory

## Slide 41: Associative Memory Cost
Match unit
  Requires 1 BRAM per 9b of key per 72 entries
  (keylen/9b) * (entries/72)
  Asymptotically optimal (keylen*entries)
    But large constants
  LZW
    4K entries
    20b key
    How many BRAMs for match?

## Slide 42: How are these values stored?
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC

## Slide 43: Step 1: Assign each a match bit
match | Key[17:9] | Key[8:0] | Value
0 | 0x001 | 0x014 | 0x01
1 | 0x001 | 0x01 | 0x34
2 | 0x0F0 | 0x014 | 0xE3
3 | 0x0C8 | 0x113 | 0xCC
Memory contents
of each BRAM?

## Slide 44: How Lookup Work?
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC
Lookup 0x214 = 0x001 0x014

## Slide 45: Code Snippet
ap_uint<216> key_low[512];
ap_uint<216> key_high[512];
int value[216];
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
res=value[addr];

## Slide 46: Software Map

## Slide 47: Software Map
Map abstraction
  void insert(key,value);
  value lookup(key);
Will typically have many different implementations

## Slide 48: Preclass 1
For a capacity of 4096
How many memory accesses needed
  When lookup fail?
  When lookup succeed (on average)?

## Slide 49: Tree Map (Preclass 2)
Build search tree
Walk down tree
For a capacity of 4096, assume balanced…
How many tree nodes visited
  When lookup fail?
  When lookup succeed (on average)?

## Slide 50: Tree Map LZW
Each character requires log2(dict) lookups
  12 for 4096
Each internal tree node hold
  Key (20b for LZW), value (12b), and 2 pointers (12b)
  7B
Total nodes 4K*2
Need 14 BRAMs for 4K chunk

## Slide 51: Tree Insert
Need to maintain balance
Doable with O(log(N)) insert
  Tricky
  See Red-Black Tree
    https://en.wikipedia.org/wiki/Red–black_tree
    https://www.geeksforgeeks.org/red-black-tree-set-1-introduction-2/

## Slide 52: High Performance Map
Would prefer not to search
Want to do better than log2(N) time
Direct lookup in arrays (memory) is good…

## Slide 53: Hash Table
Attempt to turn into direct lookup
Compute some function of key
  A hash
Perform lookup at that point
If hash maps a single entry (or no entry)
  Great, got direct lookup
    Like sparse table case
hash
Mem
key
value

## Slide 54: Preclass 3a
Average number of entries per hash when N > HASH_CAPACITY?
  Concrete example
    N= 4096
    HASH_CAPACITY=256

## Slide 55: Hash Table
Attempt to turn into direct lookup
Compute some function of key
  A hash
Perform lookup at that point
Typically, prepared for several keys to map to same hash  call it a bucket
  Keep list or tree of things in each bucket
hash
Mem
key
value

## Slide 56: Hash Table
Compute some function of key
  A hash
Perform lookup at that point
Find bucket with small number of entries
  Searching that bucket easier
  …but no absolute guarantee on maximum bucket size
hash
Mem
key
value

## Slide 57: Preclass 3b
Probability of conflict if N<<HASH_CAPACITY ?
  Concrete example
    N=4096
    HASH_CAPACITY=409600
Impact of HASH_CAPACITY on average bucket size?

## Slide 58: Preclass 4
m | 0 | 1 | 2 | 3 | 4+
C=1024 | 0.37 |  |  |  | 
C=2048 |  |  |  |  | 
C=4096 |  |  |  |  | 
N=1024

## Slide 59: Preclass 4
m | 0 | 1 | 2 | 3 | 4+
C=1024 | 0.37 | 0.37 | 0.18 | 0.061 | 0.019
C=2048 | 0.60 | 0.30 | 0.076 | 0.013 | 0.0017
C=4096 | 0.78 | 0.19 | 0.024 | 0.0020 | 0.00013
N=1024

## Slide 60: Hash
Can tune hash parameters to control distribution
Spend more memory  smaller buckets  less work finding things in buckets
  Memory-Time tradeoff
Still have possibility of large buckets
…but probability is low

## Slide 61: Idea
Hash mostly works
Engineer hash to hold most cases
  Combination of
    sparcity (entries>N)
    Hold multiple entries per hash value
Few cases that overflow
  Store in small fully associative memory

## Slide 62: Hybrid Hash+Assoc.

## Slide 63: LZW 4K Chunk Hybrid
72 entry assoc. matcn
  needs 3 match BRAMs + 1 data BRAM
  Associative match 20b key
  72 entries (72/4096=1.7% for 4096)
So, can hold ~1% conflicts in 4K hash
Hash N=4096, C=16384, m=2, store 3
  Prob 3+: <1% (see table 1024, 4096)
  20b key+12b value=4B per entry
  16384*3*4B=4*3*4 BRAMs
48+4=52 BRAMs

## Slide 64: Further Optimization
Previous example illustrative
  Not necessarily optimal (explore parameters)
May be able to do better with multiple hashes
  See Dhawan reading paper
  May need to use that design in hybrid configuration with assoc. memory like previous example

## Slide 65: 4K Chunk LZW Search
 | BRAMs | Operations
Brute Search | 1 | 4K
Tree with Dense RAM | 512 | 1
Tree with Full Assoc | 175 | 1
Tree with Tree | 14 | 12
Tree with Hybrid | 52 | 1
36Kb BRAMs on ZU3EG = 216

## Slide 66: Big Ideas
Sparse, near O(1) Map access  Hash Table
Rich design space for engineering associative map solutions

## Slide 67: Admin
First project milestone due Friday
  Including teaming