## Slide 1: ESE532: System-on-a-Chip Architecture
Day 21: November 11, 2019
Energy

## Slide 2: Today
Energy
Today’s bottleneck
What drives
Efficiency of
  Processors, FPGAs, accelerators
How does parallelism impact energy?

## Slide 3: Message
Energy dominates
  Including limiting performance
Make memories small and wires short
  Small memories cost less energy per read
Accelerators reduce energy
  Compared to processors
Can tune parallelism to minimize energy
  Typically, the more parallel implementation costs less energy

## Slide 4: Energy
Growing domain of portables
  Less energy/op  longer battery life
Global Energy Crisis
Power-envelope at key limit
  E reduce  increase compute in P-envelope
  Scaling
    Power density not transistors limit sustained ops/s
  Server rooms
    Cost-of-ownership not dominated by Silicon
      Cooling, Power bill

## Slide 5: Preclass 1--4
200K gates/mm2
5*10-15 J/gate switch
Gates on 1cm2
Energy to switch all?
Power at 1GHz?
Fraction can switch with 10W/cm2 power budget?

## Slide 6: Challenge: Power

## Slide 7: Origin of Power Challenge
Limited capacity to remove heat
  ~100W/cm2 force air
  1-10W/cm2 ambient
Transistors per chip grow at Moore’s Law rate = (1/F)2
Energy/transistor must decrease at this rate to keep constant power density
P/tr  CV2f
E/tr  CV2
  …but V scaling more slowly than F

## Slide 9: Intel Power Density

## Slide 10: Impact
Source: Carter/Intel
10
Power Limits Integration
Chart: 
| 45nm | 32nm | 22nm | 16nm | 11nm
Density Limit | 40.6041 | 55.275 | 82.5043 | 123.1472 | 183.8115
Constant Power Limit | 40.6041 | 55.275 | 79.2765 | 98.3736 | 122.0708

## Slide 11: Impact
Power density is limiting scaling
  Can already place more transistors on a chip than we can afford to turn on!
Power is potential challenge/limiter for all future chips.
  Only turn on small percentage of transistors?
  Operate those transistors at much slower frequency?

## Slide 12: Energy

## Slide 13: Leakage Energy
Ileak
  Subthreshold leakage
  (possibly) Gate-Drain leakage

## Slide 14: Switching Energy
C – driven by architecture
V – today, driven by variation, aging
a – driven by architecture, coding/information

## Slide 15: Energy

## Slide 16: Voltage
We can set voltage
Reducing voltage
  Reduces Eswitch
  Increases delay  cycle time, T
  Increases leakage

## Slide 17: Total Energy vs. Voltage

## Slide 18: Switching Energy
C – driven by architecture
  Also impacted by variation, aging
V – today, driven by variation, aging
a – driven by architecture, information

## Slide 19: Data Dependent Activity
Consider an 8b counter
  How often do each of the following switch?
    Low bit?
    High bit?
  Average switching across all 8 output bits?
Assuming random inputs
  Activity at output of xor4?
    Hint: probability of output of xor4 being 0? 1?
  Activity at output of nand4?

## Slide 20: Gate Output Switching (random inputs)
Prev.
Next
0
1
Pswitch=P(0@i)*P(1@i+1)
+P(1@i)*P(0@i+1)

## Slide 21: Switching Energy
Ci == capacitance driven by each gate (including wire)

## Slide 22: Switching Rate (ai) Varies
Different logic (low/high bits, gate type)
Different usage
  Gate off unused functional units
Data coded
Entropy in data
Average a 5--15% plausible

## Slide 23: Switching Energy
C – driven by architecture
V – today, driven by variation, aging
a – driven by architecture, information

## Slide 24: Wire Driven
Gates drive
  Self
  Inputs to other gates
  Wire routing between self and other gates
Typically:

## Slide 25: Wire Capacitance
How does wire capacitance relate to wire length?

## Slide 26: Wire Capacitance
C=eA/d = eW*Lwire/d = Cunit * Lwire
Wire capacitance is linear in wire length
E.g. 1.7pF/cm (preclass)
Remains true if buffer wire
  Add buffered segment at fixed lengths
  [different use of word buffer than normal in this class – here we’re talking about adding a repeater to perform electrical signal restoration]

## Slide 27: Wire Driven Implications
Care about locality
  Long wires are higher energy
  Producers near consumers
  Memories near compute
  Esp. for large ai’s
Care about size/area
  Reduce (worst-case) distance must cross
Care about minimizing data movement
  Less data, less often, smaller distances
Care about size of memories

## Slide 28: Preclass 5
Primary switching capacitance in wires
C: How does energy of a read grow with capacity (N) of a memory bank?
D: Energy per bit?

## Slide 29: Memory Implications
Memory energy can be expensive
Small memories cost less energy than large memories
  Use data from small memories as much as possible
Cheaper to re-use data item from register than re-reading from memory

## Slide 30: Architectural Implications

## Slide 31: Component Numbers
[Dally, March 2004 ACM Queue]

## Slide 32: Component Numbers
Processor instruction 100x more than arithmetic
Register read 2x
RAM read 10x
Why processor instruction > arith operation?
[Dally, March 2004 ACM Queue]

## Slide 33: Processors and Energy
Very little into actual computation
Determine and Fetch Instruction
Read and Write data from memories
[Dally et al. /
Computer 2008]

## Slide 34: ARM Cortex A9
Estimate find: 0.5W at 800MHz in 40nm
0.5/0.8 x 10-9 J/instr
~600pJ/instr
Scale to 28nm
  maybe 0.7*600—0.5*600
  300—400pJ/instr ?
Is superscalar w/ neon, so not as simple a processor as previous example

## Slide 35: Zynq (7-series, 28nm)
ARM A9 instruction 300—400pJ
ARM A9 L1 cache read 23pJ
Xilinx UG585 – Zynq TRM

## Slide 36: Compare
Assume ARM Cortex A9 executes 4x32b Neon vector add instruction for 300pJ
Compare to 32b adds on FPGA?

## Slide 37: Compare
Assume ARM Cortex A9 executes 8x16b Neon vector multiply instruction for 300pJ
Compare to 16x16 multiplies on FPGA?

## Slide 38: Programmable Datapath
Performing an operation in a pipelined datapath can be orders of magnitude less energy than on a processor
  ARM 300pJ vs. 1.3pJ 32b add
  Even neon 300pJ vs. 4x1.3pJ for 4x32b add
  300pJ vs. 8x8pJ for 8 16x16b multiplies

## Slide 39: Zynq
Reading from OCM order of magnitude less than from DRAM
…and BRAM half that
Xilinx UG585 – Zynq TRM

## Slide 40: FPGA vs. Std Cell Energy
90nm
FPGA: Stratix II
STMicro CMOS090
[Kuon/Rose TRCADv26n2p203--215 2007]

## Slide 41: FPGA Disadvantage to Custom
Interconnect Energy
  Long wires  more capacitance  more E
  Switch Energy is an overhead
[Tuan et al./FPGA 2006]

## Slide 42: Simplified Comparison
Processor two orders of magnitude higher energy than custom accelerator
FPGA accelerator in between
  Order of magnitude lower than processor
  Order of magnitude higher than custom

## Slide 43: Parallelism and Energy

## Slide 44: Preclass 6
Energy
  Per read from M=106 memory?
  Per read from 106/4 memory?

## Slide 45: Local Consumption
To exploit, we must consume the data local to the memory.

## Slide 46: Cheat?
What if we broke the memory into 4 blocks, but still routed to a single processor?
  Hint: Interconnect energy reading from top right?

## Slide 47: Cheat?
E=Emem(M/4) + 2*sqrt(M/4)*Cwire
(simplify assume 2Cwire~= unit)
E=sqrt(M/4) + sqrt(M/4) ≅ sqrt(M)

## Slide 48: Cheat?
Near mem = E(M/4)=(1/2) sqrt(M)
Far mem = sqrt(M) [previous slide]
Other two = E(M/4)+sqrt(M/4)*Cwire = (1/2+1/4)sqrt(M)
Average:
  Sqrt(M)*(1/4)(1/2+2*3/4+1)
  = ¾ sqrt(M)

## Slide 49: Exploit Locality
Must consume data near computation

## Slide 50: Inter PE Communication
May need to communicate between parallel processing elements [PEs] (and memories)
Must pay for energy to move data between PEs

## Slide 51: Preclass 7
Energy: Read 4 memories 106/4, route 4x4 crossbar, write 4 106/4 memories?
Energy: 4 reads from 106 memory, 4 writes from 106 memory?

## Slide 52: Parallel Larger
More parallel design
  Has more PEs
  Adds interconnect
Total area > less parallel design
  More area  longer wires  more energy in communication between PEs
Could increase energy!

## Slide 53: Continuum Question
Where do we minimize total energy?
  Both memory and communication
Design axis P – number of PEs
  What P minimizes energy?

## Slide 54: Simple Model
Emem=sqrt(M)
Communication = Exbar(I,O)=4*I*O
P Processors
N total data
Possibly communicate each result to other PEs

## Slide 55: Simple Model: Memory
Divide N data over P memories
Emem=sqrt(N/P)
N total memory operations
Memory energy: N*sqrt(N/P)
Memory energy decrease with P

## Slide 56: Simple Model: Communication
Crossbar with P inputs and P outputs
Exbar=4*P*P
Crossbar used N/P times
Crossbar energy: 4*N*P
Communication energy increase with P

## Slide 57: Simple Model

## Slide 58: Preclass 8
For N=106
Per operation becomes:

## Slide 59: Preclass 8
Energy for:
  P=1
  P=4
  P=100
Energy minimizing P?
  Energy?

## Slide 60: Graph

## Slide 61: High Locality
If communication is local, don’t need crossbar
Communication energy scales less than P2
Can scale as low as P

## Slide 62: Model for High Locality
Ecomm=constant
Ecomm=10
Total comm:
  N*10

## Slide 63: Preclass 9
What is energy minimizing P?

## Slide 64: Task Locality Matters
Optimal P depends on communication locality
  Very local problems always benefit from parallelism
  Highly interconnected problems must balance energies  intermediate parallelism

## Slide 65: Tune Parallelism: Stratix-IV
[Kadric, FPGA 2015]

## Slide 66: PE Scaling with Problem Size
[Kadric, TRETS 2016]

## Slide 67: Power vs. Energy
Notice: main comparisons are energy for operation
  Not power
Power is rate of energy use
  Can slow down clock to reduce power
  Power alone doesn’t tell us energy requirement or energy efficiency
    Need to also know time
Most questions on project are about energy

## Slide 68: Big Ideas
Energy dominance
With power-density budget
  The most energy efficient architecture delivers the most performance
Make memories small and wires short
SoC, accelerators reduce energy by reducing processor instruction execution overhead
Parallel design exploit localityreduce energy
Optimal parallelism for problem
  Driven by communication structure, size

## Slide 69: Admin
P3 I/O and Energy Milestone
  Due Friday