## Slide 1: ESE532: System-on-a-Chip Architecture
Day 22: November 13, 2019
VLIW
(Very Long Instruction Word Processors)

## Slide 2: Today
VLIW (Very Large Instruction Word)
Exploiting Instruction-Level Parallelism (ILP)
Demand
Basic Model
Costs
Tuning

## Slide 3: Message
VLIW as a Model for
  Instruction-Level Parallelism (ILP)
  Customizing Datapaths
  Area-Time Tradeoffs

## Slide 4: Register File
Small Memory
Usually with multiple ports
  Ability to perform multiple reads and writes simultaneously
Small
  To make it fast (small memories fast)
  Multiple ports are expensive
Day 6

## Slide 5: Preclass 1
Cycles per multiply-accumulate
  Spatial Pipeline
  Processor

## Slide 6: Preclass 1
How different?
  Resources
    Number of units can perform adds
    Number of simultaneous memory reads
  Ability to use resources
    What resources can use in same cycle

## Slide 7: Computing Forms
Processor – does one thing at a time
Spatial Pipeline – can do many things, but always the same
Vector – can do the same things on many pieces of data

## Slide 8: In Between
What if…
Want to
  Do many things at a time (ILP)
  But not the same (DLP)

## Slide 9: In Between
What if…
Want to
  Do many things at a time (ILP)
  But not the same (DLP)
Want to use resources concurrently

## Slide 10: In Between
What if…
Want to
  Do many things at a time (ILP)
  But not the same (DLP)
Want to use resources concurrently
Want to
  Accelerate specific task
  But not go to spatial pipeline extreme

## Slide 11: VLIW Feature: Supply Independent Instructions
Provide instruction per ALU (resource)
Instructions more expensive than Vector
  But more flexible

## Slide 12: VLIW
The “instruction”
  The bits controlling the datapath
…becomes long
Hence:
  Very Long Instruction Word (VLIW)
long
instruction

## Slide 13: Control Heterogeneous Units
Control each unit simultaneously and independently
  More expensive than processor
    Memory ports and/or interconnect
  But more parallelism

## Slide 14: VLIW
Very Long Instruction Word
Set of operators
  Parameterize number, distribution (X, +, sqrt…)
    More operators less time, more area
    Fewer operators more time, less area
Memories for intermediate state
+
X
X

## Slide 15: VLIW
Very Long Instruction Word
Set of operators
  Parameterize number, distribution (X, +, sqrt…)
    More operators less time, more area
    Fewer operators more time, less area
Memories for intermediate state
Memory for “long” instructions
+
X
X
Address
Instruction
Memory

## Slide 16: VLIW
+
X
X
Address
Instruction
Memory

## Slide 17: VLIW
Very Long Instruction Word
Set of operators
  Parameterize number, distribution (X, +, sqrt…)
    More operators less time, more area
    Fewer operators more time, less area
    Continuum for operator allocation
Memories for intermediate state
Memory for “long” instructions
General framework for specializing to problem
  Wiring, memories get expensive
  Opportunity for further optimizations
General way to tradeoff area and time

## Slide 18: VLIW
+
X
X
Address
Instruction
Memory

## Slide 19: VLIW w/ Multiport RF
Simple, full-featured model use common Register File
  Memory(Words, WritePorts, ReadPorts)

## Slide 20: Processor Unbound
Can (design to) use all operators at once

## Slide 21: Processor Unbound
Schedule Preclass 1 on this VLIW

## Slide 22: Schedule
Cycle | Branch | ALU | Multiply | LD/ST
0 |  | Sub r2,r1,r3 |  | 
1 | Bzneq r3,end | Add r4 |  | 
2 |  | Add r5 |  | Ld r4,r6
3 |  |  |  | Ld r5,r7
4 |  | Add r1,#1,r1 | Mpy r7,r8,r8 | 
5 | B top | Add r7,r8,r8 |  | 

## Slide 23: VLIW Operator Knobs
Choose collection of operators and the numbers of each
  Match task
  Tune resources

## Slide 24: Schedule
Choose collection of operators and the numbers of each
  Match task
  Tune resources
What operator might we add
to accelerate this loop?
Cycle | Branch | ALU | Multiply | LD/ST
0 |  | Sub r2,r1,r3 |  | 
1 | Bzneq r3,end | Add r4 |  | 
2 |  | Add r5 |  | Ld r4,r6
3 |  |  |  | Ld r5,r7
4 |  | Add r1,#1,r1 | Mpy r7,r8,r8 | 
5 | B top | Add r7,r8,r8 |  | 

## Slide 25: Preclass 2a
res[i]=sqrt(x[i]*x[i]+y[i]*y[i]+z[i]*z[i]);
II with one operator of each?

## Slide 26: Schedule
Cycle | LD | ST | Multiply | Add | incr | sqrt
0 |  |  |  | i<MAX | &X[i] | 
1 | X[i] |  |  |  | &Y[i] | 
2 | Y[i] |  | X[i]*X[i] |  | &Z[i] | 
3 | Z[i] |  | Y[i]*Y[i] |  |  | 
4 |  |  | Z[i]*Z[i] | X2+Y2 |  | 
5 |  |  |  | (X2+Y2)+Z2 |  | 
6 |  |  |  |  |  | Sqrt()
7 |  | Res[i] |  |  | i | 

## Slide 27: Preclass 2b
res[i]=sqrt(x[i]*x[i]+y[i]*y[i]+z[i]*z[i]);
Minimum II achievable?
  Latency lower bound

## Slide 28: Critical Path
(Increment pointers / branch)
Load
Multiplies
Add
Add
Squareroot
Writeback

## Slide 29: Preclass 2c
res[i]=sqrt(x[i]*x[i]+y[i]*y[i]+z[i]*z[i]);
How many operators of each type to achieve minimum II (latency lower bound)?

## Slide 30: Schedule w/ 2c Resources
 | LD | LD | ST | * | * | + | i | i | sqrt
0 |  |  |  |  |  | < | &x | &y | 
1 | X[i] | Y[i] |  |  |  |  | &z |  | 
2 | Z[i] |  |  | x | y |  |  |  | 
3 |  |  |  | z |  | x+y |  |  | 
4 |  |  |  |  |  | +z |  |  | 
5 |  |  |  |  |  |  |  |  | sqrt
6 |  |  | Res[i] |  |  |  | i |  | 

## Slide 31: Schedule w/ 2d Resources
 | LD | LD | LD | ST | * | * | * | + | i | i | i | sqrt
0 |  |  |  |  |  |  |  | < | &x | &y | &z | 
1 | X[i] | Y[i] | Z[i] |  |  |  |  |  |  |  |  | 
2 |  |  |  |  | x | y | z |  |  |  |  | 
3 |  |  |  |  |  |  |  | X+y |  |  |  | 
4 |  |  |  |  |  |  |  | +z |  |  |  | 
5 |  |  |  |  |  |  |  |  |  |  |  | sqrt
6 |  |  |  | Res[i] |  |  |  |  | i |  |  | 
What is disappointing about this schedule?

## Slide 32: Preclass 2d
res[i]=sqrt(x[i]*x[i]+y[i]*y[i]+z[i]*z[i]);
res[i+1]=sqrt(x[i+1]*x[i+1]+y[i+1]*y[i+1]+z[i+1]*z[i+1]);
res[i+2]=sqrt(x[i+2]*x[i+2]+y[i+2]*y[i+2]+z[i+2]*z[i+2]);
res[i+3]=sqrt(x[i+3]*x[i+3]+y[i+3]*y[i+3]+z[i+3]*z[i+3]);
Schedule

## Slide 33: Unroll 4
 | LD | LD | LD | ST | * | * | * | + | + | i | i | i | sqrt
0 |  |  |  |  |  |  |  | < |  | x0 | y0 | z0 | 
1 | x0 | y0 | z0 |  |  |  |  |  |  | x1 | y1 | z1 | 
2 | x1 | y1 | z1 |  | x0 | y0 | z0 |  |  | x2 | y2 | z2 | 
3 | x2 | y2 | z2 |  | x1 | y1 | z1 | xy0 |  | x3 | y2 | z3 | 
4 | x3 | y2 | z3 |  | x2 | y2 | z2 | xy1 | +z0 |  |  |  | 
5 |  |  |  |  | x3 | y2 | z3 | xy2 | +z1 |  |  |  | 0
6 |  |  |  | 0 |  |  |  | xy3 | +z2 |  |  |  | 1
7 |  |  |  | 1 |  |  |  |  | +z3 |  |  |  | 2
8 |  |  |  | 2 |  |  |  |  |  |  |  |  | 3
9 |  |  |  | 3 |  |  |  |  |  | i |  |  | 

## Slide 34: Time Points
4 iterations in 10 cycles = 2.5 cycles/iter
Compared to 1 iteration in 7
Compared to 1 iteration in 8

## Slide 35: Preclass 2e
res[i]=sqrt(x[i]*x[i]+y[i]*y[i]+z[i]*z[i]);
Area comparison?

## Slide 36: Data Storage and Movement

## Slide 37: Multiport RF
Multiported memories are expensive
  Need input/output lines for each port
  Makes large, slow
Simplified preclass model:
  Area(Memory(n,w,r))=n*(w+r+1)/2

## Slide 38: Alternate: Crossbar (Xbar)
Provide programmable connection between all sources and destinations
Any destination can be connected to any single source
Day 11

## Slide 39: Preclass 3
Operator area?
Xbar(5,1) area
Memory area, each case
Total area
How does area of memories, xbar compare to datapath operators in each case?

## Slide 40: Split RF Cheaper
At same capacity, split register file cheaper
  2R+1W  2 per word
  5R+10W  8 per word

## Slide 41: Split RF
Xbar(5,5) cost?
Total Area?

## Slide 42: Split RF Full Crossbar
Cycles each for: (A*B+C)/(D*E+F)
  Assume A..F start as shown
A,B
D,E
C
F

## Slide 43: VLIW Memory Tuning
Can select how much sharing or independence in local memories

## Slide 44: Split RF, Limited Crossbar
What limitation does the one crossbar output pose?
  Cycles for same task: (A*B+C)/(D*E+F)
A,B
D,E
C
F
A,B
D,E
C
F

## Slide 45: VLIW Schedule
Need to schedule Xbar output(s) as well as operators.
cycle | * | * | + | + | / | Xbar
0 |  |  |  |  |  | 
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 

## Slide 46: VLIW Interconnect Tuning
Can decide how rich to make the interconnect
  Number of outputs to support
  How to depopulate crossbar
  Use more restricted network

## Slide 47: Commercial: Xilinx AI Engine
6-way VLIW Vector
https://www.xilinx.com/support/documentation/white_papers/wp506-ai-engine.pdf
Xilinx WP506

## Slide 48: VLIW vs. SuperScalar
Modern, high-end proc. (incl. ARM on Zynq)
  Do support ILP
  Issue multiple instructions per cycle
  …but, from a single, sequential instruction stream
SuperScalar – dynamic issue and interlock on data hazards – hide # operators
  Must have shared, multiport RF
VLIW – offline scheduled
  No interlocks, allow split RF
  Lower area/operator – need to recompile code

## Slide 49: Big Ideas:
VLIW as a Model for
  Instruction-Level Parallelism (ILP)
  Customizing Datapaths
  Area-Time Tradeoffs
Customize VLIW
  Operator selection
  Memory/register file setup
  Inter-functional unit communication network

## Slide 50: Admin
P4 out
P3 due Friday

## Slide 51: Loop Overhead
Bonus slides:
not expect to cover in lecture

## Slide 52: Loop Overhead
Can handle loop overhead in ILP on VLIW
  Increment counters, branches as independent functional units

## Slide 53: VLIW Loop Overhead
Can handle loop overhead in ILP on VLIW
…but paying a full issue unit and instruction costs overhead

## Slide 54: Zero-Overhead Loops
Specialize the instructions, state, branching for loops
  Counter rather than RF
  One bit to indicate if counter decrement
  Exit loop when decrement to 0

## Slide 55: Simplification

## Slide 56: Zero-Overhead Loop Simplify
Share port – simplify further

## Slide 57: Zero-Overhead Loop Example (preclass 1)
repeat r3:
addi r4,#4,r4;
addi r5,#4,r5; ld r4,r6
ld r5,r7
mul r6,r7,r7
add r7,r8,r8

## Slide 58: Zero-Overhead Loop
Potentially generalize to multiple loop nests and counters
Common in highly optimized DSPs, Vector units

## Slide 59: Pipelined VLIW Operators

## Slide 60: Pipelined Operators
Often seen, will have pipelined operators
  E.g. 3 cycles multiply
How complicate?

## Slide 61: Accommodating Pipeline
Schedule for when data becomes available
  Dependencies
  Use of resources
cycle | * | * | + | + | / | Xbar
0 | X*X |  |  |  |  | 
1 | Y*Y |  |  |  |  | 
2 |  |  |  |  |  | X*X
3 |  |  |  |  |  | Y*Y
4 |  |  | X2+Y2 |  |  | X2+Y2
5 |  |  |  |  | X2+Y2/Z | 
6 |  |  |  |  |  | 

## Slide 62: Accommodating Pipeline
Schedule for when data becomes available
  Dependencies
  Use of resources
cycle | * | * | + | + | / | Xbar
0 | X*X |  |  |  |  | 
1 | Y*Y |  |  |  |  | 
2 |  |  |  |  |  | X*X
3 |  |  | Q+R |  |  | Y*Y,Q+R
4 |  |  | X2+Y2 |  |  | X2+Y2
5 |  |  |  |  | X2+Y2/Z | 
6 |  |  |  |  |  | 
Impossible
schedule;
Conflict on
single Xbar
output