## Slide 1: ESE532: System-on-a-Chip Architecture
Day 23: November 18, 2019
Estimating Chip Area and Costs

## Slide 2: Today
Chip Costs from Area
Chip Area
  IO
  Interconnect – Rent’s Rule
  Infrastructure
Some Areas
  CACTI – for modeling memories

## Slide 3: Message
First order:
  Chip cost proportional to Area
  Area = Sum(Area(Components))
But appreciate the simplification:
  Yield makes cost superlinear in area
  I/O, Interconnect, infrastructure
    Can make Area > Sum(Area(Components))

## Slide 4: Wafer Cost
Incremental cost of producing a silicon wafer is fixed for a given technology
  Independent of the specific design
  E.g. $4,000
Can fill wafer with copies of chip
By German Wikipediabiatch, original upload 7.
Okt 2004 by Stahlkocher de:Bild:Wafer 2 Zoll bis 8 Zoll.jpg,
CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=928106

## Slide 5: 16nm Wafer Costs
Source: https://www.eetimes.com/author.asp?section_id=36&doc_id=1329887

## Slide 6: Preclass 1
Rough cost per mm of silicon?
  $4000 for 300mm wafer

## Slide 7: Implication
Raw silicon die cost is roughly proportional to area
  Larger the die, the fewer we get on the wafer

## Slide 8: …but
Limits to how big we can make chips
  Manufactures are prepared to create
  Can be reliably manufactured
…and how small we can make chips
  I/O pads
  Cutting/handling/marking

## Slide 9: Imaging
Limit to how large optical imaging supports
Reticle – imagable region for photo lithography
  Around 600mm2
Source
https://www.asml.com/the-asml-exposure-apparatus-is-the-most-expensive-and-complex-step-in-the-chip-fabrication-process-what-is-involved-in-the-lithography-business/ja/s28145?rid=44709

## Slide 10: Yield
Chips won’t be manufactured perfectly
  Dust particles can impact imaging
  Manufacturing processes are statistical
If chips must be defect-free,
  larger chips are more likely to have defects than smaller chips

## Slide 11: Simple Yield Model
Probability of a region being perfect
  E.g. probability of one sq. mm being defect-free
Chip yields if its entire area is defect free
(look at how to tolerate defects in a couple of weeks)

## Slide 12: Chip Yield
P = defect-free probability per sq. mm
What is probability a chip of A sq. mm yields (symbolic) ?

## Slide 13: Preclass 2
P=0.99
Probability of yield for
  10 mm2, 50 mm2, 100 mm2, 500 mm2

## Slide 14: Yielded Die
For a yield rate, Y, how many raw die need to manufacture per yielded die?

## Slide 15: Preclass 3
P=0.99
Die cost for:
  10 mm2, 50 mm2, 100 mm2, 500 mm2

## Slide 16: Yielded Die Cost

## Slide 17: Yielded Die Cost
Ultimately exponential in Area
Means
  Expensive above knee in exponential curve
  Close to linear below knee in curve
E.g.
  Below PA=0.5
    effect of Yield term is less than 2

## Slide 18: Design Dependent Cost
P can be design dependent
  More aggressive designs have higher defect rates
  Can tune design to ease manufacturing
Contrast with point that wafer manufacture cost independent of design

## Slide 19: Slightly Fuller Story
Chip cost = die + test + package

## Slide 20: Test
Testing costs proportional to test time
  Time on expensive test unit
  Depends on complexity of tests need to run
    Can motivate spending silicon area on on-chip test structures to reduce
Can dominate on small chips or complex testing

## Slide 21: Packaging
Pay for density and performance

## Slide 22: Plastic Packages
Simple plastic packages cheap
  Limited number of pins
    Limited to perimeter
  Limited heat removal (few Watts)
  Can be large (due to pins)
  Higher inductance on pins
http://wiki.electroons.com/doku.php?id=ic_packages

## Slide 23: Ceramic Packages
Better thermal characteristics
  Add heat-sink, tolerate hotter chips
    To 100 W
  More pins
  More expensive
Source: https://www.ngkntk.co.jp/english/product/semiconductor_packages/htcc.html

## Slide 24: Flip Chip Packages
Support Area-IO
  More, denser pins
  Smaller die if IO limited
  Lower inductances
  Smaller packaged chip
Source: http://mantravlsi.blogspot.com/2014/10/flip-chip-and-wire-bonding.html

## Slide 25: Flip Chip I/O
Source: https://en.wikipedia.org/wiki/Flip_chip

## Slide 26: Zynq Land Grid Package
SBVA 484 – flip chip, Ball-Grid Array (UG 1075)

## Slide 27: Don’t Forget NRE
This is all about recurring costs
Cost = RecurringCost + (NRE/NumParts)
NRE
  Mask costs in millions
  Design costs in 10s to 100s of millions

## Slide 28: Bonus: Chip Design Costs
https://wccftech.com/apple-5nm-3nm-cost-transistors/

## Slide 29: Putting Together
100mm2 die -- $5.6 raw
  Maybe $6--16 yielded -- call it $7
NRE $100 M -- $1
  Sell 100 M units
Put in $1 packge -- $1
Test -- $1
Total: $10

## Slide 30: Price vs. Cost
…and this is all about cost
  What it takes to manufacture
Price
  What people will pay for it
Profit = Price - Cost

## Slide 31: Area

## Slide 32: Area
Simple story
  Sum up component areas

## Slide 33: Too Simplistic
Area may be driven by
  I/O
  Interconnect
Will need to pay for infrastructure
  Clocking, Power

## Slide 34: I/O Pads
Must go on edge for wire bonding
  Esp. for cheap packages
Source: https://commons.wikimedia.org/wiki/File:DIP_package_sideview.PNG
Src: http://en.wikipedia.org/wiki/File:Wirebonding2.svg

## Slide 35: Pad Ring
Pads must go on side of chip
Pad spacing large to permit bonding
I/O pads may set lower bound on chip size

## Slide 36: Preclass 4
400 pads
25mm pad spacing
Square chip dimensions?

## Slide 37: I/O Limits
Perimeter grows as 4s
Area grows as s2
Area grows (NumIO/4)2
IO may drive chip area

## Slide 38: Area I/O
Put I/O in grid over chip
I/O pads still large and take up space
Avoid perimeter scaling
Requires more expensive flip-chip package

## Slide 39: Flip Chip, Area IO
www.microwavejournal.com
http://www.izm.fraunhofer.de/en/abteilungen/high_density_interconnectwaferlevelpackaging/arbeitsgebiete/arbeitsgebiet1.html

## Slide 40: Interconnect
Long wires need buffering
Buffers take up space
  Weren’t in simple accounting of logic and memory blocks

## Slide 41: Interconnect
Wires take up space
Similar issue to pad I/O
  Wires crossing into region grow as perimeter
  Logic inside grows as area
Region size may be dictated by wires entering/leaving

## Slide 42: Wiring Requirements
Wires 50nm pitch
Gates 500nm on side
  (500nm x 500nm)
How many wires fit across the side of one gate?

## Slide 43: Wiring Requirements
Wires 50nm pitch
Gates 500nm on side
  (500nm x 500nm)
Wires/gate side (prev slide)
If have SxS gate on left, how many wires can cross over the line of S gates at the right?
What if need more wires to cross to right?

## Slide 44: Bisection Width
Partition design into two equal size halves
  Minimize wires (nets) with ends in both halves
Number of wires crossing is bisection width
  Information crossing
lower bw = more locality
N/2
N/2
bisection
width

## Slide 45: Rent’s Rule
If we recursively bisect a graph, attempting to minimize the cut size, we typically get:
BW=IO = c Np
  0p1
  p1 means many inputs come from within a partition
[Landman and Russo,
IEEE TR Computers p1469, 1971]

## Slide 46: Rent and Locality
Rent and IO quantifying locality
  local consumption
  local fanout
IO = c Np

## Slide 47: Common Applications
Rent p=0
  Shift-register, 1D filter
Rent p=0.5
  Array multiplier
  2D Window Filter
  nearest-neighbor
Rent p=1.0
  FFT, Sort
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
Bit
Mpy
bit

## Slide 48: VLSI Interconnect Area
Bisection width is lower-bound on IC width
  When wire dominated, may be tight bound
(recursively)
Rent’s Rule tells us how big our chip must be

## Slide 49: As a function of Bisection
Achip  N  Agate
Achip  Nhorizontal Wwire  Nvertical Wwire
Nhorizontal = Nvertical = IO = cNp
Achip  (cN)2p
If p<0.5
  Achip  N
If p>0.5
  Achip  N2p

## Slide 50: In terms of Rent’s Rule
If p<0.5, Achip  N
If p>0.5, Achip  N2p
Typical designs have p>0.5
  interconnect dominates
  Achip > S Aelements

## Slide 51: Rent Network Richness

## Slide 52: Infrastructure: Clocking
PLL (Phased-Lock-Loop) to generate and synchronize clock
Clock drivers are big (drive big load)
Need buffering all over chip

## Slide 53: Infrastructure: Power
Need many I/O Pads
  Carry current
  Keep inductance low
Wires to distribute over chip
Maybe
  Capacitance to stabilize power
  Voltage converters

## Slide 54: Area
Mostly sum of components, but…
Area may be driven by
  I/O
  Interconnect A ≥ N2p
Will need to pay for infrastructure
  Clocking, Power

## Slide 55: Some Areas

## Slide 56: Processor Areas
ARM Cortex A53 about 2mm2 in 28nm
  Zynq UltraScale+ processor
  SuperScalar core
A5 (scalar) about 0.25mm2
A9 (superscalar) about 1mm2
A15 (higher performance) about 3mm2
A57 (big core to A53 little) about 3mm2

## Slide 57: R-Car H3 from Rensas Quad A57, Quad A53
https://en.wikichip.org/wiki/arm_holdings/microarchitectures/cortex-a53

## Slide 58: Zynq Compute Blocks
Crude estimate, including interconnect
2000 6-LUTs per sq. mm
DSP Block ~ 0.1 sq. mm

## Slide 59: CACTI
Standard program for modeling memories and caches
  More sophisticated version of the simple modeling we’ve been doing
Will ask you to use for custom area estimates (P4 milestone, final report)

## Slide 60: CACTI Parameters
Technology
Capacity
Output Width
Ports
Cache ways

## Slide 61: Example Output
- Total cache size (bytes): 32768
Number of banks: 1
Associativity: 4
Block size (bytes): 64
Read/write Ports: 1
Read ports: 0
Write ports: 0
Technology size (nm): 32
Access time (ns): 1.09421
Cycle time (ns): 1.25458
Total dynamic read energy per access (nJ): 0.0234295
Total dynamic write energy per access (nJ): 0.018806
Total leakage power of a bank without power gating, including its network outside (mW): 0.00787646
Cache height x width (mm): 0.152304 x 0.523289

## Slide 62: CACTI – Memories on Zynq
32nm (closest technology it models to 28nm in Zynq)
36Kb BRAMs 0.025mm
  2 port, 72b output
ARM L1 cache 0.08mm
  32KB 4-way associative (previous slide)
ARM L2 cache 1.5 mm
  512KB 8-way associative
  (older, not yours)

## Slide 63: Zynq Component Estimates
6-LUT 0.0005 mm2
DSP Block 0.1 mm2
36Kb BRAMs 0.025mm2
ARM L1 cache 0.08mm2
ARM L2 cache (512KB, 8-way)1.5 mm2
ARM Cortex A53 2.0 mm2

## Slide 65: Apple A12
84mm2, 7nm
7 Billion Tr.
iPhone XS
6 ARM cores
  2 fast
  4 low energy
4 custom GPUs
Neural Engine
  5 Trillion ops/s?

## Slide 66: A12 Die Areas
https://www.anandtech.com/print/13393/techinsights-publishes-apple-a12-die-shot-our-take

## Slide 67: A13 Die Areas
https://en.wikipedia.org/wiki/Apple_A13
SoC | A13 (7 nm) | A12 (7 nm)
Process Node | TSMC N7P | TSMC N7
Total Die | 98.48 | 83.27
Big Core | 2.61 | 2.07
Small Core | 0.58 | 0.43
CPU Complex (incl. cores) | 13.47 | 11.16
GPU Core | 3.25 | 3.23
GPU Total | 15.28 | 14.88
NPU | 2.09 | 1.23

## Slide 68: Big Ideas
First order:
  Chip cost proportional to Area
  Area = Sum(Area(Components))
But appreciate the simplification:
  Yield makes cost superlinear in area
    Limited range over which “linear” accurate
  I/O, Interconnect, infrastructure
    Can make Area > Sum(Area(Components))

## Slide 69: Admin
P4 due Friday