## Slide 1: ESE532: System-on-a-Chip Architecture
Day 24: November 20, 2019
Software Pipelining

## Slide 2: Previously: VLIW [Day 22]
Very Long Instruction Word
Set of operators
  Parameterize number, distribution (X, +, sqrt…)
    More operators less time, more area
    Fewer operators more time, less area
Memories for intermediate state
  Also parameterize memories and how connected
Memory for “long” instructions
General framework for specializing to problem
General way to tradeoff area and time

## Slide 3: VLIW
+
X
X
Address
Instruction
Memory

## Slide 4: Today
Software Pipelining
VLIW (as time permits)
  Zero-Overhead Loops

## Slide 5: Message
Pack computations more tightly by scheduling multiple loop instances (loop bodies for multiple indices) together
  Exploiting pipelining of computation
  II < latency bound

## Slide 6: Problem [Day 22]
Low utilization of parallel functional units for a single loop body
 | LD | LD | LD | ST | * | * | * | + | i | i | i | sqrt
0 |  |  |  |  |  |  |  | < | &x | &y | &z | 
1 | X[i] | Y[i] | Z[i] |  |  |  |  |  |  |  |  | 
2 |  |  |  |  | x | y | z |  |  |  |  | 
3 |  |  |  |  |  |  |  | X+y |  |  |  | 
4 |  |  |  |  |  |  |  | +z |  |  |  | 
5 |  |  |  |  |  |  |  |  |  |  |  | sqrt
6 |  |  |  | Res[i] |  |  |  |  | i |  |  | 

## Slide 7: Unroll 4 [Day 12]
 | LD | LD | LD | ST | * | * | * | + | + | i | i | i | sqrt
0 |  |  |  |  |  |  |  | < |  | x0 | y0 | z0 | 
1 | x0 | y0 | z0 |  |  |  |  |  |  | x1 | y1 | z1 | 
2 | x1 | y1 | z1 |  | x0 | y0 | z0 |  |  | x2 | y2 | z2 | 
3 | x2 | y2 | z2 |  | x1 | y1 | z1 | xy0 |  | x3 | y2 | z3 | 
4 | x3 | y2 | z3 |  | x2 | y2 | z2 | xy1 | +z0 |  |  |  | 
5 |  |  |  |  | x3 | y2 | z3 | xy2 | +z1 |  |  |  | 0
6 |  |  |  | 0 |  |  |  | xy3 | +z2 |  |  |  | 1
7 |  |  |  | 1 |  |  |  |  | +z3 |  |  |  | 2
8 |  |  |  | 2 |  |  |  |  |  |  |  |  | 3
9 |  |  |  | 3 |  |  |  |  |  | i |  |  | 

## Slide 8: Observation: Pipeline
for (i=0;i<MAX;i++)
  c+=a[i]*b[i];
When we pipeline we use all the resources
But, we don’t operate on a single loop body instance at a time
We cannot hit II=1 for VLIW schedule of a single loop body because of path latency

## Slide 9: Preclass 1
for (i=0;i<MAX;i++)
  c+=a[i]*b[i];
Pipeline not operate on a single loop body instance at a time
Assume add is working on a[0]*b[0] in same cycle,
  What i is a[i]*b[i]?
  What i is lookup ld a[i], b[i]?

## Slide 10: Observation: Unroll
Works like a pipeline
Only works because overlap data among loop instances
 | LD | LD | LD | ST | * | * | * | + | + | i | i | i | sqrt
0 |  |  |  |  |  |  |  | < |  | x0 | y0 | z0 | 
1 | x0 | y0 | z0 |  |  |  |  |  |  | x1 | y1 | z1 | 
2 | x1 | y1 | z1 |  | x0 | y0 | z0 |  |  | x2 | y2 | z2 | 
3 | x2 | y2 | z2 |  | x1 | y1 | z1 | xy0 |  | x3 | y3 | z3 | 
4 | x3 | y3 | z3 |  | x2 | y2 | z2 | xy1 | +z0 |  |  |  | 
5 |  |  |  |  | x3 | y3 | z3 | xy2 | +z1 |  |  |  | 0
6 |  |  |  | 0 |  |  |  | xy3 | +z2 |  |  |  | 1
7 |  |  |  | 1 |  |  |  |  | +z3 |  |  |  | 2
8 |  |  |  | 2 |  |  |  |  |  |  |  |  | 3
9 |  |  |  | 3 |  |  |  |  |  | i |  |  | 

## Slide 11: Observation: Unroll
Works like a pipeline
If keep going, fill like pipeline…
 | LD | LD | LD | ST | * | * | * | + | + | i | i | i | sqrt
0 |  |  |  |  |  |  |  | < |  | x0 | y0 | z0 | 
1 | x0 | y0 | z0 |  |  |  |  |  |  | x1 | y1 | z1 | 
2 | x1 | y1 | z1 |  | x0 | y0 | z0 |  |  | x2 | y2 | z2 | 
3 | x2 | y2 | z2 |  | x1 | y1 | z1 | xy0 |  | x3 | y3 | z3 | 
4 | x3 | y3 | z3 |  | x2 | y2 | z2 | xy1 | +z0 | x4 | y4 | z4 | 
5 | x4 | y4 | z4 |  | x3 | y3 | z3 | xy2 | +z1 | x5 | y5 | z5 | 0
6 | x5 | y5 | z5 | 0 | x4 | y4 | z4 | xy3 | +z2 | x6 | y6 | z6 | 1
7 | x6 | y6 | z6 | 1 | x5 | y5 | z5 | xy4 | +z3 | x7 | y7 | z7 | 2
8 | x7 | y7 | z7 | 2 | x6 | y6 | z6 |  | +z4 | x8 | y8 | z8 | 3
9 | x8 | y8 | z8 | 3 | x7 | y7 | z7 |  | +z5 | x9 | y9 | z9 | 4

## Slide 12: Observation: Pipeline
for (i=0;i<MAX;i++)
  c+=a[i]*b[i];
Pipeline not operate on a single loop body instance at a time
II of pipeline is 1
What is latency bound for c+a[i]*b[i] ?

## Slide 13: Observation
To have II < Latency Bound
  (for a loop body)
…must spread one loop body calculation over multiple loop iterations

## Slide 14: Idea: Software Pipelining
Schedule VLIW operators across multiple loop iterations
Treat execution on operators as pipeline

## Slide 15: Pipeline
Fully pipelined
  Computation in a pipeline stage in a cycle, depends on output of a different stage on previous cycle
What we compute in each cycle
  is a set of pipeline stages
  each operating on a different set of input data items

## Slide 16: Pipeline Rewrite
for (i=0;i<MAX;i++)
  c+=a[i]*b[i];
for (i=0;i<MAX;i++) {
  aptr++; bptr++;
  la=*aptr; lb=*bptr;
  prod=la*lb;
  c=c+prod;
  }
  Rewrite body to match cycle of pipeline
prod
c
la
lb
aptr
bptr
Goal: each register
compute based
on value set
previous cycle.

## Slide 17: Pipeline Rewrite
for (i=0;i<MAX;i++)
  c+=a[i]*b[i];
for (i=0;i<MAX;i++) {
  aptr++; bptr++;
  la=*aptr; lb=*bptr;
  prod=la*lb;
  c=c+prod;
  }
  Rewrite body to match cycle of pipeline
prod
c
la
lb
aptr
bptr
Goal: each register
compute based
on value set
previous cycle.
{ c=c+prod;
??
}

## Slide 18: Software Pipelined Version
for (i=0;i<MAX;i++)
  { c=c+prod; prod=la*lb; la=a[i]; lb=b[i];}
Use this to compact schedule

## Slide 19: Schedule Software Pipelined (Preclass 3)
Cycle | Branch | ALU | ALU | Multiply | Ld/St
0 |  |  |  |  | 
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
How many cycles for preclass 3 schedule?

## Slide 20: Schedule Software Pipelined (Preclass 3)
Cycle | Branch | ALU | ALU | Multiply | Ld/St
0 | Bzneq | Add r8 | Add r1 | Mul r6 | Ld r4
1 |  | Add r4 | Add r5 |  | Ld r5
2 | Br top | Sub r2 |  |  | 

## Slide 21: Prime Pipeline (as in ``Priming the Pump”)
For this body to work, will need to setup the steady state condition for the pipeline
for (i=2;i<MAX;i++)
  { c=c+prod; prod=la*lb; la=a[i]; lb=b[i];}

## Slide 22: Prefix
What need to do to define the loop variables used in the pipeline?
  prod?
  la, lb?
for (i=2;i<MAX;i++)
  { c=c+prod; prod=la*lb; la=a[i]; lb=b[i];}

## Slide 23: With Prefix
prod=a[0]*b[0];
la=a[1]; lb=b[1];
for (i=2;i<MAX;i++)
  { c=c+prod; prod=la*lb; la=a[i]; lb=b[i];}

## Slide 24: Flush Pipeline
For this body to work, will need to finish the pipeline
for (i=2;i<MAX;i++)
  { c=c+prod; prod=la*lb; la=a[i]; lb=b[i];}
What need to do after loop?
  Hint: what does c, prod, la, lb hold at loop exit?

## Slide 25: With Suffix
prod=a[0]*b[0];
la=a[1]; lb=b[1];
for (i=2;i<MAX;i++)
  { c=c+prod; prod=la*lb; la=a[i]; lb=b[i];}
c=c+prod;
c=c+la*lb;

## Slide 26: Full Software Pipelined Loop
prod=a[0]*b[0];
la=a[1]; lb=b[1];
for (i=2;i<MAX;i++)
  { c=c+prod; prod=la*lb; la=a[i]; lb=b[i];}
c=c+prod;
c=c+la*lb;
Software pipelined loop requires a loop prologue and loop epilogue

## Slide 27: Software Pipeline

## Slide 28: Preclass 4 Revisit Day 22, Preclass 2
for (xptr=&x;xptr<XMAX;xptr++)
res[i]=sqrt(x[i]*x[i]+y[i]*y[i]+z[i]*z[i]);
<XMAX;xptr++; yptr++; zptr++; ld x; ldy; ldz; x[i]2; y[i]2; z[i]2; x[i]2+y[i]2; +z[i]2; sqrt; res[i]
What resources would it take to achieve each II by resource bound?
II | Ld | St | * | + | inc | sqrt
3 |  |  |  |  |  | 
2 |  |  |  |  |  | 
1 |  |  |  |  |  | 

## Slide 29: Revisit Day 22, Preclass 2
Schedule for II=3 (work back from res store)
<XMAX;xptr++; yptr++; zptr++; ld x; ldy; ldz; x[i]2; y[i]2; z[i]2; x[i]2+y[i]2; +z[i]2; sqrt; res[i]
Cycle | Br | ALU | Mpy | RP | WP | Incr | Sqrt
0 |  |  |  |  |  |  | 
1 |  |  |  |  |  |  | 
2 |  |  |  |  | res 0 |  | 

## Slide 30: II=3
Cycle | Br | ALU | Mpy | RP | WP | Incr | Sqrt
0 | < | +z0 | x1 | x[i] 2 |  | xptr 2 | 
1 |  |  | y1 | y[i] 2 |  | yptr 2 | sqrt0
2 |  | x+y1 | z1 | z[i] 2 | res0 | zptr 2 | 
Operations | Instance
Incr | +2
ld | +2
x2 , y2, z2 | +1
x2+y2 | +1
+z2 | +0
sqrt | +0
st | +0

## Slide 31: II=2
Cyc | Br | ALU | Mpy | Mpy | RP | RP | WP | i | i | sqrt
0 | < | x+y1 | x2 | y2 | x3 | y3 |  | x4 | y4 | sqrt0
1 |  | +z1 | z2 |  | z3 |  | res0 | z4 |  | 
Operations | Instance
Incr | +4
ld | +3
x2 | +2
x2+y2 | +1
+z2 | +1
sqrt | +0
st | +0

## Slide 32: II=1
 | Br | A | A | M | M | M | RP | RP | RP | WP | i | i | i | sqrt
 | < | +y 3 | +z 2 | x4 | y4 | z4 | x5 | y5 | z5 | Res 0 | x6 | y6 | z6 | xyz1
Operations | Instance
Incr | +6
ld | +5
x2 | +4
x2+y2 | +3
+z2 | +2
sqrt | +1
st | +0

## Slide 33: Software Pipelining
Observe
  For cases without loop dependencies,
  if willing to mix any number of loop instances,
  can achieve resource bound
May require more registers to hold state

## Slide 34: More Registers Example
May require more registers to hold state
  Implement: Y=a*(b+c*(d+e))
  r1=d+e; r1=c*r1; r1=b+r1; r1=a*r1;
  r1=a*r2; r2=b+r3; r3=c*r4; r4=d+e

## Slide 35: Compare to Day 22 (no software pipelining)
[for preclass 4]
One of each operator: II=8
  Software pipelined 3
Latency lower bound (roughly II=1 hardware here)
  II=7
  II=2.5 for unroll 4 iterations (10 cycles)
  Software pipelined 1

## Slide 36: Lessons
VLIW provides rich area-time tradeoffs
Pipelining not just for hardware
  Already seen for coarse operation pipelining, even with processors
    Process- or thread-level parallelism
  Saw for Compute/Communicate overlap
    async / wait
  Now see for ILP (instruction-level parallelism)
  Necessary to achieve II < Latency Bound

## Slide 37: Automation
Good compiler should do this for you
Worth understanding to reason about II should achieve
If compiler not achieving, hint may need to check if there’s a dependency the compiler thinks exists
Gives you an idea of how to disambiguate for the compiler

## Slide 38: Looping
(if time permits)

## Slide 39: Loop Overhead
Can handle loop overhead in ILP on VLIW
  Increment counters, branches as independent functional units

## Slide 40: VLIW Loop Overhead
Can handle loop overhead in ILP on VLIW
…but paying a full issue unit and instruction costs overhead

## Slide 41: Zero-Overhead Loops
Specialize the instructions, state, branching for loops
  Counter rather than RF
  One bit to indicate if counter decrement
  Exit loop when decrement to 0

## Slide 42: Simplification

## Slide 43: Zero-Overhead Loop Simplify
Share port – simplify further

## Slide 44: Zero-Overhead Loop Example (with software pipelining)
repeat r3:
addi r5,#4,r5; ld r4,r6
addi r4,#4,r4; ld r5,r7
add r9,r8,r8; mul r6,r7,r9

## Slide 45: Zero-Overhead Loop
Potentially generalize to multiple loop nests and counters
Common in highly optimized
  DSPs, Vector units
  Embedded, real-time
    Where loop bounds simple, often constant

## Slide 46: Big Ideas:
Pipelining of data processing useful for software scheduled on processors
  VLIW (and pipelined, superscalar)
  Not just hardware pipelines

## Slide 47: Admin
P4 due Friday
Next week
  Lecture on Monday as normal
  Wednesday is a virtual Friday
    Will not meet
  Nothing due
    …but project due following Friday (12/6)