## Slide 1: ESE532: System-on-a-Chip Architecture
Day 25: November 25, 2019
Reduce

## Slide 2: Today
Reduce
Associative Operations
Model
Latency Bound Implications and Implementations
Parallel Prefix
Broad Application

## Slide 3: Message
Aggregation is a common need that is not strictly data parallel
…but admits to parallel computation

## Slide 4: Reduce
Reduce – combining a collection of data into a single value
  Converting a vector into a scalar

## Slide 5: Sum Reduce
Simplest and most common
  Add up all the values in a vector or array
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i];

## Slide 6: Sum Reduce
What’s II?
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i];

## Slide 7: Sum Reduce
What’s latency bound?
  Assuming associativity holds for addition
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i];

## Slide 8: Associative Operations
Associativity means can group together operations in any way
Normal sequential:
  (((a[0]+a[1])+a[2])+a[4])+…
Associative regroup:
  (a[0]+((((a[1]+(a[2]+a[3]))+a[4])+(…)))

## Slide 9: Associative Operations
Associativity means can group together operations in any way
Normal sequential:
  (((a[0]+a[1])+a[2])+a[4])+…
Regroup parallelism:
  (((a[0]+a[1])+(a[2]+a[3]))+((a[4]+a[5])+(a[6]+a[7])))

## Slide 10: Associative Tree Reduce
Add pairs – cut numbers in half
Repeat adding pairs until single value
How deep?

## Slide 11: Latency Bounds
Associative reduces typically contribute log terms to latency bounds
  …as you’ve seen on many previous midterms and finals

## Slide 12: Sum Reduce
Data Parallel?
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i];

## Slide 13: Sum Reduce
How exploit 4 cores to compute?
  (assume a very large, like 1 million)
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i];

## Slide 14: Model: Data Parallel+Reduce
Data Parallel + Reduce
  Very common to perform a data parallel operation then a reduce on results
Example: dot product
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i]*b[i];

## Slide 15: Dot Product
Latency bound for dot product
  Assume 1 cycle add, 3 cycle multiply
Example: dot product
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i]*b[i];

## Slide 16: Model: Data Parallel+Reduce
Data Parallel + Reduce
  Very common to perform a data parallel operation then a reduce on results
General form
  int res=0;
  for (int i=0;i<N; i++)
  res=assoc_op(res,f(a[i],b[i], …))

## Slide 17: What else Associative?
Beyond addition, what other associative operations do we often see as reductions?

## Slide 18: Associative Operations
Add
Multiply
Max
Min
AND
OR
Max/min
  And keep associated values
Find First

## Slide 19: Optimization Loop
int minval=f(0);
int min=0;
for (i=1;i<N;i++) {
int val=f(i);
if (val<minval) {
minval=val; min=i;
}
}

## Slide 20: Rendering Decomposed
Pipeline of
  Projection
    Where do the points of this triangle end up in the viewed image?
    Matrix-multiplication to translate points
  Rasterization
    Turn into pixels
    Fill pixels for triangle
  Z-buffer
    Keep only the ones on top (not hidden)
      2D image + Z-depth – keep smallest
Figures from: https://commons.wikimedia.org/wiki/File:Perspective_Projection_Principle.jpg
https://en.wikipedia.org/wiki/Rasterisation#/media/File:Raster_graphic_fish_20x23squares_sdtv-example.png
Day 15

## Slide 21: Z-Buffering
Storing into Z–buffer is an associative reduce operation
  Min reduce (keep nearest pixel) on depth with an associated value
Parallel strategy
  Split triangles into sets
  Project, rasterize, Z-buffer in parallel
  Assoc. reduce Z-buffer pixels across parallel Z-buffers

## Slide 22: Implementations
Data Parallel+Preduce

## Slide 23: Threaded: Data Parallel+Reduce
Break into P threads
  0 to N/P-1, N/P to 2N/P-1, …
Run fraction of data and reduce on each
Then bring results together to sum
  P small, on one processor
  P large, as tree

## Slide 24: Model: Data Parallel+Reduce
What’s cycle  what’s II?
General form
  int res=0;
  for (int i=0;i<N; i++)
  res=assoc_op(res,f(a[i],b[i], …))

## Slide 25: Pipeline: Data Parallel + Reduce
Pipeline f
Cycle on assoc_op

## Slide 26: Pipeline: Data Parallel + Reduce
Pipeline f
Cycle on assoc_op
Avoid cycle, II=1 for commutative
  Run interleaved
    C-slow (C=II)
  Combine at end
Commutative operation
  Can reorder operands

## Slide 27: 2-Slow Simple Cycle
Replace register with pair
Retime
Observe independence of red/blue computations
Day 7

## Slide 28: II=2 Commutative Pipelined Reduce
2-slow transformation
Combine independent (red, blue) reduces

## Slide 29: Pipeline: Data Parallel + Reduce
Pipeline f
Cycle on assoc_op
Avoid cycle, II=1 for associative
  Gather up II values
  Run through pipelined assoc. reduce tree
  Drop into assoc_op cycle every II cycles

## Slide 30: Model: Data Parallel+Reduce
Conclude: associative reduce can achieve II of 1
General form
  int res=0;
  for (int i=0;i<N; i++)
  res=assoc_op(res,f(a[i],b[i], …))

## Slide 31: Vector: Data Parallel + Reduce
Some vector/SIMD machines will have dedicated reduce hardware
E.g. vector-add operator
NEON
  Not have vector reduce
  Does have VPADAL
Use VL adds for course-grained reduce
for (i=0;i<N;i+=VL) {
avl=a[i]…a[i+VL-1]
VADD(res,avl, res);
}
Use VPADAL to complete

## Slide 32: Unrolled Pipeline: Data Parallel + Reduce
Unroll computation
Perform f ops in parallel pipelines
Pipelined tree reduce

## Slide 33: Parallel Prefix

## Slide 34: What if want Prefix?
Sum Reduce
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i];
Sum Prefix
  int sum[N];
  sum[0]=a[0];
  for (int i=1;i<N; i++)
  sum[i]=a[i]+sum[i-1];

## Slide 35: Prefix
Aggregate (vector) output where item i is the reduce of the input vector 0 through i
  prefix[0]=a[0];
  for (int i=1;i<N; i++)
  prefix[i]=op(prefix[i-1],f(a[i]…));

## Slide 36: Latency Bound
What’s the latency bound for the prefix when op is associative?
  Assume op is 1 cycle
  How cylces(op)>1 change?
  prefix[0]=a[0];
  for (int i=1;i<N; i++)
  prefix[i]=op(prefix[i-1],f(a[i]…));

## Slide 37: Resources?
How much hardware to achieve latency bound?
  prefix[0]=a[0];
  for (int i=1;i<N; i++)
  prefix[i]=op(prefix[i-1],f(a[i]…));

## Slide 38: Latency Bound?
What’s the latency bound for this operation?
boolean a[i],b[i],s[i]
for (i=0;i<N;i++) {
  cn=(a[i]&&b[i])|| (a[i]&&c)||
  (b[i]&&c);
  s[i]=a[i] ^ b[i] ^ c;
  c=cn;
  }

## Slide 39: Associative
Is the carry operation in addition an associative operation?
Operation:
  MAJ=majority = A&&B || B&&C || A&&B

## Slide 40: Carry Computation
Think about each adder bit as a computing a function on the carry in
  C[i]=g(c[i-1])
  Particular function f will depend on a[i], b[i]
  g=f(a,b)

## Slide 41: Functions
What are the functions g(c[i-1])?
  g(c)=carry(a=0,b=0,c)
  g(c)=carry(a=1,b=0,c)
  g(c)=carry(a=0,b=1,c)
  g(c)=carry(a=1,b=1,c)

## Slide 42: Functions
What are the functions g(c[i-1])?
  g(x)=1 Generate
    a[i]=b[i]=1
  g(x)=x Propagate
    a[i] xor b[i]=1
  g(x)=0 Squash
    a[i]=b[i]=0

## Slide 43: Combining
Want to combine functions
  Compute c[i]=gi(gi-1(c[i-2]))
  Compute compose of two functions
What functions will the compose of two of these functions be?
  Same as before
    Propagate, generate, squash

## Slide 44: Compose Rules (LSB MSB)
GG
GP
GS
PG
PP
PS
SG
SP
SS
[work on board]

## Slide 45: Compose Rules (LSB MSB)
GG = G
GP = G
GS = S
PG = G
PP = P
PS = S
SG = G
SP = S
SS = S

## Slide 46: Combining
Do it again…
Combine g[i-3,i-2] and g[i-1,i]
What do we get?

## Slide 47: Associative Reduce Tree

## Slide 48: Reduce Tree
Sq=/A*/B
Gen=A*B
Sqout=Sq1+/Gen1*Sq0
Genout=Gen1+/Sq1*Gen0

## Slide 49: Reduce Tree
Sq=/A*/B
Gen=A*B
Sqout=Sq1+/Gen1*Sq0
Genout=Gen1+/Sq1*Gen0
Delay and Area? (work next few slides)

## Slide 50: Reduce Tree
Sq=/A*/B
Gen=A*B
Sqout=Sq1+/Gen1*Sq0
Genout=Gen1+/Sq1*Gen0
A(Encode)=2
D(Encode)=1
A(Combine)=4
D(Combine)=2
A(Carry)=2
D(Carry)=1

## Slide 51: Reduce Tree: Delay?
D(Encode)=1
D(Combine)=2
D(Carry)=1
Delay = 1+2log2(N)+1

## Slide 52: Reduce Tree: Area?
A(Encode)=2
A(Combine)=4
A(Carry)=2
Area= 2N+4(N-1)+2

## Slide 53: Reduce Tree: Area & Delay
Area(N) = 6N-2
Delay(N) = 2log2(N)+2

## Slide 54: Compute Carry[N]

## Slide 55: Need Prefix
Need PG[i:0] forall i

## Slide 56: Reduce Tree
While computing PG[0,N] compute many PG[0,j]’s
  PG[1,0], PG[0,3], PG[0,7] ….

## Slide 57: Prefix Tree
While computing PG[0,N] only get
  PG[0,2n-1]
How fillin holes?
– e.g. how get PG[0,11]?

## Slide 58: Prefix Tree
Look at Symmetric stage (with respect to middle=PG[0N] stage) and combine to fillin

## Slide 59: Prefix Tree

## Slide 60: Prefix Tree

## Slide 61: Prefix Tree
Bring in Carry and compute each intermediate carry-in

## Slide 62: Prefix Tree
Note: prefix-tree is same size as reduce tree
  Always matched same number of elements in symmetric stage

## Slide 63: Parallel Prefix Area and Delay?
Roughly twice the area/delay
Area= 2N+4N+4N+2N
= 12N
Delay = 4log2(N)+2
Conclude: can add in log time with linear area.

## Slide 64: Parallel Prefix
Important Pattern
Applicable any time operation is associative
  Or can be made assoc. as in MAJ case
Function Composition is always associative
Logarithmic delay
Linear area
Notes: Non-associative example: nor2 ? (strictly if start with nors…but of course nor-n is associative in terms of the Ors)

## Slide 65: Parallel Prefix Sum
  prefix[0]=a[0];
  for (int i=1;i<N; i++)
  prefix[i]=op(prefix[i-1],f(a[i]…));

## Slide 66: Broader Application

## Slide 67: Cast Associative
If you can cast it into an associative operation, you can apply
  Associative Reduce
  Parallel Prefix

## Slide 68: Examples
Saturated Addition
  Not associative
Floating-Point Addition
Finite Automata Evaluation
(papers in supplemental reading)

## Slide 69: Big Ideas:
Reduce from aggregate to scalar
  is a common operation
  not strictly data parallel
  Associative reduce admits to parallelism
    log(N) latency bound
    II=1
    Linear area
Prefix when want reduce of all prefixes
  Also log(N) latency bound
  Linear area

## Slide 70: Admin
Wednesday is a virtual Friday
  Will not meet
  Happy Thankgiving
  Nothing due Friday (virtual or real)
Project due following Friday (12/6)