## Slide 1: ESE532: System-on-a-Chip Architecture
Day 27: December 4, 2019
Defect Tolerance

## Slide 2: Today
Reliability Challenges
Defect Tolerance
  Memories
  Interconnect
  FPGA
FPGA Variation and Energy
  (time permitting)

## Slide 3: Message
At small feature sizes, not viable to demand perfect fabrication of billions of transistors on a chip
Modern ICs are like snowflakes
  Everyone is different, changes over time
Reconfiguration allows repair
  Finer grain  higher defect rates
  Tolerate variation  lower energy

## Slide 4: Intel Xeon Phi Offerings
Part # | Cores
7290F | 72
7250F | 68
7230F | 64
http://www.intel.com/content/www/us/en/products/processors/xeon-phi/xeon-phi-processors.html

## Slide 5: Intel Xeon Phi Offerings
Part # | Cores
7290F | 72
7250F | 68
7230F | 64
Is Intel producing 3 separate chips?

## Slide 6: Preclass 1 and Intel Xeon Phi Offerings
Part # | Cores
7290F | 72
7250F | 68
7230F | 64
Cost ratio between 72 and 64 processor
assuming fixed mm2 per core?

## Slide 7: Intel Xeon Phi Pricing

## Slide 8: Intel Knights Landing
https://www.nextplatform.com/2016/06/20/intel-knights-landing-yields-big-bang-buck-jump/
[Intel, Micro 2016]

## Slide 9: Knights Landing Xeon Phi
[Intel, Micro 2016]

## Slide 10: What’s happening?
Fabricated chip has 76 cores
Not expect all to work
Selling based on functional cores
  72, 68, 64
Charge premium for high core counts
  Don’t yield as often, people pay more
Do see design to accommodate defects
https://www.nextplatform.com/2016/08/22/intel-tweaking-xeon-phi-deep-learning/
[Intel, Micro 2016]

## Slide 11: Warmup Discussion
Where else do we guard against defects today?
  Where do we accept imperfection today?

## Slide 12: Motivation: Probabilities
Given:
  N objects
  Pg yield probability
What’s the probability for yield of composite system of N items? [Preclass 2]
  Assume iid (independent, identically distributed) faults
  P(N items good) = (Pg)N

## Slide 13: Probabilities
  Pall_good(N)= (Pg)N
P=0.999999
N | Pall_good(N)
104 | 
105 | 
106 | 
107 | 

## Slide 14: Probabilities
  Pall_good(N)= (Pg)N
P=0.999999
N | Pall_good(N)
104 | 0.99
105 | 0.90
106 | 0.37
107 | 0.000045

## Slide 15: Simple Implications
As N gets large
  must either increase reliability
  …or start tolerating failures
N
  memory bits
  disk sectors
  wires
  transmitted data bits
  processors
  transistors
  molecules
As devices get smaller, failure rates increase
chemists think P=0.95 is good
As devices get faster, failure rate increases

## Slide 16: Failure Rate Increases
[Nassif / DATE 2010]
1-Pg

## Slide 17: Quality Required for Perfection?
How high must Pg be to achieve 90% yield on a collection of 1011 devices?
[preclass 4]
Pg>1-10-12

## Slide 18: Failure Rate Increases
[Nassif / DATE 2010]
1-Pg

## Slide 19: Challenge
Feature size scales down (S)
Capacity (area)  increases (1/S2)
  N increase
Reliability per device goes down
  Pg decrease
  P(N items good) = (Pg)N

## Slide 20: Defining Problems

## Slide 21: Three Problems
Defects: Manufacturing imperfection
  Occur before operation; persistent
    Shorts, breaks, bad contact
Transient Faults:
  Occur during operation; transient
    node X value flips: crosstalk, ionizing particles, bad timing, tunneling, thermal noise
Lifetime “wear” defects
  Parts become bad during operational lifetime
    Fatigue, electromigration, burnout….
  …slower
    NBTI, Hot Carrier Injection

## Slide 22
Shekhar Bokar
Intel Fellow
Micro37 (Dec.2004)

## Slide 23: First Step to Recover
Admit you have a problem
(observe that there is a failure)

## Slide 24: Detection
How do we determine if something wrong?
  Some things easy
    ….won’t start
  Others tricky
    …one and gate computes False & TrueTrue
Observability
  can see effect of problem
  some way of telling if defect/fault present

## Slide 25: Detection
Coding
  space of legal values << space of all values
  should only see legal
  e.g. parity, ECC (Error Correcting Codes)
Explicit test (defects, recurring faults)
  ATPG = Automatic Test Pattern Generation
  Signature/BIST=Built-In Self-Test
  POST = Power On Self-Test
Direct/special access
  test ports, scan paths

## Slide 26: Coping with defects/faults?
Key idea: redundancy
Detection:
  Use redundancy to detect error
Mitigating: use redundant hardware
  Use spare elements in place of faulty elements (defects)
  Compute multiple times so can discard faulty result (faults)

## Slide 27: Defect Tolerance

## Slide 28: Three Problems
Defects: Manufacturing imperfection
  Occur before operation; persistent
    Shorts, breaks, bad contact
Transient Faults:
  Occur during operation; transient
    node X value flips: crosstalk, ionizing particles, bad timing, tunneling, thermal noise
Lifetime “wear” defects
  Parts become bad during operational lifetime
    Fatigue, electromigration, burnout….
  …slower
    NBTI, Hot Carrier Injection

## Slide 29: Two Models
Disk Drives (defect map)
Memory Chips (perfect chip)

## Slide 30: Disk Drives
Expose defects to software
  software model expects defects
    Create table of good (bad) sectors
  manages by masking out in software
    (at the OS level)
    Never allocate a bad sector to a task or file
  yielded capacity varies

## Slide 31: Memory Chips
Provide model in hardware of perfect chip
Model of perfect memory at capacity X
Use redundancy in hardware to provide perfect model
Yielded capacity fixed
  discard part if not achieve

## Slide 32: Example: Memory
Correct memory:
  N slots
  each slot reliably stores last value written
Millions, billions, etc. of bits…
  have to get them all right?

## Slide 33: Failure Rate Increases
[Nassif / DATE 2010]
1-Pg

## Slide 34: Memory Defect Tolerance
Idea:
  few bits may fail
  provide more raw bits
  configure so yield what looks like a perfect memory of specified size

## Slide 35: Memory Techniques
Row Redundancy
Column Redundancy
Bank Redundancy

## Slide 36: Yield M of N
Preclass 5: Probability of yielding 3 of 5 things?
  Symbolic?
  Numerical for Pg=0.9?

## Slide 37: Yield M of N
P(M of N) = P(yield N)
  (N choose N-1) P(exactly N-1)
  (N choose N-2) P(exactly N-2)…
  (N choose N-M) P(exactly N-M)…
  [think binomial coefficients]

## Slide 38: M of 5 example
1*P5 + 5*P4(1-P)1+10P3(1-P)2+10P2(1-P)3+5P1(1-P)4 + 1*(1-P)5
Consider P=0.9
  1*P5 0.59 M=5 P(sys)=0.59
  5*P4(1-P)1 0.33 M=4 P(sys)=0.92
  10P3(1-P)2 0.07 M=3 P(sys)=0.99
  10P2(1-P)3 0.008
  5P1(1-P)4 0.00045
  1*(1-P)5 0.00001
Can achieve higher
system yield than
individual components!

## Slide 39: Possible Yield of 76 cores@ P=0.9
Processors Yield | Prob Exact | Prob at least
76 | 0.001 | 0.001
75 | 0.004 | 0.005
74 | 0.016 | 0.020
73 | 0.041 | 0.061
72 | 0.079 | 0.140
71 | 0.119 | 0.259
70 | 0.148 | 0.407
69 | 0.156 | 0.562
68 | 0.141 | 0.704
67 | 0.112 | 0.816
66 | 0.079 | 0.895
65 | 0.050 | 0.945
64 | 0.028 | 0.973

## Slide 40: Possible Yield of 76 cores@ P=0.9
Processors Yield | Prob at least
76 | 0.001
75 | 0.005
74 | 0.020
73 | 0.061
72 | 0.140
71 | 0.259
70 | 0.407
69 | 0.562
68 | 0.704
67 | 0.816
66 | 0.895
65 | 0.945
64 | 0.973
Out of 100 chips, how many?
Sell with 72:
Sell with 68:
Sell with 64:
Discard:

## Slide 41: Intel Xeon Phi Pricing

## Slide 42: Repairable Area
Not all area in a RAM is repairable
  memory bits spare-able
  io, power, ground, control not redundant

## Slide 43: Repairable Area
P(yield) = P(non-repair) * P(repair)
P(non-repair) = PNnr
  Nnr<<Ntotal
  P > Prepair
    e.g. use coarser feature size
    Differential reliability
P(repair) ~ P(yield M of N)

## Slide 44: Consider a Crossbar
Allows us to connect any of N things to each other
  E.g.
    N processors
    N memories
    N/2 processors
    N/2 memories

## Slide 45: Crossbar Buses and Defects
Two crossbar multibus
Wires may fail
Switches may fail
How tolerate
  Wire failures between crossbars?
  Switch failures?

## Slide 46: Crossbar Buses and Defects
Two crossbars
Wires may fail
Switches may fail
Provide more wires
  Any wire fault avoidable
    M choose N

## Slide 47: Crossbar Buses and Defects
Two crossbars
Wires may fail
Switches may fail
Provide more wires
  Any wire fault avoidable
    M choose N

## Slide 48: Crossbar Buses and Faults
Two crossbars
Wires may fail
Switches may fail
Provide more wires
  Any wire fault avoidable
    M choose N

## Slide 49: Crossbar Buses and Faults
Two crossbars
Wires may fail
Switches may fail
Provide more wires
  Any wire fault avoidable
    M choose N
  Same idea

## Slide 50: Simple System
P Processors
M Memories
Wires
Memory, Compute, Interconnect

## Slide 51: Simple System w/ Spares
P Processors
M Memories
Wires
Provide spare
  Processors
  Memories
  Wires

## Slide 52: Simple System w/ Defects
P Processors
M Memories
Wires
Provide spare
  Processors
  Memories
  Wires
...and defects

## Slide 53: Simple System Repaired
P Processors
M Memories
Wires
Provide spare
  Processors
  Memories
  Wires
Use crossbar to switch together good processors and memories

## Slide 54: Simple System Repaired
What are the costs?
  Area
  Energy
  Delay

## Slide 55: In Practice
Crossbars are inefficient
Use switching networks with
  Locality
  Segmentation
…but basic idea for sparing is the same

## Slide 56: FPGAs

## Slide 57: Modern FPGA
Has 10,000 to millions of LUTs
Hundreds to thousands of
  Memory banks
  Multipliers
Reconfigurable interconnect

## Slide 58: ZU3EG (Ultra96)
6-LUTs: 70,560
DSP Blocks: 360
  18x27 multiply
  48b accumulate
BRAMs: 216
  36Kb
  Dual port
  Up to 72b wide (512x72)

## Slide 59: Modern FPGA
Has 10,000 to millions of gates
Hundreds to thousands of
  Memory banks
  Multipliers
Reconfigurable interconnect
If a few resources don’t work
  avoid them

## Slide 60: Granularity
Consider two cases
  Knight’s Bridge with 76 64b processors
  FPGA with 1 Million 6-LUTs
10 defects (bad transistors)
How much capacity lost? [worst-case, as percentage]
  Knight’s Bridge?
  1M 6-LUT FPGA?

## Slide 61: Observe
Finer granularity sparing
  Lose fewer resources per defect
    Losing processor vs. losing 6-LUT
    Losing memory row vs. losing entire memory bank
  Pay more for reconfiguration
Finer grained designs
  Tolerate higher defect rates

## Slide 62: Interconnect Defects
Route around interconnect defects

## Slide 63: Defect-Level Viable with FPGAs
Fine-grained repair
Avoiding routing defects
  Tolerates >20% switch defects
[Rubin/PhD Thesis 2018]

## Slide 64: FPGAs Variation and Energy
(if time permits)

## Slide 65: Variation
Modern ICs are like Snowflakes
  Each one is different
[Gojman, FPGA2013]

## Slide 66: Variation Challenge
Use of high Vth resource forces high supply voltage (Vdd) to meet timing requirement
Delay: CV/I and I goes as (Vdd-Vth)2

## Slide 67: Component-Specific
Use defect idea to avoid high Vth resource
Allow lower supply voltage (Vdd) to meet timing requirement
Delay: CV/I and I goes as (Vdd-Vth)2

## Slide 68: Energy vs Vdd
Nominal uses minimum size
[Mehta, FPGA 2012]

## Slide 69: Energy vs Vdd (des)
Nominal uses minimum size
Oblivious must use larger
  Higher C, Area
Energy
Margin
[Mehta, FPGA 2012]

## Slide 70: Energy vs Vdd (des)
Nominal uses minimum size
Oblivious must use larger
  Higher C, Area
Delay-aware routing reduces energy margins
  Smaller sizes
Energy
Savings
(Sizing)
[Mehta, FPGA 2012]

## Slide 71: Energy vs Vdd (des)
Nominal uses minimum size
Delay-aware routing reduces energy margins
  Smaller sizes
  Lower voltages
Energy
Savings
(Vdd)
[Mehta, FPGA 2012]

## Slide 72: Energy vs Vdd (des)
Nominal uses minimum size
Delay-aware routing reduces energy margins
  Smaller sizes
  Lower voltages
  Less Leakage
Energy
Savings
(Total)
[Mehta, FPGA 2012]

## Slide 73: Big Ideas
At small feature sizes, not viable to demand perfect fabrication of billions of transistors on a chip
Modern ICs are like snowflakes
  Everyone is different, changes over time
Reconfiguration allows repair
  Finer grain  higher defect rates
  Tolerate variation  lower energy

## Slide 74: Admin
Project due Friday
  Reminder turnin
    Report
    Code
    Binaries: Bitstream, elf, decoder
Wrapup lecture on Monday by Eric
  This was last lecture from André
  Plan to return boards, cables, cards
    Watch piazza for more details