## Slide 1: ESE532: System-on-a-Chip Architecture
Day 3: September 9, 2019
Memory

## Slide 2: Today
Memory
Memory Bottleneck
Memory Scaling
Latency Engineering
  Scheduling
  Data Reuse: Scratchpad and cache
Bandwidth Engineering
  Wide word
  Banking (form of parallelism for data)

## Slide 3: Message
Memory throughput (bandwidth) and latency can be bottlenecks
Minimize data movement
Exploit small, local memories
Exploit data reuse

## Slide 4: Memory Scaling

## Slide 5: On-Chip Delay
Delay is proportional to distance travelled
Make a wire twice the length
  Takes twice the latency to traverse
  (can pipeline)
Modern chips
  Run at 100s of MHz to GHz
    (sub 10ns, 1ns cycle times)
  Take 10s of ns to cross the chip
  Takes 100s of ns to reference off-chip data
What does this say about placement of computations and memories?

## Slide 6: Random Access Memory
A Memory:
  Series of locations (slots)
  Can write values a slot (specified by address)
  Read values from (by address)
  Return last value written
Notation:
slash on wire
means multiple bits wide

## Slide 7: Memory Operation
Memory Read
  Present Address
  Decoder Matches
  Charge word line
  Enables Memory Cell to charge bitlines (column)
  SenseAmp detections bitline
  Buffered for output
1
2
3
4
5
6

## Slide 8: Memory Block
Linear wire delay with distance
Assume constant area/memory bit
N-bit memory, arranged in square
  As shown N=64, width=depth=8
  N=width*depth (since square)
4x capacity (N) delay change?
  (e.g. 1Gbit to 4Gbit)
width
depth

## Slide 9: Memory Block
Linear wire delay with distance
Assume constant area/memory bit
N-bit memory, arranged in square
Width relate to N?
Depth?
Delay scale N?
width
depth

## Slide 10: Memory Block Bandwidth
Bandwidth: data throughput
  How many bits per second can we transfer
N-bit memory, arranged in square
Bits/cycle scale with N?
  (not quite bandwidth)

## Slide 11: Memory Block Energy
Assume read full width,
  Energy scales with N
    Activate sqrt(N) wires
    Each wire sqrt(N) long
  Or, energy/bit scales as sqrt(N)
Larger memories cost more energy

## Slide 12: Memory Block Density
Address, sense amplifies are large
How do address bits scale with N?
Scale slower than bit area
  Bits scale N
  Address sqrt(N)*log(N)
  Sense amps sqrt(N)
Large memories pay less per bit
  denser

## Slide 13: Compactness vs. Memory Size

## Slide 14: Memory Scaling
Small memories are fast
  Large memories are slow
Small memories low energy
  Large memories high energy
Large memories dense
  Small memories cost more area per bit
Combining:
  Dense memories are slow

## Slide 15: Latency Engineering Scheduling

## Slide 16: Preclass 2
Issue one read/write per cycle
10 cycle latency to memory
Memory read concurrent with compute
  only wait for memory when need value
Throughput (iters/cycle) in each case?

## Slide 17: Lesson
Long memory latency can impact throughput
  When must wait on it
  When part of a cyclic dependency
Overlap memory access with computations when possible
  exploit parallelism between compute and memory access

## Slide 18: Latency Engineering Data Reuse

## Slide 19: Preclass 3abc
MAX=106 WSIZE=5
How many times execute t+=x[]*w[] ?
How many reads to x[] and w[]?
Runtime read x,w 20 t+=… 5

## Slide 20: Preclass 3c
T=MAX*WSIZE(Tcomp+Tx+Tw)
T=106*5*(5+20+20)
T=2.25*108

## Slide 21: Preclass 3d
How many distinct x[], w[] read?

## Slide 22: Strategy
Add small, local memory bank
  Small memories are faster

## Slide 23: Preclass 3e
How use local memory to reduce large memory reads to 3d?
How much local memory need?
How much faster might small memory be?

## Slide 24: Preclass 3

## Slide 25: Preclass 3
WSIZE*Tw
WSIZE*Tx
WSIZE*MAX*Tlocal
MAX*Tx
WSIZE*MAX*Tcomp
WSIZE*MAX*2*Tlocal

## Slide 26: Preclass 3
WSIZE*MAX*(Tcomp+3*Tlocal)
+WSIZE*(Tw+Tx)
+MAX*Tx
5*106*(5+3)
+5*(20+20)
+106*20
6*107

## Slide 27: Preclass 3
2.25*108 6*107
3.75x

## Slide 28: Lesson
Data can often be reused
  Keep data needed for computation in
    Closer, smaller (faster, less energy) memories
  Reduces latency costs
  Reduces bandwidth required from large memories
Reuse hint: value used multiple times
  Or value produced/consumed

## Slide 29: Processor Data Caches
Traditional Processor Data Caches are a heuristic instance of this
  Add a small memory local to the processor
    It is fast, low latency
  Store anything fetched from large/remote memory in local memory
    Hoping for reuse in near future
  On every fetch, check local memory before go to large memory

## Slide 30: Cache
Goal: performance of small memory with density of large memory

## Slide 31: Processor Data Caches
Demands more than a small memory
  Need to sparsely store address/data mappings from large memory
  Makes more area/delay/energy expensive than just a simple memory of capacity
Don’t need explicit data movement
Cannot control when data moved/saved
  Bad for determinism
Limited ability to control what stays in small memory simultaneously

## Slide 32: Terminology
Cache
  Hardware-managed small memory in front of larger memory
Scratchpad
  Small memory
  Software (or logic) managed
  Explicit reference to scratchpad vs. large (other) memories
  Explicit movement of data

## Slide 33: Terminology: Unroll Loop
Replace loop with instantiations of body
For WSIZE=5

## Slide 34: Terminology: Unroll Loop
Replace loop with instantiations of body
For WSIZE=5

## Slide 35: Terminology: Unroll Loop
Can unroll partially
For WSIZE even

## Slide 36: Amdahl’s Law

## Slide 37: Amdahl’s Law
If you only speedup Y(%) of the code, the most you can accelerate your application is 1/(1-Y)
Tbefore = 1*Y + 1*(1-Y)
Speedup by factor of S
Tafter=(1/S)*Y+1*(1-Y)
Limit Sinfinity Tbefore/Tafter=1/(1-Y)

## Slide 38: Amdahl’s Law
Tbefore = 1*Y + 1*(1-Y)
Speedup by factor of S
Tafter=(1/S)*Y+1*(1-Y)
Y=70%
  Possible speedup (Sinfinity) ?
  Speedup if S=10?

## Slide 39: Amdahl’s Law
If you only speedup Y(%) of the code, the most you can accelerate your application is 1/(1-Y)
Implications
  Amdhal: good to have a fast sequential processor
  Keep optimizing
    Tafter=(1/S)*Y+1*(1-Y)
    For large S, bottleneck now in the 1-Y

## Slide 40: Bandwidth Engineering

## Slide 41: Bandwidth Engineering
High bandwidth is easier to engineer than low latency
  Wide-word
  Banking
    Decompose memory into independent banks
    Route requests to appropriate bank

## Slide 42: Wide Memory
Relatively easy to have a wide memory
As long as we share the address
  One address to select wide word or bits
Efficient if all read together

## Slide 43: Revisit Preclass 3
Use wide memory access to move 8 words (x[]) between large and small memory in a single cycle

## Slide 44: Preclass 3 + wide
Impact of 8 word datapath between large and local memory?
WSIZE*MAX*(Tcomp+3*Tlocal)
+WSIZE*(Tw+Tx)
+MAX*Tx
5*106*(5+3)
+5*(20+20)
+106*20
6*107
What term most impacted?

## Slide 45: Preclass 3 + wide
WSIZE*MAX*(Tcomp+3*Tlocal)
+WSIZE*(Tw+Tx)
+MAX/8*Tx
+MAX*(Tlocal+2)
5*106*(5+3)
+5*(20+20)
+106*20/8
+106*3
4.55*107

## Slide 46: Preclass 4
Cycles reading from large memory for a, b
 | a[i]*b[i] | a[b[i]]
1-word wide |  | 
8-word wide |  | 
Cycles reading a, b from large memory.
20 cycle read latency; MAX=106

## Slide 47: Lesson
Cheaper to access wide/contiguous blocks memory
  In hardware
  From the architectures typically build
Can achieve higher bandwidth on large block data transfer
  Than random access of small data items

## Slide 48: Bank Memory
Break memory into independent banks
  Allow banks to operate concurrently

## Slide 49: Bank Memory
Break memory into independent banks
  Allow banks to operate concurrently

## Slide 50: Preclass 4 Banked
20 cycle read latency; MAX=106
Put odd a, b in one bank, even in other.
Cycles reading a, b from large memory?

## Slide 51: Preclass 4 Banked
20 cycle read latency; MAX=106
Put odd a, b in one bank, even in other.
Cycles reading a, b from large memory?

## Slide 52: Banking Costs
Area compare
  One memory bank
    Depth 1024, width 64
  Two memory banks
    Depth 1024, width 32
Which smaller?
What is difference?

## Slide 53: Memory Organization
Architecture contains
  Large memories
    For density, necessary sharing
  Small memories local to compute
    For high bandwidth, low latency, low energy
Need to move data
  Among memories
    Large to small and back
    Among small

## Slide 54: Big Ideas
Memory bandwidth and latency can be bottlenecks
Exploit small, local memories
  Easy bandwidth, low latency, energy
Exploit data reuse
  Keep in small memories
Minimize data movement
  Small, local memories keep distance short
  Minimally move into small memories

## Slide 55: Admin
Reading for Wednesday on canvas
HW2 due Friday