## Slide 1: ESE532: System-on-a-Chip Architecture
Day 4: September 11, 2019
Parallelism Overview
Pickup:
1 Preclass
1 Lego instructions
1 feecback
1 bag of Legos

## Slide 2: Today
Compute Models
  How do we express and reason about parallel execution freedom
Types of Parallelism
  How can we slice up and think about parallelism?

## Slide 3: Message
Many useful models for parallelism
  Help conceptualize
One-size does not fill all
  Match to problem

## Slide 4: Parallel Compute Models

## Slide 5: Sequential Control Flow
Control flow
Program is a sequence of operations
Operation reads inputs and writes outputs into common store (memory)
One operation runs at a time
  defines successor
Model of correctness is sequential execution
Examples
C (Java, …)
Finite-State Machine (FSM) / Finite Automata (FA)

## Slide 6: Parallelism can be explicit
State which operations occur on a cycle
Multiply, add for quadratic equation
cycle | mpy | add
1 | B,x | 
2 | x,x | (Bx)+C
3 | A,x2 | 
4 |  | Ax2+(Bx+C)

## Slide 7: Parallelism can be implicit
Sequential expression
Infer data dependencies
T1=x*x
T2=A*T1
T3=B*x
T4=T2+T3
Y=C+T4
Or
Y=A*x*x+B*x+C

## Slide 8: Implicit Parallelism
d=(x1-x2)*(x1-x2) + (y1-y2)*(y1-y2)
What parallelism exists here?

## Slide 9: Parallelism can be implicit
Sequential expression
Infer data dependencies
for (i=0;i<100;i++)
y[i]=A*x[i]*x[i]+B*x[i]+C
Why can these operations be performed in parallel?

## Slide 10: Term: Operation
Operation – logic computation to be performed

## Slide 11: Dataflow / Control Flow
Dataflow
Program is a graph of operations
Operation consumes tokens and produces tokens
All operations run concurrently
Control flow (e.g. C)
Program is a sequence of operations
Operation reads inputs and writes outputs into common store
One operation runs at a time
  defines successor

## Slide 12: Token
Data value with presence indication
  May be conceptual
    Only exist in high-level model
    Not kept around at runtime
  Or may be physically represented
    One bit represents presence/absence of data

## Slide 13: Token Examples?
How ethernet know when a packet shows up?
  Versus when no packets are arriving?
How serial link know character present?
How signal miss in processor data cache and processor needs to wait for data?

## Slide 14: Operation
Takes in one or more inputs
Computes on the inputs
Produces results
Logically self-timed
  “Fires” only when input set present
  Signals availability of output

## Slide 16: Dataflow Graph
Represents
  computation sub-blocks
  linkage
Abstractly
  controlled by data presence

## Slide 17: Dataflow Graph Example

## Slide 18: Sequential / FSM
FSM is degenerate dataflow graph where there is exactly one token
cycle | mpy | add | next
S1 | B,x |  | x-->S2, else S1
S2 | x,x | (Bx)+C | S3
S3 | A,x2 |  | S4
S4 |  | Ax2+(Bx+C) | S1
S1
S2
S3
S4
x not
present?

## Slide 19: Sequential / FSM
FSM is degenerate dataflow graph where there is exactly one token
cycle | mpy | add | next
S1 | B,x |  | x-->S2, else S1
S2 | x,x | (Bx)+C | S3
S3 | A,x2 |  | S4
S4 |  | Ax2+(Bx+C) | S1
S1
S2
S3
S4

## Slide 20: Communicating Threads
Computation is a collection of sequential/control-flow “threads”
Threads may communicate
  Through dataflow I/O
  (Through shared variables)
View as hybrid or generalization
CSP – Communicating Sequential Processes  canonical model example

## Slide 21: Video Decode
Parse
Audio
Sync to HDMI
Video
Why might need to synchronize to send to HDMI?

## Slide 22: Compute Models

## Slide 23: Value of Multiple Models
When you have a big enough hammer, everything looks like a nail.
Many stuck on single model
  Try to make all problems look like their nail
Value to diversity / heterogeneity
  One size does not fit all

## Slide 24: Types of Parallelism

## Slide 25: Types of Parallelism
Data Level – Perform same computation on different data items
Thread or Task Level – Perform separable (perhaps heterogeneous) tasks independently
Instruction Level – Within a single sequential thread, perform multiple operations on each cycle.

## Slide 26: Pipeline Parallelism
Pipeline – organize computation as a spatial sequence of concurrent operations
  Can introduce new inputs before finishing
  Instruction- or thread-level
  Use for data-level parallelism
  Can be directed graph

## Slide 27: Sequential
Single person build E
Latency?
Throughput?
Build 1

## Slide 28: Data Parallel
Everyone in class build own E
Latency?
Throughput?
Ideal speedup?
Resource Bound?
  100 Es, 12 people
When useful?

## Slide 29: Data-Level Parallelism
Data Level – Perform same computation on different data items
Ideal: Tdp = Tseq/P
(with enough independent problems, match our resource bound computation)

## Slide 30: Thread Parallel
Each person build indicated letter
Latency?
Throughput?
Speedup over sequential build of 6 letters?
Build 2

## Slide 31: Thread-Level Parallelism
Thread or Task Level – Perform separable (perhaps heterogeneous) tasks independently
Ideal: Ttp = Tseq/P
Ttp=max(Tt1,Tt2,Tt3,…)
  Less speedup than ideal if not balanced
Can produce a diversity of calculations
  Useful if have limited need for the same calculation

## Slide 32: Instruction-Level Parallelism
Build single letter in lock step
Groups of 3
Resource Bound for 3 people building 9-brick letter?
Announce steps from slide
  Stay in step with slides
Build 3

## Slide 33: Group Communication
Groups of 3
Note who was person 1 task
2, 3 will need to pass completed substructures

## Slide 34: Step 0

## Slide 35: Step 1

## Slide 36: Step 2

## Slide 37: Step 3

## Slide 38: Instruction-Level Parallelism (ILP)
Latency?
Throughput?
Can reduce latency for single letter
Ideal: Tlatency = Tseqlatency/P
  …but critical path bound applies, dependencies may limit

## Slide 39: Bonus (time permit): Instruction-Level Pipeline
Each person adds one brick to build
Resources? (people in pipeline?)
Run pipeline once alone
Latency? (brick-adds to build letter)
Then run pipeline with 5 inputs
Throughput? (letters/brick-add-time)
Build 4

## Slide 40: Thread Graph
How would we build with task level parallelism?
  Tasks?
  Dependencies?

## Slide 41: Types of Parallelism
Data Level – Perform same computation on different data items
Thread or Task Level – Perform separable (perhaps heterogeneous) tasks independently
Instruction Level – Within a single sequential thread, perform multiple operations on each cycle.

## Slide 42: Pipeline Parallelism
Pipeline – organize computation as a spatial sequence of concurrent operations
  Can introduce new inputs before finishing
  Instruction- or thread-level
  Use for data-level parallelism
  Can be directed graph

## Slide 43: Big Ideas
Many parallel compute models
  Sequential, Dataflow, CSP
Find natural parallelism in problem
Mix-and-match

## Slide 44: Admin
Reading Day 5 on web
HW2 due Friday
HW3 out
Return Legos 
Recitation in here at noon
  Will take questions after class in hall