## Slide 1: ESE532: System-on-a-Chip Architecture
Day 13: October 19, 2020
Vitis OpenCL
Data Transfer Model

## Slide 2: Previously
Value of small, local memories
Tune local memories in C
DMA as data-movement threads

## Slide 3: Today
Vitis/OpenCL Interface
Execution Model (Part 1)
Host-Side Programming (Part 2)
FPGA-Side Programming (Part 3)

## Slide 4: Message
Vitis uses an explicit DMA transfer interface
Can build our streaming model on top of primitives offers
Will need to tune parameters and use carefully to get maximize performance
  Good and bad  largely exposed

## Slide 5: Note
OpenCL interface in Vitis is new
In past SDSoC took care of some of this
Still figuring out how to use interfaces to get the implementations that we know are possible on the FPGA
  A few things in lecture will be more tentative
  HW6 experimentation and delay

## Slide 6: Execution Model(s)
Part 1

## Slide 7: Model
Host and Accelerator
Host control
  Set accelerator arguments
  Tell it to start
  DMA bulk data to accelerator
  Run as independent thread
  Synchronize on data return

## Slide 8: Remember: Preclass 4a
Set arguments to accelerator
Accelerator
Uses to
grab inputs

## Slide 9: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 10: Function Call
Host and Accelerator
Host control
  Set accelerator arguments
  Tell it to start
  DMA bulk data to accelerator
  DMA result back
  Host program wait on accelerator completion

## Slide 11: Separate Accelerator Thread
Host and Accelerator
Host control
  Set accelerator arguments
  Tell it to start
  DMA bulk data to accelerator
  DMA result back
  Host execute something else
  Host program synchronize before use accelerator result

## Slide 12: PS<->PL Interface
Xilinx UG1393, Fig. 2 (Ch. 3)
Part 2
Part 3

## Slide 13: Minimal
Simple case one host process, one accelerator

## Slide 14: Accelerator Stream
Dataflow stream accelerators on host side

## Slide 15: Streaming
Map general streaming
Use multiple threads
  Even processors

## Slide 16: Streaming
Map general streaming
Use multiple threads
  Even processors
… and multiple accelerators
Given space, any streaming case
  DMA buffers cross PS<->PL

## Slide 17: Data Movement (Options)
Access from global memory
Configure DMA/accelerator with main-memory pointer
DMA copy into BRAM memories
  Built on top of other with DMA copy loop

## Slide 18: Remember: Preclass 4a

## Slide 19: Host-Side Programming
Part 2

## Slide 20: Outline
Platform
Device
Context
Command Queue
Load FPGA
Buffers and Transfer
Kernel Execution
Synchronize on Result
Overlap Data and Compute
Running Multiple Kernels

## Slide 21: Platform
For general case where have multiple OpenCL platforms
Silly for Ultra96 SoC
  and, looks like we can partially hide

## Slide 22: Device
For case of multiple FPGAs  which FPGA
Also somewhat silly for Ultra96 with single FPGA (PL)
F1.x16large has multiple FPGAs

## Slide 23: Device
Our Utilities.cpp,h – hide Platform
  std::vector<cl::Device> devices = get_xilinx_devices();
  devices.resize(1);
  cl::Device device = devices[0];
Get away with simplification
  Know what only Xilinx platform
  Know only one device (F1.x2large, Ultra96)

## Slide 24: Context
Context for device
  Not sure what flexibility/differentiation this is giving
  Supports some error callback
  Maybe just for compatibility with OpenCL

## Slide 25: Command Queue
Setup queue to issue commands
For “programming” interactions with accelerators
Use to set them up to happen as separate thread

## Slide 26: Load Bitstream on FPGA
Where we actually reconfigure FPGA
  Option to choose which to load
  Option to reconfigure during operation under host control
    Probably not one we’ll exercise this term

## Slide 27: Kernels
Setup the actual accelerators to call
  Extract handle to reference them from the loaded bitstream (program)
  Just naming them at this point

## Slide 28: Preclass 1
Kernel with
  10ms input transfer
  30ms compute
  5ms outputs
Latency?
Throughput if must serialize?
Throughput if overlap data transfers and computation?

## Slide 29: Preclass 1

## Slide 30: Host and Device Memory View
Host pointers not necessarily meaningful to device
  Need to map
  Different memories? (may depend on platform?)
  Virtual vs. Physical addresses?
  Same memory, different address map?

## Slide 31: Buffers and Transfer
Create
Buffers
Set kernel
pointers
Host side pointers
Fill with host data
Launch data transfer
(enqueue)

## Slide 32: Remember: Preclass 4a
clSetKernelArg
Use
dev_mem_ptr

## Slide 33: Movement Options
clEnqueueReadBuffer (WriteBuffer)
  Not guarantee timing of transfer
clEnqueueMigrateObjects
  Supports overlap of compute and communicate
  recommended

## Slide 34: Remap Device Pointer
Migration remap dev_mem_ptr
(don’t know if this is happening this way)

## Slide 35: Kernel Invocation
After
  Kernel arguments set
  Buffer transfers have been enqueued
Causes to actual run on data transfered

## Slide 36: Synchronize
Transfers, kernel concurrently
Must synchronize to know finished
q.enqueueMigrateMemObjects({in1_buf, in2_buf}, 0, NULL, &event_sp);
clWaitForEvents(1, (const cl_event *)&event_sp);
q.enqueueTask(krnl_mmult, NULL, &event_sp);
clWaitForEvents(1, (const cl_event *)&event_sp);

## Slide 37: Preclass 2a
Break kernel into there 10ms pieces and use dataflow between them
  10ms input transfer
  10ms compute x 3
  5ms output transfer
Throughput?

## Slide 38: Preclass 1 and 2

## Slide 39: Dataflow: Host-to-kernel
Create a dataflow stream between host process and accelerator
  Like DATAFLOW pragma
  Control on FPGA/kernel side (coming up)
Overlap next computation (setup) on host with FPGA kernel
USG1393 says embedded platforms not support?

## Slide 40: Preclass 2b
How many additional inputs send before get associated output? (pipeline depth)

## Slide 41: Kernel Completion/ Synchronization
Don’t have to synchronize right after an operation
Can have several in flight (in pipeline)
Synchronize only after sending several (pipeline depth) inputs

## Slide 42: Kernel Completion/ Synchronization
Example, slightly simpler
Don’t have to synchronize right after an operation
Can start several kernel invocations
Defer wait until later

## Slide 43: Run Multiple Tasks
for (int i=0; i<num_iter; i++) {
q.enqueueMigrateMemObjects({subbuf_doc_words[i]}, 0, &wordWait, &buffDone); wordWait.push_back(buffDone); q.enqueueTask(kernel, &wordWait, &krnlDone); krnlWait.push_back(krnlDone); q.enqueueMigrateMemObjects({subbuf_inh_flags[i]}, CL_MIGRATE_MEM_OBJECT_HOST, &krnlWait, &flagDone); flagWait.push_back(flagDone);
}
// then synchronize
for (int i=0; i<num_iter; i++) { flagWait[i].wait(); }

## Slide 44: Overlapping Data and Compute
Use control of when synchronize to overlap data and compute
Start (queue up) next data transfer and invocation before dataflow pipeline finishes
Need to reason about (or experiment with) how many to in flight
  When to synchronize

## Slide 45: Running Multiple Kernel Instances
Can have multiple instances of same kernel on FPGA
Dispatch from Out-of-Order command queue
Will distribute among identical kernels

## Slide 46: Parallelism
Pipeline/Dataflow
  With Host Dataflow
Task Parallelism
  Launch multiple accelerator
Data Parallelism
  Define multiple instances of one accelerator and enqueue work for

## Slide 47: Cleanup
Need to release/free resources setup

## Slide 48: FPGA-Side Programming
Part 3

## Slide 49: Interface Pragmas
Assign AXI
  Bundles
Host-to-Kernel
Burst read
Interface width

## Slide 50: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 51: Programmable SoC
AXI Channels
128b wide
@ 333 MHz
=5.3GB/s

## Slide 52: AXI Channels
Can tell it to use AXI Channels
By default (as shown above) all share same channel

## Slide 53: AXI Channels
Separate names to use different
Note, not naming to match ZCU3EG names
  Portability across targets

## Slide 54: Older and Defaults
2019.2:
#pragma HLS INTERFACE s_axilite port = in1 bundle = control
#pragma HLS INTERFACE s_axilite port = in2 bundle = control
#pragma HLS INTERFACE s_axilite port = out_r bundle = control
#pragma HLS INTERFACE s_axilite port = size bundle = control
#pragma HLS INTERFACE s_axilite port = return bundle = control
#pragma HLS INTERFACE m_axi port=in1 offset=slave bundle=gmem
#pragma HLS INTERFACE m_axi port=in2 offset=slave bundle=gmem
#pragma HLS INTERFACE m_axi port=out_r offset=slave bundle=gmem
2020.1:
#pragma HLS INTERFACE m_axi port=in1 bundle=gmem
#pragma HLS INTERFACE m_axi port=in2 bundle=gmem
#pragma HLS INTERFACE m_axi port=out_r bundle=gmem

## Slide 55: Programmable SoC
AXI Channels
128b wide
@ 333 MHz
=5.3GB/s

## Slide 56: Older and Defaults
2019.2:
#pragma HLS INTERFACE s_axilite port = in1 bundle = control
#pragma HLS INTERFACE s_axilite port = in2 bundle = control
#pragma HLS INTERFACE s_axilite port = out_r bundle = control
#pragma HLS INTERFACE s_axilite port = size bundle = control
#pragma HLS INTERFACE s_axilite port = return bundle = control
#pragma HLS INTERFACE m_axi port=in1 offset=slave bundle=gmem
#pragma HLS INTERFACE m_axi port=in2 offset=slave bundle=gmem
#pragma HLS INTERFACE m_axi port=out_r offset=slave bundle=gmem
2020.1:
#pragma HLS INTERFACE m_axi port=in1 bundle=gmem
#pragma HLS INTERFACE m_axi port=in2 bundle=gmem
#pragma HLS INTERFACE m_axi port=out_r bundle=gmem

## Slide 57: Remember: Preclass 4a
S-AXI Control – load pointers
M-AXI transfer
Using pointers

## Slide 58: Host-to-kernel Dataflow
ap_control_chain

## Slide 59: Burst Transfer
Where have we seen this before?

## Slide 60: Remember: Preclass 4a

## Slide 61: Burst Transfer
Use Dataflow to setup as separate threads on accelerator side
Believe this is way to burst copy into local memory

## Slide 62: Data Movement (Options)
Access from global memory
Configure DMA/accelerator with main-memory pointer
DMA burst copy into BRAM memories
  Built on top of other with DMA copy loop

## Slide 63: Preclass 3, 4
333MHz cycle time on bus
Peak bandwidth if transfer per cycle
  32b
  64b
  128b
Memory at 4 GB/s
  Which widths make bus the bottleneck?
  Memory?

## Slide 64: Width
Will transfer at width of data type give
May need to pack and unpack data to exploit full width

## Slide 65: Big Ideas
Data between PS and PL managed as DMA
Can exploit familiar parallelism
  Thread, Data, Streaming Dataflow
  Overlap compute and communicate
Must manage some pieces pretty explicitly

## Slide 66: Admin
Feedback
Reading for Wednesday on web
HW6
  Out soon?
    Delayed…as mentioned earlier new interface
    Figuring out what that means about deadlines…
  Uses Ultra96
  At least one partner has Ultra96