## Slide 1: ESE532: System-on-a-Chip Architecture
Day 15: October 26, 2020
Development by
Incremental Refinement

## Slide 2: Today
Incremental Refinement
  Demand
  Benefits
  Simplifications (Part 2)
    Example: render
  Interfaces (Part 3)
  Defensive Programming
Source Code Repositories

## Slide 3: Message
Focus on interfaces early
  Integrate first
Start with something simple that works end-to-end and incrementally refine
  May lack features
  May perform poorly
  …but it lets you resolve interfaces early

## Slide 4: Common Mistake
Build pieces, then integrate at the end
Spend most of available time on components
  Then try to integrate for first time near deadline
  Not enough time to integrate/debug at end
    Worst-case don’t have a working solution
    Spend more time fixing than if had identified incompatibilities early

## Slide 5: Standard Chip Aphorism
Almost all ASICs work when first fabricated
  …until you put them on the board.
    Then maybe 50%
[usually say “first spin” – where each “spin” is a separate manufacturing run]
ASIC: Application Specific Integrated Circuit
  (custom chip)

## Slide 6: Recommended Approach
Decompose problem
Focus on how components interact
Figure out simplified functionality easy to assemble
Get minimum functionality end-to-end system running early
  Even if means cut corners, solve simplified piece of problem
Chart path to refine pieces to goal

## Slide 7: Benefits

## Slide 8: Benefits: Overview
Agree on interfaces up front
Supports parallel development, testing, debugging
Confidence-boosting win of having something that works
Digest problem -- supports work in small bursts

## Slide 9: Interface First
Agree on interfaces up front
Each component knows interface
Can replace each component independently
Simple baseline provides scaffolding

## Slide 10: Parallel Development
With interfaces defined…
Each component can be (mostly) independently developed and refined
Simple baseline provides scaffolding
  Framework to test each component independently as develop and refine
Particularly important for team
  …helpful for individual, too
    Contains what need to think about at a time

## Slide 11: Confidence Boost
Get to see it working
Know you have something
  Just a question of how sophisticated can you make it?

## Slide 12: Digested Problem
Easier to concentrate on what need to do for this piece
Can make tangible process in short bursts
  …time can find between lectures…

## Slide 13: Continuous Integration
Pieces always fit into interface scaffold
Add pieces, functionality as available
See improvement
Identify interface problems early
  …and refine them

## Slide 14: Part 2: Example
Rendering

## Slide 15: Rendering Example
Create a 2D (video) image of a 3D object (set of objects)
For: computer-generated graphics
  Movies
  Video games

## Slide 16: Rendering
Input:
  collection of triangles
    Each 3 (x,y,z) positions
  Viewpoint
    Another (x,y,z) point
Output
  2D raster image (what you see on screen)
    Showings what’s visible
      Some things will be hidden behind others

## Slide 17: Rendering Decomposed
Pipeline of
  Projection
    Where do the points of this triangle end up in the viewed image?
    Matrix-multiplication to translate points
https://commons.wikimedia.org/wiki/File:Perspective_Projection_Principle.jpg

## Slide 18: Rendering Decomposed
Pipeline of
  Projection
    Where do the points of this triangle end up in the viewed image?
    Matrix-multiplication to translate points
  Rasterization
    Turn into pixels
    Fill pixels for triangle
https://commons.wikimedia.org/wiki/File:Perspective_Projection_Principle.jpg
https://commons.wikimedia.org/wiki/File:Raster_graphic_fish_20x23squares_sdtv-example.png
de:Benutzer Diskussion:Andreas -horn- Hornig/Bildwerkstatt

## Slide 19: Rasterization
By Drummyfish - Own work, CC0, https://commons.wikimedia.org/w/index.php?curid=80204437

## Slide 20: Rendering Decomposed
Pipeline of
  Projection
    Where do the points of this triangle end up in the viewed image?
    Matrix-multiplication to translate points
  Rasterization
    Turn into pixels
    Fill pixels for triangle
https://commons.wikimedia.org/wiki/File:Perspective_Projection_Principle.jpg
https://commons.wikimedia.org/wiki/File:Raster_graphic_fish_20x23squares_sdtv-example.png
de:Benutzer Diskussion:Andreas -horn- Hornig/Bildwerkstatt

## Slide 21: Rendering Decomposed
Pipeline of
  Projection
    Where do the points of this triangle end up in the viewed image?
    Matrix-multiplication to translate points
  Rasterization
    Turn into pixels
    Fill pixels for triangle
  Z-buffer
    Keep only the ones on top (not hidden)
      2D image + Z-depth – keep smallest
https://commons.wikimedia.org/wiki/File:Perspective_Projection_Principle.jpg
https://commons.wikimedia.org/wiki/File:Raster_graphic_fish_20x23squares_sdtv-example.png
de:Benutzer Diskussion:Andreas -horn- Hornig/Bildwerkstatt

## Slide 22: What’s Hard (Preclass 1)
What’s hard about each part?
  Projection?
  Rasterization?
  Z-Buffering?

## Slide 23: Simplifications

## Slide 24: Simplification: Overview
Solve simpler problem
Handle special subset of cases
  Avoid hard corner cases
Don’t worry about performance
Placeholder – stand in for real task
  Do minimal thing
  Use existing code

## Slide 25: Simple Placeholder
Identity function work?
  Pass input to output
Get form right in simple way?
  E.g. compression
    Drop samples/images/pixels to get down?

## Slide 26: Simplify (Preclass 3)
How could we simplify
  Projection?
  Rasterization?
  Z-Buffering?

## Slide 27: Simplified Projection Example
Projection as identity function?
  Will definitely give wrong image
    Except when viewpoint 0,0,0…. And all triangles at same depth…
  But the output of projection is triangles
    …so has right form for communication

## Slide 28: Simplified Rasterization
Maybe: Just put output pixels for triangle corners?
  Definitely wrong
  Has right form

## Slide 29: Simplified Z-Buffer Example
Intended
  Z-buffer
    Keep only the ones on top (not hidden)
      2D image + Z-depth – keep smallest
Simplified
  Just keep last value given
  If nothing overlaps  correct
    test with non-overlapping objects
  Even if overlap
    Looks wrong, but data has correct output form

## Slide 30: Solve Subset
Are there cases that are easier and cases that are harder?
  Can arrange input/tests to only include easier cases first
Solve the simple cases first
  E.g. non-overlapping objects in Z-buffer
Add support for harder cases later

## Slide 31: Parallel Rendering Example
Exploit data parallelism in rasterization
  Cut image into pieces
    Simplest: top half, bottom half
  Separate threads to rasterize each piece

## Slide 32: Parallel Rendering
Maybe ideal: rasterization sends triangle to appropriate rasterization thread
  If in top half
    send to top
  Else
    Send to bottom
What could make hard?

## Slide 33: Parallel Rasterization
Simple
  Triangles exclusively in one region
    One half
  Send to appropriate half
Hard
  Triangle in multiple halves
    Send to all (both)
    Or compute what goes in each and send triangles to each

## Slide 34: Parallel Rasterization Refinement
Start simple
  Assume only in one half, and only send there
  Use test cases split by halves
Incrementally get more sophisticated
  Sometimes send to both
Incrementally more
  Compute triangles for each region

## Slide 35: What makes hard?
Can avoid that on initial pass?
  E.g. – avoid computing what part of triangle is in each region

## Slide 36: Solve Small Instances?
If challenge is scale (handling large problems)
  Solve small problems first
  E.g. work on 64x64 image
    If trying to hit real time, easier with small image
    Small image may fit in BRAM (on-chip memory)
      Avoid complexities of data movement initally

## Slide 37: Non-Optimized Implementation
Often complexity comes from optimized implementation
  Start with simplest, non-optimized version as placeholder
  E.g.
    Brute force solution instead of clever algorithm
      Perhaps my most common mistake
    Large, inefficient data structure
      Instead of a more complicated, compact one

## Slide 38: Window Filter
Compute based on neighbors
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++)
  o[y][x]=F(d[y-1][x-1],d[y-1][x],d[y-1][x+1], d[y][x-1],d[y][x],d[y][x+1], d[y+1][x-1],d[y+1][x],d[y+1][x+1]);
Day 14

## Slide 39: Window Filter
Single read and write from dym, dy
for (y=0;y<YMAX;y++) for (x=0;x<XMAX;x++) {
  dypxm=dypx; dypx=dnew; dnew=d[y+1][x+1];
  dyxm=dyx; dyx=dyxp; dyxp=dy[x+1];
  dymxm=dymx; dymx=dymxp; dymxp=dym[x+1];
  o[y][x]=F(dymxm,dymx,dymxp, dyxm,dyx,dyxp, dypxm,dypx,dnew);
  dym[x-1]=dyxm;dy[x-1]=dypxm; }
Day 14

## Slide 40: Software First
Functional placeholder in software first

## Slide 41: Leverage Existing Solutions
Run some existing package, library to get the right answer
  E.g.
    call MATLAB to solve a matrix
    Invoke unix sort routine to get sorted data
    Invoke stand-alone image compressor or renderer

## Slide 42: What components depend upon?
Can a component output any data (random data?) and be adequate to exercise components interacts with?
  E.g. if feed into an integrator/accumulator
Need to output data of a given size?
Output need to maintain some property?
  Sorted?
  Unique?
Ok if doesn’t do its intended job well?
  E.g. intended to compress…

## Slide 43: Interfaces
Part 3

## Slide 44: Division of Task
Who is expected to do what?
  E.g.,
    Which piece discards duplicates?
    Which piece removes/flags invalid input?
  E.g. Renderer
    Does Projection only send in-bound triangles to each region rasterizer?
    Or does each region rasterizer need to deal with out-of-bounds triangle coordinates?

## Slide 45: Need to Know
What information does each component need to know?
How do we get that information to each component?

## Slide 46: Rendering Interface (Preclass 4)
What need to communicate between
  Projection  Rasterization
  Rasterization  Z-Buffering

## Slide 47: 3D Rendering: Need to Know
Projection
  How many triangles
  Triangle points (x,y,z) triples, – float + color
  Viewpoint x,y,z
Rasterization
  How many projected triangles (for region)
  Triangle points (x,y,z) triples + color-- short
Z-buffer
  (x,y,z,color) points – short
  How many (when done)?

## Slide 48: How Communicate?
Arrays
Streams
Shared memory locations?
Variable lengths?

## Slide 49: 3D Rendering
All naturally streaming
All potentially variable
  Triangles depend on object complexity and number of objects
  Projected depend on number in each region
    Not know in advance
  Pixels sent depends on size of projected triangles which changes with viewpoint
    Not know in advance

## Slide 50: 3D Rendering
Triangles and pixels unknown up front
How might we communicate number of triangles/pixels – communicate when done?

## Slide 51: 3D Rendering
Triangles and pixels unknown up front
How communicate?
  Send a record that means end-of-image?
    Extra bit?
    struct send_triangle { short p1x,p1y,p1z, p2x,p2y,p2z, p3x,p3y,p3z,
    color; Boolean last; }
    161b

## Slide 52: 3D Rendering
Triangles and pixels unknown up front
How communicate?
  Send a record that means end-of-image?
    Extra bit?
  Send in blocks with maximum size
    Accompany each block with a length
    Length is a separate stream from data
    For(i=0;i<TRIANGLES;i+=5)
      block_size.write(5);
      For(j=0;j<5;j++) triangles.write(t[i+j]);
    If (i!=TRIANGLES)
      block_size.write(TRIANGLES-i);
      for(j=0;j<TRIANGLES-I;j++)
        ….

## Slide 53: Properties components can assume?
Sorted?
Non–duplicate?
All in-bound?
Bound on input size in a block?

## Slide 54: Interfaces May Change
Interface first
  Means less surprise later
  Doesn’t mean know everything up front
Experience making simple work … and refining simple
  Often best way to understand needs of problem
Refine the interfaces incrementally, too

## Slide 55: 3D Rendering Start
Might start
  Projection = identity (convert short)
  Rasterization = triangle corners
  Z-buffer = save last
  Connect with streams
    Streams data has one bit for last triangle, pixel
Can put together quickly

## Slide 56: Rendering Start Placeholder
for(int i=0;i<TRIANGLES;i++)
struct triangle2d t2d;
t2d.p1x=tr[i].p1x;
t2d.p1y=tr[i].p1y;
t2d.p1z=tr[i].p1z;
// same for p2, p3
t2d.color=tr[i].color;
t2d.last=(i==TRIANGLES-1);
rasterize_in.write(t2d);

## Slide 57: Rendering Start Placeholder
While (true)
rt2d=rasterize_in.read();
pt.x=rt2d.p1x; pt.y=rt2d.p1y; // and z
pt.last=false; pt.color=r2d.color;
zin.write(pt);
pt.x=rt2d.p2x; pt.y=rt2d.p2y; // z
pt.last=false; pt.color=r2d.color;
zin.write(pt);
pt.x=rt2d.p3x; pt.y=rt2d.p3y; // z
pt.last=tr2d.last; pt.color=r2d.color;
zin.write(pt);
if (tr2d.last) break;

## Slide 58: Rendering Start Placeholder
while (true)
zpt=zin.read()
image[zpt.y][zpt.x]=zpt.color;
if (zpt.last) break;

## Slide 59: Rendering Start Refine
while (true)
zpt=zin.read()
if (z[zpt.y][zpt.x]>zpt.z) {
image[zpt.y][zpt.x]=zpt.color;
z[zpt.y][zpt.x]=zpt.z; }
if (zpt.last) break;

## Slide 60: Rendering Start Refine
// initialize z[] to MAXVAL
while (true)
zpt=zin.read()
if (z[zpt.y][zpt.x]>zpt.z) {
image[zpt.y][zpt.x]=zpt.color;
z[zpt.y][zpt.x]=zpt.z; }
if (zpt.last) break;
// large image – may need to split?
// … move off chip?
// represent in clever way

## Slide 61: 3D Rendering Independent Refinement
Projection – actually calculate projected coordinates
Rasterization – calculate pixels per triangle
  Test just fine using identity from projection
Z-buffer – add in Z-ordering
  Also testable with placeholder results

## Slide 62: 3D Rendering Refinement
Put them back together and work with interface defined
Could decide to change to communicating with blocks
Could refine for parallel rasterization
  …and could do that in pieces

## Slide 63: Defensive Programming

## Slide 64: Validate Assumptions/Requirements
If require a property on input of a module
  Good to have (optional) code to test for it
  [add that code second]
    Adds code/complexity to check
    E.g. check actually is in-bounds if should be
  Condition it in #ifdef so can disable for production, and re-enable for debug
  Good to catch invalid assumptions early
    …rather than spend time debugging to discover
    Setup discussion about interface…which part got it wrong

## Slide 65: Swap Modules
Make it easy to swap out implementations
  Swap between placeholders and refined implementations
  Swap among implementation versions
  Good to understand where problems introduced

## Slide 66: Source Code Repositories
git, svn

## Slide 67: Repository Message
When working on a project, especially with other people, want to use a source code repository
We’ve encouraged you to use for HWs
Start one for project group as soon as you create a project team

## Slide 68: Basic Idea
Central authoritative home for code
  Everyone can access
    Even if someone gets sick, laptop crashes
Keeps track of all versions
  As iterate and refine
Maybe keep track of multiple, in-use versions at once  branches

## Slide 69: Basic Benefits
Keep organized
  Common place for everything
Keep track of history
  Can go back to previous versions
    If screw up; if thought worked before
    Lowers chance of accidentally deleting
    …or losing when laptop disk crashes
Able to work on independently
  Share/integrate as stable
Branches
  Experiment without breaking main version
  E.g. change an interface…

## Slide 70: Big Ideas:
Integrate first
  Focus on interfaces early
Start simple
  Something that works end-to-end
Improve incrementally and iteratively

## Slide 71: Admin
Feedback
Project out and introduction Wednesday
HW6 due Friday