## Slide 1: ESE532: System-on-a-Chip Architecture
Day 17: Nov. 2, 2020
LZW, Associative Maps, Hash Tables

## Slide 2: Today
LZW Compression (Part 1)
Associative Memory (Part 2)
  Custom
  FPGA
Software Maps
  Tree (Part 3)
  Hash Tables (Part 4)
Hardware (FPGA) Hash Maps (Part 5)
  (probably next time)

## Slide 3: Message
Rich design space for Maps
Hash tables are useful tools

## Slide 4: Part 1: LZW Compression Lempel-Ziv-Welch

## Slide 5: Preclass 1
I AM S<2,3><5,4><0,4>
Message?
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
I |  | A | M |  | S | A | M |  | S | A | M |  | I |  | A | M

## Slide 6: Preclass 2, 3
Bits in unencoded (decoded) message?
  Assume 8b char
Bits for encoded message?
  Assume 9b for character
    1 bit to say is a character, then 8b char
  And 9b for <x,y> pair
    1 bit char, 4b for each of x and y

## Slide 7: Idea
Use data already sent as the dictionary
  Give short names to things in dictionary
  Don’t need to pre-arrange dictionary
  Adapt to common phrases/idioms in a particular document

## Slide 8: Encoding
Greedy simplification
  Encode by successively selecting the longest match between the head of the remaining string to send and the current window

## Slide 9: Algorithm Concept
While data to send
  Find largest match in window of data sent
  If length too small (length=1)
    Send character
  Else
    Send <x,y> = <match-pos,length>
  Add data encoded into sent window

## Slide 10: Preclass 4
How many comparisons per invocation?

## Slide 11: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
Only check position 0 for “starts with I”

## Slide 12: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
T-dictionary:
  Tap, The, Their, Then, There, Tuesday

## Slide 13: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
T-dictionary:
  Tap, The, Their, Then, There, Tuesday
If prefix same, why check redundantly?
  Generalize: Store things with common prefix together
    Share prefix among substrings
  Represent all strings as prefix tree

## Slide 14: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
If prefix same, why check redundantly?
  Store things with common prefix together
  Share prefix among substrings
  Represent all strings as prefix tree
Follow prefix trees with fixed work per input character

## Slide 15: Tree Example
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E

## Slide 16: Tree Algorithm
Tree Root for each character
Follow tree according to input until no more match
Send <name of last tree node>
  An <x,y> pair
Extend tree with new character
Start over with this character

## Slide 17: Tree Example
Label with <lastpos,len> pair
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E
<0,1>
<1,2>
<2,3>
<3,4>
<12,4>
<13,5>
<19,4>
<4,5>
<20,5>
T | H | E | N |  | A | N | D |  | T | H | E | R | E | , |  | T | H | E | Y
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
(only showing
Root for ’T’)

## Slide 18: Large Memory Implementation
int encode[SIZE][256];
Name tree node by position in chunk
  lastpos
c is a character
Encode[lastpos][c] holds the next tree node that extends tree node lastpos by c
  Or NONE if there is no such tree node

## Slide 19: Tree Example
Label with <lastpos,len> pair
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E
<0,1>
<1,2>
<2,3>
<3,4>
<12,4>
<13,5>
<19,4>
<4,5>
<20,5>
T | H | E | N |  | A | N | D |  | T | H | E | R | E | , |  | T | H | E | Y
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
encode[2][‘N’]=3
encode[2][‘R’]=12
encode[2][‘Y’]=19
encode[2][‘A’]=NONE
(only showing
Root for ’T’)

## Slide 20: Large Table for Tree
Addr | spc | A | … | D | E | … | H | … | N | … | R | S | T | … | Y
-1 |  | 5 |  |  |  |  |  |  |  |  |  |  | 0 |  | 
0 |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 
1 |  |  |  |  | 2 |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 3 |  | 12 |  |  |  | 19
3 | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  | 6 |  |  |  |  |  | 
6 |  |  |  | 7 |  |  |  |  |  |  |  |  |  |  | 
7 | 8 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 21: Memory Tree Algorithm
curr – pointer into input chunk
// follow tree
y=0; x=-1; // for no match, yet…
while(encode[x][input[curr+y]]!=NONE)
x=encode[x][input[curr+y]]; y++;
If (y>0)
send <x,y>
else
send input[curr+y]
encode[x][input[curr+y]]=curr+y
curr=curr+y+1

## Slide 22: Memory Tree Algorithm
curr – pointer into input chunk
// follow tree
y=0; x=-1; // for no match, yet…
while(encode[x][input[curr+y]]!=NONE)
x=encode[x][input[curr+y]]; y++;
If (y>0)
send <x,y>
else
send input[curr+y]
encode[x][input[curr+y]]=curr+y
curr=curr+y+1
Follow
Tree

## Slide 23: Memory Tree Algorithm
curr – pointer into input chunk
// follow tree
y=0; x=-1; // for no match, yet.
while(encode[x][input[curr+y]]!=NONE)
x=encode[x][input[curr+y]]; y++;
If (y>0)
send <x,y>
else
send input[curr+y]
encode[x][input[curr+y]]=curr+y
curr=curr+y+1
How much work per
character to encode?
Hint:
1) match case
2) not match

## Slide 24: Compact Memory
int encode[SIZE][256];
How many entries in this table are not NONE?
  Hint: SIZE is total number of positions. How many characters process? How many insertions per character processed?

## Slide 25: Compact Memory
int encode[SIZE][256];
Table is very sparse
If store as associative memory
  At most SIZE entries
Look at how to implement associative memories next

## Slide 26: LZW So Far – 4KB chunks
Brute Force
  Needs one byte per byte = 4KB = 1 BRAM
  DICT_SIZE=4096 comparisons per byte
Dense memory encode[SIZE][256]
  Need 2*256B per byte = 512*4KB = 512 BRAMs
  1 comparison and lookup per byte

## Slide 27: Associative Memories
Part 2

## Slide 28: Associative Memory
Maps from a key to a value
Key not necessarily dense
  Contrast simple RAM
  Cannot afford 2256 word memory
Day 16 Review

## Slide 29: Deduplicate
Compute chunk hash
Use chunk hash to lookup known chunks
  Data already have on disk
  Data already sent to destination, so destination will know
If lookup yields a chunk with same hash
  Check if actually equal (maybe)
If chunks equal
  Send (or save) pointer to existing chunk
Day 16 Review

## Slide 30: Deduplication Architecture
Day 16 Review

## Slide 31: Custom Hardware Associative Memory

## Slide 32: Memory Block Review
Match on address
Select wordline for a row
Reads out a word
Address dense and hardwired
One row for each 2Abits values
width
depth

## Slide 33: Address Blocks
Each address match is AND
width
depth
/A2&/A1&/A0
/A2&/A1&A0

## Slide 34: Address Blocks

## Slide 35: Memory Block Associative
Want address as key
Word is value
Key sparse
Rows<2keybits
Entries<2keybits
Key programmable
width
depth

## Slide 36: Programmable Key
Make row select programmable

## Slide 37: Contrast Assoc. and Dense Memory

## Slide 38: Associative Memory Bank

## Slide 39: Programmable Key
Assoc: 5b key, 8 entries, 8b value
How many memory bits?
Direct: 8 entries, 8b value
How many memory bits?

## Slide 40: Associative Memory Bank
Memory cells = entries*(keybits+valuebits)

## Slide 41: Associative Memory Bank
Will need to be able to write into key
  Another “fixed” decoder to generate key-word line for programming

## Slide 42: Associate Memory Cost
More expensive than equal capacity SRAM memory bank
  Memory cells in decoder
  Need to support write into key

## Slide 43: Associate Memory Cost
Physical associative memory for 4KB LZW Chunk tree encode
  4K entries
  12b output
  12b+8b=20b key
Memory cells assoc.?
Compare direct 4Kx12 memory (cells)?
  How much larger is assoc. for same capacity?
Compare 4096*256 with 12b result for dense LZW case (cells)?
  How much larger to solve same problem

## Slide 44: FPGA
Has BRAMs – normal memories, not associative
36Kb BRAM
  512x72
Can be 9b key  72b value assoc.
  Just using the memory sparsely
Or interpret as programmable decoder with 72 match lines

## Slide 45: Assoc. Mem from BRAM
For wider match
Cover 9b of key with each BRAM
Use 72 output bits to indicate if one of 72 entries match
AND together corresponding entries
Get 72 match bits
Re-encode match bits to lookup value

## Slide 46: BRAM Associative Memory
Previous slide expands match width
How would we expand capacity?

## Slide 47: BRAM Associative Memory

## Slide 48: Associative Memory Cost
Match unit
  Requires 1 BRAM per 9b of key per 72 entries
  (keylen/9b) * (entries/72)
  Asymptotically optimal (keylen*entries)
    But large constants
  LZW
    4K entries
    20b key
    How many BRAMs for match?

## Slide 49: Example Stored Values
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC

## Slide 50: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 51: Code Snippet
ap_uint<72> key_low[512];
ap_uint<72> key_high[512];
int value[72];
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
res=value[addr];

## Slide 52: How Lookup Work?
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC
Lookup 0x214 = 0x001 0x014

## Slide 53: Code Snippet
ap_uint<72> key_low[512];
ap_uint<712> key_high[512];
int value[72];
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
res=value[addr];

## Slide 54: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 55: Add another entry
How BRAM contents change to add this entry
for 0x19001
match | Key[17:9] | Key[8:0] | Value
0 | 0x001 | 0x014 | 0x01
1 | 0x001 | 0x01 | 0x34
2 | 0x0F0 | 0x014 | 0xE3
3 | 0x0C8 | 0x113 | 0xCC
4 | 0x0C8 | 0x01 | 0x2B

## Slide 56: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 0x2B
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 57: What does binary_encode do?
binary_encode(0000000…010000)=0x40
10000…0  71
0000…01  0
0000…010  1
for (i=0<i<72;i++)
  If (bit[i]==1) return i
Return(MISS); // if not find (all 0’s)
Technicalities – maybe check only one 1

## Slide 58: Class Ended Here

## Slide 59: Software Map
Part 3

## Slide 60: Software Map
Map abstraction
  void insert(key,value);
  value lookup(key);
Will typically have many different implementations

## Slide 61: Preclass 6
For a capacity of 4096
How many memory accesses needed
  When lookup fail?
  When lookup succeed (on average)?

## Slide 62: Tree Map (Preclass 7)
Build search tree
Walk down tree
For a capacity of 4096, assume balanced…
How many tree nodes visited
  When lookup fail?
  When lookup succeed (on average)?

## Slide 63: Tree Map LZW
Each character requires log2(dict) lookups
  12 for 4096
Each internal tree node hold
  Key (20b for LZW), value (12b), and 2 pointers (12b)
  7B
Total nodes 4K*2
Need 14 BRAMs for 4K chunk

## Slide 64: Tree Insert
Need to maintain balance
Doable with O(log(N)) insert
  Tricky
  See Red-Black Tree
    https://en.wikipedia.org/wiki/Red–black_tree
    https://www.geeksforgeeks.org/red-black-tree-set-1-introduction-2/

## Slide 65: 4K Chunk LZW Search
 | BRAMs | Operations
Brute Search | 1 | 4K
Tree with Dense RAM | 512 | 1
Tree with Full Assoc | 175 | 1
Tree with Tree | 14 | 12
Tree with Hybrid (still to come) | 52 | 1
36Kb BRAMs on ZU3EG = 216

## Slide 66: Hash Tables
Part 4

## Slide 67: High Performance Map
Would prefer not to search
Want to do better than log2(N) time
Direct lookup in arrays (memory) is good…

## Slide 68: Hash Table
Attempt to turn into direct lookup
Compute some function of key
  A hash
Perform lookup at that point
If hash maps a single entry (or no entry)
  Great, got direct lookup
    Like sparse table case
hash
Mem
lookup_key
match_key, value
Miss =
(match_key!=lookup_key)

## Slide 69: Preclass 8a
Average number of entries per hash when N > HASH_CAPACITY?
  Concrete example
    N= 4096
    HASH_CAPACITY=256

## Slide 70: Hash Table
Attempt to turn into direct lookup
Compute some function of key
  A hash
Perform lookup at that point
Typically, prepared for several keys to map to same hash  call it a bucket
  Keep list or tree of things in each bucket
hash
Mem
lookup_key
Bucket =
<k1,v1>,
<k2,v2>,
<k3,v3>

## Slide 71: Hash Table
Compute some function of key
  A hash
Perform lookup at that point
Find bucket with small number of entries
  Searching that bucket easier
  …but no absolute guarantee on maximum bucket size
hash
Mem
Bucket =
<k1,v1>,
<k2,v2>,
<k3,v3>
lookup_key

## Slide 72: Preclass 8b
Probability of conflict if N<<HASH_CAPACITY ?
  Concrete example
    N=4096
    HASH_CAPACITY=409600
Impact of HASH_CAPACITY on average bucket size?

## Slide 73: Hardware Hash Tables
Part 5
Skip to wrapup

## Slide 74: Hardware Hash
Want to avoid variable size buckets
  So can read in one lookup
    Can make wider for some fixed number of slots
  So can resolve in one cycle
hash
Mem
Bucket =
<k1,v1>,
<k2,v2>,
<k3,v3>
lookup_key

## Slide 75: Hash Size Distribution
Look at what the distribution looks like for number of entries
N – number of entries
C – HASH_CAPACITY
m – number of items in a slot
Compute distribution for each bucket size

## Slide 76: Preclass 9
m | 0 | 1 | 2 | 3 | 4+
C=1024 | 0.37 |  |  |  | 
C=2048 |  |  |  |  | 
C=4096 |  |  |  |  | 
N=1024

## Slide 77: Preclass 9
m | 0 | 1 | 2 | 3 | 4+
C=1024 | 0.37 | 0.37 | 0.18 | 0.061 | 0.019
C=2048 | 0.60 | 0.30 | 0.076 | 0.013 | 0.0017
C=4096 | 0.78 | 0.19 | 0.024 | 0.0020 | 0.00013
N=1024

## Slide 78: Hash
Can tune hash parameters to control distribution
Spend more memory  smaller buckets  less work finding things in buckets
  Memory-Time tradeoff
Still have possibility of large buckets
  …but probability is low

## Slide 79: Idea
Hash mostly works
Engineer hash to hold most cases
  Combination of
    sparcity (entries>N)
    Hold multiple entries per hash value
Few cases that overflow
  Store in small fully associative memory

## Slide 80: Hybrid Hash+Assoc.

## Slide 81: LZW 4K Chunk Hybrid
72 entry assoc. match
  needs 3 match BRAMs + 1 data BRAM
  Associative match 20b key
  72 entries (72/4096=1.7% for 4096)
So, can hold ~1% conflicts in 4K hash
Hash N=4096, C=16384, m=2, store 3
  Prob 3+: <1% (see table 1024, 4096)
  20b key+12b value=4B per entry
  16384*3*4B=4*3*4 BRAMs
48+4=52 BRAMs

## Slide 82: Further Optimization
Previous example illustrative
  Not necessarily optimal (explore parameters)
May be able to do better with multiple hashes
  See Dhawan reading paper
  May need to use that design in hybrid configuration with assoc. memory like previous example

## Slide 83: Hash Complexity
Want to compute these lookup hashes for hardware fast
  In a single cycle to keep II down for LZW
  Can xor-together a set of bits quickly in hardware
    Any 6-bits for one output bit in a single 6-LUT
    Means capacity must be power-of-2

## Slide 84: 4K Chunk LZW Search
 | BRAMs | Operations
Brute Search | 1 | 4K
Tree with Dense RAM | 512 | 1
Tree with Full Assoc | 175 | 1
Tree with Tree | 14 | 12
Tree with Hybrid | 52 | 1
36Kb BRAMs on ZU3EG = 216

## Slide 85: Big Ideas
Sparse, near O(1) Map access  Hash Table
Rich design space for engineering associative map solutions

## Slide 86: Admin
Feedback (including HW6)
Reading for Wednesday on Web
First project milestone due Friday
  Including teaming