## Slide 1: ESE532: System-on-a-Chip Architecture
Day 25: December 2, 2020
Real-Time Scheduling

## Slide 2: Today
Real Time
Part 1: Synchronous Reactive Model
Part 2: Interrupts and IO
  Polling alternative
  Timer?
Part 3: Resource Scheduling Graphs

## Slide 3: Message
Scheduling is key to real time
  Analysis
  Guarantees

## Slide 4: Synchronous Circuit Model
A simple synchronous circuit is a good “model” for real-time task
  Run at fixed clock rate
  Take input every cycle
  Produce output every cycle
  Complete computation between input and output
  Designed to run at fixed-frequency
    Critical path meets frequency requirement

## Slide 5: Synchronous Reactive Model
Discipline for Real-Time tasks
Embodies “synchronous circuit model”

## Slide 6: Synchronous Reactive
There is a rate for interaction with external world (like the clock)
Computation scheduled around these clock ticks (or time-slices)
  Continuously running threads
  Each thread performs action per tick
Inputs and outputs processed at this rate
Computation can “react” to events
  Reactions finite and processed before next tick

## Slide 7: Thread Form
while (1) { tick(); }
tick() -- yields after doing its work
  May be state machine
    May change state and have different behavior based on state
  May trigger actions to respond to events (inputs)

## Slide 8: Thread Model

## Slide 9: Tick Rate
Driven by application – demands of external control
  Control loop 100 Hz
    Robot, airplane, car, manufacturing plant
  Video at 33 fps
  Game with 20ms response
  Router with 1ms packet latency
    12ms

## Slide 10: Tick Rate
Multiple rates
  May need master tick as least-common multiple of set of interaction rates
    …and lower freq. events scheduled less frequently
  E.g. 100Hz control loop and 33Hz video
    Master at 10ms
    Schedule video over 3 10ms time-slots
      May force decompose into tasks fit into smaller time window since must schedule events at highest frequency

## Slide 11: Synchronous Reactive
Ideal model
  Per tick reaction (task processing) instantaneous
Separate function from compute time
Separate function from technology
  Feature size, processor mapped to
Like synchronous circuit
  If logic correct, works when run clock slow enough
  Works functionally when change technology
  Then focus on reducing critical path
     making timing work

## Slide 12: Timing and Function
Why want to separate function from technology and timing?
What happens when get faster (slower) processor?

## Slide 13: Synchronous Reactive Timing
Once functional,
  need to guarantee all tasks (in all states)
    Can complete in tick time-slot
    On particular target architecture
Identify WCET (worst-case execution time)
  Like critical path in FSM circuit
  Time of task on processor target

## Slide 14: Preclass 1
Time available to process objects?

## Slide 15: Preclass 1
Worst-case object processing time?

## Slide 16: Preclass 1
Maximum number of objects on single GHz processor?

## Slide 17: Synchronous Reactive Timing
Once functional,
  need to guarantee all tasks (in all states) can complete in tick time-slot
  On particular target architecture
Identify WCET
  Like critical path in FSM circuit
  Time of task on processor target
Schedule onto platform
  Threads onto processor(s)

## Slide 18: Threads Mapped to Processor

## Slide 19: Platforms
Platform 1: fast processor
Platform 2: many slow processors

## Slide 20: Synchronous Reactive Model
Discipline for Real-time tasks
Embodies the “synchronous circuit model”
  Master clock rate
  Computation decomposed per clock
  Functionality assuming instantaneous compute
  On platform, guarantee runs fast enough to complete critical path at “clock” rate

## Slide 21: Interrupts and IO
Part 2

## Slide 22: Interrupt
External event that redirects processor flow of control
Typically forces a thread switch
Common for I/O, Timers
  Indicate a need for attention

## Slide 23: Interrupts
Why would we use interrupts for I/O?

## Slide 24: Interrupts: Good
Allow processor to run some other work
Infrequent, irregular task service with low response service latency
  Low latency
  Low throughput

## Slide 25: Interrupts: Bad
Time predictability
  Real-time for computing tasks interrupted
Processor usage
  Costs time to switch contexts
Concurrency management
  Must deal with tasks executing non-atomically
    Interleave of interrupted service tasks
    Perhaps interleave of any task

## Slide 26: Interrupted Task
Add to list
  atmp=a
  new->next =atmp
  a=new
Remove from list
  removed=a->value
  rtmp=a->next
  a=rtmp
Running something that removes from list
Interrupt involves adding to list

## Slide 27: What can happen?
Add to list
  atmp=a
  new->next =atmp
  a=new
Remove from list
  removed=a->value
  rtmp=a->next
  a=rtmp
Sequence
  remove=a->tmp
  rtmp=a->next
  <interrupt>
  atmp=a
  new->next=atmp
  a=new
  <return>
  a=rtmp
What goes wrong?

## Slide 28: Interrupts: Bad
Time predictability
  Real-time for computing tasks interrupted
Processor usage
  Costs time to switch contexts
Concurrency management
  Must deal with tasks executing non-atomically
    Interleave of interrupted service tasks
    Perhaps interleave of any task

## Slide 29: Polling Discipline
Alternate to I/O interrupts
Every I/O task is a thread
Budget time and rate it needs to run
  E.g. 10,000 cycles every 5ms
  Likely tied to
    Buffer sizes
    Response latency
Schedule I/O threads as real-time tasks
  Some can be DMA channels

## Slide 30: IO Thread
while (1) { process_input(); }
Like tick() -- yields after doing its work

## Slide 31: Preclass 2
Input at 100KB/s
30ms time-slot window
Size of buffer?
100 cycles/byte, GHz processor – runtime of service routine?
  Fraction of processor capacity?

## Slide 32: Scheduling I/O Tasks

## Slide 33: Timer Interrupts
Why do we have timer interrupts in conventional operating systems?
  E.g. in linux?

## Slide 34: Timer Interrupts
Best effort tasks (i.e. non-real-time tasks)
  Have no guarantee to finish in bounded time
  Timer interrupts necessary
    to allow other threads to run
    fairness
    to switch to real-time service tasks
Need timer interrupts if need to share processor with real-time threads
  Alternate: Easier to segregate real-time and best-effort threads onto different processors

## Slide 35: Timer Interrupts?
Bounded-time tasks
  E.g. reactive tasks in real-time
  Task has guarantee to release processor within time window
  Not need timer interrupts to regain control from task
  (Maybe use deadline operations [Day24] for timer)

## Slide 36: Greedy Strategy
Schedule real-time tasks
  Scheduled based on worst-case, so may not use all time allocated
Run best-effort tasks at end of time-slice after complete real-time tasks
  Timer-interrupt to recover processor in time for start of next scheduling time slot
(adds complexity)

## Slide 37: Real-Time Tasks
Interrupts less attractive
  More disruptive
Scheduled polling better predictability
Fits with Synchronous Reactive Model

## Slide 38: Resource Scheduling Graphs
Part 3

## Slide 39: Scheduling
Useful to think about scheduling a processor by task usage
Useful to budget and co-schedule required resources
  Bus
  Memory port
  DMA channel

## Slide 40: Simple Task Model
Task requires
  Data to be transferred
  Local storage state
  Computational cycles
  (Result data to be transferred)
Uses resources
  Bus/channel to transfer data
    (in and out)
  Space in memory on accelerator
  Cycles on accelerator

## Slide 41: One Task
P1 |  |  |  |  |  |  |  |  | 
P2 |  |  |  |  |  |  |  |  | 
Bus |  |  |  |  |  |  |  |  | 
Mem |  |  |  |  |  |  |  |  | 

## Slide 42: Several Tasks
Resource | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
P1 |  |  |  |  |  |  |  |  | 
P2 |  |  |  |  |  |  |  |  | 
Bus |  |  |  |  |  |  |  |  | 
Mem |  |  |  |  |  |  |  |  | 

## Slide 43: Resource Schedule Graph
Extend as necessary to capture potentially limiting resources and usage
  Regions in memories
  Memory ports
  I/O channels

## Slide 44: Extended Details
Resource | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
P1 |  |  |  |  |  |  |  |  | 
P1 M0 |  |  |  |  |  |  |  |  | 
P1 M1 |  |  |  |  |  |  |  |  | 
P2 |  |  |  |  |  |  |  |  | 
P2 M0 |  |  |  |  |  |  |  |  | 
P2 M1 |  |  |  |  |  |  |  |  | 
Bus1 |  |  |  |  |  |  |  |  | 
Bus2 |  |  |  |  |  |  |  |  | 
OCM |  |  |  |  |  |  |  |  | 
DRAM |  |  |  |  |  |  |  |  | 

## Slide 45: Several Tasks
Resource | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
P1 |  |  |  |  |  |  |  |  | 
P1 M0 |  |  |  |  |  |  |  |  | 
P1 M1 |  |  |  |  |  |  |  |  | 
P2 |  |  |  |  |  |  |  |  | 
P2 M0 |  |  |  |  |  |  |  |  | 
P2 M1 |  |  |  |  |  |  |  |  | 
Bus1 |  |  |  |  |  |  |  |  | 
Bus2 |  |  |  |  |  |  |  |  | 
OCM |  |  |  |  |  |  |  |  | 
DRAM |  |  |  |  |  |  |  |  | 

## Slide 46: Approach
Ideal/initial – look at processing requirements
  Resource bound on processing
Look for bottlenecks / limits with Resource Bounds independently
  Add buses, memories, etc.
Plan/schedule with Resource Schedule Graph

## Slide 47: Preclass 3a
Resource Bound
  Data movement over bus?
  Compute on 2 processors?
  Compute on 2 processors when processor must wait while local memory is written?
Task | Data (bytes) | Compute cycles | Data+Compute Work
A | 1600 | 2600 | 
B | 200 | 600 | 
C | 800 | 3200 | 
D | 200 | 600 | 
E | 400 | 400 | 

## Slide 48: Resource Bound wait Transfer
Total processor cycles when processor must idle during transfer
  Cyclesproc =
RBproc=(Cyclesproc)/2
RBbus=
RB=max(Rbbus, RBproc)

## Slide 49: Preclass 3b Schedule
Processor wait for data load
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
P1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
P2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
200 cycle intervals

## Slide 50: Double Buffering
Common trick to overlap compute and communication
Reserve two buffers input (output)
Alternate buffer use for input
Producer fills one buffer while consumer working from the other
Swap between tasks
Tradeoff memory for concurrency
Sub-buffers in Vitis clEnqueueMigrateObjects

## Slide 51: Double Buffer

## Slide 52: Preclass 3c Schedule
Double Buffer
Minimum local memory space required?
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
P1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
P2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
200 cycle intervals

## Slide 53: Resource Schedule Graphs
Useful to plan/visualize resource sharing and bottlenecks in SoC
Supports scheduling
Necessary for real-time scheduling

## Slide 54: Big Ideas:
Scheduling is key to real time
  Analysis, Guarantees
Synchronous reactive
  Scheduling worst-case tasks “reactions” into master time-slice matching rate
Schedule I/O with polling threads
  Avoid interrupts
Schedule dependent resources
  Buses, memory ports, memory regions…

## Slide 55: Admin
Feedback
Reading for Monday online
P4 due Friday