## Slide 1: ESE532: System-on-a-Chip Architecture
Day 28: December 10, 2020
Wrapup

## Slide 2: Today
Part 1:
  What was course about
  Final
Part 2: Review w/ Simple Models
Part 3
  Other Courses
  Questions/Discussion

## Slide 3: Goal
How to design/select/map to SoC to reduce Energy/Area/Delay.

## Slide 4: Outcomes
Design, optimize, and program a modern System-on-a-Chip.
Analyze, identify bottlenecks, design-space
Decompose into parallel components
Characterize and develop real-time solutions
Implement both hardware and software solutions
Formulate hardware/software tradeoffs, and perform hardware/software codesign
Day 1

## Slide 5: Outcomes
Understand the system on a chip from gates to application software, including:
  on-chip memories and communication networks, I/O interfacing, RTL design of accelerators, processors, firmware and OS/infrastructure software.
Understand and estimate key design metrics and requirements including:
  area, latency, throughput, energy, power, predictability, and reliability.
Day 1

## Slide 6: Message for Day
Identify the Bottleneck
  May be in compute, I/O, memory, data movement
Focus and reduce/remove bottleneck
  More efficient use of resources
  More resources
Repeat
Day 2

## Slide 7: Abstract Approach
Identify requirements, bottlenecks
Decompose Parallel Opportunities
  At extreme, how parallel could make it?
  What forms of parallelism exist?
    Thread-level, data parallel, instruction-level
Design space of mapping
  Choices of where to map, area-time tradeoffs
Map, analyze, refine
Day 1

## Slide 8: SoC Designer Hardware Building Blocks
Computational blocks
  Adders, multipliers, dividers, ALUs
Data Storage
  Registers
  Memory blocks
Communication blocks
  Busses
  Multiplexers, Crossbars
  DMA Engines
Processors
I/O blocks
  Ethernet, USB, PCI, DDR, Gigabit serial links

## Slide 9: Final

## Slide 10: Final
Analysis
  Bottleneck
  Amdhal’s Law Speedup
  Computational requirements
  Resource Bounds
  Critical Path
  Latency/throughput/II
Model/estimate speedup, area, energy, yield
From Code
Forms of Parallelism
Dataflow, SIMD, VLIW, hardware pipeline, threads, reduce
Map/schedule task graph to (multiple) target substrates
Memory assignment and movement
Area-time points
Real Time

## Slide 11: Final
Like midterm
  Content
  Style
  Open book, notes
  Calculators allowed (encouraged)
Previous years final and solutions
  Linked to Fall 2019, Fall 2018, Fall 2017 syllabus (Spring 2017)
Friday, December 18
  Any time in 24 hour window
  2 hours (standard final exam period)

## Slide 12: Review
Part 2

## Slide 13: Sequential Computation
Computation requires a collection of operations
  Arithmetic
  Logical
  Data storage/retrieval

## Slide 14: Computations in C
Express computations in a programming language, such as C
Can execute computation in many different ways
  Sequential, parallel, spatial hardware
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 15: Memory Characteristics
Small memories
  Fast
  Low energy
  Not dense
    (high area per bit)
Large memories
  Slow
  High energy
  Dense (less area per bit)

## Slide 16: Memory and Compute
Computation involves both arith/logical ops and memory ops

## Slide 17: Memory and Compute
Computation involves both arith/logical ops and memory ops
Either can dominate
  Be bottleneck

## Slide 18: Memory and Compute
Timing
  Tmem=10
  Talu=1
Nmpy=
Nadd=
Nmem=
Total Time, T?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}
(not count loop, indexing costs in this sequence)

## Slide 19: Memory and Compute
Where bottleneck?
  Tmem=10
  Talu=1
Nmpy=16
Nadd=15
Nmem=95
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 20: Data Reuse
Reduce memory operations to large memory by storing in
  Registers
  Small memories
Tlmem>Tsmem

## Slide 21: Memory and Compute
a,b in large mem
y,z in small mem
  Tlmem=10
  Tsmem=1
  Talu=1
Nmpy=16
Nadd=15
Nlmem=?
Nsmem=?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 22: Memory and Compute
a,b in large mem
y,z in small mem
  Tlem=10
  Tsem=1
  Talu=1
Nmpy=16
Nadd=15
Nlmem=32
Nsmem=63
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}
Performance impact?

## Slide 23: Task Parallel
Can run unrelated tasks concurrently
Ideal: T(p) = T(1)/p

## Slide 24: Data Parallel
Can run same task on independent data in parallel
Ideal: T(p) = T(1)/p

## Slide 25: Data Parallel
Where reduce?
What’s data parallel?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 26: Vector/SIMD
Can perform same operation on a set of data items
Ideal: T(VL) = T(1)/VL
(Vector Length)

## Slide 27: Vector/SIMD
Can perform same operation on a set of data items
  Not everything vectorizable

## Slide 28: Vector/SIMD
What’s vectorizable?
Speedup vector piece VL=4
  (assume both memory and compute speedup)
Overall speedup
Amdahl’s Law speedup for VLinfintiy?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 29: Dataflow Pipeline
With no cycles in flowgraph
  (no feedback)
  (no loop carried dependencies)
Producer and consumer can operate concurrently
Prod
Consume

## Slide 30: Data Flow Pipeline
Producer/consumer here?
Time each
  Assuming Tmem=1
Granularity of dataflow pipeline
Size of buffer needed to allow concurrent operation?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 31: Data Flow Pipeline
(note changed second loop)
Granularity of dataflow pipeline
Size of buffer needed to allow concurrent operation?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[15]=y[15];
for (i=14;i>=0;i--)
z[i]=z[i+1]+y[i];
}

## Slide 32: Spatial Pipeline
Can build spatial pipeline of hardware operators to compute a dataflow graph
With no feedback: T=1
With feedback limit II: T=II

## Slide 33: Initiation Interval
What’s II?
  a, b still Tmem=1
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 34: Initiation Interval
What’s II?
  a, b, c Tmem=1
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i]+c[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 35: Initiation Interval
First loop (Tmem=1)
  Latency of loop body?
  II?
while(true) {
g=0;
for (i=0;i<16;i++) {
t=a[i]*b[i]+c[g];
y[i]=t;
g=t%16; }
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 36: Spatial Pipeline
Back to original code
Pipeline taking one a[i], b[i] per cycle?
  Tmem=1
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 37: Reduce
(note slightly different second loop)
Common pattern is a reduce operation
  Combine a set of data into a single value
Latency bound for second loop?
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z=0;
for (i=0;i<16;i++)
z+=y[i];
}

## Slide 38: Log-Depth Associative Reduce

## Slide 39: VLIW
Can control datapath to perform multiple, heterogeneous operations per cycle
  Tune parallelism
Op types: A, B, C
  Ops NA, NB, NC
  Number of Hardware Units HA, HB, HC
TRB=max(NA/HA, NB/HB, NC/HC,…)≤TVLIW
TCP≤TVLIW

## Slide 40: VLIW
VLIW
  1 load/store (a,b,z)
    Assume single cycle
  1 mpy
  1 add
  (ignoring increment for simplicity/consistent)
RB
CP
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 41: VLIW
VLIW
  1 load/store (a,b,z)
    Assume single cycle
  1 mpy
  1 add
  1 incr
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}
Cycle | mpy | add | Ld/st
0 | a*b 0 |  | a1
1 |  | +y[i] 0 | b1
2 |  |  | Z0

## Slide 42: VLIW
VLIW
  4 load/store (a,b,z)
    Assume single cycle
  2 mpy
  2 add
RB
CP
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 43: Memory Bottleneck
Memory can end up being bottleneck
Ideal: T(p) = Tcomp(1)/p+Tmem

## Slide 44: Memory Bottleneck
Pipeline to perform one multiply per cycle
Memory supplies one data item from large memory (a,b) every 10 cycles
Performance?
  (number of cycles)
while(true) {
for (i=0;i<16;i++)
y[i]=a[i]*b[i];
z[0]=y[0];
for (i=1;i<16;i++)
z[i]=z[i-1]+y[i];
}

## Slide 45: Memory Bottleneck
Memory can end up being bottleneck
Ideal: T(p) = Tcomp(1)/p+Tmem/Membw

## Slide 46: Memory Bottleneck
Invest in higher bandwidth
  Wider memory
  More memory banks
Exploit data reuse
  Smaller memories may have more bandwidth
  Smaller memories are additional banks
    More bandwidth

## Slide 47: Communication
Once parallel, communication may be bottleneck
Ideal (like VLIW):
  T≤max(Tcomp/p,Tmem/membw,Tcomm/netbw)

## Slide 48: Area
Can model area of various solutions
  Sum of component areas
  (watch interconnect)
Cost proportional A/Pchip
Without sparing
  Pchip = (Pmm)A
Sparing (did not cover this year)
  Pmofn

## Slide 49: Multi-Objective Optimization
Many forms of parallelism
Given fixed area (resources, energy)
  Maximize performance
  Select best architecture
Given fixed performance goal (Real Time)
  Find architecture that achieves
  With minimum area (energy, cost)

## Slide 50: Final
Analysis
  Bottleneck
  Amdhal’s Law Speedup
  Computational requirements
  Resource Bounds
  Critical Path
  Latency/throughput/II
Model/estimate speedup, area, energy, yield
From Code
Forms of Parallelism
Dataflow, SIMD, VLIW, hardware pipeline, threads, reduce
Map/schedule task graph to (multiple) target substrates
Memory assignment and movement
Area-time points
Real Time

## Slide 51: Other Courses Wrapup, Questions
Part 3

## Slide 52: Distinction
CIS240, 571(471)
Best Effort Computing
  Run as fast as you can
Binary compatible
ISA separation
Shared memory parallelism
Caching – automatic memory management
Superscalar
Pipelined processor
ESE532
Hardware-Software codesign
  Willing to recompile, maybe rewrite code
  Define/refine hardware
Real-Time
  Guarantee meet deadline
Non shared-memory models
Explicit memory management
VLIW

## Slide 53: Abstraction Stack
ESE539 HW/SW ML
Transistors
Devices: ESE521
(ESE218)
Digital:
ESE370/570
Processor Arch:
CIS 471/571
(CIS240)
SoC Arch:
ESE 532
Circuits/VLSI
Gates, Memories
Processors
Systems
Mixed Signal:
ESE 568
ADC, DAC
Switched Capacitors
Analog:
ESE419/572
Amplifier, Compare
Voltage/Current Ref.
Embedded Sys:
ESE350/519
Software

## Slide 54: Circuits and Computer Engineering
ESE370
Circuit Level Modeling & Optimization of Dig. Systems
Transistor models, CMOS logic, delay, scaling, energy, interconnects, flip-flops, noise, T-lines, RAM design
ESE578
RF Integrated
Circuits Design
m-wave Eng overview, T-line, Smith-chart, S-parameters, matching, passive devices, small signal amplifier, LNA and PA, mixed signal on chip
ESE319
Electronics
Diode & Transistor Circuits, Single Stage & Diff. Amplifiers, Filters, Oscillators
ESE419 (572)
Analog Integrated Circuits
MOSFET circuits, Ampl. Stages, I-Mirrors, Op-Amps, Feedback, Stability, Root Locus, Cascode Ampl.
or
Digital
Analog
ESE350
Embedded Systems
m-controller architectures, Interfacing, ADC, sensor and actuator control, ROS, network protocols
Embedded
(uP/uC)
ESE570
Digital Integrated Circuits
MOSFET Trans Models, Inverter switching, MOS Logic, Memories, Implementation methods, Layout.
ESE532
SoC Architecture
Hardware/Software
Codesign,
Parallelism, Analysis, Real-Time
ESE672
Integrated Communication Circuits
Receivers, Low-noise amplifiers, mixers, oscillators, phase lock loops, power amplifiers
CIS541
Embedded Cyber Physical Systems
Life-Critical, Real-Time,
Analysis,
Implementations
Validation/verification
ESE568 (Fall)
Mixed-Signal Circuits
A/D, D/A, sampling…
or
ESE519
Real-Time &
Embedded Systems
m-controller architectures, Interfacing, ADC, sensor and actuator control, ROS, network protocols
or
Notes: Simple Story

## Slide 55: Other Courses
Security: CIS331, CIS551
Networking: ESE407, CIS553
GPGPU (graphics focus): CIS565
Machine Learning: ESE539
  (was 680 this term)

## Slide 56: Message
Any interesting, challenging computation will require both hardware and software
SoC powerful implementation platform
  Target pre-existing
  Design customized for problem
  Exploit heterogeneous parallelism
Understand and systematically remove bottlenecks
  Compute, memory, communicate, I/O

## Slide 57: Admin
Feedback
Project Report due Today
Final: Friday, Dec. 18

## Slide 58: Question/Discussion