## Slide 1: ESE532: System-on-a-Chip Architecture
Day 6: September 23, 2020
Data-Level Parallelism

## Slide 2: Today
Data-level Parallelism
For Parallel Decomposition (Part 1)
Architectures (Part 2)
Concepts (Part 3)
NEON

## Slide 3: Message
Data Parallelism easy basis for decomposition
  When things are data parallel, exploiting for parallelism relatively easy
Data Parallel architectures can be compact
  pack more computations onto a fixed-size Integrated Circuit chip
  OR perform computation in less area

## Slide 4: Preclass 1
400 news articles
Count total occurrences of a string
How can we exploit data-level parallelism on task?
How much parallelism can we exploit?

## Slide 5: Parallel Decomposition

## Slide 6: Data Parallel
Data-level parallelism can serve as an organizing principle for parallel task decomposition
Run computation on independent data in parallel

## Slide 7: Exploit
Can exploit with
  Threads
  Pipeline Parallelism
  Instruction-level Parallelism
  Fine-grained Data-Level Parallelism

## Slide 8: Performance Benefit
Ideally linear in number of processors (resources)
Resource Bound:
  Tdp = (TsingleNdata )/ P
Tsingle = Latency on single data item
Tdp = Tsingle

## Slide 9: SPMD
Single Program Multiple Data
Only need to write code once
Get to use many times

## Slide 10: Preclass 2 Common Examples
What are common examples of DLP?
  Simulation
  Numerical Linear Algebra
  Signal or Image Processing
  Optimization

## Slide 11: Hardware Architectures
Part 2

## Slide 12: Idea
If we’re going to perform the same operations on different data, exploit that to reduce area, energy
Reduced area means can have more computation on a fixed-size IC chip.

## Slide 13: SIMD
Single Instruction Multiple Data

## Slide 14: Ripple Carry Addition
Can define logic for each bit, then assemble:
  bit slice

## Slide 15: Arithmetic Logic Unit (ALU)
Observe:
  with small tweaks can get many functions with basic adder components

## Slide 16: Arithmetic and Logic Unit

## Slide 17: ALU Functions
A+B w/ Carry
B-A
A xor B (squash carry)
A*B (squash carry)
/A
Key observation: every ALU bit does the same thing
on different bits of the data word(s).

## Slide 18: ARM v7 Core
ALU is Key compute operator in a processor

## Slide 19: W-bit ALU as SIMD
Familiar idea
A W-bit ALU (W=8, 16, 32, 64, …) is SIMD
Each bit of ALU works on separate bits
  Performing the same operation on it
    Trivial to see bitwise AND, OR, XOR
    Also true for ADD (each bit performing Full Adder)
Share one instruction across all ALU bits

## Slide 20: ALU Bit Slice

## Slide 21: Preclass 4
What do we get when add 65280 to 257
  32b unsigned add?
  16b unsigned add?

## Slide 22: ALU vs. SIMD ?
What’s different between
  128b wide ALU
  SIMD datapath supporting eight 16b ALU operations

## Slide 23: ALU vs. SIMD Example
Concretely show:
  16b wide ALU
  SIMD datapath with two 8b wide ALUs

## Slide 24: ALU vs. SIMD ?
How could we get both operations from the same hardware?
  128b wide ALU
  SIMD datapath supporting eight 16b ALU operations

## Slide 25: Segmented Datapath
Add a few gates to convert a wide datapath into one supporting a set of smaller operations
  Just need to squash the carry at points

## Slide 26: Segmented Datapath
Add a few gates to convert a wide datapath into one supporting a set of smaller operations
  Just need to squash the carry at points
But need to keep instructions (description) small
  So typically have limited, homogeneous widths supported

## Slide 27: Segmented 128b Datapath
1x128b, 2x64b, 4x32b, 8x16b

## Slide 28: Terminology: Vector Lane
Each of the separate segments called a Vector Lane
For 16b data on 128b datapath, this provides 8 vector lanes

## Slide 29: Performance
Ideally, pack into vector lanes
Resource Bound: Tvector = Nop/VL

## Slide 30: Register File
Small Memory
Usually with multiple ports
  Ability to perform multiple reads and writes simultaneously
Small
  To make it fast (small memories fast)
  Multiple ports are expensive

## Slide 31: SIMD Datapath
Logical View:
Layout View:

## Slide 32: Preclass 5
W | A(W) | % datapath | Instances | Peak 16b ops
16 |  |  |  | 
64 |  |  |  | 
128 |  |  |  | 
256 |  |  |  | 

## Slide 33: Preclass 5
W | A(W) x10^6 | % datapath | Instances | Peak 16b ops | Ratio
16 | 1.1 | 9 | 91 | 91 | 1.00
64 | 1.4 | 28 | 71 | 284 | 3.16
128 | 1.8 | 43 | 56 | 448 | 4.90
256 | 2.5 | 60 | 39 | 640 | 6.85
(c) |  |  |  |  | 
Why?

## Slide 34: To Scale Comparison

## Slide 35: To Scale W=1024

## Slide 36: Preclass 5
W | A(W) x106 | % datapath | Instances | Peak 16b ops | Ratio
16 | 1.1 | 9 | 91 | 91 | 1.00
64 | 1.4 | 28 | 71 | 284 | 3.16
128 | 1.8 | 43 | 56 | 448 | 4.90
256 | 2.5 | 60 | 39 | 640 | 6.85
(c) 16,500 | 100 | 100-epsilon | 1 | 1031 | 11.32
Why?

## Slide 37: Preclass 6: Vector Length
May not match physical hardware length
  Logical (application need): Vector Length
  Physical (hardware provide): Vector Lanes
vadd(int *a, int *b, int *res,
int vector_length) {
for (int i=0;i<vector_length;i++)
    res[i]=a[i]+b[i];
    }

## Slide 38: Preclass 6: Vector Length
May not match physical hardware length
  Logical (application need): Vector Length
  Physical (hardware provide): Vector Lanes
What happens when
  Vector length > Vector Lanes?
  Vector length < Vector Lanes?
  Vector length % (Vector Lanes) !=0
    E.g. vector length 13, for 8 vector lanes

## Slide 39: Performance
Resource Bound
  Tvector = Tcycle

## Slide 40: Preclass 3: Opportunity
Don’t need 64b variables for lots of things
Natural data sizes?
  Audio samples?
  Input from A/D?
  Video Pixels?
  X, Y coordinates for 4K x 4K image?

## Slide 41: Vector Computation
Easy to map to SIMD flow if can express computation as operation on vectors
  Vector Add
  Vector Multiply
  Dot Product

## Slide 42: Concepts
Part 3

## Slide 43: Terminology: Scalar
Simple: non-vector
When we have a vector unit controlled by a normal (non-vector) processor core often need to distinguish:
  Vector operations that are performed on the vector unit
  Normal=non-vector=scalar operations performed on the base processor core

## Slide 44: Vector Register File
Need to be able to feed the SIMD compute units
  Not be bottlenecked on data movement to the SIMD ALU
Wide RF to supply
With wide path to memory

## Slide 45: Point-wise Vector Operations
Easy – just like wide-word operations (now with segmentation)

## Slide 46: Point-wise Vector Operations
…but alignment matters.
If not aligned, need to perform data movement operations to get aligned

## Slide 47: Ideal
for (i=0;i<64;i=i++)
  c[i]=a[i]+b[i]
No data dependencies
Access every element
Number of operations is a multiple of number of vector lanes

## Slide 48: Skipping Elements?
How does this work with datapath?
  Assume loaded a[0], a[1], …a[63] and b[0], b[1], …b[63] into vector register file
for (i=0;i<64;i=i+2)
  c[i/2]=a[i]+b[i]

## Slide 49: Stride
Stride: the distance between vector elements used
for (i=0;i<64;i=i+2)
  c[i/2]=a[i]+b[i]
Accessing data with stride=2

## Slide 50: Load/Store
Strided load/stores
  Some architectures will provide strided memory access that compact when read into register file
Scatter/gather
  Some architectures will provide memory operations to grab data from different places to construct a dense vector

## Slide 51: Neon
ARM Vector Accelerator

## Slide 52: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 53: APU MPcore
UG1085
Xilinx
UltraScale
Zynq
TRM
(p53)

## Slide 54: Neon Vector
128b wide register file, 16 registers
Support
  2x64b
  4x32b (also Single-Precision Float)
  8x16b
  16x8b

## Slide 55: Sample Instructions
VADD – basic vector
VCEQ – compare equal
  Sets to all 0s or 1s, useful for masking
VMIN – avoid using if’s
VMLA – accumulating multiply
VPADAL – maybe useful for reduce
  Vector pair-wise add
VEXT – for “shifting” vector alignment
VLDn – deinterleaving load

## Slide 56: ARM Cortex A72 (a1-metal)
3-issue
2 NEON pipes
128b wide
Out-of-Order
16-stage pipe
https://cdn.mos.cms.futurecdn.net/jZpgkw43zy48UUofST6d5Z.png
Notes: https://www.tomshardware.com/reviews/arm-cortex-a72-architecture,4424.html
https://www.anandtech.com/show/9184/arm-reveals-cortex-a72-architecture-details

## Slide 57: ARM Cortex A53 (Ultra96) (similar to A-7 Pipeline)
https://arstechnica.com/gadgets/2011/10/arms-new-cortex-a7-is-tailor-made-for-android-superphones/
https://www.anandtech.com/show/8718/the-samsung-galaxy-note-4-exynos-review/3
2-issue
In-order
1 NEON pipe
64b wide
8-stage pipe

## Slide 58: Big Ideas
Data Parallelism easy basis for decomposition
Data Parallel architectures can be compact – pack more computations onto a chip
  SIMD, Pipelined
  Benefit by sharing (instructions)
  Performance can be brittle
    Drop from peak as mismatch

## Slide 59: Admin
Remember feedback
Reading for Day 7 online
HW3 due Friday
HW4 out soon…. (not, yet)