## Slide 1: ESE532: System-on-a-Chip Architecture
Day 7: September 28, 2020
Pipelining
Make sure can load Google doc
interaction – will flip to as
examples come up.
Notes: Background from: https://www.adhesivesmag.com/articles/97744-north-american-printed-circuit-board-industry-sees-spike-in-shipments-due-to-pandemic

## Slide 2: Previously
Pipelining in the large
  Not just for gate-level circuits
Throughput and Latency
Pipelining as a form of parallelism

## Slide 3: Today
Pipelining details (for gates, primitive ops)
Systematic Approach (Part 1)
Justify Operator and Interconnect Pipelining (Part 2)
Loop Bodies
Cycles in the Dataflow Graph (Part 3)
C-slow [probably separate record] (Part 4)

## Slide 4: Message
Pipelining is an efficient way to reuse hardware to perform the same set of operations at high throughput

## Slide 5: Multiplexer Gate
MUX
  When S=0, output=i0
  When S=1, output=i1
S | i0 | i1 | Mux2(S,i0,i1)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 6: Cycle
Two uses of term in this lecture:
Repetitive waveform
  E.g. sine wave or square wave
Graph cycle

## Slide 7: Waveform Cycles
How many cycles showing of sine wave?
How many cycles of square wave?

## Slide 8: Waveform Cycles
How many cycles showing of sine wave?
How many cycles of square wave?
Note: clock on which we pipeline is a square wave
  Talk about what happens in a clock cycle
  Talk about number of clock cycles

## Slide 9: Latch
Element that can hold a previous value of an input

## Slide 10: Register
Use a pair to create a flip-flop
  Also call register
What happens when
  CLK is low (0) ?
  CLK is high (1) ?
  CLK transitions from 0 to 1?

## Slide 11: Register
Use a pair to create a flip-flop
  Also call register
Sample D input on 01 transition of clock (CLK)
Never an open path from DQ
  One of the mux latches always in hold state

## Slide 12: Synchronous Circuit Discipline
Registers that sample inputs at clock edge and hold value throughout clock period
Compute from registers-to-registers
Clock Cycle time large enough for longest logic path between registers
Min cycle = Max path delay between registers
Comb
logic

## Slide 13: Preclass 1
Delay between registers as shown?

## Slide 14: Preclass 1
Move registers so can clock at adder delay? [show on Google Doc]

## Slide 15: Pipeline Reuse
Lower delay between clocks
  Higher clock rate
  Higher potential throughput
  Faster we reuse our logic
  More capacity get out of design
    Assuming registers cheap in area and time overhead
      Tsetup, Tclk->q ~ 20ps, Tadd ~ 500ps
      Registers ~ 10 transistors/bit
      Adder ~ 40—50 transistors/bit

## Slide 16: Preclass 2: What Happens?
What would be wrong with this pipelining?
For this initial design:

## Slide 17: Behavior

## Slide 18: Equations

## Slide 19: Behavior Add Register

## Slide 20: Equations

## Slide 21: Note Registers on Links
Some links end up with multiple registers.
Why?

## Slide 22: Consistent Pipelining
Makes sure a consistent input set arrives at each gate/operator
  Don’t get mixing between input sets

## Slide 23: Legal Register Moves
Retiming Lag/Lead
Lag: remove register every input add register every output
Lead: remove register every output add register every input

## Slide 24: Preclass 1
Retime using Lead/Lag

## Slide 25: Preclass 1 (revisited)

## Slide 26: Add Registers and Move
If we’re willing to add pipeline delay
  Add any number of pipeline registers at input
  Move registers into circuit to reduce cycle time
    Reduce max delay between registers

## Slide 27: Add Registers at Input

## Slide 28: Add Register and Retime
Add chain of registers on every input
Retime registers into circuit
  Minimizing delay between registers

## Slide 29: Add Registers and Retime
Lets us think about behavior
  What the pipelining is doing to cycles of delay
Separate from details of how redistribute registers
Behavioral equivalence between the registers-at-front and properly retimed version of circuit

## Slide 30: Justify Pipelining
(or composing pipelined operators)
Part 2

## Slide 31: Handling Pipelined Operators
Given a pipelined operator
  (or a pipelined interconnect)
Discipline of picking a frequency target and designing everything for that
  May be necessary to pipeline operator since its delay is too high
Due to hierarchy
  Pipelined this operator and now want to use it as a building block

## Slide 32: Examples
Run at 500MHz
Floating-point unit that takes 9ns
  Can pipeline into 5, 2ns stages
Multiplier that takes 6ns
Memory can access in 2ns
  Only if registers on address/inputs and output
  i.e. exist in own clock stage

## Slide 33: Interconnect Delay
Chips >> Clock Cycles
May have chip 100s of Operators wide
May only be able to reach across 10 operators in a 2ns cycle
Must pipeline long interconnect links

## Slide 34: Interconnect Example

## Slide 35: Methodology: Pipelined Operator Graph
Start with logical, unpipelined graph
Treat each pipelined operator as a set of unit-delay operators of mandatory depth
Treat each interconnect pipeline stage as a unit-delay buffer
Add registers at input
Retime into graph

## Slide 36: Model
3-stage Multiplier
Interconnect Delay
M1
M2
M3
I1
I2
I3
A
B

## Slide 37: Pipeline Loop
(and use for justify pipeline example)

## Slide 38: Preclass 4
Logical (unpipelined) dataflow graph for loop body

## Slide 39: Example Operators
Operator and Interconnect delays
  Multiplier 3 cycles
  Reading from Input array
    Memory op is cycle after computing address
    Takes one cycle delay bring data back to multiplier (or adder)

## Slide 40: Illustrate Need
What happens if just use graph as is (with operators pipelined as required)?

## Slide 41: Model Graph
Revised graph for modeling

## Slide 42: Pipeline Graph
Result after pipelining? [Google doc]

## Slide 43: Pipeline Graph
Result after pipelining?

## Slide 44: Pipelining Lesson
Can always pipeline an acyclic graph (no graph cycles) to fixed frequency target
  fixed pipelining of primitive operators
  Pipeline interconnect delays
Need to keep track of registers to balance paths
  So see consistent delays to operators

## Slide 45: Graph Cycles
Watch: Clock cycle Cycle time
Cycle in Graph
Part 3

## Slide 46: Preclass 3
Can we retime to reduce clock cycle time?
  [Google Doc show retiming]

## Slide 47: Retiming Limits?
What prevents us from retiming?

## Slide 48: (Graph) Cycle Observation
Retiming does not allow us to change the number of registers inside a graph cycle.
Limit to clock cycle time
  Max delay in graph cycle / Registers in graph cycle
Pipelining doesn’t help inside graph cycle
  Cannot push registers into graph cycle

## Slide 49: Simple Graph Cycle
Delay of graph cycle?
Registers in graph cycle?
What happens to graph cycle if try to apply lead/lag?

## Slide 50: Retiming

## Slide 51: Loop
Consider
  [multiply and mod each take 3 cycles]
For (i=0;i<N;i++)
  C[i]=(C[i-1]*A[i])%N;

## Slide 52: Loop
For (i=0;i<N;i++)
  C[i]=(C[i-1]*A[i])%N;

## Slide 53: Initiation Interval (II)
Cyclic dependencies in a dataflow graph can limit throughput
Due to data-dependent cycles in graph,
  May not be able to initiate a new computation on every clock cycle
II – clock cycles (delay) before can initiate
Throughput = 1/II

## Slide 54: Loop
For (i=0;i<N;i++)
  C[i]=(C[i-1]*A[i])%N;
Initiation Interval?

## Slide 55: Initial Interval
Delay Around graph cycle?
  Assume multiply 3, add 1
Registers in graph cycle?
Retiming clock cycle bound = II ?
Achievable?

## Slide 56: Retimed

## Slide 57: II and Latency
Actually is a cycle
  II?
  Latency?

## Slide 58: II and Latency
II? (assume willing to pipeline inputs)
Latency?

## Slide 59: II and Latency

## Slide 60: Lesson
Cyclic dependencies limit throughput on single task or data stream
  Cycle-length / registers-in-cycle

## Slide 61: Vector Pipelines
Data Parallel Vector Operations are interesting even when Vector Lanes<Vector Length
Within Vector operation, data parallel so no cyclic dependencies
  So get an II=1 issuing Vector Lane operations
  May have data dependences between Vector operations

## Slide 62: Vector Pipeline Example
for (int i=0;i<32; i++)
  c[i]+=a[i]*b[i]

## Slide 63: Dependence between Vector Operations
for (int i=0;i<32; i++)
  c[i]+=a[i]*b[i]
for (int i=0;i<32; i++)
  c[i]+=d[i]*e[i]

## Slide 64: Big Ideas
Pipeline computations to reuse hardware and maximize computational capacity
Can compose pipelined operators and accommodate fixed-frequency target
  Be careful with data retiming
Graph cycles limit pipelining on single stream -- II
C-slow to share hardware among multiple, data-parallel streams (part 4)

## Slide 65: Admin
Remember Feedback form
  Including HW3
Reading for Day 8 on web
HW4 due Friday
Extra ”HW/Quiz” to get information for Ultra96 (hw) distribution coming

## Slide 66: C-Slow
(Probably record separately)
Part 4

## Slide 67: Problem
Pipelining cannot push registers into a graph cycle
Graph cycles can prevent running at full pipeline target (maximum clock frequency)
If not reusing operators at full pipeline target are underutilizing resources
Can we use the resources for something?

## Slide 68: C-Slow
Observation: if we have data-level parallelism, can use to solve independent problems on same hardware
Transformation: make C copies of each register
Guarantee: C computations operate independently
  Do not interact with each other

## Slide 69: 2-Slow Simple Cycle
Replace register with pair
Retime

## Slide 70: 2-Slow Simple Cycle
Replace register with pair
Retime
Observe independence of red/blue computations

## Slide 71: Equivalence
The 2-slow operator is equivalent to two data parallel operators running at half the speed
  E.g. processing separate audio channels

## Slide 72: Automation
No mainstream tool today will perform C-slow transformation for you automatically
Synthesis tools will retime registers

## Slide 73: Lesson
Cyclic dependencies limit throughput on single task or data stream
  II=Cycle-length / registers-in-cycle
Can use on C (C<=II) independent (data parallel) tasks

## Slide 74: Big Ideas
Pipeline computations to reuse hardware and maximize computational capacity
Can compose pipelined operators and accommodate fixed-frequency target
  Be careful with data retiming
Graph cycles limit pipelining on single stream -- II
C-slow (C<=II) to share hardware among multiple, data-parallel streams (part 4)