## Slide 1: ESE532: System-on-a-Chip Architecture
Day 8: September 30, 2020
Spatial Computations

## Slide 2: Today
Accelerator Pipelines (Part 1)
FPGAs (Part 2)
Computational Capacity (Part 3)
  Zynq, F1

## Slide 3: Message
Custom accelerators efficient for large computations
  Exploit Instruction-level parallelism
  Run many low-level operations in parallel
Field-Programmable Gate Arrays (FPGAs)
  Allow post-fabrication configuration of custom accelerator pipelines
  Can offer high computational capacity

## Slide 4: Accelerator Datapaths

## Slide 5: Pipeline Graph
Last time: pipelined simple loop

## Slide 6: Pipeline for Unrolled Loop

## Slide 7: Preclass 1
For fully unrolled loop shown, how many instructions per pipeline cycle?
  Add
  Mpy
  Load
  Store

## Slide 8: Spatial Pipeline
Can compute equivalent of tens of “instructions” in a cycle
Wire up primitive operators
  No indirection through register file, memory
Pipeline for operator latencies
Any dataflow graph of computational operations

## Slide 9: Operators
Can assemble any custom operators
  Ones may not have in generic processor
Processor
  Add, bitwise-xor/and/or
  Maybe: floating-point add, multiply
Less likely
  Square-root, exponent, cosine, encryption (AES) step, polynomial evaluate, log-number-system

## Slide 10: Accelerators
Compression/decompression
Encryption/decryption
Encoding (ECC, Checksum)
Discrete Cosine Transform (DCT)
Sorter
Taylor Series Approximation of function
Transistor evaluator
Tensor or Neural Network evaluator

## Slide 11: Streaming Dataflow
Replace operator with custom accelerator
Stream data to/from it

## Slide 12: Streaming Dataflow Example

## Slide 13: Application-Specific SoCs
For dedicated applications may build custom hardware for accelerators
  Layout VLSI, fab unique chips
  ESE370, 570
Video-encoder – include custom DCT, motion-estimation engines

## Slide 14: Apple A13 Bionic
98mm2, 7nm
8.5 Billion Tr.
iPhone 11 +
6 ARM cores
  2 fast (2.6GHz)
  4 low energy
4 custom GPUs
Neural Engine
  5 Trillion ops/s?

## Slide 15: Customizable Accelerators
With post-fabrication configurability can exploit without unique fabrication
Need programmable substrate that allows us to wire-up computations

## Slide 16: Field-Programmable Gate Arrays
FPGAs
Part 2

## Slide 17: FPGA
Idea: Can wire up programmable gates in the “field”
  After fabrication
  At your desk
  When part “boots”
Like a “Gate Array”
  But not hardwired

## Slide 18: Gate Array
Idea: Provide a collection of uncommitted gates
Create your “custom” logic by wiring together the gates
Less layout, fewer masks than full custom
  Since only wiring together pre-fab gates
   lower cost (fewer masks)
   lower manufacturing delay

## Slide 19: Gate Array

## Slide 20: GAFPGA
Remove the need to even fabricate the wiring mask
Make “customization” soft
Key trick:
  Use reprogrammable configuration bits
  Typically: static-RAM bits
    Like SRAM cells or latches in memory
    Hold a configuration value

## Slide 21: Multiplexer Gate
MUX
  When S=0, output=i0
  When S=1, output=i1
  Out = /s*i0 + s*i1

## Slide 22: Mux with configuration bits = programmable gate

## Slide 23: Preclass 4a
How do we program to behave as and2?

## Slide 24: Preclass 4b
How do we program to behave as xor2?

## Slide 25: Mux as Logic
Just by “configuring” data into this mux4,
  Can select any two input function

## Slide 26: LUT – LookUp Table
When use a mux as programmable gate
  Call it a LookUp Table (LUT)
  Implementing the Truth Table for small # of inputs
    # of inputs =k (need mux-2k)
  Just lookup the output result in the table

## Slide 27: Preclass 6
How do we program full adder?

## Slide 28: FPGA
Programmable gates + wiring
  (both built from muxes w/ config. bits)
Can wire up any collection of gates
  Like a gate array

## Slide 29: Simplistic FPGA (illustrate possibility)
Every LUT input has a mux
Every such mux has m=(N+I) inputs
  An input for each LUT output (N 2-LUTs)
  An input for each Circuit Input (I Circuit inputs)
Each Circuit Output has an m-input mux

## Slide 30: Simplistic FPGA (illustrate possibility)
N 2-LUTs, I Circuit Inputs, O Circuit Outputs
2N+O muxes to connect
Can build any combinational logic circuit that doesn’t need more than N 2-input gates, I inputs, O outputs

## Slide 31: Preclass 3 How big is an m-input mux?
In terms of 2-input muxes?
  Warmup: how many for 4-input (Preclass 2)
  Warmup: how many for 8-input (below)
m inputs – what we are selecting from
log2(m) bits
to select
which input
routed to
output

## Slide 32: Math: Series Sums
A0(1+r+r2+r3+r4+…)
A0(1+r+r2+r3+r4+…)*(1-r) =A0+ A0 r+ A0 r2+ A0 r3+ A0 r4+… - A0 r - A0 r2 - A0 r3 - A0 r4-… = A0 (when r<1)
A0(1+r+r2+r3+r4+…)*(1-r)=A0
A0(1+r+r2+r3+r4+…)=A0/(1-r)

## Slide 33: Receding Sum

## Slide 34: Simplistic FPGA (illustrate possibility…and expense)
2N+O m-input muxs; m=N+I
Each m-input mux is m-1 2-input muxes
Requires: (2N+O)*(N+I-1) 2-input muxes
Mux area grows as ~N2
  when gate (LUT) area grows as N

## Slide 35: Interconnect
Fully connected mux input is too expensive, growing as N2
  …and not necessary
Want
  To be able to wire up gates
  Economical with wires and muxes
    …and configuration bits
  Exploit locality (keep wires short)

## Slide 36: Simple FPGA

## Slide 37: Simple FPGA

## Slide 38: Register
Want to be able to pipeline logic
…and generally hold state
  E.g. implement hold Input-N in preclass 1
Add optional register on each gate

## Slide 39: Simple FPGA

## Slide 40: FPGA Design
Raises many architectural design questions
  How big (many inputs) should the gates have?
    Are LUTs really the right thing…
  How rich is the interconnect?
    Wires/channel
    Wire length
    Switching options

## Slide 41: Modern FPGAs
Logic Blocks
  hardwired fast-carry logic
    Can implement adder bit in single “LUT”
  Speed optimized: 6-LUTs
  Energy, Cost optimization: 4-LUTs
  Clusters many LUTs into a tile
Interconnect
  Mesh, segments of length 4 and longer

## Slide 42: More than LUTs
Should there be more than LUTs in the “array” fabric?
What else might we want?

## Slide 43: Embedded Memory
One flip-flop per LUT doesn’t store state densely
Want memory close to logic

## Slide 44: Embed Memory in Array
Replace logic clusters
Convenient to replace columns
  Since area of memory may not match area of logic cluster

## Slide 45: Embedded Memory in FPGA
Logic
Cluster
Memory
Bank
Memory
Frequency
Memory banks on Xilinx called BRAMs (Block RAMs)

## Slide 46: Hardwired Multipliers
Can build multipliers out of LUTs
  Just as can implement multiplies on processor out of adds
But, custom multiplier is smaller than LUT-configured multiplier
  …and multipliers common in signal processing, scientific/engineering compute

## Slide 47: Multiplier Integration
Integrate like memories
  Replace columns

## Slide 48: More FPGA Architecture Design Questions
Size of Memories? Multipliers?
Mix of LUTs, Memories, Multipliers?
Add processors? Floating-point?
Other hardwired blocks?
How manage configuration?

## Slide 49: Midterm (10/7 – next Wed.)
Analysis
  Bottleneck
  Amdhal’s Law Speedup
  Computational requirements
  Resource Bounds
  Critical Path
  Latency/throughput/II
Will be calculating/estimating runtimes
From Code
Forms of Parallelism
Dataflow, SIMD, hardware pipeline, threads
Pipelining/Retiming
Map/schedule task graph to (multiple) target substrates
Memory assignment and movement
Area-time points

## Slide 50: Midterm
Online Canvas quiz
Open book, notes, etc.
Calculators allowed (encouraged)
Drawing programs required
Read midterm details posted on web
Last four midterms, finals online
  Both without answers (for practice)
  …and with answers (check yourself)
  Check syllabus for previous terms
Midterm comes earlier this year

## Slide 51: Zynq MPSoC
Part 3

## Slide 52: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 53: ZU3EG (Ultra96)
6-LUTs: 70,560
DSP Blocks: 360
  18x27 multiply, 48b accumulate
Block RAMs (BRAMs): 216
  36Kb
  Dual port
  Up to 72b wide (512x72)

## Slide 54: DSP48
Xilinx UG579 UltraScale DSP Slice User’s Guide

## Slide 55: Preclass 5
Approximating | Resources | Cycle | Per second
Zynq LUTs | 70,000 adder bits | 0.5 GHz | 
4x ARM Scalar | 4x2x64 adder bits | 1.2 GHz | 
4x ARM Neon | 4x1x64 adder bits | 1.2 GHz | 
Zynq DSP | 360 multiply-accumulates | 0.5 GHz | 
4x ARM Scalar | 4x(1 mpy+1add) | 1.2 GHz | 
4x ARM Neon | 4x1x4 multiply-accumulates | 1.2 GHz | 
How compare between ARM scalar, ARM NEON and FPGA array?
  Adder-bits/second?
  Multiply-accumulators/second?

## Slide 56: Capacity  Density
Says Zynq has high computational capacity in FPGA
More broadly
  FPGA can have more compute/area than processor
    E.g., more adder bits in some fixed area
  SIMD can have more compute/area than processor (Day 6)
    How wide SIMD can you exploit?

## Slide 57: VU9P (Amazon F1)
6-LUTs: 1,182,240
DSP Blocks: 6,840
  18x27 multiply, 48b accumulate
Block RAMs (BRAMs): 2,160
  36Kb
  Dual port
  Up to 72b wide (512x72)

## Slide 58: VU9P (Amazon F1)
Approximating | Resources | Cycle | Per second
Zynq LUTs | 70,000 adder bits | 0.5 GHz | 
4x ARM Scalar | 4x2x64 adder bits | 1.2 GHz | 
4x ARM Neon | 4x1x64 adder bits | 1.2 GHz | 
Zynq DSP | 360 multiply-accumulates | 0.5 GHz | 
4x ARM Scalar | 4x(1 mpy+1add) | 1.2 GHz | 
4x ARM Neon | 4x4x4 multiply-accumulates | 1.2 GHz | 
VU9P LUTs | 1,182,000 adder bits | 0.8 GHz | 
VU9P DSP | 6,840 multiply-accumulates | 0.8 GHz | 

## Slide 59: FPGA Potential
FPGA Array has high raw capacity
Exploitable when computation has high regularity
  Uses the same computation over-and-over
  High throughput on a computation
  Build customized accelerator pipeline to match the computation
Low-hanging fruit
  Operator/function takes most of the compute time

## Slide 60: 90/10 Rule
Observation that code is not used uniformly
90% of the time is spent in 10% of the code
Knuth: 50% of the time in 2% of the code
Opportunity
  Build custom datapath in FPGA (hardware) for that 10% (or 2%) of the code

## Slide 61: Big Ideas
Custom accelerators efficient for large computations
  Exploit Instruction-level parallelism
  Run many low-level operations in parallel
Field Programmable Gate Arrays (FPGAs)
  Allow post-fabrication configuration of custom accelerator pipelines
  Can offer high computational capacity

## Slide 62: Admin
Reading for Day 9 on canvas
HW4 due on Friday
Hardware Distribution Survey due Monday
  Mechanism-wise, warmup for midterm
Midterm on Wednesday
  No assignment due on Friday (10/9)
  Previous midterms (with solutions) on web syllabus of previous years
HW5 out soon
  Heavier – start early…have more than week
  Vivado HLS synthesis slow (plan for it)