## Slide 1: ESE532: System-on-a-Chip Architecture
Day 1: September 1, 2021
Introduction and Overview
(lecture start target 10:20am)
Note: both preclass and feedback linked to web (also slides)
www.seas.upenn.edu/~ese532/fall2021/fall2021.html
Preclass (work now)
Feedback form (turn in end of lecture)

## Slide 2: Today
Part 1: Case for Programmable SoC
Part 2
  Course Goals
  Outcomes
  Evovling Course, Risks, Tools
Part 3: Sample Optimization
Part 4: This course
  (incl. policies, logistics)

## Slide 3: Apple A14 Bionic
88mm2, 5nm
11.8 Billion Tr.
iPhone 12
6 ARM cores
  2 fast (2.9--3GHz)
  4 low energy
4 custom GPUs
16 Neural Engines
  11 Trillion ops/s?
Image from https://www.extremetech.com/computing/318715-comparison-of-apple-m1-a14-shows-differences-in-soc-design
details: https://www.tomshardware.com/news/apple-a14-bionic-revealed
https://www.anandtech.com/show/16226/apple-silicon-m1-a14-deep-dive/2

## Slide 4: Apple A13 Bionic
98mm2, 7nm
8.5 Billion Tr.
iPhone 11 +
6 ARM cores
  2 fast (2.6GHz)
  4 low energy
4 custom GPUs
Neural Engine
  5 Trillion ops/s?

## Slide 5: Questions
Why do today’s SoC look like they do?
How approach programming modern SoCs?
How design a custom SoC?
When building a System-on-a-Chip (SoC)
  How much area should go into:
    Processor cores, GPUs, FPGA logic, memory, interconnect, custom functions (which) …. ?

## Slide 6: FPGA Field-Programmable Gate Array
K-LUT (typical k=4 or 6)
Compute block
w/ optional
output Flip-Flop
ESE150, CIS571

## Slide 7: Case for Programmable SoC

## Slide 8: End of uProcessor Scaling
Old
Moore’s Law scaling delivered faster transistors
Processors rode Moore’s Law
  Turning transistors into performance
Could wait and ride technology curve
Now
Dennard’s Law kicked in
uP were burning more power
Lost ability to scale down voltage
Processor performance stalled

## Slide 10: The Way things Were
30 years ago
Wanted programmability
  used a processor
Wanted it a little faster
  Next year’s processor would run faster…
Wanted high-throughput
  used a custom IC
Wanted product differentiation
  Got it at the board level
  Select which ICs and how wired
Build a custom IC
  It was about gates and logic

## Slide 11: Today
Microprocessor may not be fast enough
  (but often it is)
  Or low enough energy
Single core processor scaling has ended
Time and Cost of a custom IC is too high
  $100M’s of dollars for development, Years
FPGAs promising
  But build everything from prog. gates?
Premium for small part count
  And avoid chip crossing
  ICs with Billions of Transistors

## Slide 12: Non-Recurring Engineering (NRE) Costs
Costs spent up front on development
  Engineering Design Time
  Prototypes
  Mask costs
Recurring Engineering
  Costs to produce each chip

## Slide 13: NRE Costs

## Slide 14: NRE Cost (continued)
https://semiengineering.com/how-much-will-that-chip-cost/

## Slide 15: Amortize NRE with Volume

## Slide 16: Economics
Economics force fewer, more customizable chips
  Mask costs in the millions of dollars
  Custom IC design NRE 10s—100s of millions of dollars
    Need market of billions of dollars to recoup investment
    With fixed or slowly growing total IC industry revenues
     Number of unique chips must decrease
    Chips must be programmable
Forcing fewer,
more customizable
chips

## Slide 17: Large ICs
Now contain significant software
  Almost all have embedded processors
Must co-design SW and HW
Must solve complete computing task
  Tasks has components with variety of needs
  Some don’t need custom circuit
  90/10 Rule

## Slide 18: Given Demand for Programmable
How do we get higher performance than a processor, while retaining programmability?

## Slide 19: Programmable SoC
Implementation Platform for innovation
  This is what you target (avoid NRE)
  Implementation vehicle

## Slide 20: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 21: Then and Now
30 years ago
Programmability?
  use a processor
Faster
  Processors scaled
High-throughput
  used a custom IC
Wanted product differentiation
  board level
  Select & wired IC
Build a custom IC
  It was about gates and logic
Today
Programmability?
  uP, FPGA, GPU, PSoC
Faster
  Can’t get with single core
High-throughput
  FPGA, GPU, PSoC, custom
Wanted product differentiation
  Program FPGAs, PSoC
Build a custom IC
  System and software

## Slide 22: Part 2: Course Goals, Outcomes

## Slide 23: Goals
Create Computer Engineers
  SW/HW divide is wrong, outdated
  Computer engineers understand computation
    HW and SW are just tools and design options
  Parallelism, data movement, resource management, abstractions
  Cannot build a chip without software
SoC user – know how to exploit
SoC designer – architecture space, hw/sw codesign
Project experience – design and optimization

## Slide 24: Roles
PhD Qualifier
  One broad Computer Engineering
CMPE Concurrency
Hands-on Project course

## Slide 25: Outcomes
Design, optimize, and program a modern System-on-a-Chip.
Analyze, identify bottlenecks, design-space
  Modeling  write equations to estimate
Decompose into parallel components
Characterize and develop real-time solutions
Implement both hardware and software solutions
Formulate hardware/software tradeoffs, and perform hardware/software codesign

## Slide 26: Outcomes
Understand the system on a chip from gates to application software, including:
  on-chip memories and communication networks, I/O interfacing, design of accelerators, processors, firmware and OS/infrastructure software.
Understand and estimate key design metrics and requirements including:
  area, latency, throughput, energy, power, predictability, and reliability.

## Slide 27: Evolving Course
Spring 2017 – first offering
  Raw, all assignments new, buggy, too tedious, long
Fall 2017 – second offering
  Refine assignments, project; increased explicit modeling emphasis
  Hard, not insane
Fall 2018 – third offering (similar 2017)
  Added real-time ethernet data handling; project groups of 3
  Many students challenged with C and software engineering
  Stream debug and performance challenging
Fall 2019 – fourth (structure same)
  Try front-load more C, better introduce Stream optimization and debug
  Group writeup on projects

## Slide 28: Evolving Course
Fall 2018 – third offering (similar 2017)
  Added real-time ethernet data handling; project groups of 3
  Many students challenged with C and software engineering
  Stream debug and performance challenging
Fall 2019 – fourth (structure same)
  Try front-load more C, better introduce Stream optimization and debug
  Group writeup on projects
Fall 2020 – fifth (structure same)
  Move to Vitis (from SDSoC)
  Use Amazon cloud for first half; F1 instance for FPGA access HW
  Then transition to Ultra96 (SoC FPGA) for projects
Fall 2021 – sixth
  Stay with Vitis; use DFX (see next slide)
  Ultra96; no Amazon cloud
  Introduce project components earlier

## Slide 29: Tools
Are complex
Will be challenging, but good for you to build confidence can understand and master
Tool runtimes can be long
  Maybe DFX will help
  DFX – Dynamic Function Exchange
    Partial reconfiguration
Learning and sharing experience will be part of assignments

## Slide 30: Distinction
CIS240, 371, 471, 571
Best Effort Computing
  Run as fast as you can
Binary compatible
ISA separation
Shared memory parallelism
ESE532
Hardware-Software codesign
  Willing to recompile, maybe rewrite code
  Define/refine hardware
Real-Time
  Guarantee meet deadline
Non shared-memory parallelism models

## Slide 31: Distinction
ESE539: Hardware/Software Co-Design for Machine Learning
Deep on Application (ML)
More accessible to CS
  Less previous experience with circuits and architecture
Won’t be as deep on understanding HW and optimization
Program in Pytorch, OpenCL
ESE532:
Deep computer engineering
Broad application
Program in C
Suitable followup if want to dig deeper

## Slide 32: Abstraction Stack
ESE539 HW/SW ML
Transistors
Devices: ESE521
(ESE218)
Digital:
ESE370/570
Processor Arch:
CIS 471/571
(CIS240)
SoC Arch:
ESE 532
Circuits/VLSI
Gates, Memories
Processors
Systems
Mixed Signal:
ESE 568
ADC, DAC
Switched Capacitors
Analog:
ESE419/572
Amplifier, Compare
Voltage/Current Ref.
Embedded Sys:
ESE350/519
Software

## Slide 33: Part 3: Approach -- Example

## Slide 34: Abstract Approach
Identify requirements, bottlenecks
Decompose Parallel Opportunities
  At extreme, how parallel could make it?
  What forms of parallelism exist?
    Thread-level, data parallel, instruction-level
Design space of mapping
  Choices of where to map, area-time tradeoffs
Map, analyze, refine
  Write equations to understand, predict

## Slide 35: Example SPICE Circuit Simulator

## Slide 36: Example: SPICE Circuit Simulator
Example: Kapre+DeHon, TRCAD 2012
Matrix Solve
Ax=B
A matrix
B vector
x unknown vector
Solve for x
= KCL, KVL *
Linear Algebra
solving n eqns
in n unknowns.
* Kirchhoff {Current,Voltage} Laws

## Slide 37: Analyze

## Slide 38: Analyze
T=Tmodeleval+Tmatsolve+Tctrl

## Slide 39: Speedup
T=Tmodeleval+Tmatsolve+Tctrl
What should we speedup first?
What happens if only speedup modeleval?
  T=Tmatsolve+(Tmodeleval)/S+Tctrl

## Slide 40: Analyze
If only accelerated model evaluation only about 2x speedup
If want better than 14x speed, must also attack control

## Slide 41: Model Evaluation: Trivial Hardware Implementation
*
*
-
*
÷
÷
ex
c
d
e
a
b
f
Verilog-AMS as Domain-Specific Language

## Slide 42: Spatial, Pipelined Parallelism
Every operation (*, + /) gets dedicated hardware.
Implement task in space  use additional area for each operator.
Parallel – all operations occur simultaneously.
*
*
-
*
÷
÷
ex
c
d
e
a
b
f

## Slide 43: Parallelism: Model Evaluation Data Parallel
Every device independent
Many of each type of device
Can evaluate in parallel
  T=Tseq/Nproc
Build pipelined circuit for model
  Tseq=Ncomp*Tcycle vs. Tpipe=Tcycle

## Slide 44: Spatial Too Big?
*
*
-
*
÷
÷
ex
c
d
e
a
b
f
*
+
÷
ex
Fully spatial circuit
~100x Speedup
Multiple FPGAs
~10x Speedup
1 FPGA (2010)
Custom VLIW
VLIW=Very Long Instruction Word
exploits Instruction-Level Parallelism

## Slide 45: Parallelism: Model Evaluation
Spatial end up bottlenecked by other components
Use custom evaluation engines
…or GPUs

## Slide 46: Parallelism: Matrix Solve
Needed direct solver?
E.g. Gaussian elimination
Data dependence on previous reduce
  Limited data parallelism
Parallelism in subtracts
Some row independence

## Slide 47: Example Matrix

## Slide 48: Example Matrix

## Slide 49: Example Matrix
Reduce to critical path:
from 9 sequential operations
to path of 5 operations.

## Slide 50
Dataflow Processing Element (PE)
*
+
÷
Dataflow trigger
Incoming Messages
Outgoing Messages
Graph
Nodes
Graph
Fanout

## Slide 51: Matrix Solve Only
~2.4x mean

## Slide 52: Parallelism: Matrix Solve
Settled on constructing dataflow graph
Graph can be iteration independent
  Statically scheduled
  (cheaper)
This is bottleneck to further acceleration

## Slide 53: Parallelism Controller?
Could leave sequential
For some designs, becomes the bottleneck once others accelerated
Has internal parallelism in condition evaluation
  T=Tmodeleval/S1+(Tmatsolve)/S2+Tctrl

## Slide 54: Parallelism Controller
Customized datapath controller
Tseqctrl=Nadd+Nmul+10*Ndivide
Tvliwctrl=Max(Nadd/2,Nmul,10*Ndivide)

## Slide 55: Single-Chip Solution

## Slide 56: Area-Time for Each
[1 Slice = 4 LUTs]

## Slide 57
Composite Speedup

## Slide 58: Modern SoC

## Slide 59: Part 4: Class Components

## Slide 60: Class Components
Lecture (incl. preclass exercise)
  Slides on web before class
    (you can print if want a follow-along copy)
  N.B. I encourage class participation
    In class/synch recording; Questions (“warm” calls)
  Daily Quiz
Reading [~1 required paper/lecture]
  online: Canvas, IEEE, ACM, also ZynqBook,
  Parallel Programming for FPGAs
Homework
  (1 per week due F5pm Eastern)
Project – open-ended (~6 weeks)
Note syllabus, course admin online

## Slide 61: First Half
Quickly cover breadth
Metrics, bottlenecks
Memory
Parallel models
SIMD/Data Parallel
Thread-level parallelism
Spatial, C-to-gates
Line up with homeworks

## Slide 62: Second Half
Use everything on project
Schedule more tentative
  Adjust as experience and project demands
Going deeper
Real-time
Reactive
Memory
Networking
Energy
Scaling
Chip Cost
Verification

## Slide 63: Teaming
HomeWorks (HW) in Groups of 2
HW: we assign
Individual assignment writeup
Project in Groups of 3
Project: you propose team of 3, we review
  Most portions group writeup
  Few components individual writeup

## Slide 64: Office & Lab Hours
Andre: T 4:15pm—5:30pm
  Levine 270, Zoom
  See canvas
TAs -- Detkin
  Tuesday 5 pm
  Wednesday 5 pm (not today)
  Thursday 5—7pm (first office hours tomorrow)

## Slide 65: C Review
Course will rely heavily on C
  Program both hardware and software in C
HW1 has some C warmup problems
TAs will hold C review
  on Sept. 7th, 5:00pm
  (before our next class meeting since Monday 9/6 is Labor day)

## Slide 66: Preclass Exercise
Motivate the topic of the day
  Introduce a problem
  Introduce a design space, tradeoff, transform
Available before lecture (and in lecture)
  (only available for 24-48 hours; download)
  Should work before lecture starts
Do bring/use calculator
  Will be numerical examples

## Slide 67: Diagnostic Quiz
Count for Engagement Points
Only available until next lecture
Incentive to keep up with material

## Slide 68: Lecture Timeline
Preclass available before class
  In class hardcopy circa 10:10am
Start lecture at 10:20am
Lecture until 11:40am
(most days) stay for remaining questions
  Pending course after us
Post video to canvas later in day

## Slide 69: Feedback
Will have anonymous feedback {paper, google forms} for each lecture
  Clarity?
  Speed?
  Vocabulary?
  General comments
Paper hardcopy for in-person
Linked on syllabus for not in-person:
  https://forms.gle/FWdNWjCsnv6F4pGf8

## Slide 70: Policies
Canvas turn-in of assignments
No handwritten work
Due on time
  Individual assignments only
    3 free late days total
Collaboration
  Tools – allowed
  Designs – limited to project teams as specified on assignments
See web page

## Slide 71: Hybrid
Uncertain how hybrid zoom/in-person will work
  Setup a bit of a challenge
  Interactive work?

## Slide 72: Admin
Your action:
  Find course web page
    Read it, including the policies
    Find Syllabus
      Find homework 1
      Find lecture slides
        Will try to post before lecture
      Find reading assignments
  Find reading for lecture 2 on canvas and web
    …for this lecture if you haven’t already
  Find/join piazza group for course
  Signup for detkin/ketterer access

## Slide 73: Big Ideas
Programmable Platforms
  Key delivery vehicle for innovative computing applications
  Reduce TTM (Time-to-Market), risk
  More than a microprocessor
  Heterogeneous, parallel
Demand hardware-software codesign
  Soft view of hardware
  Resource-aware view of parallelism

## Slide 74: Questions?