## Slide 1: ESE532: System-on-a-Chip Architecture
Day 17: Nov. 1, 2021
LZW, Associative Maps, Hash Tables

## Slide 2: Today
LZW Compression (Part 1)
Associative Memory (Part 2)
  Custom
  FPGA
Software Maps
  Tree (Part 3)
  Hash Tables (Part 4)
    (time permit – else next time)

## Slide 3: Message
Rich design space for Maps
Hash tables are useful tools

## Slide 4: Part 1: LZW Compression Lempel-Ziv-Welch

## Slide 5: Idea
Use data already sent as the dictionary
  Give short names to things in dictionary
  Don’t need to pre-arrange dictionary
  Adapt to common phrases/idioms in a particular document
Day 16 Reminder

## Slide 6: Encoding
Greedy simplification
  Encode by successively selecting the longest match between the head of the remaining string to send and the current window
Day 16 Reminder

## Slide 7: Algorithm Concept
While data to send
  Find largest match in window of data sent
  If length too small (length=1)
    Send character
  Else
    Send <x,y> = <match-pos,length>
  Add data encoded into sent window
Day 16 Reminder

## Slide 8: Day 16: Preclass 4
How many comparisons per invocation?

## Slide 9: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
Only check position 0 for “starts with I”

## Slide 10: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
T-dictionary:
  Tap, The, Their, Then, There, Tuesday

## Slide 11: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
T-dictionary:
  Tap, The, Their, Then, There, Tuesday
If prefix same, why check redundantly?
  Generalize: Store things with common prefix together
    Share prefix among substrings
  Represent all strings as prefix tree

## Slide 12: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
If prefix same, why check redundantly?
  Store things with common prefix together
  Share prefix among substrings
  Represent all strings as prefix tree
Follow prefix trees with fixed work per input character

## Slide 13: Tree Example
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E

## Slide 14: Tree Algorithm
Tree Root for each character
Follow tree according to input until no more match
Send <name of last tree node>
  An <x,y> pair
Extend tree with new character
Start over with this character

## Slide 15: Tree Example
Label with <lastpos,len> pair
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E
<0,1>
<1,2>
<2,3>
<3,4>
<12,4>
<13,5>
<19,4>
<4,5>
<20,5>
T | H | E | N |  | A | N | D |  | T | H | E | R | E | , |  | T | H | E | Y
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
(only showing
Root for ’T’)

## Slide 16: Large Memory Implementation
int encode[SIZE][256];
Name tree node by position in chunk
  lastpos
c is a character
Encode[lastpos][c] holds the next tree node that extends tree node lastpos by c
  Or NONE if there is no such tree node

## Slide 17: Tree Example
Label with <lastpos,len> pair
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E
<0,1>
<1,2>
<2,3>
<3,4>
<12,4>
<13,5>
<19,4>
<4,5>
<20,5>
T | H | E | N |  | A | N | D |  | T | H | E | R | E | , |  | T | H | E | Y
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
encode[2][‘N’]=3
encode[2][‘R’]=12
encode[2][‘Y’]=19
encode[2][‘A’]=NONE
(only showing
Root for ’T’)

## Slide 18: Large Table for Tree
Addr | spc | A | … | D | E | … | H | … | N | … | R | S | T | … | Y
-1 |  | 5 |  |  |  |  |  |  |  |  |  |  | 0 |  | 
0 |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 
1 |  |  |  |  | 2 |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 3 |  | 12 |  |  |  | 19
3 | 4 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  | 6 |  |  |  |  |  | 
6 |  |  |  | 7 |  |  |  |  |  |  |  |  |  |  | 
7 | 8 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 19: Memory Tree Algorithm
curr – pointer into input chunk
// follow tree
y=0; x=-1; // for no match, yet…
while(encode[x][input[curr+y]]!=NONE)
x=encode[x][input[curr+y]]; y++;
If (y>0)
send <x,y>
else
send input[curr+y]
encode[x][input[curr+y]]=curr+y
curr=curr+y+1

## Slide 20: Memory Tree Algorithm
curr – pointer into input chunk
// follow tree
y=0; x=-1; // for no match, yet…
while(encode[x][input[curr+y]]!=NONE)
x=encode[x][input[curr+y]]; y++;
If (y>0)
send <x,y>
else
send input[curr+y]
encode[x][input[curr+y]]=curr+y
curr=curr+y+1
Follow
Tree

## Slide 21: Memory Tree Algorithm
curr – pointer into input chunk
// follow tree
y=0; x=-1; // for no match, yet.
while(encode[x][input[curr+y]]!=NONE)
x=encode[x][input[curr+y]]; y++;
If (y>0)
send <x,y>
else
send input[curr+y]
encode[x][input[curr+y]]=curr+y
curr=curr+y+1
How much work per
character to encode?
Hint:
1) match case
2) not match

## Slide 22: Compact Memory
int encode[SIZE][256];
How many entries in this table are not NONE?
  Hint: SIZE is total number of positions. How many characters process? How many insertions per character processed?

## Slide 23: Compact Memory
int encode[SIZE][256];
Table is very sparse
If store as associative memory
  At most SIZE entries
Look at how to implement associative memories next

## Slide 24: LZW So Far – 4KB chunks
Brute Force
  Needs one byte per byte = 4KB = 1 BRAM
  DICT_SIZE=4096 comparisons per byte
Dense memory encode[SIZE][256]
  Need 2*256B per byte = 512*4KB = 512 BRAMs
  1 comparison and lookup per byte

## Slide 25: Associative Memories
Part 2

## Slide 26: Associative Memory
Maps from a key to a value
Key not necessarily dense
  Contrast simple RAM
  Cannot afford 2256 word memory
Day 16 Review

## Slide 27: Associative Memories
Use for deduplication
Also may use in LZW to reduce BRAMs
  Just saw
    Problem: Simple 2D tree table requires too many BRAMs
    Opportunity: Tree table sparse

## Slide 28: Deduplicate
Compute chunk hash
Use chunk hash to lookup known chunks
  Data already have on disk
  Data already sent to destination, so destination will know
If lookup yields a chunk with same hash
  Check if actually equal (maybe)
If chunks equal
  Send (or save) pointer to existing chunk
Day 16 Review

## Slide 29: Deduplication Architecture
Day 16 Review

## Slide 30: Custom Hardware Associative Memory

## Slide 31: Memory Block Review
Match on address
Select wordline for a row
Reads out a word
Address dense and hardwired
One row for each 2Abits values
width
depth

## Slide 32: Address Blocks
Each address match is AND
width
depth
/A2&/A1&/A0
/A2&/A1&A0

## Slide 33: Address Blocks

## Slide 34: Memory Block Associative
Want address as key
Word is value
Key sparse
Rows<2keybits
Entries<2keybits
Key programmable
width
depth

## Slide 35: Programmable Key
Make row select programmable

## Slide 36: Contrast Assoc. and Dense Memory

## Slide 37: Associative Memory Bank

## Slide 38: Programmable Key
Assoc: 5b key, 8 entries, 8b value
How many memory bits?
Direct: 8 entries, 8b value
How many memory bits?

## Slide 39: Associative Memory Bank
Memory cells = entries*(keybits+valuebits)

## Slide 40: Associative Memory Bank
Will need to be able to write into key
  Another “fixed” decoder to generate key-word line for programming

## Slide 41: Associate Memory Cost
More expensive than equal capacity SRAM memory bank
  Memory cells in decoder
  Need to support write into key

## Slide 42: Associate Memory Cost
Physical associative memory for 4KB LZW Chunk tree encode
  4K entries
  12b output
  12b+8b=20b key
Memory cells assoc.?
Compare direct 4Kx12 memory (cells)?
  How much larger is assoc. for same capacity?
Compare 4096*256 with 12b result for dense LZW case (cells)?
  How much larger to solve same problem

## Slide 43: FPGA
Has BRAMs – normal memories, not associative
36Kb BRAM
  512x72
Can be 9b key  72b value assoc.
  Just using the memory sparsely
Or interpret as programmable decoder with 72 match lines

## Slide 44: Assoc. Mem from BRAM
For wider match
Cover 9b of key with each BRAM
Use 72 output bits to indicate if one of 72 entries match
AND together corresponding entries
Get 72 match bits
Re-encode match bits to lookup value

## Slide 45: BRAM Associative Memory
Previous slide expands match width
How would we expand capacity?
  Hint: how get a wider word (144b word)?

## Slide 46: BRAM Associative Memory

## Slide 47: Associative Memory Cost
Match unit
  Requires 1 BRAM per 9b of key per 72 entries
  ✖️
  Asymptotically optimal (keylen*entries)
    But large constants
  LZW
    4K entries
    20b key
    How many BRAMs for match?

## Slide 48: 4K LZW Chunk Search: Fully associative
Match BRAMs:
  Match key: 20b
  Entries: 4096
Value BRAMS:
  20b (key) + 12b (state)
  32b x 4096 entries

## Slide 49: Example Stored Values
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC

## Slide 50: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 51: Code Snippet
ap_uint<72> key_low[512];
ap_uint<72> key_high[512];
int value[72];
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
res=value[addr];

## Slide 52: How Lookup Work?
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC
Lookup 0x214 = 0x001 0x014

## Slide 53: Code Snippet
ap_uint<72> key_low[512];
ap_uint<712> key_high[512];
int value[72];
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
res=value[addr];

## Slide 54: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
What match_low, match_high?

## Slide 55: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
What match?

## Slide 56: What does binary_encode do?
binary_encode(0000000…010000)=0x40
10000…0  71
0000…01  0
0000…010  1
for (i=0<i<72;i++)
  If (bit[i]==1) return i
Return(MISS); // if not find (i.e., all 0’s)
Technicalities – maybe check only one 1

## Slide 57: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
What addr?

## Slide 58: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM
res=value[addr];
What res?

## Slide 59: How Lookup Work?
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC
Lookup 0x214 = 0x001 0x014

## Slide 60: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 61: Add another entry
How BRAM contents change to add this entry
for 0x19001
match | Key[17:9] | Key[8:0] | Value
0 | 0x001 | 0x014 | 0x01
1 | 0x001 | 0x01 | 0x34
2 | 0x0F0 | 0x014 | 0xE3
3 | 0x0C8 | 0x113 | 0xCC
4 | 0x0C8 | 0x01 | 0x2B

## Slide 62: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 63: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 0x2B
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 64: 4K Chunk LZW Search
 | BRAMs | Operations
Brute Search | 1 | 4K
Tree with Dense RAM | 512 | 1
Tree with Full Assoc | 175 | 1
36Kb BRAMs on ZU3EG = 216

## Slide 65: Software Map
Part 3

## Slide 66: Software Map
Map abstraction
  void insert(key,value);
  value lookup(key);
Will typically have many different implementations

## Slide 67: Preclass 1
For a capacity of 4096
How many memory accesses needed
  When lookup fail?
  When lookup succeed (on average)?

## Slide 68: Tree Map (Preclass 2)
Build search tree
Walk down tree
For a capacity of 4096, assume balanced…
How many tree nodes visited
  When lookup fail?
  When lookup succeed (on average)?

## Slide 69: Tree Map LZW
Each character requires log2(dict) lookups
  12 for 4096
Each internal tree node hold
  Key (20b for LZW), value (12b), and 2 pointers (12b)
  7B
Total nodes 4K*2
Need 14 BRAMs for 4K chunk

## Slide 70: Tree Insert
Need to maintain balance
Doable with O(log(N)) insert
  Tricky
  See Red-Black Tree
    https://en.wikipedia.org/wiki/Red–black_tree
    https://www.geeksforgeeks.org/red-black-tree-set-1-introduction-2/

## Slide 71: 4K Chunk LZW Search
 | BRAMs | Operations
Brute Search | 1 | 4K
Tree with Dense RAM | 512 | 1
Tree with Full Assoc | 175 | 1
Tree with Tree | 14 | 12
36Kb BRAMs on ZU3EG = 216

## Slide 72: Hash Tables
Part 4

## Slide 73: High Performance Map
Would prefer not to search
Want to do better than log2(N) time
Direct lookup in arrays (memory) is good…

## Slide 74: Hash Table
Attempt to turn into direct lookup
Compute some function of key
  A hash
Perform lookup at that point
If hash maps a single entry (or no entry)
  Great, got direct lookup
    Like sparse table case
hash
Mem
lookup_key
match_key, value
Miss =
(match_key!=lookup_key)

## Slide 75: Preclass 3a
Average number of entries per hash when N > HASH_CAPACITY?
  Concrete example
    N= 4096
    HASH_CAPACITY=256

## Slide 76: Hash Table
Attempt to turn into direct lookup
Compute some function of key
  A hash
Perform lookup at that point
Typically, prepared for several keys to map to same hash  call it a bucket
  Keep list or tree of things in each bucket
hash
Mem
lookup_key
Bucket =
<k1,v1>,
<k2,v2>,
<k3,v3>

## Slide 77: Hash Table
Compute some function of key
  A hash
Perform lookup at that point
Find bucket with small number of entries
  Searching that bucket easier
  …but no absolute guarantee on maximum bucket size
    Problem for hardware [next time]
hash
Mem
Bucket =
<k1,v1>,
<k2,v2>,
<k3,v3>
lookup_key

## Slide 78: Preclass 3b
Probability of conflict if N<<HASH_CAPACITY ?
  Concrete example
    N=4096
    HASH_CAPACITY=409600
Impact of HASH_CAPACITY on average bucket size?

## Slide 79: Big Ideas
Rich design space for engineering associative map solutions
Sparse, near O(1) Map access  Hash Table

## Slide 80: Admin
Feedback (including HW7)
Reading for Wednesday on Web
First project milestone due Friday
  Including teaming