## Slide 1: ESE532: System-on-a-Chip Architecture
Day 21: November 15, 2021
Reduce

## Slide 2: Today
Part 1
  Reduce
  Associative Operations
  Model
Part 2
  Latency Bound Implications and Implementations
Part 3
  Parallel Prefix
  Broad Application
Bonus: Binary Arithmetic

## Slide 3: Message
Aggregation is a common need that is not strictly data parallel
…but admits to parallel computation with a slightly different pattern that is worth knowing

## Slide 4: Reduce
Reduce – combining a collection of data into a single value
  Converting a vector into a scalar
    E.g. sum elements

## Slide 5: Sum Reduce
Simplest and most common
  Add up all the values in a vector or array
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i];

## Slide 6: Sum Reduce
What’s II? (unit delay add)
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i];

## Slide 7: Sum Reduce
What’s latency bound?
  Assuming associativity holds for addition
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i];

## Slide 8: Associative Operations
Associativity means can group together operations in any way
Normal sequential:
  (((a[0]+a[1])+a[2])+a[3])+…
Associative regroup:
  (a[0]+((((a[1]+(a[2]+a[3]))+a[4])+(…)))

## Slide 9: Associative Operations
Associativity means can group together operations in any way
Normal sequential:
  (((a[0]+a[1])+a[2])+a[3])+…
Regroup parallelism:
  (((a[0]+a[1])+(a[2]+a[3]))+((a[4]+a[5])+(a[6]+a[7])))

## Slide 10: Associative Tree Reduce
Add pairs – cut numbers in half
Repeat adding pairs until single value
How deep?

## Slide 11: Associative Tree Reduce
Add pairs – cut numbers in half
Repeat adding pairs until single value
How deep?
N*(1/2)k=1
N=2k
k=log2(N)

## Slide 12: Latency Bounds
Associative reduces typically contribute log terms to latency bounds
  …as you’ve seen on many previous midterms and finals

## Slide 13: Sum Reduce
Data Parallel?
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i];

## Slide 14: Sum Reduce
How exploit 4 cores to compute?
  (assume a very large, like 1 million)
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i];

## Slide 15: Model: Data Parallel+Reduce
Data Parallel + Reduce
  Very common to perform a data parallel operation then a reduce on results
Example: dot product
  (core in DNN, Matrix-Multiply)
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i]*b[i];

## Slide 16: Dot Product
Latency bound for dot product
  Assume 1 cycle add, 3 cycle multiply
Example: dot product
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i]*b[i];

## Slide 17: Model: Data Parallel+Reduce
Data Parallel + Reduce
  Very common to perform a data parallel operation then a reduce on results
General form
  int res=0;
  for (int i=0;i<N; i++)
  res=assoc_op(res,f(a[i],b[i], …))

## Slide 18: What else Associative?
Beyond addition, what other associative operations do we often see as reductions?

## Slide 19: Associative Operations
Add
Multiply
Max
Min
AND
OR
Max/min
  And keep associated position
Find First

## Slide 20: Optimization Loop
int minval=f(0);
int min=0;
for (i=1;i<N;i++) {
int val=f(i);
if (val<minval) {
minval=val; min=i;
}
}

## Slide 21: Min keeping Position
if (val<minval) {
minval=val; min=i;
}
Each operation: min1,val1,min2,val2  min,val
if(val1<=val2) // keep first position found
{min=min1; val=val1;}
else
{min=min2; val=val2;}

## Slide 22: Optimization Loop
int minval=f(0);
int min=0;
for (i=1;i<N;i++) {
int val=f(i);
if (val<minval) {
minval=val; min=i;
}
}

## Slide 23: Rendering Decomposed
Pipeline of
  Projection
    Where do the points of this triangle end up in the viewed image?
    Matrix-multiplication to translate points
  Rasterization
    Turn into pixels
    Fill pixels for triangle
  Z-buffer
    Keep only the ones on top (not hidden)
      2D image + Z-depth – keep smallest
Figures from: https://commons.wikimedia.org/wiki/File:Perspective_Projection_Principle.jpg
https://en.wikipedia.org/wiki/Rasterisation#/media/File:Raster_graphic_fish_20x23squares_sdtv-example.png
Day 15

## Slide 24: Z-Buffering
Storing into Z–buffer is an associative reduce operation
  Min reduce (keep nearest pixel) on depth with an associated value
Parallel strategy
  Split triangles into sets
  Project, rasterize, Z-buffer in parallel
  Assoc. reduce Z-buffer pixels across parallel Z-buffers

## Slide 25: Not Associative: Floating Point
Floating-Point Addition
  Due to rounding
  (1+1E100)-1E100 = 0
  1+(1E100-1E100) = 1

## Slide 26: Not Associative: Saturated Addition
Saturated Addition
  tmp=a+b;
  if (tmp>MAXVAL) sum=MAXVAL;
  else sum=tmp;
MAXVAL=255
  254+(20-3) = 255
  (254+20)-3 = 252

## Slide 27: Majority Associative?
Carry=MAJ=majority = A&&B || B&&C || A&&C
Is Majority Associative ?
Hint: What are each of following?
  MAJ(1,1,MAJ(1,1,MAJ(1,0,0)))
  MAJ(MAJ(MAJ(1,1,1),1,1),0,0)

## Slide 28: Teaser
Can recast into associative operations
  saturated add
  Majority (bonus at end)
Can still use ideas with Floating Point

## Slide 29: Implementations
Part 2: Data Parallel+Reduce

## Slide 30: Threaded: Data Parallel+Reduce
Break into P threads
  0 to N/P-1, N/P to 2N/P-1, …
Run fraction of data and reduce on each
Then bring results together to sum
  P small, on one processor
  P large, as tree

## Slide 31: Vector: Data Parallel + Reduce
Some vector/SIMD machines will have dedicated reduce hardware
E.g. vector-add operator
NEON
  Not have vector reduce
  Does have VPADAL
    Pairwise adds
Use VL adds for course-grained reduce
for (i=0;i<N;i+=VL) {
avl=a[i]…a[i+VL-1]
VADD(res,avl, res);
}
Use VPADAL to complete
Cycles?

## Slide 32: Unrolled Pipeline: Data Parallel + Reduce
Unroll computation
Perform f ops in parallel pipelines
Pipelined tree reduce
Latency?
  N f ops
  Delay f – 3
  Delay commute -- 2
[also assoc_op;
pix shows commutative]

## Slide 33: Model: Data Parallel+Reduce
What’s cycle  what’s II?
General form
  int res=0;
  for (int i=0;i<N; i++)
  res=assoc_op(res,f(a[i],b[i], …))

## Slide 34: Pipeline: Data Parallel + Reduce
Pipeline f
Cycle on assoc_op

## Slide 35: Pipeline: Data Parallel + Reduce
Pipeline f
Cycle on assoc_op
Avoid cycle, II=1 for associative
  Gather up II values
  Run through pipelined assoc. reduce tree
  Drop into assoc_op cycle every II cycles
Shown
II=2

## Slide 36: Pipeline: Data Parallel + Reduce
Pipeline f
Cycle on assoc_op
Avoid cycle, II=1 for associative
  Gather up II values
  Run through pipelined assoc. reduce tree
  Drop into assoc_op cycle every II cycles
Solves, but underutilizes at ¼ clock
Shown
II=4

## Slide 37: Model: Data Parallel+Reduce
Conclude: associative reduce can achieve II of 1
General form
  int res=0;
  for (int i=0;i<N; i++)
  res=assoc_op(res,f(a[i],b[i], …))

## Slide 38: Pipeline: Data Parallel + Reduce
Alternate, less efficient
  …but setting up next

## Slide 39: Pipeline: Data Parallel + Reduce
C-slow uses
Front-end
Full speed

## Slide 40: Pipeline: Data Parallel + Reduce
Continue
To use
C-slow
For final

## Slide 41: Implement Reduce
Can exploit with all of our parallel implementation forms
  Multi-thread (multi-processor)
  SIMD/Vector
  Instruction
  Pipeline
  Spatial (unrolled)

## Slide 42: Parallel Prefix
Part 3

## Slide 43: What if want Prefix?
Sum Reduce
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i];
Sum Prefix
  int sum[N];
  sum[0]=a[0];
  for (int i=1;i<N; i++)
  sum[i]=a[i]+sum[i-1];

## Slide 44: Integers 1--5
Sum Reduce
  int sum=0;
  for (int i=0;i<N; i++)
  sum+=a[i];
   sum=1+2+3+4+5=15

## Slide 45: Integers 1--5
Sum Reduce = 15
Sum Prefix
  int sum[N];
  sum[0]=a[0];
  for (int i=1;i<N; i++)
  sum[i]=a[i]+sum[i-1];
   {1, 3, 6, 10, 15}

## Slide 46: Prefix
Aggregate (vector) output where item i is the reduce of the input vector 0 through i
  prefix[0]=a[0];
  for (int i=1;i<N; i++)
  prefix[i]=op(prefix[i-1],f(a[i]…));
``Prefix’’ because given reduce of each prefix subset 0 to i

## Slide 47: Latency Bound
What’s the latency bound for the prefix when op is associative?
  Assume op is 1 cycle
  prefix[0]=a[0];
  for (int i=1;i<N; i++)
  prefix[i]=op(prefix[i-1],f(a[i]…));

## Slide 48: Latency Bound
Simple (not area efficient) answer:
  Compute reduce for each prefix[i] in parallel
  Latency bound? (single cycle op)
  prefix[0]=a[0];
  for (int i=1;i<N; i++)
  prefix[i]=op(prefix[i-1],f(a[i]…));

## Slide 49: Resources?
How much hardware to achieve within 2x latency bound?
  Hint: can do better than simple case previous slide
  prefix[0]=a[0];
  for (int i=1;i<N; i++)
  prefix[i]=op(prefix[i-1],f(a[i]…));

## Slide 50: Reduce Tree
While computing Sum[0,N-1] compute many Sum[0,j]’s
  Sum[0,1], Sum[0,3], Sum[0,7] ….

## Slide 51: Prefix Tree
While computing Sum[0,N-1] only get
  PG[0,2n-1]
How fillin holes?
– e.g. how get Sum[0,11]?

## Slide 52: Prefix Tree
Look at Symmetric stage (with respect to middle=Sum[0,N-1] stage) and combine to fill in

## Slide 53: Prefix Tree

## Slide 54: Prefix Tree

## Slide 55: Prefix Tree
Note: prefix-tree is same size as reduce tree

## Slide 56: Parallel Prefix Area and Delay?
Roughly twice the area/delay
Area= 2N
Delay = 2log2(N)
Conclude: can compute prefix in log time with linear area.

## Slide 57: Latency Bound
What’s the latency bound for the prefix when op is associative?
  When cycles(op)>1 change?
  prefix[0]=a[0];
  for (int i=1;i<N; i++)
  prefix[i]=op(prefix[i-1],f(a[i]…));

## Slide 58: Parallel Prefix
Important Pattern
Applicable any time operation is associative
  Or can be made associative
Function Composition is always associative
  (see Bonus at end)
Logarithmic delay
Linear area
Notes: Non-associative example: nor2 ? (strictly if start with nors…but of course nor-n is associative in terms of the Ors)

## Slide 59: Parallel Prefix Sum
  prefix[0]=a[0];
  for (int i=1;i<N; i++)
  prefix[i]=op(prefix[i-1],f(a[i]…));

## Slide 60: Broader Application

## Slide 61: Cast Associative
If you can cast it into an associative operation, you can apply
  Associative Reduce
  Parallel Prefix

## Slide 62: Examples
Saturated Addition
  Not associative
Floating-Point Addition
Finite Automata Evaluation
(papers in supplemental reading)

## Slide 63: Majority Associative?
Carry=MAJ=majority = A&&B || B&&C || A&&C
Is Majority Associative ?
Hint: What are each of following?
  MAJ(1,1,MAJ(1,1,MAJ(1,0,0)))
  MAJ(MAJ(MAJ(1,1,1),1,1),0,0)

## Slide 64: Binary Addition
Binary addition needs parallel prefix on majority
Adding 2 W-bit numbers
  What’s the latency bound?
  Area to achieve?
boolean a[i],b[i],s[i]
for (i=0;i<W;i++) {
  cn=(a[i]&&b[i])|| (a[i]&&c)||
  (b[i]&&c);
  s[i]=a[i] ^ b[i] ^ c;
  c=cn;
  }

## Slide 65: Categorization
To minimize confusion, will typically ask you to characterize:
  Data parallel
  Reduce
  Sequential

## Slide 66: Big Ideas:
Reduce from aggregate to scalar
  is a common operation
  not strictly data parallel
  Associative reduce admits to parallelism
    log(N) latency bound
    II=1
    Linear area
Prefix when want reduce of all prefixes
  Also log(N) latency bound
  Linear area

## Slide 67: Admin
Wednesday – recorded only
  No live or synchronous lecture
No required reading for Wednesday
Feedback (including p2)
P3 due Friday

## Slide 68: Binary Addition
Bonus

## Slide 69: Latency Bound?
What’s the latency bound for this operation?
boolean a[i],b[i],s[i]
for (i=0;i<N;i++) {
  cn=(a[i]&&b[i])|| (a[i]&&c)||
  (b[i]&&c);
  s[i]=a[i] ^ b[i] ^ c;
  c=cn;
  }

## Slide 70: Associative
Is the carry operation in addition an associative operation?
Operation:
  MAJ=majority = A&&B || B&&C || A&&C

## Slide 71: Carry Computation
Think about each adder bit as a computing a function on the carry in
  C[i]=g(c[i-1])
  Particular function f will depend on a[i], b[i]
  g=f(a,b)

## Slide 72: Functions
Carry=MAJ=majority = A&&B || B&&C || A&&C
What are the functions g(c[i-1])?
  g(c)=carry(a=0,b=0,c)
  g(c)=carry(a=1,b=0,c)
  g(c)=carry(a=0,b=1,c)
  g(c)=carry(a=1,b=1,c)

## Slide 73: Functions
What are the functions g(c[i-1])?
  g(x)=1 Generate
    a[i]=b[i]=1
  g(x)=x Propagate
    a[i] xor b[i]=1
  g(x)=0 Squash
    a[i]=b[i]=0

## Slide 74: Combining
Want to combine functions
  Compute c[i]=gi(gi-1(c[i-2]))
  Compute compose of two functions
What functions will the compose of two of these functions be?
  Same as before
    Propagate, generate, squash

## Slide 75: Compose Rules (LSB MSB)
GG
GP
GS
PG
PP
PS
SG
SP
SS
[work on board]

## Slide 76: Compose Rules (LSB MSB)
GG = G
GP = G
GS = S
PG = G
PP = P
PS = S
SG = G
SP = S
SS = S

## Slide 77: Combining
Do it again…
Combine g[i-3,i-2] and g[i-1,i]
What do we get?

## Slide 78: Associative Reduce Tree

## Slide 79: Reduce Tree
Sq=/A*/B
Gen=A*B
Sqout=Sq1+/Gen1*Sq0
Genout=Gen1+/Sq1*Gen0

## Slide 80: Reduce Tree
Sq=/A*/B
Gen=A*B
Sqout=Sq1+/Gen1*Sq0
Genout=Gen1+/Sq1*Gen0
Delay and Area? (work next few slides)

## Slide 81: Reduce Tree
Sq=/A*/B
Gen=A*B
Sqout=Sq1+/Gen1*Sq0
Genout=Gen1+/Sq1*Gen0
A(Encode)=2
D(Encode)=1
A(Combine)=4
D(Combine)=2
A(Carry)=2
D(Carry)=1

## Slide 82: Reduce Tree: Delay?
D(Encode)=1
D(Combine)=2
D(Carry)=1
Delay = 1+2log2(N)+1

## Slide 83: Reduce Tree: Area?
A(Encode)=2
A(Combine)=4
A(Carry)=2
Area= 2N+4(N-1)+2

## Slide 84: Reduce Tree: Area & Delay
Area(N) = 6N-2
Delay(N) = 2log2(N)+2

## Slide 85: Compute Carry[N]

## Slide 86: Need Prefix
Need PG[i:0] forall i

## Slide 87: Prefix Tree
Bring in Carry and compute each intermediate carry-in

## Slide 88: Parallel Prefix Area and Delay?
Roughly twice the area/delay
Area= 2N+4N+4N+2N
= 12N
Delay = 4log2(N)+2
Conclude: can add in log time with linear area.