## Slide 1: ESE532: System-on-a-Chip Architecture
Day 22: November 17, 2021
Estimating Chip Area and Costs

## Slide 2: Today
Part 1: Chip Costs from Area
Part 2: Chip Area
  IO
  Interconnect – Rent’s Rule
  Infrastructure
Part 3: Some Areas

## Slide 3: Message
First order:
  Chip cost proportional to Area
  Area = Sum(Area(Components))
But appreciate the simplification:
  Yield makes cost superlinear in area
  I/O, Interconnect, infrastructure
    Can make Area > Sum(Area(Components))

## Slide 4: Wafer Cost
Incremental cost of producing a silicon wafer is fixed for a given technology
  Independent of the specific design
  E.g. $4,000
Can fill wafer with copies of chip
By German Wikipediabiatch, original upload 7.
Okt 2004 by Stahlkocher de:Bild:Wafer 2 Zoll bis 8 Zoll.jpg,
CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=928106

## Slide 5: 16nm Wafer Costs
Source: https://www.eetimes.com/author.asp?section_id=36&doc_id=1329887

## Slide 6: Preclass 1
Rough cost per mm of silicon?
  $4000 for 300mm wafer

## Slide 7: Implication
Raw silicon die cost is roughly proportional to area
  Larger the die, the fewer we get on the wafer

## Slide 8: …but
Limits to how big we can make chips
  Manufactures are prepared to create
  Can be reliably manufactured
…and how small we can make chips
  I/O pads
  Cutting/handling/marking

## Slide 9: Imaging
Limit to how large optical imaging supports
Reticle – imagable region for photo lithography
  Around 600mm2
Source
https://www.asml.com/the-asml-exposure-apparatus-is-the-most-expensive-and-complex-step-in-the-chip-fabrication-process-what-is-involved-in-the-lithography-business/ja/s28145?rid=44709

## Slide 10: Yield
Chips won’t be manufactured perfectly
  Dust particles can impact imaging
  Manufacturing processes are statistical
If chips must be defect-free,
  larger chips are more likely to have defects than smaller chips

## Slide 11: Simple Yield Model
Probability of a region being perfect
  E.g. probability of one sq. mm being defect-free
Chip yields if its entire area is defect free

## Slide 12: Chip Yield
P = defect-free probability per sq. mm
What is probability a chip of A sq. mm yields (symbolic) ?

## Slide 13: Preclass 2
P=0.99
Probability of yield for
  10 mm2, 50 mm2, 100 mm2, 500 mm2
Area (mm2) | Yield Rate
10 | 
50 | 
100 | 
500 | 

## Slide 14: Preclass 2
P=0.99
Probability of yield for
  10 mm2, 50 mm2, 100 mm2, 500 mm2
Area (mm2) | Yield Rate
10 | 0.90
50 | 0.60
100 | 0.37
500 | 0.0066

## Slide 15: Yielded Die
For a yield rate, Y, how many raw die need to manufacture per yielded die?

## Slide 16: Preclass 3
P=0.99
Die cost for:
  10 mm2, 50 mm2, 100 mm2, 500 mm2
Area | Raw Cost | Yield Rate | Cost/Yielded Chip
10 |  | 0.90 | 
50 |  | 0.60 | 
100 |  | 0.37 | 
500 |  | 0.0066 | 

## Slide 17: Preclass 3
P=0.99
Die cost for:
  10 mm2, 50 mm2, 100 mm2, 500 mm2
Area | Raw Cost | Yield Rate | Cost/Yielded Chip
10 | 0.60 | 0.90 | 
50 | 3.00 | 0.60 | 
100 | 6.00 | 0.37 | 
500 | 30.00 | 0.0066 | 
0.06 / mm2

## Slide 18: Preclass 3
P=0.99
Die cost for:
  10 mm2, 50 mm2, 100 mm2, 500 mm2
Area | Raw Cost | Yield Rate | Cost/Yielded Chip
10 | 0.60 | 0.90 | 0.67
50 | 3.00 | 0.60 | 5.00
100 | 6.00 | 0.37 | 16.22
500 | 30.00 | 0.0066 | 4500
0.06 / mm2

## Slide 19: Yielded Die Cost

## Slide 20: Yielded Die Cost
Ultimately exponential in Area
Means
  Expensive above knee in exponential curve
  Close to linear below knee in curve
E.g.
  Below PA=0.5
    effect of Yield term is less than 2

## Slide 21: Design Dependent Cost
P can be design dependent
  More aggressive designs have higher defect rates
  Can tune design to ease manufacturing
Contrast with point that wafer manufacture cost independent of design

## Slide 22: Slightly Fuller Story
Chip cost = die + test + package

## Slide 23: Test
Testing costs proportional to test time
  Time on expensive test unit
  Depends on complexity of tests need to run
    Can motivate spending silicon area on on-chip test structures to reduce
Can dominate on small chips or complex testing

## Slide 24: Packaging
Pay for density and performance

## Slide 25: Plastic Packages
Simple plastic packages cheap
  Limited number of pins
    Limited to perimeter
  Limited heat removal (few Watts)
  Can be large (due to pins)
  Higher inductance on pins
http://wiki.electroons.com/doku.php?id=ic_packages

## Slide 26: Ceramic Packages
Better thermal characteristics
  Add heat-sink, tolerate hotter chips
    To 100 W
  More pins
  More expensive
Source: https://www.ngkntk.co.jp/english/product/semiconductor_packages/htcc.html

## Slide 27: Flip Chip Packages
Support Area-IO
  More, denser pins
  Smaller die if IO limited
  Lower inductances
  Smaller packaged chip
Source: http://mantravlsi.blogspot.com/2014/10/flip-chip-and-wire-bonding.html

## Slide 28: Zynq Land Grid Package
SBVA 484 – flip chip, Ball-Grid Array (UG 1075)

## Slide 29: Don’t Forget NRE
This is all about recurring costs
Cost = RecurringCost + (NRE/NumParts)
NRE
  Mask costs in millions
  Design costs in 10s to 100s of millions

## Slide 30: Bonus: Chip Design Costs
https://wccftech.com/apple-5nm-3nm-cost-transistors/

## Slide 31: Putting Together
100mm2 die -- $5.6 raw
  Maybe $6--16 yielded -- call it $7
NRE $100 M -- $1
  Sell 100 M units
Put in $1 packge -- $1
Test -- $1
Total: $10

## Slide 32: Price vs. Cost
…and this is all about cost
  What it takes to manufacture
Price
  What people will pay for it
Profit = Price - Cost

## Slide 33: Area
Part 2

## Slide 34: Area
Simple story
  Sum up component areas

## Slide 35: Too Simplistic
Area may be driven by
  I/O
  Interconnect
Will need to pay for infrastructure
  Clocking, Power
  …maybe linear overhead factor

## Slide 36: I/O Pads
Must go on edge for wire bonding
  Esp. for cheap packages
Source: https://commons.wikimedia.org/wiki/File:DIP_package_sideview.PNG
Src: http://en.wikipedia.org/wiki/File:Wirebonding2.svg

## Slide 37: Pad Ring
Pads must go on side of chip
Pad spacing large to permit bonding
I/O pads may set lower bound on chip size

## Slide 38: Preclass 4
400 pads
25mm pad spacing
Square chip dimensions?

## Slide 39: I/O Limits
Perimeter grows as 4s
Area grows as s2
Area grows (NumIO/4)2
IO may drive chip area

## Slide 40: Area I/O
Put I/O in grid over chip
I/O pads still large and take up space
Avoid perimeter scaling
Requires more expensive flip-chip package

## Slide 41: Flip Chip I/O
Source: https://en.wikipedia.org/wiki/Flip_chip

## Slide 42: Flip Chip, Area IO
www.microwavejournal.com
http://www.izm.fraunhofer.de/en/abteilungen/high_density_interconnectwaferlevelpackaging/arbeitsgebiete/arbeitsgebiet1.html

## Slide 43: Flip Chip Packages
Support Area-IO
  More, denser pins
  Smaller die if IO limited
  Lower inductances
  Smaller packaged chip
Source: http://mantravlsi.blogspot.com/2014/10/flip-chip-and-wire-bonding.html

## Slide 44: Interconnect
Long wires need buffering
Buffers take up space
  Weren’t in simple accounting of logic and memory blocks

## Slide 45: Interconnect
Wires take up space
Similar issue to pad I/O
  Wires crossing into region grow as perimeter
  Logic inside grows as area
Region size may be dictated by wires entering/leaving

## Slide 46: Wiring Requirements
Wires 50nm pitch
Gates 500nm on side
  (500nm x 500nm)
How many wires fit across the side of one gate?

## Slide 47: Wiring Requirements
Wires 50nm pitch
Gates 500nm on side
  (500nm x 500nm)
Wires/gate side (prev slide)
If have SxS gate on left, how many wires can cross over the line of S gates at the right?
What if need more wires to cross to right?

## Slide 48: Need More Wires
What if need more wires to cross to right?

## Slide 49: Bisection Width
Partition design into two equal size halves
  Minimize wires (nets) with ends in both halves
Number of wires crossing is bisection width
  Information crossing
lower bw = more locality
N/2
N/2
bisection
width

## Slide 50: Rent’s Rule
If we recursively bisect a graph, attempting to minimize the cut size, for an N-node graph, we typically get:
BW=IO = c Np
  0p1
  p1 means many inputs come from within a partition
[Landman and Russo,
IEEE TR Computers p1469, 1971]

## Slide 51: Rent and Locality
Rent and IO quantifying locality
  local consumption
  local fanout
IO = c Np

## Slide 52: Common Applications
Rent p=0
  Shift-register, 1D filter
Rent p=0.5
  Array multiplier
  2D Window Filter
  nearest-neighbor
Rent p=1.0
  FFT, Sort
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
reg
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
bit
Mpy
Bit
Mpy
bit

## Slide 53: VLSI Interconnect Area
Bisection width is lower-bound on IC width
  When wire dominated, may be tight bound
(recursively)
Rent’s Rule tells us how big our chip must be

## Slide 54: As a function of Bisection
Achip  N  Agate
Achip  Nhorizontal Wwire  Nvertical Wwire
Nhorizontal = Nvertical = IO = cNp
Achip  (cN)2p
If p<0.5
  Achip  N
If p>0.5
  Achip  N2p

## Slide 55: In terms of Rent’s Rule
If p<0.5, Achip  N
If p>0.5, Achip  N2p
Typical designs have p>0.5
  interconnect dominates
  Achip > S Aelements

## Slide 56: Rent Network Richness

## Slide 57: Infrastructure: Clocking
PLL (Phased-Lock-Loop) to generate and synchronize clock
Clock drivers are big (drive big load)
Need buffering all over chip

## Slide 58: Infrastructure: Power
Need many I/O Pads
  Carry current
  Keep inductance low
Wires to distribute over chip
Maybe
  Capacitance to stabilize power
  Voltage converters

## Slide 59: Area
Mostly sum of components, but…
Area may be driven by
  I/O
  Interconnect A ≥ N2p
Will need to pay for infrastructure
  Clocking, Power
  Include as components
  Then linear factor for distribution

## Slide 60: Some Areas
Part 3

## Slide 61: Processor Areas
ARM Cortex A53 about 2mm2 in 28nm
  Zynq UltraScale+ processor
  SuperScalar core
A5 (scalar) about 0.25mm2
A9 (superscalar) about 1mm2
A15 (higher performance) about 3mm2
A57 (big core to A53 little) about 3mm2
A72 (Amazon a1) about 4.6mm2
  (ARM claim1.15mm2 in 16nm FinFet)

## Slide 62: R-Car H3 from Rensas Quad A57, Quad A53
https://en.wikichip.org/wiki/arm_holdings/microarchitectures/cortex-a53

## Slide 63: Zynq Compute Blocks
Crude estimate, including interconnect
2000 6-LUTs per sq. mm
DSP Block ~ 0.1 sq. mm

## Slide 64: CACTI
Standard program for modeling memories and caches
  More sophisticated version of the simple modeling we’ve been doing

## Slide 65: CACTI – Memories on Zynq
32nm (closest technology it models to 28nm in Zynq)
36Kb BRAMs 0.025mm2
  2 port, 72b output
ARM L1 cache 0.08mm2
  32KB 4-way associative
ARM L2 cache 1.5 mm2
  512KB 8-way associative
  (older, not yours)

## Slide 66: Zynq Component Estimates
6-LUT 0.0005 mm2
DSP Block 0.1 mm2
36Kb BRAMs 0.025mm2
ARM L1 cache 0.08mm2
ARM L2 cache (512KB, 8-way)1.5 mm2
ARM Cortex A53 2.0 mm2

## Slide 69: Apple A13 Bionic
98mm2, 7nm
8.5 Billion Tr.
iPhone 11 +
6 ARM cores
  2 fast (2.6GHz)
  4 low energy
4 custom GPUs
Neural Engine
  5 Trillion ops/s?

## Slide 70: A13 Die Areas
https://en.wikipedia.org/wiki/Apple_A13
SoC | A13 (7 nm) | A12 (7 nm)
Process Node | TSMC N7P | TSMC N7
Total Die | 98.48 | 83.27
Big Core | 2.61 | 2.07
Small Core | 0.58 | 0.43
CPU Complex (incl. cores) | 13.47 | 11.16
GPU Core | 3.25 | 3.23
GPU Total | 15.28 | 14.88
NPU | 2.09 | 1.23

## Slide 71: Big Ideas
First order:
  Chip cost proportional to Area
  Area = Sum(Area(Components))
But appreciate the simplification:
  Yield makes cost superlinear in area
    Limited range over which “linear” accurate
  I/O, Interconnect, infrastructure
    Can make Area > Sum(Area(Components))

## Slide 72: Admin
Reading for Monday on Web
P3 due Friday
P4 posted
  due 2 weeks, next Friday Thanksgiving break