## Slide 1: ESE532: System-on-a-Chip Architecture
Day 9: October 4, 2021
High-Level Synthesis (HLS)
C-to-gates
More accurate: C-for-gates

## Slide 2: Today
Motivation
Spatial Computations from C specification
  Variables and expression (pre-lecture)
  Simple Conditionals (Part 1)
  Functions (part 2)
  Globals
  Loops and Arrays (Part 3)

## Slide 3: Message
C (or any programming language) specifies a computation
C can describe spatial computation
  A dataflow graph with physical operators for each operation
Underlying semantics is sequential
  Watch for unintended sequentialization
  Write C for spatial differently than you write C for processors

## Slide 4: Coding Accelerators
Want to exploit FPGA logic on F1, Zynq to accelerate computations
Traditionally has meant develop accelerators in
  Hardware Description Language (HDL)
    E.g. Verilog  see in CIS371, CIS501
  Directly in schematics

## Slide 5: Course “Hypothesis”
C-to-gates synthesis mature enough to use to specify hardware
  Leverage fact everyone knows C
    (must, at least, know C to develop embedded code)
  Avoid taking time to teach Verilog or VHDL
    Or making Verilog a pre-req.
  Focus on teaching how to craft hardware
    Using the C already know
    …may require thinking about the C differently

## Slide 6: Discussion [open]
Is it obvious we can write C to describe hardware?
What parts of C translate naturally to hardware?
What parts of C might be problematic?
What parts of hardware design might be hard to describe in C?

## Slide 7: Three Perspectives
How express spatial/hardware computations in C
  May want to avoid some constructs in C
How express computations
  Hopefully, equally accessible to spatial and sequential implementations
Given C code: how could we implement in spatial hardware
  Some corner cases and technicalities make tricky
[copy to board]

## Slide 8: Advantage
Use C for hardware and software
  Test out functionality entirely in software
    Debug code before put on hardware
      where harder to observe what’s happening
    …without spending time in place and route
      …which you soon see is slow…
  Explore hardware/software tradeoffs by targeting same code to either hardware or software

## Slide 9: Context
C most useful for describing behavior of operators
C alone doesn’t naturally capture task parallelism

## Slide 10: Preclass F
Ready for preclass f?
Skip to preclass f

## Slide 11: C Primitives Arithmetic Operators
Unary Minus (Negation) -a
Addition (Sum) a + b
Subtraction (Difference) a - b
Multiplication (Product) a * b
Division (Quotient) a / b
Modulus (Remainder) a % b
Things might have a hardware operator for…

## Slide 12: C Primitives Bitwise Operators
Bitwise Left Shift a << b
Bitwise Right Shift a >> b
Bitwise One's Complement ~a
Bitwise AND a & b
Bitwise OR a | b
Bitwise XOR a ^ b
Things might have a hardware operator for…

## Slide 13: C Primitives Comparison Operators
Less Than a < b
Less Than or Equal To a <= b
Greater Than a > b
Greater Than or Equal To a >= b
Not Equal To a != b
Equal To a == b
Logical Negation !a
Logical AND a && b
Logical OR a || b
Things might have a hardware operator for…

## Slide 14: Expressions: combine operators
a*x+b
A connected set of operators
 Graph of operators
*
+
a
x
b

## Slide 15: Expressions: combine operators
a*x+b
a*x*x+b*x+c
a*(x+b)*x+c
((a+10)*b < 100)
A connected set of operators
 Graph of operators

## Slide 16: C Assignment
Basic assignment statement is:
Location = expression
f=a*x+b
*
+
a
x
b
f

## Slide 17: Straight-line code
a sequence of assignments
What does this mean?
  g=a*x;
  h=b+g;
  i=h*x;
  j=i+c;
b
c
*
a
x
g
+
h
*
i
+
j

## Slide 18: Variable Reuse
Variables (locations) define flow between computations
Locations (variables) are reusable
  t=a*x;
  r=t*x;
  t=b*x;
  r=r+t;
  r=r+c;

## Slide 19: Variable Reuse
Variables (locations) define flow between computations
Locations (variables) are reusable
  t=a*x; t=a*x;
  r=t*x; r=t*x;
  t=b*x; t=b*x;
  r=r+t; r=r+t;
  r=r+c; r=r+c;
Sequential assignment semantics tell us which definition goes with which use.
  Use gets most recent preceding definition.

## Slide 20: Dataflow
Can turn sequential assignments into dataflow graph through defuse connections
  t=a*x; t=a*x;
  r=t*x; r=t*x;
  t=b*x; t=b*x;
  r=r+t; r=r+t;
  r=r+c; r=r+c;
*
*
*
+
+
a
x
b
c

## Slide 21: Dataflow Height
t=a*x; t=a*x;
  r=t*x; r=t*x;
  t=b*x; t=b*x;
  r=r+t; r=r+t;
  r=r+c; r=r+c;
Height (delay) of DF graph may be less than # sequential instructions.
*
*
*
+
+
a
x
b
c

## Slide 22: Lecture Checkpoint
Happy with ?
  Straight-line code
  Variables
Graph for preclass f

## Slide 23: Straight Line Code
C is fine for expressing straight-line code and variables
  Has limited data types
    Address with tricks like masking
    Address with user-defined types

## Slide 24: Optimizations can probably expect compiler to do
Constant propagation: a=10; b=c[a];
Copy propagation: a=b; c=a+d;  c=b+d;
Constant folding: c[10*10+4];  c[104];
Identity Simplification: c=1*a+0;  c=a;
Strength Reduction: c=b*2;  c=b<<1;
Dead code elimination
Common Subexpression Elimination:
  C[x*100+y]=A[x*100+y]+B[x*100+y]
  t=x*100+y; C[t]=A[t]+B[t];
Operator sizing: for (i=0; i<100; i++) b[i]=(a&0xff+i);

## Slide 25: Conditionals
What can we do for simple conditionals?
if (a<b)
  res=b-a
Else
  res=a-b

## Slide 26: Simple Control Flow
If (cond) { … } else { …}
Assignments become conditional
In simplest cases (no memory ops), can treat as dataflow node
cond
choose
then
else

## Slide 27: Simple Conditionals
if (a>b)
c=b*c;
else
c=a*c;
a>b
b*c
a*c
c

## Slide 28: Simple Conditionals
v=a;
if (b>a)
v=b;
If not assigned, value flows from before assignment
b>a
b
a
v

## Slide 29: Simple Conditionals
max=a;
min=a;
if (a>b)
{min=b;
c=1;}
else
{max=b;
c=0;}
May (re)define many values on each branch.
a>b
b
a
min
1
0
max
c

## Slide 30: Preclass G
Graph for preclass g as mux-conversion?

## Slide 31: Part 2
Functions and Globals

## Slide 32: Function Call
What computation is this describing?
What role does the function call play?
int f(int a, int b)
  return(sqrt(a*a+b*b));
for(i=0;i<MAX;i++)
  D[i]=f(A[i],B[i]);

## Slide 33: Inline Transformation
Inline a function
  Copy the body of function
  Into the point of call
  Replacing the function arguments
  With the arguments supplied in the call
int f(int a, int b)
  return(sqrt(a*a+b*b));
for(i=0;i<MAX;i++)
  D[i]=f(A[i],B[i]);
for(i=0;i<MAX;i++)
  D[i]=sqrt(A[i]*A[i] +B[i]*B[i]);

## Slide 34: Inline
int p(int a)
  return(a*a+2*a-1);
for(i=0;i<MAX;i++)
  D[i]=p(A[i])-p(B[i]);
for(i=0;i<MAX;i++)
D[i]=A[i]*A[i]+2*A[i]-1
  - (B[i]*B[i]+2*B[i]-1);
Functions provide descriptive convenience and compactness.
…but don’t need to force implementation.

## Slide 35: Treat as data flow
Implement function as an operation
Send arguments as input tokens
Get result back as token
Functions provide potential division between substrates?
Assign different functions to
different substrate (proc, fpga)

## Slide 36: Shared Function
Functions express shared operators.
F1(A,B);
// Transpose(A,Aprime);
// matmul(Aprime,c1,B);
F2(B,C);
// matmul(B,c2,Cpre);
// normalize(Cpre,C);
if (A<B)
{
matmul(A,c1,B);
}
else
{
matmul(D,c3,E);
}

## Slide 37: Recursion?
int fib(int x) {
if ((x==0) || (x==1)) return(1);
else
return(
fib(x-1) + fib(x-2));
}
In general won’t work.
  Problem?
Smart compiler might be able to turn some cases into iterative loop.
…but don’t count on it.
  VivadoHLS will not

## Slide 38: Global Variables
int a=0;
int f1(int *A) {
for (int i=0;i<a;i++)
sum+=A[i];
return(sum); }
void f2(int *A) {
while (A[a]!=0);
a++;
}
f2(input);
isum=f1(input);
Variables not declared in a function resolve to outer context

## Slide 39: Treat as data flow
Functions provide potential division between substrates.
Impact on global variables?
Run on processor
Run on FPGA
int a=0;
int f1(int *A) {
for (int i=0;i<a;i++)
sum+=A[i];
return(sum); }
void f2(int *A) {
while (A[a]!=0);
a++; }
f2(input);
isum=f1(input);

## Slide 40: Treat as data flow
Functions provide potential division between substrates.
Impact on global variables?
Correct thing
  Reflect change in variable between substrates
Evidence Vivado HLS
  Not synchronized with host C on globals
Run on processor
Run on FPGA

## Slide 41: Global Variables
int a=0;
int f1(int *A) {
for (int i=0;i<a;i++)
sum+=A[i];
return(sum); }
void f2(int *A) {
while (A[a]!=0);
a++;
}
f2(input);
isum=f1(input);
Globals generally considered bad coding practice
  Obfuscate flow of data even for human
Avoid Gobals
With hardware, have extra reason avoid

## Slide 42: Global Variables
int f1(int *A, int len) {
for (int i=0;i<len;i++)
sum+=A[i];
return(sum); }
int f2(int *A) {
int len=0;
while (A[len]!=0);
len++;
return(len)
}
len=f2(input);
isum=f1(input,len);
int a=0;
int f1(int *A) {
for (int i=0;i<a;i++)
sum+=A[i];
return(sum); }
void f2(int *A) {
while (A[a]!=0);
a++;
}
f2(input);
isum=f1(input);
Bad
Better

## Slide 43: Part 3
Loops and Arrays

## Slide 44: Loops…
From an express computation standpoint, have several roles
  Compact code
  Unbounded computation
From describe hardware
  Compact expression of parallel hardware
  Express pipelines
  Express data-level parallelism
  Express area-time tradeoff

## Slide 45: Loop Compact Expression
What express?
  Sequential, fully unrolled, partially unrolled?

## Slide 46: Sequential

## Slide 47: Spatial = fully unrolled

## Slide 48: Stream
Logical abstraction of a persistent point-to-point communication link between operators
  Has a (single) source and sink
  Carries data presence / flow control
  Provides in-order (FIFO) delivery of data from source to sink
stream
Day 5

## Slide 49: Stream
For the moment assume way to read and write to streams:
  stream.read() – return next value on stream
  stream.write(val); put val onto stream
stream

## Slide 50: Unbounded, Pipelined Operator
What C code describe?

## Slide 51: Unbounded, Pipelined Operator
What describe?
int c=12;
while(true)
  {
  int aval=astream.read();
  int bval=bstream.read();
  int res=a*b+c;
  resstream.write(res);
    }

## Slide 52: With function call, loop in function
int c=12;
while(true)
  {
  int aval=astream.read();
  int bval=bstream.read();
  int res=multiply(a,b)+c;
  resstream.write(res);
    }

## Slide 53: Compact Expression: Arrays
Useful to be able to refer to different values (a large number of values) with the same code.
Arrays + Loops: give us a way to do that
Useful:
  general expression
  hardware description

## Slide 54: Compact Expression: Arrays+Logic
Vector sum:
  c3=a3+b3; c2=a2+b2; c1=a1+b1; c0=a0+b0;
  for(i=0;i<3;i++) c[i]=a[i]+b[i];
Chose small length to fit non-array on slide
  #define K 16
  for(i=0;i<K;i++) c[i]=a[i]+b[i];

## Slide 55: Compact Expression: Arrays+Logic
Dot Product:
  Y=a3*b3+a2*b2+a1*b1+a0*b0;
  Y=0; for(i=0;i<3;i++) Y+=a[i]*b[i];

## Slide 56: Compact Expression: Arrays+Logic
Vector sum:
  c3=a3+b3; c2=a2+b2; c1=a1+b1; c0=a0+b0;
  for(i=0;i<3;i++) c[i]=a[i]+b[i];
These array elements may be nodes in dataflow graph, just like the variables we saw for function f
  Express large dataflow graphs
  Make area-time choices for implementation

## Slide 57: Foreshadowing: C Array Challenge
C programmers think of arrays as memory (or memory as arrays)
  …and sometimes we will want to
Be careful understanding (and expressing) arrays that don’t have to be memories
  …and treated with memory semantics

## Slide 58: Loop Interpretations
What does a loop describe?
  Sequential behavior [when to execute]
  Spatial construction [when create HW]
  Data Parallelism [sameness of compute]
We will want to use for all 3
Sometimes need to help the compiler understand which we want

## Slide 59: Easy Loop (for contrast)
for (i=0;i<10;i++)
sum+=a[i];
How many times loop execute?
If unroll, which i for each loop instance?

## Slide 60: Loop Bounds
Loops without constant bounds
  while (sum+a[i]<100) {
  sum+=a[i];
  b[i]=a[i]>>2;
  i++; }
How many times loop execute?
Typically forces sequentialization
  Cannot unroll into hardware

## Slide 61: Loop Increment
Loops with variable increment also force sequentialization
  for (i=0;i<100;i+=f(i))
  { b[i]=a[i]; sum+=a[i]; }
What are values of i for which evaluate body?

## Slide 62: Loop Interpretations
What does a loop describe?
  Sequential behavior [when execute]
  Spatial construction [when create HW]
  Data Parallelism [sameness of compute]
We will want to use for all 3
C allows expressive loops
  Some expressiveness
    Not compatible with spatial hardware construction

## Slide 63: Unroll
Vivado HLS has pragmas for unrolling
UG901: Vivado HLS User’s Guide
  P180—229 for optimization and directives
#pragma HLS UNROLL factor=…
Use to control area-time points
  Use of loop for spatial vs. temporal description

## Slide 64: Big Ideas:
C (any prog lang) specifies a computation
Can describe spatial computation
  Has some capabilities that don’t make sense in hardware
    Shared memory pool, globals, recursion
  Watch for unintended sequentialization
C for spatial is coded differently from C for processor
  …but can still run on processor
Good for leaf functions (operations)
  Limiting for full task

## Slide 65: Admin
Feedback, incl. HW4
Midterm on Wednesday
  Here at lecture time
  See details on web
  Previous midterms on web
  Parts 1—3 today are relevant to exam
  No office hour Wed.
  Extended TA office hours Tuesday 5—7pm
HW5 due Wednesday 10/13
  Several long compiles
  Get started early