## Slide 1: ESE5320: System-on-a-Chip Architecture
Day 13: October 17, 2022
Vitis OpenCL
Data Transfer Model

## Slide 2: Previously
Value of small, local memories
Tune local memories in C
DMA as data-movement threads

## Slide 3: Today
Vitis/OpenCL Interface
Execution Model (Part 1)
Host-Side Programming (Part 2)
FPGA-Side Programming (Part 3)

## Slide 4: Message
Vitis uses an explicit DMA transfer interface
Can build our streaming model on top of primitives offered
Will need to tune parameters and use carefully to get maximize performance
  Good and bad  largely exposed

## Slide 5: OpenCL
OpenCL – Open Computing Language
  Standard for programming accelerators
  Open alternative to CUDA
  Write things in one language
    Compile to many compute platforms
Xilinx(AMD) uses for host interface to accelerator
  Won’t be using for kernel computation on FPGA

## Slide 6: Execution Model(s)
Part 1

## Slide 7: Model
Host and Accelerator
Host control
  Set accelerator arguments
  DMA bulk data to and from accelerator
  Tell it to start
  DMA, Accelerator runs as independent thread
  Synchronize on data return

## Slide 8: Remember: Preclass 4a
Where do we set DMA arguments?

## Slide 9: Remember: Preclass 4a
Set arguments to accelerator
Accelerator
Uses to
grab inputs

## Slide 10: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 11: Function Call
Host and Accelerator
Host control
  Set accelerator arguments
  DMA bulk data to accelerator
  Tell it to start
  DMA result back
  Host program wait on accelerator completion

## Slide 12: Separate Accelerator Thread
Host and Accelerator
Host control
  Set accelerator arguments
  Tell it to start
    accelerator
      DMA bulk data to accelerator
      DMA result back
    Host: execute something else
  Host program synchronize before use accelerator result

## Slide 13: PS<->PL Interface
Xilinx UG1393, Fig. 2 (Ch. 3)
Part 2
Part 3

## Slide 14: Minimal
Simple case one host process, one accelerator

## Slide 15: Accelerator Stream
Dataflow stream accelerators on host side

## Slide 16: Streaming
Map general streaming
Use multiple threads
  Even processors

## Slide 17: Streaming
Map general streaming
Use multiple threads
  Even processors
… and multiple accelerators
Given space, any streaming case
  DMA buffers cross PS<->PL

## Slide 18: Data Movement (Options)
Access from global memory
Configure DMA/accelerator with main-memory pointer
DMA copy into BRAM memories
  Built on top of other with DMA copy loop

## Slide 19: Remember: Preclass 4a

## Slide 20: Data Movement (Options)
How copy loop improve performance?
  Assume dataflow streaming between copy loop and accelerator computation?

## Slide 21: Copy Loop Benefits
Run concurrently – improve throughput
  Overlap compute and communication
Hide latency of read

## Slide 22: Host-Side Programming
Part 2

## Slide 23: Outline
Platform
Device
Context
Command Queue
Load FPGA
Buffers and Transfer
Kernel Execution
Synchronize on Result
Overlap Data and Compute
Running Multiple Kernels

## Slide 24: Platform
For general case where have multiple OpenCL platforms
Silly for Ultra96 SoC
  and, looks like we can partially hide

## Slide 25: Device
For case of multiple FPGAs  which FPGA
Also somewhat silly for Ultra96 with single FPGA (PL)
Amazon F1.x16large has multiple FPGAs

## Slide 26: Device
Our Utilities.cpp,h – hide Platform
  std::vector<cl::Device> devices = get_xilinx_devices();
  devices.resize(1);
  cl::Device device = devices[0];
Get away with simplification
  Know want only Xilinx platform
  Know only one device (Ultra96)

## Slide 27: Context
Context for device
  Not sure what flexibility/differentiation this is giving
    maybe for DFX overlay shells
  Supports some error callback

## Slide 28: Command Queue
Setup queue to issue commands
For “programming” interactions with accelerators
Use to set them up to happen as separate thread
  Separate when host requests and when accelerator actually run

## Slide 29: Load Bitstream on FPGA
Where we actually reconfigure FPGA
  Not really for our current platform
    But confirms bitstream using
    …and needs read some information from xclbin
  For Partial Reconfiguration (DFX) platform
    Option to choose which to load
    Option to reconfigure during operation under host control
      not one we’ll exercise this term

## Slide 30: Kernels
Setup the actual accelerators to call
  Extract handle to reference them from the loaded bitstream (program)
  Just naming them at this point

## Slide 31: Preclass 1
Kernel with
  10ms input transfer
  30ms compute
  5ms outputs
Latency?
Throughput if must serialize?
Throughput if overlap data transfers and computation?

## Slide 32: Preclass 1

## Slide 33: Host and Device Memory View
Host pointers not necessarily meaningful to device
  Need to map
  Different memories? (depend on platform)
    Embedded incl. Ultra96 (same), data-center (may be different)
  Virtual vs. Physical addresses?
  Same memory, different address map?

## Slide 34: Buffers and Transfer
Create
Buffers
Set kernel
pointers
Host side pointers
Fill with host data
Launch data transfer
(enqueue)

## Slide 35: Remember: Preclass 4a
clSetKernelArg
Use
dev_mem_ptr

## Slide 36: Movement Options
clEnqueueReadBuffer (WriteBuffer)
  Not guarantee timing of transfer
clEnqueueMigrateObjects
  Supports overlap of compute and communicate
  recommended

## Slide 37: Remap Device Pointer
Migration remap dev_mem_ptr
(don’t know if this is happening this way)

## Slide 38: Kernel Invocation
After
  Kernel arguments set
  Buffer transfers have been enqueued
Causes to actual run on data transferred
Commands – command queue
Kernel – naming of kernel to run
Last two arguments for synchronization

## Slide 39: Synchronize
Options to synchronize in calls
Must synchronize to know finished
q.enqueueMigrateMemObjects({in1_buf, in2_buf}, 0, NULL, &event_sp);
clWaitForEvents(1, (const cl_event *)&event_sp);
q.enqueueTask(krnl_mmult, NULL, &exec_event_sp);
clWaitForEvents(1,
(const cl_event *)&exec_event_sp);

## Slide 40: Synchronize
q.enqueueMigrateMemObjects({in1_buf, in2_buf}, 0, NULL, &event_sp);
clWaitForEvents(1, (const cl_event *)&event_sp);
q.enqueueTask(krnl_mmult, NULL, &exec_event_sp);
clWaitForEvents(1,
(const cl_event *)&exec_event_sp);
But, don’t always want to synchronize after every operation

## Slide 41: Preclass 2a
Break kernel into three 10ms pieces and use dataflow between them
  10ms input transfer
  10ms compute x 3
  5ms output transfer
Throughput?

## Slide 42: Preclass 1 and 2

## Slide 43: Dataflow: Host-to-kernel
Create a dataflow stream between host process and accelerator
  Like DATAFLOW pragma
  Control on FPGA/kernel side (coming up)
Overlap next computation (setup) on host with FPGA kernel
UG1393 says embedded platforms not support?
  …but maybe not need since single global memory

## Slide 44: Running Multiple Kernel Instances
Can have multiple instances of same kernel on FPGA
Dispatch from Out-of-Order command queue
Will distribute among identical kernels
Out-of-Order queue
  Helps with compute/communication overlap for single kernel. (see HW6)
  Not force synchronization on return result.

## Slide 45: Parallelism
Pipeline/Dataflow
  With Host Dataflow
  DMA transfers and compute
  Within compute
Thread Parallelism
  Launch multiple accelerator
Data Parallelism
  Define multiple instances of one accelerator and enqueue work for

## Slide 46: Cleanup
Need to release/free resources setup

## Slide 47: FPGA-Side Programming
Part 3

## Slide 48: Interface Pragmas
Assign AXI
  Bundles
Host-to-Kernel
Burst read
Interface width

## Slide 49: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 50: Programmable SoC
AXI Channels
128b wide
@ 333 MHz
=5.3GB/s

## Slide 51: AXI Channels
Can tell it to use AXI Channels
By default (as shown above) all share same channel

## Slide 52: AXI Channels
Separate names to use different
Note, not naming to match ZCU3EG names
  Portability across targets

## Slide 53: Programmable SoC
AXI Channels
128b wide
@ 333 MHz
=5.3GB/s

## Slide 54: Older and Defaults
2019.2:
#pragma HLS INTERFACE s_axilite port = in1 bundle = control
#pragma HLS INTERFACE s_axilite port = in2 bundle = control
#pragma HLS INTERFACE s_axilite port = out_r bundle = control
#pragma HLS INTERFACE s_axilite port = size bundle = control
#pragma HLS INTERFACE s_axilite port = return bundle = control
#pragma HLS INTERFACE m_axi port=in1 offset=slave bundle=gmem
#pragma HLS INTERFACE m_axi port=in2 offset=slave bundle=gmem
#pragma HLS INTERFACE m_axi port=out_r offset=slave bundle=gmem
2020.1:
#pragma HLS INTERFACE m_axi port=in1 bundle=gmem
#pragma HLS INTERFACE m_axi port=in2 bundle=gmem
#pragma HLS INTERFACE m_axi port=out_r bundle=gmem

## Slide 55: Remember: Preclass 4a
S-AXI Control – load pointers
M-AXI transfer
Using pointers

## Slide 56: Host-to-kernel Dataflow
ap_ctrl_chain

## Slide 57: Burst Transfer
Where have we seen this before?

## Slide 58: Remember: Preclass 4a

## Slide 59: Burst Transfer
Use Dataflow to setup as separate threads on accelerator side
May also be able to use C memcpy
  Vitis UG1399 (2020.1, p. 212)

## Slide 60: Data Movement (Options)
Access from global memory
Configure DMA/accelerator with main-memory pointer
DMA burst copy into BRAM memories
  Built on top of other with DMA copy loop

## Slide 61: Preclass 3, 4
333MHz cycle time on bus
Peak bandwidth if transfer per cycle
  32b
  64b
  128b
Memory at 4 GB/s
  Which widths make bus the bottleneck?
  Memory?

## Slide 62: Width
In some cases will auto size data transfer
  See Vitis UG 1399 (2020.1) p. 214 “Automatic Port Width Resizing”
Others transfer at width of data type give
  May need to pack and unpack data to exploit full width

## Slide 63: Big Ideas
Data between PS and PL managed as DMA
Can exploit familiar parallelism
  Thread, Data, Streaming Dataflow
  Overlap compute and communicate
Must manage some pieces pretty explicitly

## Slide 64: Admin
Feedback
Reading for Wednesday on web
HW6
  Due on Friday
My office hours today cancelled