## Slide 1: ESE5320: System-on-a-Chip Architecture
Day 17: Oct. 31, 2022
LZW, Associative Maps

## Slide 2: Today
LZW Compression (Part 1)
Associative Memory (Part 2)
  Custom
  FPGA
Software Maps
  Tree (Part 3)

## Slide 3: Message
Can adaptively compress data using recurring substrings
Rich design space for Maps

## Slide 4: Part 1: LZW Compression Lempel-Ziv-Welch

## Slide 5: Idea
Use data already sent as the dictionary
  Give short names to things in dictionary
  Don’t need to pre-arrange dictionary
  Adapt to common phrases/idioms in a particular document
Day 16 Reminder

## Slide 6: Encoding
Greedy simplification
  Encode by successively selecting the longest match between the head of the remaining string to send and the current window
Day 16 Reminder

## Slide 7: Algorithm Concept
While data to send
  Find largest match in window of data sent
  If length too small (length=1)
    Send character
  Else
    Send <x,y> = <match-pos,length>
    (actually, send dictionary entry)
  Add data encoded into sent window
  Expand dictionary
Day 16 Reminder

## Slide 8: Day 16: Preclass 7
How many comparisons per invocation?

## Slide 9: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
Only check position 0 for “starts with I”

## Slide 10: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
T-dictionary:
  Tap, The, Their, Then, There, Tuesday

## Slide 11: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
T-dictionary:
  Tap, The, Their, Then, There, Tuesday
If prefix same, why check redundantly?
  Generalize: Store things with common prefix together
    Share prefix among substrings
  Represent all strings as prefix tree

## Slide 12: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
If prefix same, why check redundantly?
  Store things with common prefix together
  Share prefix among substrings
  Represent all strings as prefix tree
Follow prefix trees with fixed work per input character

## Slide 13: Tree Algorithm
Tree Root for each character
Follow tree according to input until no more match
Send <name of last tree node>
  Dictionary entry
    Named sequentially by insertion
Extend tree (dictionary) with new character
Start over with this character

## Slide 14: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 

## Slide 15: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc

## Slide 16: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A

## Slide 17: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M

## Slide 18: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc

## Slide 19: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S

## Slide 20: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A

## Slide 21: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 

## Slide 22: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM | 262 | 258<-spc

## Slide 23: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> |  |  | 

## Slide 24: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S | 263 | 260<-A

## Slide 25: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S | 263 | 260<-A
M | <nothing> |  |  | 

## Slide 26: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S | 263 | 260<-A
M | <nothing> |  |  | 
 | <nothing> |  |  | 

## Slide 27: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S | 263 | 260<-A
M | <nothing> |  |  | 
 | <nothing> |  |  | 
I | 262 | AM spc | 264 | 262<-I

## Slide 28: Tree Example
I AM SAM SAM I AM
65
258
262
A
M
spc
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | 2A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S | 263 | 260<-A
M | <nothing> |  |  | 
 | <nothing> |  |  | 
S | 262 | AM spc | 264 | 262<-I

## Slide 29: Large Memory Implementation
int encode[SIZE][256];
Name tree node by insertion order
c is a character
Encode[x][c] holds the next tree node that extends tree node x by symbol c
  Or NONE if there is no such tree node

## Slide 30: Memory Tree Algorithm
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict[i]= symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
x=input[curr];
while(encode[x][input[curr]]!=NONE)
x=encode[x][input[curr]]; curr++;
send x
tree[nextdict].parent=x;
tree[nextdict].sym=input[curr];
encode[x][input[curr]]=nextdict++;

## Slide 31: Memory Tree Algorithm
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict[i]= symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
x=input[curr];
while(encode[x][input[curr]]!=NONE)
x=encode[x][input[curr]]; curr++;
send x
tree[nextdict].parent=x;
tree[nextdict].sym=input[curr];
encode[x][input[curr]]=nextdict++;
Follow
Tree

## Slide 32: Memory Tree Algorithm
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict[i]= symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
x=input[curr];
while(encode[x][input[curr]]!=NONE)
x=encode[x][input[curr]]; curr++;
send x
tree[nextdict].parent=x;
tree[nextdict].sym=input[curr];
encode[x][input[curr]]=nextdict++;
65
258
262
A
M
spc

## Slide 33: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S | 263 | 260<-A
M | <nothing> |  |  | 
 | <nothing> |  |  | 
I | 262 | AM spc | 264 | 262<-I

## Slide 34: Memory Tree Algorithm
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict[i]= symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
x=input[curr];
while(encode[x][input[curr]]!=NONE)
x=encode[x][input[curr]]; curr++;
send x
tree[nextdict].parent=x;
tree[nextdict].sym=input[curr];
encode[x][input[curr]]=nextdict++;
How much work per
character to encode?
Hint:
always go thru tree loop at least once

## Slide 35: Map
In Part 3 will talk about higher-level maps
Version of encode/decode in
  Geeks-for-Geeks description
  Decoder we provide
Based on Maps of strings
  Simpler to state
  Likely not O(1) per symbol
  More expensive implementation in hardware
    Version here better for simple hardware

## Slide 36: Algorithm with Map
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict initialized symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
x=String(input[curr]);
while(dict.lookup(x+input[curr])!=NONE)
x=x+input[curr]; curr++;
send dic.lookup(x);
dict.insert(x+input[curr],nextdict++);

## Slide 37: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I spc
A | 32 | spc | 257 | spc A
M | 65 | A | 258 | AM
 | 77 | M | 259 | M spc
S | 32 | spc | 260 | spc S
A | 83 | S | 261 | SA
M | <nothing> |  |  | 
 | 258 | AM | 262 | AM spc
S | <nothing> |  |  | 
A | 260 | spc S | 263 | spc SA
M | <nothing> |  |  | 
 | <nothing> |  |  | 
I | 262 | AM spc | 264 | AM spc I

## Slide 38: Compact Memory
int encode[SIZE][256];
How many entries in this table are not NONE?
  Hint: SIZE is total number of positions. How many characters process? Maximum number of insertions per character processed?

## Slide 39: Compact Memory
int encode[SIZE][256];
Table is very sparse
If store as associative memory
  At most SIZE entries
Look at how to implement associative memories next

## Slide 40: LZW So Far – 4KB chunks
Brute Force
  Needs one byte per byte = 4KB = 1 BRAM
  DICT_SIZE=4096 comparisons per byte
Dense memory encode[SIZE][256]
  12b key (1.5B)
  Need 1.5*4096*256= 384*4KB = 384 BRAMs
  1 comparison and lookup per byte
  (maybe should be SIZE+256)

## Slide 41: Complexity
Reminder from Day 15
  Optimized implementations tend to be more complex
  Seeing examples of that today…

## Slide 42: Associative Memories
Part 2

## Slide 43: Associative Memory
Maps from a key to a value
Key not necessarily dense
  Contrast simple RAM
  Cannot afford 2256 word memory
Day 16 Review

## Slide 44: Associative Memories
Use for deduplication
Also may use in LZW to reduce BRAMs
  Just saw
    Problem: Simple 2D tree table requires too many BRAMs
    Opportunity: Tree table sparse

## Slide 45: Deduplicate
Compute chunk hash
Use chunk hash to lookup known chunks
  Data already have on disk
  Data already sent to destination, so destination will know
If lookup yields a chunk with same hash
  Check if actually equal (maybe)
If chunks equal
  Send (or save) pointer to existing chunk
Day 16 Review

## Slide 46: Deduplication Architecture
Day 16 Review

## Slide 47: Custom Hardware Associative Memory

## Slide 48: Memory Block Review
Match on address
Select wordline for a row
Reads out a word
Address dense and hardwired
One row for each 2Abits values
width
depth

## Slide 49: Address Blocks
Each address match is AND
width
depth
/A2&/A1&/A0
/A2&/A1&A0

## Slide 50: Address Blocks

## Slide 51: Memory Block Associative
Want address as key
Word is value
Key sparse
Rows<2keybits
Entries<2keybits
Key programmable
width
depth

## Slide 52: Programmable Key
Make row select programmable

## Slide 53: Contrast Assoc. and Dense Memory

## Slide 54: Associative Memory Bank

## Slide 55: Programmable Key
Assoc: 5b key, 8 entries, 8b value
How many memory bits?
Direct: 8 entries, 8b value
How many memory bits?

## Slide 56: Associative Memory Bank
Memory cells = entries*(keybits+valuebits)

## Slide 57: Associative Memory Bank
Will need to be able to write into key
  Another “fixed” decoder to generate key-word line for programming

## Slide 58: Associate Memory Cost
More expensive than equal capacity SRAM memory bank
  Memory cells in decoder
  Need to support write into key

## Slide 59: Associate Memory Cost
Physical associative memory for 4KB LZW Chunk tree encode
  4K entries
  12b (pos) output
  12b (pos)+8b (char)=20b key
Memory cells assoc.?
Compare direct 4Kx12 memory (cells)?
  How much larger is assoc. for same capacity?
Compare 4096*256 with 12b result for dense LZW case (cells)?
  How much larger to solve same problem

## Slide 60: FPGA
Has BRAMs – normal memories, not associative
36Kb BRAM
  512x72
Can be 9b key  72b value assoc.
  Just using the memory sparsely
Or interpret as programmable decoder with 72 match lines

## Slide 61: Assoc. Mem from BRAM
For wider match
Cover 9b of key with each BRAM
Use 72 output bits to indicate if one of 72 entries match
AND together corresponding entries
Get 72 match bits
Re-encode match bits to lookup value

## Slide 62: BRAM Associative Memory
Previous slide expands match width
How would we expand capacity?
  Hint: how get a wider word (144b word)?

## Slide 63: BRAM Associative Memory

## Slide 64: Associative Memory Cost
Match unit
  Requires 1 BRAM per 9b of key per 72 entries
  ✖️
  Asymptotically optimal (keylen*entries)
    But large constants
  LZW
    4K entries
    20b key
    How many BRAMs for match?

## Slide 65: 4K LZW Chunk Search: Fully associative
Match BRAMs:
  Match key: 20b
  Entries: 4096
Value BRAMS:
  12b (state [position])
  12b x 4096 entries
  Takes 2 BRAMs

## Slide 66: Example Stored Values
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC

## Slide 67: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 68: Code Snippet
ap_uint<72> key_low[512];
ap_uint<72> key_high[512];
int value[72];
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
res=value[addr];

## Slide 69: How Lookup Work?
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC
Lookup 0x214 = 0x001 0x014

## Slide 70: Code Snippet
ap_uint<72> key_low[512];
ap_uint<712> key_high[512];
int value[72];
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
res=value[addr];

## Slide 71: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
What match_low, match_high?

## Slide 72: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
What match?

## Slide 73: What does binary_encode do?
binary_encode(0000000…010000)=0x40
10000…0  71
0000…01  0
0000…010  1
for (i=0<i<72;i++)
  If (bit[i]==1) return i
Return(MISS); // if not find (i.e., all 0’s)
Technicalities – maybe check only one 1

## Slide 74: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
What addr?

## Slide 75: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM
res=value[addr];
What res?

## Slide 76: How Lookup Work?
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC
Lookup 0x214 = 0x001 0x014

## Slide 77: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 78: Add another entry
How BRAM contents change to add this entry
for 0x19001
match | Key[17:9] | Key[8:0] | Value
0 | 0x001 | 0x014 | 0x01
1 | 0x001 | 0x01 | 0x34
2 | 0x0F0 | 0x014 | 0xE3
3 | 0x0C8 | 0x113 | 0xCC
4 | 0x0C8 | 0x01 | 0x2B

## Slide 79: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 80: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 0x2B
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 81: 4K Chunk LZW Search
 | BRAMs | Operations
Brute Search | 1 | 4K
Tree with Dense RAM | 384 | 1
Tree with Full Assoc | 173 | 1
36Kb BRAMs on ZU3EG = 216

## Slide 82: Checkpoint
Notice levels of mapping:
  Prefix Tree algorithm
  Formulated on a 2D memory
  Then implemented in assoc. memory
    (later with Tree … hash table)

## Slide 83: Lecture Ended Here

## Slide 84: Software Map
Part 3

## Slide 85: Software Map
Map abstraction
  void insert(key,value);
  value lookup(key);
Will typically have many different implementations

## Slide 86: Preclass 1
For a capacity of 4096
How many memory accesses needed
  When lookup fail?
  When lookup succeed (on average)?

## Slide 87: Tree Map (Preclass 2)
Build search tree
Walk down tree
For a capacity of 4096, assume balanced…
How many tree nodes visited
  When lookup fail?
  When lookup succeed (on average)?

## Slide 88: Tree Map LZW
Each character requires log2(dict) lookups
  12 for 4096
Each internal tree node hold
  Key (20b for LZW), value (12b), and 2 pointers (12b)
  7B
Total nodes 4K*2
Need 14 BRAMs for 4K chunk

## Slide 89: Tree Insert
Need to maintain balance
Doable with O(log(N)) insert
  Tricky
  See Red-Black Tree
    https://en.wikipedia.org/wiki/Red–black_tree
    https://www.geeksforgeeks.org/red-black-tree-set-1-introduction-2/

## Slide 90: 4K Chunk LZW Search
 | BRAMs | Operations
Brute Search | 1 | 4K
Tree with Dense RAM | 384 | 1
Tree with Full Assoc | 173 | 1
Tree with Tree | 14 | 12
36Kb BRAMs on ZU3EG = 216

## Slide 91: Big Ideas
Can adaptively compress data using recurring substrings
  With constant work for symbol
Rich design space for engineering associative map solutions

## Slide 92: Admin
Feedback (including HW7)
Reading for Wednesday on Web
First project milestone due Friday
  Including teaming