## Slide 1: ESE5320: System-on-a-Chip Architecture
Day 10: October 4, 2023
Coding HLS for Accelerators

## Slide 2: Previously
We can describe computational operations in C
    Primitive operations (add, sub, multiply, and, or)
    Dataflow graphs primitives
    To bit level
    Conditionals and loops
    Function abstraction
    Loops, Arrays

## Slide 3: Today
Arrays and Memory Sequentialization – Part 1
Controlling Parallelism in Vitis HLS C – Part 2
Controlling Memories in Vitis HLS C – Part 3
Time permitting – Part 4
  malloc, pointers
Supplement – Part 5
  more dependencies

## Slide 4: Message
Can specify HW computation in C
Vitis HLS gives control over how design mapped (area-time, streaming…)
Code may need some care and stylization to feed data efficiently
Read UG 1393 – Profiling, Optimizing, and Debugging > Optimizing C++ Kernels

## Slide 5: Three Perspectives
How express spatial/hardware computations in C
  May want to avoid some constructs in C
How express computations
  Hopefully, equally accessible to spatial and sequential implementations
Given C code: how could we implement in spatial hardware
  Some corner cases and technicalities make tricky
Day 9

## Slide 6: Arrays and Memories

## Slide 7: Loop Interpretations
What does a loop describe?
  Sequential behavior [when execute]
  Spatial construction [when create HW]
  Data Parallelism [sameness of compute]
We will want to use for all 3
C allows expressive loops
  Some expressiveness
    Not compatible with spatial hardware construction

## Slide 8: Arrays as Memory Banks
If single memory has only one port
  Can perform only one memory operation per cycle
  What II if a, b, c all in bigmem?
for (i=0;i<1024;i++)
  c[i]=a[i]*b[i];

## Slide 9: Arrays as Memory Banks
Hardware expression: Sometimes we will want to describe computations with separate memory banks
int a[1024], b[1024], c[1024];
for(i=0;i<1024;i++)
  a[i]=bigmem[offset+i];
for (i=0;i<1024;i++)
  c[i]=a[i]*b[i];

## Slide 10: Physical Memory Port as Limited Shared Resource
Typically single memory port
  Must sequentialize on use of memory port
  Reason for memory banking
    Put in separate memories, so operations can occur simultaneously
Ultra96 DRAM 1 port
Virtex BRAM 2 ports

## Slide 11: Arrays as things to put in Memory Banks
Computational expression:
  sometimes it is useful to express computation
  then decide how to pack array state into memory banks for different
    Hardware availability
    Area-Time tradeoffs

## Slide 12: Arrays as Local Memory
Hardware/Computational expression: natural way of describing local state
hist(int a[SIZE], out[EVENTS]) {
int local[EVENTS];
for(i=0;i<EVENTS;i++)
local[i]=0;
for(i=0;i<SIZE;i++)
local[a[i]]++;
for(i=0;i<EVENTS;i++)
out[i]=local[i];
}

## Slide 13: Arrays as Inputs and Outputs
Computational Expression: arrays are often a natural way of expressing set of inputs and outputs
int c=12;
while(true)
  {
  int aval=astream.read();
  int bval=bstream.read();
  int res=aval*bval+c;
  resstream.write(res);
    }
void op(int a[BLOCK], int b[BLOCK], int out[BLOCK]) {
for (i=0;i<BLOCK;i++)
  {
  out[i]=a[i]*b[i]+c;
    }
  }

## Slide 14: Array Interpretations
What does an array describe?
  Compact expression [write less code]
  Memory banks [where place data]
    Things put in separate memory banks
  Local memory [not need to be shared]
  I/O [source and sink of data]
We will want to use for all 4
C allows expressive use of arrays/memories
  Some expressiveness will inhibit efficient hardware

## Slide 15: C Memory Model
One big linear address space of locations
Most recent definition to location is value
Sequential flow of statements
000
001
002
005
006
007
008
009
010
011
004
Addr
New value
Current value

## Slide 16: Challenge: C Memory Model
One big linear address space of locations
Assumes all arrays live in same memory
Assumes arrays may overlap?
000
001
002
005
006
007
008
009
010
011
004
Addr
New value
Current value

## Slide 17: C Memory/Pointer Sequentialization
Must preserve ordering of memory operations
  A read cannot be moved before write to memory which may redefine the location of the read
    Conservative: any write to memory
    Sophisticated analysis may allow us to prove independence of read and write
  Writes which may redefine the same location cannot be reordered

## Slide 18: C Memory/Pointer Sequentialization
Must preserve ordering of memory operations
  A read cannot be moved before write to memory which may redefine the location of the read
  Writes which may redefine the same location cannot be reordered
Challenge for single array
  Does A[B[i]] refer to same location as A[C[i]]?
  So expression issue broader than C

## Slide 19: C Memory/Pointer Sequentialization
Must preserve ordering of memory operations
Challenge for single array:
  Does A[B[i]] refer to same location as A[C[i]]?
Challenge multiple arrays:
  Out-of-bounds reference for one array reference another?
  void fun(int a[100], int b[100], int c[100])
    { for (int i=0;i<100;i++) c[i]=a[b[i]]; }
  What if called: fun(a,perm,a);

## Slide 20: Consequence
Expressions and operations through variables (whose address is never taken) can be executed at any time
  Just preserve the dataflow
Memory assignments must execute in strict order
  Ideally: partial order
  Conservatively: strict sequential order of C

## Slide 21: More at end of lecture
More on Sequentialization and Dependencies
  Slides there to review
  Won’t cover

## Slide 22: Vivado HLS Mapping Control: Compute Parallelism Loops, Dataflow
Part 2

## Slide 23: Terminology Warning
Course talk about “Pipelining” generally
  Same concept apply at gate level and at operator thread level
In this section, need to talk about both
  …and how they compose
  So, need to be clear about when “thread pipelining” and when “gate”/”instruction” pipelining
Vitis
  Calls one pipelining (gate/instruction)
  And other Dataflow (operation thread)
To further complicate things
  The operation/thread is going to come out of functions and loops (not things explicitly written as threads)

## Slide 24: Dataflow Graph
What dataflow graph does this describe?
  Assume FA, FB, FC are f(in,cout);

## Slide 25: Define: Pragma
Pragma – directive to compiler
  Usually compiler specific
    So ignored by compilers that don’t support (where not relevant)
    Gives compiler hints/direction on how to compile
    Should not change meaning of computation
      Should compute the same thing
      …but may compute differently
Use Pragmas to direct Vitis HLS on how to compile our code for FPGA

## Slide 26: Vivado HLS Pragma DATAFLOW
Enables streaming data between functions and loops
  Don’t have to wait for entire array to be produced to move data and start downstream computation
Allows concurrent streaming execution
Requires data be produced/consumed sequentially
  i.e. can connect with FIFO; not need reorder

## Slide 27: Dataflow with Arrays

## Slide 28: Streamable
When process input and output in order

## Slide 29: Cannot Stream Input
Why?
void fB (int in[100], int out[100])
{
for (int=0; i<100;i++)
out[i]=in[100-i];
}

## Slide 30: Streamable?
Can stream input?
Can stream output?
void fC (int in[100], int out[100])
{
for (int=0; i<100;i++)
out[i]=0;
for (int=0; i<100;i++)
out[in[i]%100]++;
}

## Slide 31: Vitis HLS Pragma DATAFLOW
Enables streaming data between functions and loops
Allows concurrent streaming execution
Requires data be produced/consumed sequentially
  i.e. can connect with FIFO; not need reorder
Useful to use stream data type between functions – communicates sequence
  hls::stream<TYPE>

## Slide 32: Streaming Operations
Functions can have stream inputs and outputs
  Must pass as pointers
  hls::stream<Type> &strm
Vitis HLS expressiveness to define hardware streaming operation pipelines

## Slide 34: stream_filter Pipeline

## Slide 35: Dataflow Streaming
Works between loops, as well

## Slide 36: Between Loops

## Slide 37: Vivado HLS Pragma PIPELINE
Direct a function or loop to be pipelined
Ideally start one loop or function body per cycle
  Can control II

## Slide 38
for (i=0;i<N;i++)
yout=0;
for (j=0;j<K;j++)
#pragma HLS PIPELINE
yout+=in[i+j]*w[j];
y[i]=yout;
Which solution
from preclass 3?

## Slide 39: Dataflow and pipelining
Dataflow allows coarse-grained pipelining among loops and functions
Pipeline causes loop bodies to be pipelined

## Slide 40: Dataflow and Pipelining
Cycles for top loop unpipelined?

## Slide 41: Dataflow and Pipelining
Cycles for top loop pipelined?

## Slide 42: Dataflow and Pipelining
Cycles for bottom loop unpipelined?

## Slide 43: Dataflow and Pipelining
Cycles for bottom loop pipelined?

## Slide 44: Dataflow and Pipelining
Composite time, no dataflow, no pipelining?

## Slide 45: Dataflow and Pipelining
Composite time dataflow only?

## Slide 46: Dataflow and Pipelining
Dataflow only?

## Slide 47: Dataflow and Pipelining
Composite time pipelining only?

## Slide 48: Dataflow and Pipelining
Composite time dataflow and pipelining?

## Slide 49: Compare Cases
Unpipe
Pipe
Dataflow
Dataflow
No Dataflow

## Slide 50: Compare Cases
Unpipe
Pipe
Dataflow
Dataflow
No Dataflow

## Slide 51: Unroll
Vivado HLS has pragmas for unrolling
UG902: Vivado Design Suite HLS User’s Guide
  P139—142 (2020.1, 2018.3)
#pragma HLS UNROLL factor=…
Use to control area-time points
  Use of loop for spatial vs. temporal description
https://www.xilinx.com/support/documentation/sw_manuals/xilinx2018_3/ug902-vivado-high-level-synthesis.pdf
https://docs.xilinx.com/v/u/en-US/ug902-vivado-high-level-synthesis

## Slide 52: Vivado HLS Pragma UNROLL
Unroll loop into spatial hardware
  Can control level of unrolling
Any loops inside a pipelined loop gets unrolled by the PIPELINE directive

## Slide 53
for (i=0;i<N;i++)
yout=0;
for (j=0;j<K;j++)
#pragma HLS UNROLL
yout+=in[i+j]*w[j];
y[i]=yout;

## Slide 54: With Pipelining
//Pipeline implies unroll of loop
for (i=0;i<N;i++)
yout=0;
#pragma HLS PIPELINE
for (j=0;j<K;j++)
yout+=in[i+j]*w[j];
y[i]=yout;
Which solution
from preclass 3?

## Slide 55: Dataflow, Unrolling, & Pipelining
Cycles unroll K-loop, dataflow, pipeline?

## Slide 56: Vivado HLS Pragma INLINE
Collapse function body into caller
  Eliminates interface code
  Allows optimization of inline code
Recursive option to inline a hierarchy
  Maybe useful when explore granularity of accelerator

## Slide 57: Midterm (10/11 – next Wed.)
Analysis
  Bottleneck
  Amdhal’s Law Speedup
  Computational requirements
  Resource Bounds
  Critical Path
  Latency/throughput/II
Will be calculating/estimating runtimes
From Code
Forms of Parallelism
Dataflow, SIMD, hardware pipeline, threads
Hardware (spatial) mapping
Pipelining/Retiming
Map/schedule task graph to (multiple) target substrates
Memory assignment and movement
Area-time points

## Slide 58: Midterm
In-class exam
Closed book, notes, etc.
Calculators allowed (encouraged)
Read midterm details posted on web
Last seven midterms, finals online
  Both without answers (for practice)
  …and with answers (check yourself)
  Check syllabus for previous terms
  (but note 2020 year online, open-book)
Midterm was earlier last few years

## Slide 59: Vivado HLS Mapping Control: Memories
Part 3

## Slide 60: Zynq BRAM
36Kb of memory
  Configurable width up to 72b
    512x72 or … 32Kx1
  Dual port
Can be operated as 2x18Kb memory banks
  Configurable width up to 36b
    512x36 or … 16Kx1
  Each memory dual port
Xilinx UG573, UltraScale Architecture Memory Resources User Guide

## Slide 61: Vivado HLS Pragma ARRAY_PARTITION
Spread out array over multiple BRAMs
  By default placed in single BRAM
    At most 2 ports
  Use to remove memory bottleneck that prevents pipelining (limits II)

## Slide 62: Memory Bottleneck Example
902 example p. 91-92
Xilinx UG1197 (2017.1) p. 50
What problem if put mem
in single BRAM?

## Slide 63: Array Partition
Xilinx UG902 p. 195 (145 in 2017.1 version)

## Slide 64: Array Partition Example
#pragma ARRAY_PARTITION variable=mem cylic factor=4
Xilinx UG902 p. 91

## Slide 65: Vivado HLS Pragma ARRAY_RESHAPE
Pack data into BRAM to improve access (reduce BRAMs)
  May provide similar benefit to partitioning without using more BRAMs

## Slide 66
Xilinx UG902 (2017.1) p. 173

## Slide 67
902 example p. 91-92
Xilinx UG902 p. 91
How fix if dint_t is 16b?
BRAM can be configured
for 72b wide output

## Slide 68: Array Reshape Example
#pragma ARRAY_RESHAPE variable=mem cylic factor=4 dim=1
(if din_t 16b)
Xilinx UG902 p. 91

## Slide 69: Loop Interpretations
What does a loop describe?
  Sequential behavior [when execute]
  Spatial construction [when create HW]
  Data Parallelism [sameness of compute]
We will want to use for all 3
C allows expressive loops
  Some expressiveness
    Not compatible with spatial hardware construction

## Slide 70: HLS Pragma Summary
pragmas allow us to control hardware mapping
  How interpret loops (spatial hw vs. temporal)
  How arrays get mapped to memories
  How treat function calls
  Turn area-time knobs
Could have rewritten code by hand
  Unroll, separate arrays…
  Pragmas automate; we just need to provide instruction

## Slide 71: Memory Allocation Part 4
Simple answer: “Don’t do it!”
Skip to Wrapup

## Slide 72: Demand for malloc()
Data-dependent object (array) size
Data-dependent number of objects

## Slide 73: Hardware Memory
Typically small, fixed, local memory blocks
  E.g. 36Kb BRAMs
Reuse memory blocks
  Not allocate new blocks
  Cannot make data-dependent memory sized blocks
  Cannot hold arbitrary-sized data

## Slide 74: No malloc()
Generally don’t want to use malloc with
  Hardware Accelerated functions
  Real-time computations
Vivado HLS won’t let you use malloc()
  For C running on FPGA array
Instead: statically declare arrays of maximum size data may be

## Slide 75: Pointer Passing
Be careful…

## Slide 76: Pointer Passing
What does it mean to pass a pointer into a function?

## Slide 77: Pointer Passing Interpretations
Multiple uses we may want to express
  Specify which data to work on
    Ok to copy that data to private accelerator memory and work with it
    But, how much data to copy? (length)
  Want to mutate data and have other (parallel) tasks see it OR want to see data mutated by other (parallel tasks)
    Not OK to copy to private accelerator memory
    Force use from large, shared memory
    Forces sequentialization

## Slide 78: Pointer Passing
What if accelerator doesn’t have access to the memory holding the data pointed to by the pointer?

## Slide 79: Pointer Passing
What happens if we give accelerators access to common memory holding data for pointer, but
  There’s only one port into memory
  Memory is 10 cycles away
  And there are 100 accelerators that may need access
  Memory can only handle one memory op per cycle
Maybe only reading data that will not change.

## Slide 80: Avoid Pointer Passing
Tend to copy data into / move data among hardware accelerator memories rather than passing pointers.

## Slide 81: Memory Sequentialization and Data Dependencies Part 5
(unlikely to cover in class;
Review on own)
Skip to wrapup

## Slide 82: Example
Assume a, b live in same memory
Placed in sequence as shown
What happens when
  int a[16];
  int b[16];
  Read from a[17]
  Read from b[-2]
Can inhibit separation into memory banks, parallelism

## Slide 83: Memory Operation Challenge
Memory is just a set of location
But memory expressions in C can refer to variable locations
  Does A[i], B[j] refer to same location?
  A[f(i)], B[g(j)] ?
Can inhibit banking, parallelism
  Or add expensive interconnect

## Slide 84: C Memory Consequence
Expressions and operations through variables (whose address is never taken) can be executed at any time
  Just preserve the dataflow
Memory assignments must execute in strict order
  Ideally: partial order
  Conservatively: strict sequential order of C

## Slide 85: Forcing Sequencing
Demands we introduce some discipline for deciding when operations occur
  Could be a FSM
  Could be an explicit dataflow token
  Callahan (reading) uses control register
Other uses for timing control
  Control
  Variable delay blocks
  Looping

## Slide 86: Scheduled Memory Operations
Source: Callahan

## Slide 87: Hardware/Parallelism Challenge
Can we give enough information to the compiler to
  allow it to reorder?
  allow to put in separate embedded memories (separate banks)?
Is the compiler smart enough to exploit?

## Slide 88: Mux Conversion and Memory
What might go wrong if we mux-converted the following:
if (cond)
  a[i]=0;
else
  b[i]=0;

## Slide 89: Mux Conversion and Memory
What might go wrong if we mux-converted the following:
if (cond)
  a[i]=0;
else
  b[i]=0;
Don’t want memory operations in non-taken branch to occur.

## Slide 90: Mux Conversion and Memory
if (cond)
  a[i]=0;
else
  b[i]=0;
  Don’t want memory operations in non-taken branch to occur.
Conclude: cannot mux-convert blocks with memory operations (without additional care)

## Slide 91: Conditions and Memory
if (cond)
  a[i]=0;
else
  b[i]=0;

## Slide 92: Dependence in Loops
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-1];
If a value needed by one instance of the loop is written by another instance, can create cyclic dependence.
 limit parallelism (pipeline II)

## Slide 93: Dependence in Loops
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-1];
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-2];
Dependence distance same as
# registers in cycle.

## Slide 94: Dependence Fixed/Predictable?
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-1]+Y[i-2];
for(i=0;i<K;i++)
Y[i]=a[i]*Y[b[i]];
If dependence data-dependent, forced to sequentialize.

## Slide 95: Dependence Fixed/Predictable?
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-1]+Y[i-2];
for(i=0;i<K;i++)
Y[i]=a[i]*Y[2*i+3];
If dependence linear, aggressive compliers may be able to resolve.

## Slide 96: Dependence Fixed/Predictable?
for(i=0;i<K;i++)
Y[i]=
a[i]*Y[ceil(sqrt(i)*sin(2i))];
If dependence too complicated, compiler not solve and will force sequential execution.

## Slide 97: Big Ideas
Can specify HW computation in C
Create streaming operations
  Run on processor or FPGA
Vivado HLS gives control over how map to hardware
  Area-time point

## Slide 98: Admin
Feedback
Reading for Monday
  on web and Zynq book
HW5 due Friday
  Start early; require slow builds
Midterm on Wednesday