## Slide 1: ESE5320: System-on-a-Chip Architecture
Day 17: Oct. 30, 2023
LZW, Associative Maps

## Slide 2: Today
LZW Compression Setup (Part 1)
LZW Compression Algorithm (Part 2)
Associative Memory
  Custom (part 3)
  FPGA (Part 4, time permitting, probably not)

## Slide 3: Message
Can adaptively compress data using recurring substrings
Rich design space for Maps

## Slide 4: Part 1: LZW Compression Setup

## Slide 5: Preclass 1
I AM S<2,3><5,4><0,4>
Message?
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
I |  | A | M |  | S |  |  |  |  |  |  |  |  |  |  | 

## Slide 6: Preclass 2, 3
Bits in unencoded (decoded) message?
  Assume 8b char
Bits for encoded message?
  Assume 9b for character
    1 bit to say is a character, then 8b char
  And 9b for <x,y> pair
    1 bit char, 4b for each of x and y

## Slide 7: Idea
Use data already sent as the dictionary
  Give short names to things in dictionary
  Don’t need to pre-arrange dictionary
  Adapt to common phrases/idioms in a particular document

## Slide 8: Encoding
Greedy simplification
  Encode by successively selecting the longest match between the head of the remaining string to send and the current window

## Slide 9: Algorithm Concept
While data to send
  Find largest match in window of data sent
  If length too small (length=1)
    Send character
  Else
    Send <x,y> = <match-pos,length>
  Add data encoded into sent window

## Slide 10: Preclass 4
How many comparisons per invocation?

## Slide 11: Part 2: LZW Compression Lempel-Ziv-Welch

## Slide 12: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
Only check position 0 for “starts with I”

## Slide 13: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
T-dictionary:
  Tap, The, Their, Then, There, Tuesday

## Slide 14: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
T-dictionary:
  Tap, The, Their, Then, There, Tuesday
If prefix same, why check redundantly?
  Generalize: Store things with common prefix together
    Share prefix among substrings
  Represent all strings as prefix tree

## Slide 15: Idea
Avoid O(Dictionary-size) work
  Only need to match against positions that start with the character(s) in string to encode
    Separate dictionary for each?
If prefix same, why check redundantly?
  Store things with common prefix together
  Share prefix among substrings
  Represent all strings as prefix tree
Follow prefix trees with fixed work per input character

## Slide 16: Tree Algorithm (preclass 5)
Tree Root for each character
Follow tree according to input until no more match
Send <name of last tree node>
  Dictionary entry
    Named sequentially by insertion
Extend tree (dictionary) with new character
Start over with this character

## Slide 17: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 

## Slide 18: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | ??? | I | ??? | ???

## Slide 19: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
256
I
<spc>

## Slide 20: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | ??? | spc | ??? | ???
256
I
<spc>

## Slide 21: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
256
I
<spc>
257
<spc>
A

## Slide 22: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | ?? | A | ??? | ???
256
I
<spc>
257
<spc>
A

## Slide 23: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
256
I
<spc>
257
<spc>
A
258
A
M

## Slide 24: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | ??? | M | ??? | ???
256
I
<spc>
257
<spc>
A
258
A
M

## Slide 25: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
256
I
<spc>
257
<spc>
A
258
A
M
259
M
<spc>

## Slide 26: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | ??? | spc | ??? | ???
256
I
<spc>
257
<spc>
A
258
A
M
260
M
<spc>

## Slide 27: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S

## Slide 28: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | ??? | S | ??? | ???
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S

## Slide 29: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S
261
S
A

## Slide 30: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | ??? (different) | A | ??? | ???
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S
261
S
A

## Slide 31: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S
261
S
A

## Slide 32: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | ??? | AM | ??? | ???
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S
261
S
A

## Slide 33: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
256
I
<spc>
258
A
M
259
M
<spc>
257
<spc>
A
260
S
261
S
A

## Slide 34: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
256
I
<spc>
259
M
<spc>
257
<spc>
A
260
S
261
S
A
258
A
M
262
<spc>

## Slide 35: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
S | ??? | spc | ??? | ???
256
I
<spc>
259
M
<spc>
257
<spc>
A
260
S
261
S
A
258
A
M
262
<spc>

## Slide 36: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> | spc |  | 
256
I
<spc>
259
M
<spc>
257
<spc>
A
260
S
261
S
A
258
A
M
262
<spc>

## Slide 37: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> | spc |  | 
A | ??? | spc S | ??? | ???
256
I
<spc>
259
M
<spc>
257
<spc>
A
260
S
261
S
A
258
A
M
262
<spc>

## Slide 38: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> | spc |  | 
A | 260 | spc S | 263 | 260<-A
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 39: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> | spc |  | 
A | 260 | spc S | 263 | 260<-A
M | ??? | A | ??? | ???
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 40: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> | spc |  | 
A | 260 | spc S | 263 | 260<-A
M | <nothing> | A |  | 
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 41: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> | spc |  | 
A | 260 | spc S | 263 | 260<-A
M | <nothing> | A |  | 
 | ??? | AM | ??? | ???
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 42: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> | A |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> | spc |  | 
A | 260 | spc S | 263 | 260<-A
M | <nothing> | A |  | 
 | <nothing> | AM |  | 
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 43: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S | 263 | 260<-A
M | <nothing> | A |  | 
 | <nothing> | AM |  | 
I | ??? | AM spc | ??? | ???
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 44: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S | 263 | 260<-A
M | <nothing> | A |  | 
 | <nothing> | AM |  | 
I | 262 | AM spc | 264 | 262<-I
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A

## Slide 45: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S | 263 | 260<-A
M | <nothing> | A |  | 
 | <nothing> | AM |  | 
I | 262 | AM spc | 264 | 262<-I
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A
264
I

## Slide 46: Large Memory Implementation
int encode[SIZE][256];
Name tree node by insertion order
c is a character
Encode[x][c] holds the next tree node that extends tree node x by symbol c
  Or NONE if there is no such tree node

## Slide 47: Memory Tree Algorithm
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict[i]= symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
while(encode[x][input[curr]]!=NONE)
x=encode[x][input[curr]]; curr++;
send x
tree[nextdict].parent=x;
tree[nextdict].sym=input[curr];
encode[x][input[curr]]=nextdict++;
x=input[curr]; curr++;

## Slide 48: Memory Tree Algorithm
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict[i]= symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
while(encode[x][input[curr]]!=NONE)
x=encode[x][input[curr]]; curr++;
send x
tree[nextdict].parent=x;
tree[nextdict].sym=input[curr];
encode[x][input[curr]]=nextdict++;
x=input[curr]; curr++;
Follow
Tree

## Slide 49: Memory Tree Algorithm
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict[i]= symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
while(encode[x][input[curr]]!=NONE)
x=encode[x][input[curr]]; curr++;
send x
tree[nextdict].parent=x;
tree[nextdict].sym=input[curr];
encode[x][input[curr]]=nextdict++;
x=input[curr]; curr++;
258
A
M
262
264
I
<spc>

## Slide 50: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S | 263 | 260<-A
M | <nothing> | A |  | 
 | <nothing> | AM |  | 
I | 262 | AM spc | 264 | 262<-I
256
I
<spc>
259
M
<spc>
261
S
A
<spc>
257
<spc>
A
260
S
263
A
258
A
M
262
264
I

## Slide 51: Memory Tree Algorithm
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict[i]= symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
while(encode[x][input[curr]]!=NONE)
x=encode[x][input[curr]]; curr++;
send x
tree[nextdict].parent=x;
tree[nextdict].sym=input[curr];
encode[x][input[curr]]=nextdict++;
x=input[curr]; curr++;
How much work per
character to encode?
Hint: between curr++
executions?

## Slide 52: Map
Later today or Wednesday will talk about higher-level maps
Version of encode/decode in
  Geeks-for-Geeks description
  Decoder we provide
Based on Maps of strings
  Simpler to state
  Likely not O(1) per symbol
  More expensive implementation in hardware
    Version here better for hardware (keeps simple)

## Slide 53: Algorithm with Map
curr=0; // pointer into input chunk
nextdict=NUM_SYMBOLS;
// dict initialized symbol i for i<NUM_SYMBOLS
while (curr<chunk_size)
while(dict.lookup(x+input[curr])!=NONE)
x=x+input[curr]; curr++;
send dic.lookup(x);
dict.insert(x+input[curr],nextdict++);
x=String(input[curr]); curr++;

## Slide 54: I AM SAM SAM I AM
Input | Send | Dict | Add Entry | Add What
I | <nothing> |  |  | 
 | 73 | I | 256 | I<-spc
A | 32 | spc | 257 | spc<-A
M | 65 | A | 258 | A<-M
 | 77 | M | 259 | M<-spc
S | 32 | spc | 260 | spc<-S
A | 83 | S | 261 | S<-A
M | <nothing> |  |  | 
 | 258 | AM | 262 | 258<-spc
S | <nothing> |  |  | 
A | 260 | spc S | 263 | 260<-A
M | <nothing> | A |  | 
 | <nothing> | AM |  | 
I | 262 | AM spc | 264 | 262<-I
256
I
<spc>
259
M
<spc>
261
S
A
258
A
M
262
<spc>
257
<spc>
A
260
S
263
A
264
I

## Slide 55: Compact Memory
int encode[SIZE][256];
How many entries in this table are not NONE?
  Maximum number of times execute:
  encode[x][input[curr]]=nextdict++;
  Maximum number of entries added to encode?
  Maximum number of NONE entries in encode?

## Slide 56: Compact Memory
int encode[SIZE][256];
Table is very sparse
If store as associative memory
  At most SIZE entries
    (SIZE+256 with first 256 entries for each byte value)
Look at how to implement associative memories next

## Slide 57: LZW So Far – 4KB chunks
Brute Force
  Needs one byte per byte = 4KB = 1 BRAM
  DICT_SIZE=4096 comparisons per byte
Dense memory encode[SIZE][256]
  12b node id (1.5B)
  Need 1.5*4096*256= 384*4KB = 384 BRAMs
  1 comparison and lookup per byte
  (maybe should be SIZE+256)

## Slide 58: 4K Chunk LZW Search
 | BRAMs | Operations/byte
Brute Search | 1 | 4K
Tree with Dense RAM | 384 | 1
36Kb BRAMs on ZU3EG = 216

## Slide 59: Complexity
Reminder from Day 15
  Optimized implementations tend to be more complex
  Large problems may force more complexity
    (e.g. Large window, deal with limited BRAMs on chip)
  Seeing examples of that today…

## Slide 60: Associative Memories
Part 3

## Slide 61: Associative Memory
Maps from a key to a value
Key not necessarily dense
  Contrast simple RAM
  Cannot afford 2256 word memory
Day 16 Review

## Slide 62: Associative Memories
Use for deduplication
Also may use in LZW to reduce BRAMs
  Just saw
    Problem: Simple 2D tree table requires too many BRAMs
    Opportunity: Tree table sparse

## Slide 63: Custom Hardware Associative Memory

## Slide 64: Memory Block Review
Match on address
Select wordline for a row
Reads out a word
Address dense and hardwired
One row for each 2Abits values
width
depth

## Slide 65: Address Blocks
Each address match is AND
width
depth
/A2&/A1&/A0
/A2&/A1&A0

## Slide 66: Address Blocks

## Slide 67: Memory Block Associative
Want address as key
Word is value
Key sparse
Rows<2keybits
Entries<2keybits
Key programmable
width
depth

## Slide 68: Programmable Key
Make row select programmable

## Slide 69: Contrast Assoc. and Dense Memory

## Slide 70: Associative Memory Bank

## Slide 71: Programmable Key
Assoc: 5b key, 8 entries, 8b value
How many memory bits?
Direct: 8 entries, 8b value
How many memory bits?

## Slide 72: Associative Memory Bank
Memory cells = entries*(keybits+valuebits)

## Slide 73: Associative Memory Bank
Will need to be able to write into key
  Another “fixed” decoder to generate key-word line for programming

## Slide 74: Associate Memory Cost
More expensive than equal capacity SRAM memory bank
  Memory cells in decoder
  Need to support write into key

## Slide 75: Associate Memory Cost
Physical associative memory for 4KB LZW Chunk tree encode
  4K entries
  12b (pos) output
  12b (pos)+8b (char)=20b key
Memory cells assoc.?
Compare direct 4Kx12 memory (cells)?
  How much larger is assoc. for same capacity?
Compare 4096*256 with 12b result for dense LZW case (cells)?
  How much larger to solve same problem

## Slide 76: Associative Memories FPGA
Part 4
(probably for Day 18)
Skip wrapup

## Slide 77: FPGA
Has BRAMs – normal memories, not associative
36Kb BRAM
  512x72
Can be 9b key  72b value assoc.
  Just using the memory sparsely
Or interpret as programmable decoder with 72 match lines

## Slide 78: Assoc. Mem from BRAM
For wider match
Cover 9b of key with each BRAM
Use 72 output bits to indicate if one of 72 entries match
AND together corresponding entries
Get 72 match bits
Re-encode match bits to lookup value

## Slide 79: BRAM Associative Memory
Previous slide expands match width
How would we expand capacity?
  Hint: how get a wider word (144b word)?

## Slide 80: BRAM Associative Memory

## Slide 81: Associative Memory Cost
Match unit
  Requires 1 BRAM per 9b of key per 72 entries
  ✖️
  Asymptotically optimal (keylen*entries)
    But large constants
  LZW
    4K entries
    20b key
    How many BRAMs for match?

## Slide 82: 4K LZW Chunk Search: Fully associative
Match BRAMs:
  Match key: 20b
  Entries: 4096
Value BRAMS:
  12b (state [position])
  12b x 4096 entries
  Takes 2 BRAMs

## Slide 83: Example Stored Values
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC

## Slide 84: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 85: Code Snippet
ap_uint<72> key_low[512];
ap_uint<72> key_high[512];
int value[72];
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
res=value[addr];

## Slide 86: How Lookup Work?
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC
Lookup 0x214 = 0x001 0x014

## Slide 87: Code Snippet
ap_uint<72> key_low[512];
ap_uint<712> key_high[512];
int value[72];
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
res=value[addr];

## Slide 88: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
What match_low, match_high?

## Slide 89: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
What match?

## Slide 90: What does binary_encode do?
binary_encode(0000000…010000)=0x40
10000…0  71
0000…01  0
0000…010  1
for (i=0<i<72;i++)
  If (bit[i]==1) return i
Return(MISS); // if not find (i.e., all 0’s)
Technicalities – maybe check only one 1

## Slide 91: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
(only show bottom 8 b; rest 0’s)
Key[17:9] Match BRAM
Key[8:0] Match BRAM
match_low=key_low[key%512];
match_high=key_high[(key>>9)%512];
match=match_low & match_high;
addr=binary_encode(match);
What addr?

## Slide 92: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM
res=value[addr];
What res?

## Slide 93: How Lookup Work?
Key[17:9] | Key[8:0] | Value
0x001 | 0x014 | 0x01
0x001 | 0x01 | 0x34
0x0F0 | 0x014 | 0xE3
0x0C8 | 0x113 | 0xCC
Lookup 0x214 = 0x001 0x014

## Slide 94: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 95: Add another entry
How BRAM contents change to add this entry
for 0x19001
match | Key[17:9] | Key[8:0] | Value
0 | 0x001 | 0x014 | 0x01
1 | 0x001 | 0x01 | 0x34
2 | 0x0F0 | 0x014 | 0xE3
3 | 0x0C8 | 0x113 | 0xCC
4 | 0x0C8 | 0x01 | 0x2B

## Slide 96: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 97: Memory Contents
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
0x014 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0C8 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Addr | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0x001 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0x014 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0x0C8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x0F0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0x113 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
Addr | Value
0x00 | 0x01
0x01 | 0x34
0x02 | 0xE3
0x03 | 0xCC
0x04 | 0x2B
0x05 | 
0x06 | 
(only show bottom 8 b; rest 0’s)
Value BRAM
Key[17:9] Match BRAM
Key[8:0] Match BRAM

## Slide 98: 4K Chunk LZW Search
 | BRAMs | Operations/byte
Brute Search | 1 | 4K
Tree with Dense RAM | 384 | 1
Tree with Full Assoc | 173 | 1
36Kb BRAMs on ZU3EG = 216

## Slide 99: Checkpoint
Notice levels of mapping:
  Prefix Tree algorithm
  Formulated on a 2D memory
  Then implemented in assoc. memory
    (later with Tree … hash table)

## Slide 100: Big Ideas
Can adaptively compress data using recurring substrings
  With constant work for symbol
Rich design space for engineering associative map solutions

## Slide 101: Admin
Feedback (including HW7)
Reading for Wednesday on Web
First project milestone due Friday
  Including teaming