## Slide 1: ESE5320: System-on-a-Chip Architecture
Day 5: September 18, 2023
Dataflow Process Model

## Slide 2: Today
Dataflow Process Model
Terms (part 1)
Issues
Abstraction
Performance Prospects (part 2)
Basic Approach
As time permits (part 3)
  Dataflow variants
  Motivations/demands for variants

## Slide 3: Message
Parallelism can be natural
Expression can be agnostic to substrate
  Abstract out implementation details
  Tolerate variable delays may arise in implementation
Divide-and-conquer
  Start with coarse-grain streaming dataflow
Basis for performance optimization and parallelism exploitation

## Slide 4: Programmable SoC
Implementation Platform for innovation
  This is what you target (avoid NRE)
  Implementation vehicle

## Slide 5: Reminder
Goal: exploit parallelism on heterogeneous PSoC to achieve desired performance (energy)

## Slide 6: Term: Process
Abstraction of a processor
Looks like each process is running on a separate processor
Has own state, including
  Program Counter (PC)
  Memory
  Input/output
May not actually run on processor
  Could be specialized hardware block
  May share a processor

## Slide 7: Thread
Has a separate control location (PC)
May share memory (contrast process)
  Run in common address space with other threads
May not actually run on processor
  Could be specialized hardware block
  May share a processor

## Slide 8: FIFO
Hardware Block
Outputs data in order received
  First-In, First-Out
Tell it when you are providing data
  Write
  May choose not to insert on a cycle
    Need to signal
Tell it when you are consuming data
  Read
Tells you when it’s empty and has no data to provide
Tells you when it’s full and can hold nothing else
Day 4

## Slide 9: Process
Processes (threads) allow expression of independent control
Convenient for things that advance independently
Process (thread) is the easiest way to express some behaviors
  Easier than trying to describe as a single process
Can be used for performance optimization to improve resource utilization

## Slide 10: Preclass 2
Average time for TF, SG independently?
  1 cycle 99% of time, 100 cycles 1% of time
Throughput TF->SG with no FIFO?
  Hint: what must wait on TF miss? SG miss?
Throughput with FIFO?
  How is FIFO changing?
What benefit from FIFO and processes?

## Slide 11: Preclass 2
Independent probability of miss
  Pf, Pg
Concretely
  1 cycle in map
  100 run function and put in map
If each runs independently (in isolation)
  T~= 1*(1-P)+P*100
If run together in lock step
  Either can stall: P=Pf+Pg-PfPg
  T~= 1*(1-P)+(P)*100

## Slide 12: Multithread Web Page Load
Typical browsers load images in separate threads
  Allows parallelism in image loads
  Doesn’t block display of text content (images that have already downloaded)
    Get to see that even if image load slow
  Separate thread keeps track of separate location in each image load

## Slide 13: Model (from Day 4) Communicating Threads
Computation is a collection of sequential/control-flow “threads”
Threads may communicate
  Through dataflow I/O
  (Through shared variables)
View as hybrid or generalization
CSP – Communicating Sequential Processes  canonical model example

## Slide 14: Issues
Communication – how move data between processes?
  What latency does this add?
  Throughput achievable?
Synchronization – how define how processes advance relative to each other?
Determinism – for the same inputs, do we get the same outputs?

## Slide 15: Today’s Stand
Communication – FIFO-like channels
Synchronization – dataflow with FIFOs
Determinism – how to achieve
  …until you must give it up.
    Only hint at giving up at end of lecture, time permitting

## Slide 16: Dataflow Process Model

## Slide 17: Operation/Operator
Operation – logical computation to be performed
  A process that communicates through dataflow inputs and outputs
Operator – physical block that performs an Operation
  E.g. processor, hardware block

## Slide 18: Dataflow / Control Flow
Dataflow
Program is a graph of operations
Operation consumes tokens and produces tokens
All operations run concurrently
  All processes
Control flow (e.g. C)
Program is a sequence of operations
Operation reads inputs and writes outputs into common store
One operation runs at a time
  defines successor
Day 4

## Slide 19: Token
Data value with presence indication
  May be conceptual
    Only exist in high-level model
    Not kept around at runtime
  Or may be physically represented
    One bit represents presence/absence of data
Day 4

## Slide 20: Stream
Logical abstraction of a persistent point-to-point communication link between operations (processes)
  Has a (single) source and sink
  Carries data presence / flow control
  Provides in-order (FIFO) delivery of data from source to sink (producer to consumer)
stream

## Slide 21: Streams
Captures communications structure
  Explicit producerconsumer link up
Abstract communications
  Physical resources or implementation
  Delay from source to sink
  Delay of Operators
Contrast
  C: producer->consumer implicit through memory
  Verilog/VHDL: cycles visible in implementation
  (can add on top of either C or Verilog)

## Slide 22: Variable Delay Source to Sink
How would placement of source and sink operator impact delay?
How could sharing of interconnect between source and sink impact delay?

## Slide 23: Communication Latency
Once map to multiple processors
Need to move data between processors
That costs time

## Slide 24: On-Chip Delay
Delay is proportional to distance travelled
Make a wire twice the length
  Takes twice the latency to traverse
  (can pipeline)
Modern chips
  Run at 100s of MHz to GHz
  Take 10s of ns to cross the chip
Day 3

## Slide 25: Dataflow gives Clock Independent Semantics
Interconnect
Takes n-clocks
Latency

## Slide 26: Dataflow Process Network
Collection of Operations
Connected by Streams
Communicating with Data Tokens
(CSP restricted to stream communication)

## Slide 27: Dataflow Abstracts Timing
Doesn’t say
  on which cycle calculation occurs
Does say
  What order operations occur in
  How data interacts
    i.e. which inputs get mixed together
Permits
  Scheduling on different # and types of resources
  Operators with variable delay
  Variable delay in interconnect

## Slide 28: Dataflow Graphs Parallel Performance Prospect
Part 2

## Slide 29: Some Task Graphs
Control
Motor 2

## Slide 30: Synchronous Dataflow (SDF) with fixed operators
Particular, restricted form of dataflow
Each operation
  Consumes a fixed number of input tokens
  Produces a fixed number of output tokens
  Operator performs fixed number of operations (in fixed time) – data independent
  When full set of inputs are available
    Can produce output
  Can fire any (all) operations with inputs available at any point in time

## Slide 31: SDF Operator
FFT
1024 inputs
1024 outputs
10,240 multiplies
20,480 adds
(or 30,720 primitive operations)
1024
1024
30,720

## Slide 32: Processor Model
Simple (for today’s lecture)
  Assume one primitive operation per cycle
Could embelish
  Different time per operation type
    E.g. adds: 1 cycle, multiply: 3 cycles
  Multiple memories with different timings

## Slide 33: Time for Graph Iteration on Processors
Single processor
One processor per Operation (process)
  Teach = max(Nop1,Nop2,Nop3,…)
General
c(x,y) – 1 if Processor x runs task y
(simplified resource bound model)

## Slide 34: Intel Knights Landing
https://www.nextplatform.com/2016/06/20/intel-knights-landing-yields-big-bang-buck-jump/
[Intel, Micro 2016]

## Slide 35: GRVI/Phallanx
Puts 1680 RISC-V32b Integer cores
On XCVU9P FPGA
http://fpga.org/2017/01/12/grvi-phalanx-joins-the-kilocore-club/
[Gray, FCCM 2016]

## Slide 36: Biglab

## Slide 37: Map to different processors
Map to (preclass 1)
  One processor performance?
  One process per processor performance?
  Two processors
    How?
    Performance?
  Bottleneck?
30,000
15,000
3,000
2,000

## Slide 38: Refine Data Parallel
If component is data parallel, can split out parallel tasks

## Slide 39: Refine Pipeline
If operation internally pipelineable, break out pipeline into separate tasks
6,000
6,000
6,000
6,000
6,000
7,500
3,000
2,000
Performance with one processor per operation?
Achieve same performance with how many processors?

## Slide 40: Apple A16 Bionic
? 110+mm2, 4nm
16 Billion Tr.
iPhone 14
6 ARM cores
  2 fast (3.5GHz)
  4 low energy (2GHz)
5 custom GPUs (1.4GHz)
16 Neural Engines
  17 Trillion ops/s?
https://en.wikipedia.org/wiki/Apple_A16

## Slide 42: Heterogeneous Processor
GPU perform 10 primitive FFT Ops per cycle
Fast CPU can perform 2 ops/cycle
Slow CPU 1 op/cycle
Map: FFT to GPU, Select to 2 Fast CPUs, quantize and Entropy each to own Slow CPU
Cycles/graph iteration?

## Slide 43: Heterogeneous Processor
 | GPU | Fast CPU | Slow CPU
Windowed FFT | 3,000 | 15,000 | 30,000
Select Freq. 1 |  | 3,750 | 7,500
Select Freq. 2 |  | 3,750 | 7,500
Quantize |  | 1,500 | 3,000
Entropy Encode |  | 1,000 | 2,000

## Slide 44: Heterogeneous Processor
 | GPU | Fast CPU | Slow CPU
Windowed FFT | 3,000 | 15,000 | 30,000
Select Freq. 1 |  | 3,750 | 7,500
Select Freq. 2 |  | 3,750 | 7,500
Quantize |  | 1,500 | 3,000
Entropy Encode |  | 1,000 | 2,000
Max(3000,3750,3000,2000) = 3750

## Slide 45: Heterogeneous Processor
 | GPU | Fast CPU | Slow CPU
Windowed FFT | 3,000 | 15,000 | 30,000
Select Freq. 1 |  | 3,750 | 7,500
Select Freq. 2 |  | 3,750 | 7,500
Quantize |  | 1,500 | 3,000
Entropy Encode |  | 1,000 | 2,000
General case – find assignment with optimal timing

## Slide 46: Custom Accelerator
Dataflow Process doesn’t need to be mapped to a processor
Map FFT to custom datapath on FPGA logic
  Read and produce one element per cycle
  1024 cycles to process 1024-point FFT
1024
15,000
3,000
2,000

## Slide 47: Operations
Can be implemented on different operators with different characteristics
  Small or large processor
  Hardware unit
  Different levels of internal
    Data-level parallelism
    Instruction-level parallelism
    Pipeline parallelism
May itself be described as
  Dataflow process network, sequential, hardware register transfer language

## Slide 48: Streams
Stream: logical communication link
Some implementation options:
  TCP/IP link over Internet
  On-Chip bus
  Buffer in memory
Appropriate for
  2 processes on separate processors on same chip
  2 threads on same processor
  One process at Penn, one at Amazon

## Slide 49: Add Delay
What does it do to computation if add an operation that copies inputs to outputs with some latency?
  Impact on function?
  What is throughput impact when Identity operation has
    Latency 10, throughput 1 value per cycle?
    (reminder 1024 values between FFT and Select Freq.)
15,000
3,000
2,000
30,000
1024

## Slide 50: Semantics (meaning)
Need to implement semantics
  i.e. get same result as if computed as indicated
But can implement any way we want
  That preserves the semantics
  Exploit freedom of implementation

## Slide 51: Basic Approach

## Slide 52: Approach (1)
Identify natural parallelism
Convert to streaming flow
  Initially leave operations in software
  Focus on correctness
Identify flow rates, computation per operator, parallelism needed
Refine operations
  Decompose further parallelism?
  E.g. data parallel split, ILP implementations
  model potential hardware

## Slide 53: Approach (2)
Refine coordination as necessary for implementation
Map operations and streams to resources
  Provision hardware
  Scheduling: Map operations to operators
  Memories, interconnect
Profile and tune
Refine

## Slide 54: Dataflow Variants
Part 3:
(coverage here depends on time available)

## Slide 55: Variable Delay
Two different causes of “variable” delay
  Operator-dependent
  Data-dependent
Operator-dependent
  Depends on operator select
    Fast processor, slow processor, GPU
    Fixed time once select
Data-Dependent
  Depends on data being processed
    Examples to come

## Slide 56: Motivations and Demands for Dataflow Options
Time Permitting

## Slide 57: Data-Dependent Variable Delay Operators
Why might a multiplier have data-dependent variable delay?
  Hint: consider shift-and-add multiply
    Multiply by 3 vs. multiply by 16,777,215

## Slide 58: GCD (Preclass 3)
What is delay of GCD computation?
while(a!=b)
  t=max(a,b)-min(a,b)
  a=min(a,b)
  b=t
return(a);

## Slide 59: Data-Dependent Variable Delay Operators
Operators with Data-Dependent Variable Delay
  Cached memory or computation
  Shift-and-add multiply
  Iterative divide or square-root

## Slide 60: Dynamic Rates?
Dynamic rates – use of inputs or production of outputs is data-dependent
  if (good_input(x)) out.write(x)
  If (destination_high(x) high.write(x)
  else low.write(x)
What is implication of static rates
  on compression?
  Filtering?
    (e.g. discard all spam packets)

## Slide 61: Data-Dependent Rates?
Static Rates limiting
  Compress/decompress
    Lossless
    Even Run-Length-Encoding
  Filtering
    Discard all packets from spamRus
  Anything data dependent

## Slide 62: Non-Blocking Stream Primitives
Blocking
  only primitives are read, write
  If data not present, block for data to be available
Non-blocking
  Add operations to ask if data is available (if stream ready for write)
if (not(empty(in1)) next_pkt=in1.read()
else if (not(empty(in2)) next_pkt=in2.read()

## Slide 63: When non-blocking necessary?
What are cases where we need the ability to ask if a data item is present?
Consider a server with multiple clients
  Clients requests are independent, random
    No guarantee make same number or rate of requests
  What happens if must wait for a request from each of clients?
  What would prefer to do?

## Slide 64: When non-blocking necessary?
Consider an IP packet router:
Why need non-blocking here?

## Slide 65: Non-Blocking
Removed model restriction
  Can ask if token present
Gained expressive power
  Can grab data as shows up
Weaken our guarantees
  Possible to get non-deterministic behavior
    Depends on timing
      Which we’ve said may vary with mapping
Use when necessary, avoid if possible

## Slide 66: Turing Complete
Can implement any computation describable with a Turing Machine
  (theoretical model of computing by Alan Turing)
Turing Machine – captures our notion of what is computable
  If it cannot be computed by a Turing Machine, we don’t know how to compute it

## Slide 67: Process Network Roundup
Model | Deterministic Result | Deterministic Timing | Turing Complete
SDF+fixed-delay operators | Y | Y | N
SDF+variable (data-dependent) delay operators | Y | N | N
Dynamic Rate DF blocking | Y | N | Y
Dynamic Rate DF non-blocking | N | N | Y
Good
For
correctness
Good
For
Real-Time
Completeness
(Compute
anything)

## Slide 68: Big Ideas
Capture gross parallel structure with Process Network
Use dataflow synchronization for determinism
  Abstract out timing of implementations
  Give freedom of implementation
Exploit freedom to refine mapping to optimize performance
Minimally use non-determinism as necessary

## Slide 69: Admin
Remember feedback
  Today’s lecture and HW2
Reading for Day 6 on web
HW3 due Friday
  Implementing multiprocessor solutions on homogeneous (ARM) processor cores