## Slide 1: ESE5320: System-on-a-Chip Architecture
Day 11: October 7, 2024
Data Movement
(Interconnect, DMA)

## Slide 2: Preclass 1
N processors
Each: 1 read, 10 cycle compute, 1 write
Memory: 1 read or write per cycle
How many processors can support before saturate memory capacity?

## Slide 3: Schedule Memory Port
12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
P1.1 write | P1.2 read | P2.1 write | P2.2 read | P3.1 write | P3.2 read | P4.1 write | P4.2 read | P5.1 write | P5.2 read | P6.1 write | P6.2 read | P1.2 write | P1.3 read
 |  | P1 compute f on 2nd iteration |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | P2 compute f on 2nd iteration |  |  |  |  |  |  |  |  | 

## Slide 4: Bottleneck
Sequential access to a common memory can become the bottleneck

## Slide 5: Previously
Want data in small memories
  Low latency, high bandwidth
FPGA has many memories all over fabric

## Slide 6: Embedded Memory in FPGA
Logic
Cluster
Memory
Bank
Memory
Frequency
ZU3EG (Ultra96) has 216 36Kb BRAMs
VU9P (Amazon F1) has 2,160

## Slide 7: Previously
Want data in small memories
  Low latency, high bandwidth
FPGA has many memories all over fabric
Want C arrays in small memories
  Partitioned so can perform enough reads (writes) in a cycle to avoid memory bottleneck

## Slide 8: Today
Interconnect Infrastructure (Part 1)
Peripherals (Part 2)
Data Movement Threads (Part 3)
DMA -- Direct Memory Access (Part 4)

## Slide 9: Message
Need to move data
Often use shared interconnect to make physical connections
Useful to move data as separate thread of control
  Dedicating a processor is inefficient
  Useful to have dedicated data-movement hardware: Direct Memory Access (DMA)

## Slide 10: Term: Peripheral
“On the edge (or perhiphery) of something”
Peripheral device – device used to put information onto or get information off of a computer
  E.g.
    Keyboard, mouse, modem, USB flash drive, …

## Slide 11: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 12: Memory and I/O Organization
Architecture contains
  Large memories
    For density, necessary sharing
  Small memories local to compute
    For high bandwidth, low latency, low energy
  Peripherals for I/O
Need to move data
  Among memories and I/O
    Large to small and back
    Among small
    From Inputs, To Outputs

## Slide 13: How move data?
Abstractly, using stream links.
Connect stream between producer and consumer.
Ideally: dedicated wires

## Slide 14: Dedicated Wires?
What might prevent us from having dedicated wires between all communicating units?

## Slide 15: Making Connections
Cannot always be dedicated wires
  Programmable
  Wires take up area
  Don’t always have enough traffic to consume the bandwidth of point-to-point wire
  May need to serialize use of resource
    E.g. one memory read per cycle
  Source or destination may be sequentialized on hardware

## Slide 16: Model
Programmable, possibly shared interconnect

## Slide 17: Simple Realization
Shared Bus
Write to bus with address of destination
When address match, take value off bus
Pros?
Cons?

## Slide 18: Alternate: Crossbar
Provide programmable connection between all sources and destinations
Any destination can be connected to any single source

## Slide 19: Simplistic FPGA (illustrate possibility)
Every LUT input has a mux
Every such mux has m=(N+I) inputs
  An input for each LUT output (N 2-LUTs)
  An input for each Circuit Input (I Circuit inputs)
Each Circuit Output has an m-input mux
Day 8

## Slide 20: Alternate: Crossbar
Provide programmable connection between all sources and destinations
Any destination can be connected to any single source

## Slide 21: Crossbar

## Slide 22: Preclass 2
K-input, O-output Crossbar
How many 2-input muxes?

## Slide 23: Crossbar
Provides high bandwidth
  Minimal blocking
Costs large amounts of area
  Grows fast with inputs, outputs

## Slide 24: General Interconnect
Generally, want to be able to parameterize designs
Here: tune area-bandwidth
  Control how much bandwidth provide

## Slide 25: Mux-based Bus

## Slide 26: Multiple Busses
Think of crossbar as one bus per output
Simple bus is one bus total

## Slide 27: Interconnect
How might get design points between bus and crossbar?
How could reduce number
  Inputs to crossbar?
  Outputs from crossbar?

## Slide 28: Share Crossbar Outputs
Group set of outputs together on a bus

## Slide 29: Share Crossbar Inputs
  Group number of inputs together on an input port to crossbar

## Slide 30: Delay
Delay proportional to distance
Pipeline bus to keep cycle time down
  Take many cycles to travel long distance
  …but fewer cycles when distance small
Sometimes call this a ``Ring’’

## Slide 31: Local Interconnect
How many cycles from:
  PE3 to PE2
  PE3 to PE1
  PE3 to PE4

## Slide 32: Mesh
Mesh is a set
Of Horizontal
And Vertical
Rings with
Option to switch
H to V

## Slide 33: Mesh
Delay Proportional to distance in 2D

## Slide 34: Hierarchical Busses

## Slide 35: Interconnect
Will need an infrastructure for programmable connections
Rich design space to tune area-bandwidth-locality

## Slide 36: Peripherals
Part 2

## Slide 37: Input and Output
Typical SoC has I/O with external world
  Sensors
  Actuators
  Keyboard/mouse, display
  Communications
Also accessible from interconnect

## Slide 38: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 39: High Speed I/O
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 40: Masters and Slaves
Two kinds of entities on interconnect
Master – can initiate requests
  E.g. processor that can perform a read or write
Slaves – can only respond to requests
  E.g. memory that can return the read data from a read request

## Slide 41: Simple Peripheral Model
Peripherals are slave devices
  Masters can read input data
  Masters can write output data
  To move data, master (e.g. processor) initiates

## Slide 42: Simple Peripheral Model
Peripherals are slave devices
  Masters can read input data
  Masters can write output data
  To move data, master (e.g. processor) initiates
Demanding processor touch every data item has some negative consequences

## Slide 43: Timing Demands
Must read each input before overwritten
Must write each output within real-time window
Must guarantee processor scheduled to service each I/O at appropriate frequency
How many cycles between 32b input words for 1Gb/s network and 32b, 1GHz processor?
  Consider input data shifted into register 1b per ns
  Must read out 32b register before overwritten

## Slide 44: Refine Model
Give each peripheral local FIFO
Processor must still move data
For same input data rate, how does this change requirements and impact?
  How many cycles can processor run between servicing inputs?

## Slide 45: Long Latency Memory Operations
Part 3

## Slide 46: Day 3
Large memories are slow
  Latency increases with memory size
Distant memories are high latency
  Multiple clock-cycles to cross chip
  Off-chip memories even higher latency

## Slide 47: Day 3, Preclass 2
10 cycle latency to memory
If must wait for data return, latency can degrade throughput
10 cycle latency + 10 op + (assorted)
  More than 20 cycles / result

## Slide 48: Preclass 3
Throughput using 3 threads on 3 processors: P1, P2, P3?
  Throughput of each?
  Throughput of collection?

## Slide 49: Fetch (Write) Threads
Potentially useful to move data in separate thread
  (loop that compiler implements as a thread)
Especially when
  Long (potentially variable) latency to data source (memory)
Useful to split request/response

## Slide 50: DMA Part 4
Direct Memory Access

## Slide 51: Preclass 4a

## Slide 52: Preclass 4a
What NewAdder[24] provide for WriteAstart, Write Astop?

## Slide 53: Preclass 4a
p++
p<&(a[MAX)]

## Slide 54: Preclass 4a
Astream.write
Read *p

## Slide 55: Preclass 4a
p++
p=&(a[i])
*p=a[i]
Astream
&a
&(a[MAX])

## Slide 56: Control Logic
FIFO_Write =
ReadRequest =
Incr_cnt =

## Slide 57: Control Logic
FIFO_Write = DataPresent & FIFO_Has_Space
ReadRequest = not-done
Incr_cnt = not-done
(AckDataPresent = FIFO_Write)

## Slide 58: Preclass 4
How much hardware?
  Counter bits?
  Registers?
  Comparators?
  Control Logic gates? (4cd)
Compare to MicroBlaze
  small RISC Processor optimized for Xilinx
  minimum config 630 6-LUTs
  Would take several cycles per word

## Slide 59: Observe
Modest hardware can serve as data movement thread
  Much less hardware than a processor
  Higher throughput than a processor
  Offload work from processors
Small hardware allow peripherals to be master devices on interconnect

## Slide 60: DMA
Direct Memory Access (DMA)
“Direct” – inputs (and outputs) don’t have to be indirectly handled by the processor between memory and I/O
I/O unit directly reads/write memory

## Slide 61: DMA
Direct Memory Access (DMA)
Peripheral as Master
  Can write directly into (read from) memory
  Saves processor from copying
  Reduces demand to schedule processor to service

## Slide 62: DMA Engine
Data Movement Thread
  Specialized Processor that moves data
  Another heterogeneous processing engine
Act independently (hence thread)
Implement data movement
Can build to move data between memories (Slave devices)
E.g., Implement P1, P3 in Preclass 3

## Slide 63: DMA Engine

## Slide 64: Programmable DMA Engine
What copy from?
How much?
Where copy to?
Stride?
What size data?
Loop?
Transfer Rate?

## Slide 65: Multithreaded DMA Engine
One copy task not necessarily saturate bandwidth of DMA Engine
Can share engine performing many transfers (channels)
Separate transfer state for each
  Hence thread (or channel)
Swap among threads
  Simplest: round-robin:
    1, 2, 3, .. K, 1, 2, 3, .. K, 1, ….

## Slide 66: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 67: Hardwired and Programmable
Zynq has hardwired DMA engine
  8 channels
Also build data movement engines (Data Movers) in FPGA fabric
UG1085
Xilinx
UltraScale
Zynq
TRM
Ch. 10
(p519)

## Slide 68: Example
Networking Application: inline packet encrypt
Header on processor
Payload (encrypt, checksum) on FPGA
DMA from ethernetmain memory
DMA main memoryBRAM
Stream between payload components
DMA from encrypted packet and chksum to ethernet out
header
Payload encrypt
chksum
ethernet
ethernet

## Slide 69: AXI
Advanced eXtensible Interface
  Originally developed by ARM
  On-chip communication bus standard
  Particular communication protocol
Full AXI
  Read/write operations with bursts
    Burst = single address + length
      Large, contiguous block of memory
  Separate send/receive data channels
AXI-S – for streaming connections
AXI-lite – simpler, not burst

## Slide 70: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 71: Programmable SoC
AXI Channels
128b wide
@ 333 MHz
=5.3GB/s
Separate
Data in
Data out
Paths
5.3GB/s
Each way

## Slide 72: Programmable SoC
AXI Channels
128b wide
@ 333 MHz
=5.3GB/s
Per direction
Per channel
S_ act as
master for PL
(connects to
slave ports
in PS)
M_ as slave
for PL

## Slide 73: DMA in Vitis
Vitis/OpenCL demands that we write code to perform DMA of data to and from accelerators in FPGA fabric
We will see specifics on Monday
Have some options to control
  With pragmas
  With choice of data and burst sizes
  Explore HW6

## Slide 74: Big Ideas
Need to move data
Shared Interconnect to make physical connections – can tune area/bw/locality
Useful to
  move data as separate thread of control
  Have dedicated data-movement hardware: DMA

## Slide 75: Admin
Feedback including lab
Midterm Wednesday
  Review Monday 8-9pm in Ketterer
  Here classtime
  Arrive early, start right at 10:15am
HW5 due on Friday
HW6 coming soon