## Slide 1: ESE5320: System-on-a-Chip Architecture
Day 21: November 11, 2024
Verification 2

## Slide 2: Today
Assertions (Part 1)
Proving correctness (Part 2)
  FSM Equivalence
Timing and Testing (Part 3)

## Slide 3: Message
If you don’t test it, it doesn’t work.
Testing can only prove the presence of bugs, not the absence.
  Full verification strategy is more than testing.
Valuable to decompose testing
  Functionality
  Functionality at performance

## Slide 4: Assertions

## Slide 5: Assertion
Properties expect/demand to hold
Predicate (Boolean expression) that must be true
Add to code
  Can uses variables in code to write expression
Example: assert(num<100);
Invariant
  Expect/demand this property to always hold
  Never vary  never not be true

## Slide 6: Equivalence with Reference as Assertion
Match of test and golden reference is a heavy-weight example of an assertion
r=fimpl(in);
assert (r==fgolden(in));

## Slide 7: Assertion as Invariant
May express a property that must hold without expressing how to compute it.
  Different than just a simpler way to compute
int res[2];
res=divide(n,d);
assert(res[QUOTIENT]*d+res[REMAINDER]==n);

## Slide 8: Lightweight
Typically, lighter weight (less computation) than full equivalence check
Typically, less complete than full check
Allows continuum expression

## Slide 9: Preclass 1
What property needs to hold on l?
Note: divide: s/l
s=packetsum(p);
l=packetlen(p);
res=divide(s,l);

## Slide 10: Check a Requirement
s=packetsum(p);
l=packetlen(p);
assert(l!=0);
res=divide(s,l);

## Slide 11: Preclass 2
What must be true of my_array[loc] after call?

## Slide 12: Merge using Streams
Merging two sorted list is a streaming operation
int aptr; int bptr;
astream.read(ain); bstream.read(bin)
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (ain>bin)
  { ostream.write(ain); aptr++; astream.read(ain);}
  Else
  { ostream.write(bin) bptr++; bstream.read(bin);}
  Else // copy over remaining from astream/bstream
Day 13

## Slide 13: Merge Requirement
Require: astream, bstream sorted
int aptr; int bptr;
astream.read(ain); bstream.read(bin)
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (ain>bin)
  { ostream.write(ain); aptr++; astream.read(ain);}
  Else
  { ostream.write(bin) bptr++; bstream.read(bin);}
  Else // copy over remaining from astream/bstream

## Slide 14: Merge Requirement
Require: astream, bstream sorted
Int ptr; int bptr;
astream.read(ain); bstream.read(bin)
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (ain>bin)
  { ostream.write(ain); aptr++;
  int prev_ain=ain; astream.read(ain);
  assert(prev_ain>=ain);
  }

## Slide 15: Merge with Order Assertion
When composed
  Every downstream merger checks work of predecessor
merge+alt
merge+alt
merge+alt

## Slide 16: Merge Requirement
Require: astream, bstream sorted
Requirement that input be sorted is good
  And not hard to check
Not comprehensive
  Weaker than saying output is a sorted version of input
What errors would it allow?

## Slide 17: What do with Assertions?
Include logic during testing (verification)
Omit once tested
  Compiler/library/macros (#define) omit code
  Keep in source code
Maybe even synthesize to gate logic for FPGA testing
When assertion fail
  Count
  Break program for debugging (dump core)

## Slide 18: Assertion Roles
Specification (maybe partial)
  May address state that doesn’t exist in gold reference
Documentation
  This is what I expect to be true
    Needs to remain true as modify in the future
Defensive programming
  Catch violation of input requirements
Catch unexpected events, inputs
Early failure detection
Validate that something isn’t happening

## Slide 19: Assertion Discipline
Worthwhile discipline
  Consider and document input/usage requirements
  Consider and document properties that must always hold
Good to write those down
  As precisely as possible
Good to check assumptions hold

## Slide 20: Equivalence Proof
FSM
Part 2

## Slide 21: Prove Equivalence
Testing is a subset of Verification
Testing can only prove the presence of bugs, not the absence.
Depends on picking an adequate set of tests
Can we guarantee that all behaviors are the correct? Same as reference? Seen all possible behaviors?

## Slide 22: Idea
Reason about all behaviors
  Response to all possible inputs
Try to find if there is any way to reach disagreement with specification
Or can prove that they always agree
Still demands specification
  …but we can also relax that with assertions

## Slide 23: Testing with Reference Specification
Validate the design by testing it:
Create a set of test inputs
Apply test inputs
  To implementation under test
  To reference specification
Collect response outputs
Check if outputs match
Day 19

## Slide 24: Formal Equivalence with Reference Specification
Validate the design by proving equivalence between:
implementation under consideration
reference specification

## Slide 25: Testing FSM Equivalence
Exhaustive:
  Generate all strings of length |state|
    (for larger FSM = the one with the most states)
  Feed to both FSMs with these strings
  Observe any differences?
How many such strings?
  (N binary input bits to FSM, S states)
  2N*S

## Slide 26: FSM Equivalence
Illustrate with concrete model of FSM equivalence
  Is some implementation FSM
  Equivalent to reference FSM

## Slide 27: Compare
Start with golden model setup
  Run both and compare output
Create composite FSM
  Start with both FSMs
  Connect common inputs together (Feed both FSMs)
  XOR together outputs of two FSMs
    Xor’s will be 1 if they disagree, 0 otherwise

## Slide 28: Compare
Create composite FSM
  Start with both FSMs
  Connect common inputs together (Feed both FSMs)
  XOR together outputs of two FSMs
    Xor’s will be 1 if they disagree, 0 otherwise
Ask if the new machine ever generate a 1 on an xor output (signal disagreement)
  Any 1 is a proof of non-equivalence
  Never produce a 1  equivalent

## Slide 29: Creating Composite FSM
Assume know start state for each FSM
Each state in composite is labeled by the pair {S1i, S2j}
  How many such states?
Start in {S10, S20}
For each input a, create a new edge:
  T(a,{S10, S20}) {S1i, S2j}
    If T1(a, S10) S1i, and T2(a, S20) S2j
Repeat for each composite state reached

## Slide 30: Composite FSM
How much work?
Hint:
  Maximum number of composite states
  (state pairs)
  Maximum number of edges from each state pair?
  Work per edge?

## Slide 31: Composite FSM
Work
  At most |2N|*|State1|*|State2| edges == work
Can group together original edges
  i.e. in each state compute intersections of outgoing edges
  Really at most |E1|*|E2|

## Slide 32: Non-Equivalence
State {S1i, S2j} demonstrates non-equivalence iff
  {S1i, S2j} reachable
  On some input, State S1i and S2j produce different outputs
If S1i and S2j have the same outputs for all composite states, it is impossible to distinguish the machines
  They are equivalent
A reachable state with differing outputs
  Implies the machines are not identical

## Slide 33: Answering Reachability
Start at composite start state {S10, S20}
Search for path to a differing state
Use any search
  Breadth-First Search, Depth-First Search
End when find differing state
  Not equivalent
OR when have explored entire reachable graph without finding
  Are equivalent

## Slide 34: Reachability Search
Worst: explore all edges at most once
  O(|E|)=O(|E1|*|E2|)
Can combine composition construction and search
  i.e. only follow edges which fill-in as search
  (way described)

## Slide 35: Preclass 3
s0
s1
s2
-/0
-/1
-/1
q0
q1
q3
q2
-/1
-/1
-/0
1/0
0/0
- Means don’t-care. Can read as (0 or 1) here.

## Slide 36: Creating Composite FSM
Assume know start state for each FSM
Each state in composite is labeled by the pair {S1i, S2j}
Start in {S10, S20}
For each symbol a, create a new edge:
  T(a,{S10, S20}) {S1i, S2j}
    If T1(a, S10) S1i, and T2(a, S20) S2j
    Check that both state machines produce same outputs on input symbol a
Repeat for each composite state reached

## Slide 37: Preclass 4

## Slide 38: FSM  Model Checking
FSM case simple – only deal with states
More general, need to deal with
  operators (add, multiply, divide)
  Wide word registers in datapath
    Cause state exponential in register bits
Tricks
  Treat operators symbolically
    Separate operator verification from control verif.
  Abstract out operator width
Similar flavor of case-based search
  Conditionals need to be evaluated symbolically

## Slide 39: Assertion Failure Reachability
Can use with assertions
Is assertion failure reachable?
  Can identify a path (a sequence of inputs) that leads to an assertion failure?

## Slide 40: Formal Equivalence Checking
Rich set of work on formal models for equivalence
  Challenges and innovations to making search tractable
  Used with processor validation
Common versions
  Model Checking (2007 Turing Award)
  Bounded Model Checking

## Slide 41: Timing
Part 3

## Slide 42: Issues
Cycle-by-cycle specification can be overspecified
Golden Reference Specification not run at target speed

## Slide 43: Tokens
Use data presence to indicate when producing a value
Only compare corresponding outputs
  Only store present outputs from computations, since that’s all comparing
Relevant non-Real-Time
Examples?
  (not want to match cycle-by-cycle)

## Slide 44: Timing
Record timestamp from implementation
Allow reference specification to specify its time stamps
  “Model this as taking one cycle”
  Or requirements on its timestamps
    This must occur before cycle 63
    This must occur between cycle 60 and 65
Compare values and times
More relevant Real Time
Example Real Time where exact cycle not matter?

## Slide 45: Challenge
Cannot record at full implementation rate
  Inadequate bandwidth to
    Store off to disk
    Get out of chip
Cannot record all the data you might want to compare at full rate

## Slide 46: At Speed Testing
Compiled assertions might help
  Perform the check at full rate so don’t need to record
Capture bursts to on-chip memory
  Higher bandwidth
  …but limited capacity, so cannot operate continuously

## Slide 47: Bursts to Memory
Run in bursts
Repeat
  Enable computation
  Run at full rate storing to memory buffer
  Stall computation
  Offload memory buffer at (lower) available bandwidth
  (possibly check against golden model)

## Slide 48: Generalize
Generalize to input and output
Feed from memories
Compute full rate
Write into memory
Can run at high rate for number of cycles can store inputs and outputs

## Slide 49: Generalize
Generalize to input and output
Feed from memories
Compute full rate
Write into memory
What might this fail to test?

## Slide 50: Burst Testing
Issue
  May only see high speed for computation/interactions that occur within a burst period
  May miss interaction at burst boundaries
Mitigation
  Rerun with multiple burst boundary offsets
  So all interactions occur within some burst
  Decorrelate interaction and burst boundary

## Slide 51: Timing Validation
Doesn’t need to be all testing either
Static Timing Analysis to determine viable clock frequency
  As Vivado is providing for you
Cycle estimates as get from Vivado
  II, to evaluate a function
Worst-Case Execution Time for software

## Slide 52: Decompose Verification
Breaks into two pieces:
Does it function correctly?
What speed does it operate it?
  Does it continue to work correctly at that speed?

## Slide 53: Learn More
CIS6730 – Computer Aided Verification
CIS5410 – includes verification for real-time system properties
CIS5000 – Software Foundations
  Has mechanized proofs, proof checkers

## Slide 54: Big Ideas
Assertions valuable
  Reason about requirements and invariants
  Explicitly validate
Formally validate equivalence when possible
Valuable to decompose testing
  Functionality
  Functionality at performance
…we can extend techniques to address timing and support at-speed tests

## Slide 55: Admin
Feedback
Reading for Wednesday on Canvas
P3 due Friday