## Slide 1: ESE5320: System-on-a-Chip Architecture
Day 23: November 18, 2024
VLIW
(Very Long Instruction Word Processors)

## Slide 2: Today
VLIW (Very Large Instruction Word)
Exploiting Instruction-Level Parallelism (ILP)
Part 1:
  Demand, Basic Model
Part 2:
  Tuning, Unrollling
Part 3:
  Data Movement
Part 4 (bonus, probably not cover):
  Zero-Overhead Loops, Pipelined Operators

## Slide 3: Message
VLIW as a Model for
  Instruction-Level Parallelism (ILP)
  Customizing Datapaths
  Area-Time Tradeoffs
  Real-Time, Scheduled Sequentialization

## Slide 4: Register File
Small Memory
Usually with multiple ports
  Ability to perform multiple reads and writes simultaneously
Small
  To make it fast (small memories fast)
  Multiple ports are expensive
Day 6

## Slide 5: Preclass 1
Cycles per multiply-accumulate (throughput question, not latency)
  Spatial Pipeline
  Processor

## Slide 6: Preclass 1
How different?
  Resources
    Number of units can perform adds
    Number of simultaneous memory reads
  Ability to use resources
    What resources can use in same cycle

## Slide 7: Computing Forms
Processor – does one thing at a time
Spatial Pipeline – can do many things, but always the same
Vector – can do the same things on many pieces of data

## Slide 8: In Between
What if…
Want to
  Do many things at a time (ILP)
  But not the same (DLP)
SIMD
VLIW

## Slide 9: In Between
What if…
Want to
  Do many things at a time (ILP)
  But not the same (DLP)
Want to use resources concurrently

## Slide 10: In Between
What if…
Want to
  Do many things at a time (ILP)
  But not the same (DLP)
Want to use resources concurrently
Want to
  Accelerate specific task
  But not go to spatial pipeline extreme

## Slide 11: VLIW Feature: Supply Independent Instructions
Provide instruction per ALU (resource)
Instructions more expensive than Vector
  But more flexible

## Slide 12: VLIW
The “instruction”
  The bits controlling the datapath
…becomes long
Hence:
  Very Long Instruction Word (VLIW)
long
instruction

## Slide 13: Control Heterogeneous Units
Control each unit simultaneously and independently
  More expensive than processor
    Memory ports and/or interconnect
  But more parallelism

## Slide 14: VLIW
Very Long Instruction Word
Set of operators
  Parameterize number, distribution (X, +, sqrt…)
    More operators less time, more area
    Fewer operators more time, less area
Memories for intermediate state
+
X
X

## Slide 15: VLIW
Very Long Instruction Word
Set of operators
  Parameterize number, distribution (X, +, sqrt…)
    More operators less time, more area
    Fewer operators more time, less area
Memories for intermediate state
Memory for “long” instructions
+
X
X
Address
Instruction
Memory

## Slide 16: VLIW
+
X
X
Address
Instruction
Memory

## Slide 17: VLIW
Very Long Instruction Word
Set of operators
  Parameterize number, distribution (X, +, sqrt…)
    More operators less time, more area
    Fewer operators more time, less area
    Continuum for operator allocation
Memories for intermediate state
Memory for “long” instructions
General framework for specializing to problem
  Wiring, memories get expensive
  Opportunity for further optimizations
General way to tradeoff area and time

## Slide 18: VLIW
+
X
X
Address
Instruction
Memory

## Slide 19: VLIW w/ Multiport RF
Simple, full-featured model use common Register File
  Memory(Words, WritePorts, ReadPorts)

## Slide 20: Processor Unbound
Can (design to) use all operators at once

## Slide 21: Processor Unbound
Schedule Preclass 1 on this VLIW (next slide)

## Slide 22: Schedule Preclass 1
Cycle | Branch | ALU | Multiply | LD/ST
0 |  |  |  | 
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
4 |  |  |  | 
5 |  |  |  | 

## Slide 23: Schedule
Cycle | Branch | ALU | Multiply | LD/ST
0 |  | Sub r2,r1,r3 |  | 
1 | Bzneq r3,end | Add r4 |  | 
2 |  | Add r5 |  | Ld r4,r6
3 |  |  |  | Ld r5,r7
4 |  | Add r1,#1,r1 | Mpy r7,r8,r8 | 
5 | B top | Add r7,r8,r8 |  | 

## Slide 24: Resource Bound
Can tune VLIW to directly target resource bound
  Add operators to target a particular resource bound

## Slide 25: Tuning, Unrolling
Part 2

## Slide 26: VLIW Operator Knobs (Design Space Axes)
Choose collection of operators and the numbers of each
  Match task
  Tune resources

## Slide 27: Schedule
Choose collection of operators and the numbers of each
  Match task
  Tune resources
What operator might we add
to accelerate this loop?
Cycle | Branch | ALU | Multiply | LD/ST
0 |  | Sub r2,r1,r3 |  | 
1 | Bzneq r3,end | Add r4 |  | 
2 |  | Add r5 |  | Ld r4,r6
3 |  |  |  | Ld r5,r7
4 |  | Add r1,#1,r1 | Mpy r7,r8,r8 | 
5 | B top | Add r7,r8,r8 |  | 

## Slide 28: Preclass 2a
res[i]=sqrt(x[i]*x[i]+y[i]*y[i]+z[i]*z[i]);
II with one operator of each?

## Slide 29: Schedule
Cycle | LD | ST | Multiply | Add | incr | sqrt
0 |  |  |  | i<MAX | &X[i] | 
1 | X[i] |  |  |  | &Y[i] | 
2 | Y[i] |  | X[i]*X[i] |  | &Z[i] | 
3 | Z[i] |  | Y[i]*Y[i] |  |  | 
4 |  |  | Z[i]*Z[i] | X2+Y2 |  | 
5 |  |  |  | (X2+Y2)+Z2 |  | 
6 |  |  |  |  |  | Sqrt()
7 |  | Res[i] |  |  | i | 

## Slide 30: Preclass 2b
res[i]=sqrt(x[i]*x[i]+y[i]*y[i]+z[i]*z[i]);
Minimum II achievable?
  Latency lower bound

## Slide 31: Critical Path
(Increment pointers / branch)
Load
Multiplies
Add
Add
Squareroot
Writeback

## Slide 32: Preclass 2c
res[i]=sqrt(x[i]*x[i]+y[i]*y[i]+z[i]*z[i]);
How many operators of each type to achieve minimum II (latency lower bound)?

## Slide 33: Schedule w/ 2c Resources
 | LD | LD | ST | * | * | + | i | i | sqrt
0 |  |  |  |  |  | < | &x | &y | 
1 | X[i] | Y[i] |  |  |  |  | &z |  | 
2 | Z[i] |  |  | x | y |  |  |  | 
3 |  |  |  | z |  | x+y |  |  | 
4 |  |  |  |  |  | +z |  |  | 
5 |  |  |  |  |  |  |  |  | sqrt
6 |  |  | Res[i] |  |  |  | i |  | 

## Slide 34: Schedule w/ 2d Resources
 | LD | LD | LD | ST | * | * | * | + | i | i | i | sqrt
0 |  |  |  |  |  |  |  | < | &x | &y | &z | 
1 | X[i] | Y[i] | Z[i] |  |  |  |  |  |  |  |  | 
2 |  |  |  |  | x | y | z |  |  |  |  | 
3 |  |  |  |  |  |  |  | X+y |  |  |  | 
4 |  |  |  |  |  |  |  | +z |  |  |  | 
5 |  |  |  |  |  |  |  |  |  |  |  | sqrt
6 |  |  |  | Res[i] |  |  |  |  | i |  |  | 
What is disappointing about this schedule?

## Slide 35: Preclass 2d
res[i]=sqrt(x[i]*x[i]+y[i]*y[i]+z[i]*z[i]);
res[i+1]=sqrt(x[i+1]*x[i+1]+y[i+1]*y[i+1]+z[i+1]*z[i+1]);
res[i+2]=sqrt(x[i+2]*x[i+2]+y[i+2]*y[i+2]+z[i+2]*z[i+2]);
res[i+3]=sqrt(x[i+3]*x[i+3]+y[i+3]*y[i+3]+z[i+3]*z[i+3]);
Schedule (next slide)

## Slide 36: Unroll 4 Schedule
 | LD | LD | LD | ST | * | * | * | + | + | i | i | i | sqrt
0 |  |  |  |  |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  |  |  |  |  |  | 
7 |  |  |  |  |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 37: Time Points
4 iterations in 10 cycles = 2.5 cycles/iter
Compared to 1 iteration in 7
Compared to 1 iteration in 8

## Slide 38: Unroll 4
 | LD | LD | LD | ST | * | * | * | + | + | i | i | i | sqrt
0 |  |  |  |  |  |  |  | < |  | x0 | y0 | z0 | 
1 | x0 | y0 | z0 |  |  |  |  |  |  | x1 | y1 | z1 | 
2 | x1 | y1 | z1 |  | x0 | y0 | z0 |  |  | x2 | y2 | z2 | 
3 | x2 | y2 | z2 |  | x1 | y1 | z1 | xy0 |  | x3 | y2 | z3 | 
4 | x3 | y2 | z3 |  | x2 | y2 | z2 | xy1 | +z0 |  |  |  | 
5 |  |  |  |  | x3 | y2 | z3 | xy2 | +z1 |  |  |  | 0
6 |  |  |  | 0 |  |  |  | xy3 | +z2 |  |  |  | 1
7 |  |  |  | 1 |  |  |  |  | +z3 |  |  |  | 2
8 |  |  |  | 2 |  |  |  |  |  |  |  |  | 3
9 |  |  |  | 3 |  |  |  |  |  | i |  |  | 
What happens to II (cycle/iter) as unroll more?

## Slide 39: Observation
With no data dependencies
  Unroll gets closer to resource bound

## Slide 40: Preclass 2e
res[i]=sqrt(x[i]*x[i]+y[i]*y[i]+z[i]*z[i]);
Area comparison?
Op | read | write | * | + | incr | sqrt | Area | II
A | 20 | 30 | 10 | 2 | 1 | 25 |  | 
2a | 1 | 1 | 1 | 1 | 1 | 1 |  | 8
2c |  |  |  |  |  |  |  | 7
2d | 3 | 1 | 3 | 2 | 3 | 1 |  | 2.5

## Slide 41: Take Aways
VLIW: Tune Operators to select Area-Time point
Running single iteration of loop to completion before start next
  Inefficient
  Latency bound for loop
  Benefit schedule multiple loop bodies
    Can get closer to resource bound

## Slide 42: Data Storage and Movement
Part 3

## Slide 43: Multiport RF
Multiported memories are expensive
  Need input/output lines for each port
  Makes large, slow
Simplified preclass model:
  Area(Memory(n,w,r))=n*(w+r+1)/2

## Slide 44: Alternate: Crossbar (Xbar)
Provide programmable connection between all sources and destinations
Any destination can be connected to any single source
Day 12

## Slide 45: Preclass 3
Areas? (table)
How does area of memories, xbar compare to datapath operators in each case?
 | Multiport RF | Split RF Xbar(5,5) | Split RF Xbar(5,1)
Memory |  |  | 
Operators |  |  | 
Xbar |  |  | 
Total |  |  | 

## Slide 46: Split RF Cheaper
At same capacity, split register file cheaper
  2W+2R  2.5 per word
  5W+10R  8 per word

## Slide 47: Split RF Full Crossbar
Cycles each for computing: (A*B+C)/(D*E+F)
  Assume A..F start as shown
  Hint: left first
    How work on right?
A,B
D,E
C
F

## Slide 48: Split RF Full Crossbar
Specialize connections to avoid bottleneck
A,B
D,E
C
F

## Slide 49: VLIW Memory Tuning
Can select how much sharing or independence in local memories

## Slide 50: Split RF, Limited Crossbar
What limitation does the one crossbar output pose?
  Cycles for same task: (A*B+C)/(D*E+F)
A,B
D,E
C
F
A,B
D,E
C
F

## Slide 51: Split RF, Limited Crossbar
Could specialize connections for computation
A,B
D,E
F
C
A,B
D,E
C
F

## Slide 52: VLIW Schedule
Need to schedule Xbar output(s) as well as operators.
cycle | * | * | + | + | / | Xbar
0 |  |  |  |  |  | 
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 

## Slide 53: VLIW Interconnect Tuning
Can decide how rich to make the interconnect
  Number of outputs to support
  How to depopulate (restrict) crossbar
  Use more restricted network

## Slide 54: Commercial: Xilinx AI Engine
6-way VLIW Vector
https://www.xilinx.com/support/documentation/white_papers/wp506-ai-engine.pdf
Xilinx WP506

## Slide 55: VLIW vs. SuperScalar
Modern, high-end proc. (incl. ARM on Zynq)
  Do support ILP
  Issue multiple instructions per cycle
  …but, from a single, sequential instruction stream
SuperScalar – dynamic issue and interlock on data hazards – hide # operators
  Must have shared, multiport RF
VLIW – offline scheduled (like done today)
  No interlocks, allow split RF
  Lower area/operator – need to recompile code

## Slide 56: Big Ideas:
VLIW as a Model for
  Instruction-Level Parallelism (ILP)
  Customizing Datapaths
  Area-Time Tradeoffs
  Real-Time, Scheduled Sequentialization
Customize VLIW
  Operator selection
  Memory/register file setup
  Inter-functional unit communication network

## Slide 57: Admin
Feedback (including P3)
Reading for Wednesday online
P4 due Friday

## Slide 58: Loop Overhead
Part 4: Bonus slides:
not expect to cover in lecture

## Slide 59: Loop Overhead
Can handle loop overhead in ILP on VLIW
  Increment counters, branches as independent functional units

## Slide 60: VLIW Loop Overhead
Can handle loop overhead in ILP on VLIW
…but paying a full issue unit and instruction costs overhead

## Slide 61: Zero-Overhead Loops
Specialize the instructions, state, branching for loops
  Counter rather than RF
  One bit to indicate if counter decrement
  Exit loop when decrement to 0

## Slide 62: Simplification

## Slide 63: Zero-Overhead Loop Simplify
Share port – simplify further

## Slide 64: Zero-Overhead Loop Example (preclass 1)
repeat r3:
addi r4,#4,r4;
addi r5,#4,r5; ld r4,r6
ld r5,r7
mul r6,r7,r7
add r7,r8,r8

## Slide 65: Zero-Overhead Loop
Potentially generalize to multiple loop nests and counters
Common in highly optimized DSPs, Vector units
Can think about design space options within this VLIW model framework

## Slide 66: Pipelined VLIW Operators

## Slide 67: Pipelined Operators
Often will have pipelined operators
  E.g. 3 cycles multiply
How complicate?

## Slide 68: Accommodating Pipeline
Schedule for when data becomes available
  Dependencies
  Use of resources
cycle | * | * | + | + | / | Xbar
0 | X*X |  |  |  |  | 
1 | Y*Y |  |  |  |  | 
2 |  |  |  |  |  | X*X
3 |  |  |  |  |  | Y*Y
4 |  |  | X2+Y2 |  |  | X2+Y2
5 |  |  |  |  | X2+Y2/Z | 
6 |  |  |  |  |  | 

## Slide 69: Accommodating Pipeline
Schedule for when data becomes available
  Dependencies
  Use of resources
cycle | * | * | + | + | / | Xbar
0 | X*X |  |  |  |  | 
1 | Y*Y |  |  |  |  | 
2 |  |  |  |  |  | X*X
3 |  |  | Q+R |  |  | Y*Y,Q+R
4 |  |  | X2+Y2 |  |  | X2+Y2
5 |  |  |  |  | X2+Y2/Z | 
6 |  |  |  |  |  | 
Impossible
schedule;
Conflict on
single Xbar
output

## Slide 70: Pipelined Operators
Instance of what we saw last time
Need to schedule use on all resources
Including
  Memory port
  Communications (busses, crossbars ports)
  I/O