## Slide 1: ESE5320: System-on-a-Chip Architecture
Day 25: November 25, 2024
Real Time

## Slide 2: Today
Real Time
Part 1: Demands
Part 2: Challenges
  Algorithms
  Architecture
Part 3: Disciplines to achieve

## Slide 3: Message
Real-Time applications demand different discipline from best-effort tasks
Look more like synchronous circuits
Can sequentialize, like processor
  But must avoid/rethink typical general-purpose processor common-case optimizations

## Slide 4: Real Time
“Real” – refers to physical time
  Connection to Real or Physical World
Contrast with “virtual” or “variable” time
Handles events with absolute guarantees on timing

## Slide 5: Time Constants
Many mechanical sense/response times are ~ 5-10ms
Human reaction times ~20ms

## Slide 6: Breaking
Car traveling 60 km/h
Visibility of 30 m
How long do you have to stop as soon as something comes into view?
  Simple total
    See/recognize, decide, apply breaks, breaks respond

## Slide 7: Real-Time Tasks
What timing guarantees might you like for the following tasks?
  Self-driving car detects an object in its path
    Delay from object appearing to detection
  Pacemaker stimulates your heart
  Turn steering wheel on a drive-by-wire car
    Delay to recognized and car turns
  Video playback (frame to frame delay)

## Slide 8: Real-Time Guarantees
Attention/processing within fixed interval
  Sample new value every XX ms
  Produce new frame every 30 ms
  Both: schedule to act and complete action
Bounded response time
  Respond to keypress within 20 ms
  Detect object within 100 ms
  Return search results within 200 ms

## Slide 9: Computer Response
What do these things indicate?
  When will the computer complete the task?
https://en.wikipedia.org/wiki/File:WaitCursor-300p.gif
https://en.wikipedia.org/wiki/File:Windows_8_%2B_10_wait_cursor.gif

## Slide 10: Real-Time Response
What if your car gave you a spinning wait wheel for 5 seconds when you
  Turned the wheel?
  Stepped on the brakes?

## Slide 11: Synchronous Circuit Model
A simple synchronous circuit is a good “model” for real-time task
  Run at fixed clock rate
  Take input every “cycle” (application cycle)
  Produce output every “cycle” (application cycle)
  Complete computation between input and output
  Designed to run at fixed-frequency
    Critical path meets frequency requirement

## Slide 12: Preclass 2
(Circuit) Cycle time could operate?
Assume clocked at 100Hz (application cycle)
Worst-case delay from (L)eft press to change in heading (posx,posy)?

## Slide 13: Preclass 2
Assume clocked at 100Hz (application cycle)

## Slide 14: Historically
Real-Time concerns grew up in EE
  Because an analog circuit was the only way could meet frequency demands
  …later a dedicated digital circuit…
Applications
  Signal processing, video, control, …

## Slide 15: Technological Change
Area units for spatial design shown (preclass 2c)
Fraction of processor capacity required (Prelcass 2d)
Why might prefer using a processor to using the spatial circuit?
  Hint: What does preclass 2c,d suggest?

## Slide 16: Performance Scaling
As circuit speeds increased
  Can meet real-time performance demands with heavy sequentialization
Circuit and processor clocks
  from MHz to GHz
Many real-time task rates unchanged
  44KHz audio, 33 frames/second video
Even 100MHz processor
  Can implement audio in a small fraction of its computational throughput capacity

## Slide 17: HW/SW Co-Design
Computer Engineers – know can implement anything as hardware or software
Want freedom to move between hardware and software to meet requirements
  Performance, costs, energy

## Slide 18: Real-Time Challenge
Meet real-time demands / guarantees
  Economically using programmable architectures
Sequentialize and share resources with deterministic, guaranteed timing
Spatial (all hardware, HLS synthesized) implementations are good at meeting real-time guarantees, but may be bigger than necessary

## Slide 19: Challenges
Part 2

## Slide 20: Processor Data Caches
Traditional Processor Data Caches are a heuristic instance of this
  Add a small memory local to the processor
    It is fast, low latency
  Store anything fetched from large/remote memory in local memory
    Hoping for reuse in near future
  On every fetch, check local memory before go to large memory
Day 3

## Slide 21: Processor Data Caches
Demands more than a small memory
  Need to sparsely store address/data mappings from large memory
  Makes more area/delay/energy expensive than just a simple memory of capacity
Don’t need explicit data movement
Cannot control when data moved/saved
  Bad for determinism
Limited ability to control what stays in small memory simultaneously
Day 3

## Slide 22: Processor Data Caches
Traditional Processor Data Caches are a heuristic instance of this
  Store anything fetched from large/remote memory in local memory
    Hoping for reuse in near future
  On every fetch, check local memory before go to large memory
  Stall processor while waiting for data

## Slide 23: Preclass 3: Processor Cache Timing
Assume
  cache miss (go to large memory) takes 10 cycles
  Cache hit (small memory) takes 1
  Start with empty cache
Due to memory delay, how long to execute:
b=a[0]+a[1];
c=a[1]+a[2];
d=a[2]+a[0];
b=a[i]+a[j];
c=a[k]+a[l];
d=a[m]+a[n];

## Slide 24: Scratchpad
Recall, scratchpad memory
  Small
  Explicitly managed (not dynamic like cache)
If move (DMA) data to scratchpad memory, would be deterministic
b=a[i]+a[j];
c=a[k]+a[l];
d=a[m]+a[n];
b=a[0]+a[1];
c=a[1]+a[2];
d=a[2]+a[0];

## Slide 25: Observe
Instructions on “General Purpose” processors take variable number of cycles

## Slide 26: Preclass 4
How many cycles?
  sin, cos 100 cycles each
  Assignments take 1 cycle
old_sh=sh; old_ch=ch;
if (!left || !right)
{sh=old_sh;ch=old_ch;}
else
{sh=sin(heading);
ch=cos(heading);}

## Slide 27: Preclass 5
How many cycles?

## Slide 28: Preclass 5
How many cycles?

## Slide 29: Observe
Data-dependent branching, looping
  Means variable time for operations

## Slide 30: Two Challenges
Architecture – Hardware have variable (data-dependent) delay
  Esp. for General-Purpose processors
    Instructions take different number of cycles
Algorithm – computational specification have variable (data-dependent) operations
  Different number of instructions

## Slide 31: Algorithm
What programming constructs are data-dependent (variable delay)?

## Slide 32: Programming Constructs
Conditionals: if/then/else
Loops without compile-time determined bounds
  While with termination expressions
  For with data-dependent bounds
Data-dependent recursion
Interrupts
  I/O events, time-slice
Note: 1st three were issue for HLS
  For same reason – how did we address?

## Slide 33: Programming Constructs
Dynamic Dataflow (from Day 5)
  Variable rates
  Switch/select operators

## Slide 34: Hardware Architecture
Some typical (4710,5710) processor “optimizations” can cause variable delay
  Caches
  Branch prediction
  Common-case optimizations
  Pipeline stalls
  Speculative issue

## Slide 35: Disciplines to achieve Real-Time
Part 3

## Slide 36: Already Addressed
Hardware pipelines are deterministic
  HLS limitations for hardware already drove us to fixed timing
Explicit scheduling of VLIW issue
  Can be fixed timing

## Slide 37: Open Issues
Processor Architecture
Resource Sharing

## Slide 38: What can we do to make architecture more deterministic?
Explicitly managed memory
Eliminate Branching (too severe?)
Unpipelined processors
Fixed-delay pipelines
  Offline-scheduled resource sharing
  Multi-threaded
Deadlines

## Slide 39: Explicitly Managed Memory
Make memory hierarchy visible
  Use Scratchpad memories instead of caches
Explicitly move data between memories
  E.g. movement into local memory
Already do for Register File in Processor
  Load/store between memory and RF slot
  …but don’t do for memory hierarchy

## Slide 40: Explicitly Managed Memory

## Slide 41: Offline Schedule Resource Sharing
Don’t arbitrate
Decide up-front when each shared resource can be used by each thread or processor
  Simple fixed schedule
  Detailed Schedule
What
  Memory bank, bus, I/O, network link, …

## Slide 42: Time-Multiplexed Bus
Fixed by hardware master
4 masters share a bus
Each master gets to make a request on the bus every 4th cycle
  If doesn’t use it, goes idle

## Slide 43: Time-Multiplexed Bus
Regular schedule
Fixed bus slot schedule of length N > masters
  (probably a multiple)
Assign owner for each slot
  Can assign more slots to one
E.g. N=8, for 4 masters
  Schedule (1 2 1 3 1 2 1 4)

## Slide 44: Fully Scheduled
At extreme, fully schedule which tasks gets resource on each cycle

## Slide 45: Simple Deterministic Processor with Multiplier
No branching
Unpipelined
Every operation completes in fixed time
Cycle time as shown?
Retimed cycle time?
What’s inefficient about this design?

## Slide 46: Simple Deterministic Processor with some Pipelining
No branching
Every operation completes in fixed time
Retimed cycle time?
  Hint what are cycles?
How pipelines added change behavior?
  Hint: what is sequence of addresses into Instr. Mem?

## Slide 47: Simple Deterministic Pipelined Processor
No branching
Every operation completes in fixed time
How pipelines added change behavior?
  Hint R1 value

## Slide 48: Simple Deterministic Pipelined Processor
No branching
Every operation completes in fixed time
Retimed cycle time?

## Slide 49: Deterministic Pipelines
Pipeline data updates
  Not available on next cycle, but depend on delay through logic
Delay branches
  Not happen immediately, a fixed number of clock cycles later
Schedule like VLIW

## Slide 50: Multithreaded Processor
Following slides make another point (and give another chance to look at retiming)
Trimming for time in lecture
Here as further bonus material

## Slide 51: Legal Register Moves
Retiming Lag/Lead
Day 7

## Slide 52: Reminder
Able to pipeline and retime to reduce cycle time on acyclic dataflow graphs
Day 8

## Slide 53: Step 1: lead Mux

## Slide 54: Step 2: lead M3

## Slide 55: Step 3: lead M2

## Slide 56: Step 4: lead M1

## Slide 57: Step 5: Lead ALU

## Slide 58: Step 6: Lead Data Mem

## Slide 59: Step 7: Lag Instr. Mem

## Slide 60: Step 8: Lead Mux

## Slide 61: Step 9: Lead M3

## Slide 62: Step 10: Lead M2

## Slide 63: Step 11: Lead Mux

## Slide 64: Step 12: Lead M3

## Slide 65: Step 13: Lead Mux

## Slide 66: Retimed
Max delay between
registers 1ns
Extra slides show retiming

## Slide 67: How use?
How could you usefully use
this faster processor with
the specified behavior?

## Slide 68: Deterministic Pipelines
Not how ARM, Intel (4710, 5710) processor are pipelined
Those include operations that make timing variable
  dynamic data hazards, branch speculation
Here, data becomes available after a predictable time
Branches take effect at a fixed time
  Likely delayed
Schedule to delays to get correct data

## Slide 69: Deadline Instruction
Deal with algorithmic (branching) variability
Set a hardware counter for thread
Decrement counter on each cycle
Demand counter reach 0 before thread allowed to continue at deadline instruction
  Stall if get there early
  Similar to flip-flop on a logic path
    Wait for clock edge to change or sample value
Model: fixed execution time

## Slide 70: WCET
WCET – Worst-Case Execution Time
Analysis when working with algorithms and architectures with data-dependent delay
  Need to meet real time
  Calculate the worst-case runtime of a task
    Like calculating the critical path (but harder)
    Worst-case delay of instructions
    Worst-case path through code
    Worst-case # loop iterations
  Rationale for setting Deadlines
    (like a cycle time)

## Slide 71: Different Goals
Real-Time
Willing to recompile to new hardware
Want time on hardware predictable
Willing to schedule for delays in particular hardware
General Purpose/Best Effort
ISA fixed
Want to run same assembly on different implementations
Tolerate different delays for different hardware
Run faster on newer, larger implementations

## Slide 72: SoC Opportunity
Can choose which resources are shared
Can dedicate resources to tasks
Isolate real-time tasks/portions of tasks from best-effort
  Separate hardware/processors
  Separate memories, network

## Slide 73: UltraScale+ Zynq
Has 2 “Real-Time Processor”
  ARM Cortex-R5
    32b (vs. 64b for A53 APU processor)
    ARMv7-R (vs. ARMv8)
    Single ALU, dual issue
    Branch prediction
Explicitly managed scratchpads
    Tightly-Coupled Memories
    On-Chip Memory (OCM)

## Slide 74: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 75: RPU Subsystem
UG1085
Xilinx
UltraScale
Zynq
TRM
(p65)

## Slide 76: Big Ideas:
Real-Time applications demand different discipline from best-effort tasks
Look more like synchronous circuits and hardware discipline
Avoid or use care with variable delay programming constructs
Can sequentialize, like processor
  But must avoid/rethink typical processor common-case optimizations
  Offline calculate static schedule for computation and sharing
    Instead of dynamic arbitration, stalls

## Slide 77: Admin
Feedback
Penn on Thursday-Friday schedule for tomorrow and Wednesday
   no lecture on Wednesday
Next lecture Monday
  Wrapup lecture