## Slide 1: ESE532: System-on-a-Chip Architecture
Day 6: February 1, 2017
Process and Threads

## Slide 2: Today
Dataflow Process Model
Finish Models
Aspirational Recommended Approach
Threads
Hazards
Discipline

## Slide 3: Message
Abstract the problem agnostic from implementation
Map based on
  Computational demand
  Platform
Use restricted patterns to avoid shared-memory pitfalls

## Slide 4: Dataflow Variants

## Slide 5: Synchronous Dataflow (SDF)
Particular, restricted form of dataflow
Each operation
  Consumes a fixed number of input tokens
  Produces a fixed number of output tokens
  When full set of inputs are available
    Can produce output
  Can fire any (all) operations with inputs available at any point in time

## Slide 6: Dynamic Dataflow
(Less) restricted form of dataflow
Each operation
  Conditionally consume input based on data value
  Conditionally produce output based on data value
  When full set of inputs are available
    Can (optionally) produce output
  Can fire any (all) operations with data-specified necessary inputs available at any point in time

## Slide 7: No Peaking
Key to determinism: behavior doesn’t depend on timing
  Cannot ask if a token is present
If (not_empty(in))
  Out.put(3);
Else
  Out.put(2);

## Slide 8: When peaking necessary?
What are cases where we need the ability to ask if a data item is present?

## Slide 9: When Peak Optimization?
What are cases where asking about data presence might allow performance optimization?

## Slide 10: Peaking
Removed model restriction (no peaking)
Gained expressive power
  Can grab data as shows up
Weaken our guarantees
  Possible to get non-deterministic behavior

## Slide 11: Process Network Roundup
Model | Deterministic Result | Deterministic Timing | Turing Complete
SDF+fixed-delay operators | Y | Y | N
SDF+variable delay operators | Y | N | N
DDF no peak | Y | N | Y
DDF w/ peak | N | N | Y

## Slide 12: Aspirational Approach

## Slide 13: Approach (1)
Identify natural parallelism
Convert to streaming flow
  Initially leave operators software
  Focus on correctness
Identify flow rates, computation per operator, parallelism needed
Refine operators
  Decompose further parallelism?
  E.g. SIMD changes making hw3
  model potential hardware

## Slide 14: Approach (2)
Refine coordination as necessary for implementation
Map operators and streams to resources
  Provision hardware
  Scheduling: Map operations to operators
  Memories, interconnect
Profile and tune

## Slide 15: Approach
Process Network agnostic to operator implementation
Implementation explores
  Operator mappings
    What fixed SoC provides
    Where might allocate hardware for novel SoC
  Memory allocation
    Isolated memoriescommunication explicit
  Communication mappings

## Slide 16: Preclass 1a
Throughput for 1:1 mapping of processes to SPs?
Possibly we didn’t know throughputs initially – map and measure

## Slide 17: Preclass 1b
Refine: better mapping to 3 SPs?
Throughput?

## Slide 18: Preclass 1c
Mapping 1 SIMD and 1 SP?
Throughput?
1/20
(SIMD)

## Slide 19: Approach
Once have base process network (ideally), we have reduced to working in this mapping space
Spend our time (in this class)
  Enriching and elaborating this mapping space

## Slide 20: Threads

## Slide 21: Thread
Has a separate locus of control (PC)
May share memory
  Run in common address space with other threads
  Now: look at shared memory

## Slide 22: Issues
Communication – how move data between processes?
Synchronization – how define how they advance relative to each other?
Determinism – for the same inputs, do we get the same outputs?

## Slide 23: Issues
Communication – read/write in common address space
Synchronization – get to choose
  Semaphores, locks, barriers, data presence
Determinism – not unless you’re very careful

## Slide 24: Shared Memory
Good
  Sharing easy to express
  Data movement implicit
Bad
  Easy to introduced unwanted non-determinism
  Expensive abstraction to support
    Hardware, energy
  Harder to understand and control communication
    Latency, throughput…

## Slide 25: What to watch for
Thread 1:
  Do stuff
  M[123]=12
  Do more stuff
  A=M[123]*2
Thread 2:
  Do different stuff
  M[123]=0
  Do other stuff
What value does A hold?

## Slide 26: Preclass 2a
P1:
for (i=0;i<N/2;i++)
  v=f(i);
  h[v]=h[v]+1;
P2:
for (i=N/2+1;i<N;i++)
  v=f(i);
  h[v]=h[v]+1;
What can go wrong here?

## Slide 27: Preclass 2b
P1:
for (i=0;i<N/2;i++)
  v=f(i);
  h[v]=h[v]+1;
P2:
for (i=N/2+1;i<N;i++)
  v=f(i);
  h[v]=h[v]+1;
How might we avoid hazard?

## Slide 28: Disciplines
Don’t really share
  Exploit actual sharing in limited ways
Privatize
  Local memory not really shared
  Server thread to sequentialize access to shared state (how use histogram?)
Use data presence
  Buffer
  Explicitly – presence variable and check

## Slide 29: Disciplines
Read-Only sharing OK
Barrier
  Force rendezvous at point before continue
  Like a clock edge in a circuit

## Slide 30: Expression and Implementation not 1:1
Examples
Pure DPN implemented on shared-memory processors
  Private memory, implement buffers in SM
Single threaded DP with conditionals
  Implement in multiple threads
SDF with many tasks
  Implement schedule of operations on single instruction stream

## Slide 31: SDF in single thread
While(input)
  A=Astep(in());
  B=Bstep(A);
  C=Cstep(B);

## Slide 32: Multiple Ways to Decompose
Searching for 2 targets strings in a single document
Run on 2 processor
How decompose and map?
Resource implications?
Data access implications?

## Slide 33: Approach
Identify design space of mappings
  Decomposition, hardware mapping
Analyze which meet our platform restrictions (are most efficient)
Experiment as necessary

## Slide 34: Big Ideas
Abstract the problem agnostic from implementation
Map based on
  Computational demand
  Platform
  Seldom 1:1  rich options to explore
Use restricted patterns to avoid shared-memory pitfalls

## Slide 35: Admin
Reading for Day 7 on web
HW3 due Friday
HW4 coming…