## Slide 1: ECE 252 / CPS 220 Advanced Computer Architecture I Lecture 3 Early Microarchitectures
Benjamin Lee
Electrical and Computer Engineering
Duke University
www.duke.edu/~bcl15
www.duke.edu/~bcl15/class/class_ece252fall11.html

## Slide 2
ECE 252 Administria
8 September – Homework #1 Due
Assignment on web page. Teams of 2-3.
Submit hard copy in class. Email code to TA’s
13 September – Class Discussion
Roughly one reading per class. Do not wait until the day before!
  Hill et al. “Classic machines: Technology, implementation, and economics”
  Moore. “Cramming more components onto integrated circuits”
  Radin. “The 801 minicomputer”
  Patterson et al. “The case for the reduced instruction set computer”
  Colwell et al. “Instruction sets and beyond: Computers, complexity, controversy”

## Slide 3
Microarchitectures
Instruction Set Architecture (ISA)
- Defines the hardware-software interface
- Provides convenient functionality to higher levels (e.g., software)
- Provides efficient implementation to lower levels (e.g., hardware)
Microarchitecture
- Microarchitecture implements ISA
- Implementation abstracted from programmer
Early Microarchitectures
- Stack Machines (1960s)
- Microprogrammed Machines(1970s-1980s)
- Reduced Instruction Set Computing (1990s)

## Slide 4
Essential Features
Stack operations (e.g., push/pop)
Computation (e.g., +, -, …)
Data pointer (DP) for accessing any element in data area
Program counter (PC) for accessing any instruction in code area
Stack pointer (SP) to accessing and moving any element in stack frame
Stack Machine Overview
stack
SP
DP
PC
data
.
.
.
a
b
c
push a
push b
push c
*
+
push e
/
code
Functional Units
(+, -, …)

## Slide 5
Stack Machine Overview
Processor state includes state
typical operations:
    push, pop, +, *, ...
Instructions like + implicitly
specify the top 2 elements of the stack as operands.
a
b
a
push b

c
b
a
push c

b
a
pop


## Slide 6
a
b
c
(a + b * c) / (a + d * c - e)
/
+
*
+
a
e
-
a
c
d
c
*
b
Reverse Polish
a b c * + a d c * + e - /
push a
push b
push c
multiply
*
Evaluation Stack
b * c
Expression Evaluation

## Slide 7
Stack Hardware Organization
Processor State
- Stack is part of processor state
- Stack must be bounded and small
- Max number stack elements ~ register file size, not memory size
Unbounded Stacks
- Part of stack in processor
- Remainder of stack in main memory
Stacks and Memory References
- Option 1: Top 2 stack elements in registers, remainder in memory
- Each push/pop requires memory reference; poor performance
- Option 2: Top N stack elements in registers, remainder in memory
- Overflows/underflows require memory reference; better performance
- Analogous to register spilling

## Slide 8
(a+b*c)/(a+d*c-e)  a b c * + a d c * + e - /
Stack Size & Memory References
program stack (size = 2) memory refs
push a R0 a
push b R0 R1 b
push c R0 R1 R2 c, ss(a)
* R0 R1 sf(a)
+ R0
push a R0 R1 a
push d R0 R1 R2 d, ss(a+b*c)
push c R0 R1 R2 R3 c, ss(a)
* R0 R1 R2 sf(a)
+ R0 R1 sf(a+b*c)
push e R0 R1 R2 e,ss(a+b*c)
- R0 R1 sf(a+b*c)
/ R0
4 stores, 4 fetches (implicit)

## Slide 9
(a+b*c)/(a+d*c-e)  a b c * + a d c * + e - /
Stack Size & Evaluating Expressions
a and c are loaded twice, inefficient register use
program stack (size = 4)
push a R0
push b R0 R1
push c R0 R1 R2
* R0 R1
+ R0
push a R0 R1
push d R0 R1 R2
push c R0 R1 R2 R3
* R0 R1 R2
+ R0 R1
push e R0 R1 R2
- R0 R1
/ R0

## Slide 10
vs General Purpose Register File
(a+b*c)/(a+d*c-e)  a b c * + a d c * + e - /
Efficient Register Usage
- Control register use with explicitly named registers
- Eliminate unnecessary loads and stores
- Fewer registers required but instructions are longer
Load R0 a
Load R1 c
Load R2 b
Mul R2 R1 Reuse R2
Add R2 R0
Load R3 d
Mul R3 R1 Reuse R3
Add R3 R0
Load R0 e Reuse R0
Sub R3 R0
Div R2 R3

## Slide 11
Stack vs General Purpose Register
Amdahl, Blaauw, and Brooks. “Architecture of the IBM System/360.” 1964
Stacks: access fast registers with stack operations (e.g., push, pop)
General purpose registers: access fast registers with explicit addresses (e.g., R1)
“In the final analysis, the stack organization would have been about break-even…the general-purpose objective weighed heavily in favor of the more flexible addressed register organization.”
Stack machine’s advantage is from fast registers, not how they’re used
Surfacing instructions, which bring submerged data to active positions, is profitable 50% of the time due to repeated operands.
Code density for stacks, register files is comparable
Stack depth limited by number of fast registers; requires stack management
Stacks benefit recursive sub-routines and recursion but requires independently addressed stacks (SP management)
Fitting variable-length fields into fixed-width stack is awkward

## Slide 12
Transition from Stack Machines
Stack machine’s popularity faded in the 1980s
Code Density
- Stack programs are not necessary smaller
- Consider frequent stack surfacing instructions
- Consider short register addresses
Advent of Modern Compilers
- Stack machines require stack discipline to manage finite stack
- Register allocation improves register space management
- Early language-directed architectures did not account for compilers
- B5000, B6700, HP3000, ICL 2900, Symbolics 3600

## Slide 13
Microprogrammed Machines
Why do we care?
- Provide background on CISC machines
- Illustrate small processors with complex instruction sets
- Used in most modern machines (x86, PowerPC, IBM360)
- Introduce machine structures
- Provide context for RISC machines
ISA favors particular microarchitecture style
- CISC: microprogrammed
- RISC: hardwired, pipelined - VLIW: fixed latency, in-order pipelines
- JVM: software interpretation
ISA can use any microarchitecture style
- Core2 Duo: hardwired, pipelined CISC (x86) w/ microcode support
- This Lecture: Microcoded RISC (MIPS) machine

## Slide 14
Hardware Organization
Structure: How are components connected? Statically
Behavior: How does data move between components? Dynamically
controller
data
path
control
points
status
lines

## Slide 15
Microcontrol Unit
- Maurice Wilkes, 1954
- Embed control logic state table in a memory array
Matrix A
Matrix B
Decoder
Next state
op conditional
code flip-flop
 address
Control lines to
ALU, MUXs, Registers

## Slide 16
Microcoded Microarchitecture
Memory
(RAM)
Datapath
mcontroller
(ROM)
Addr
Data
zero?
busy?
opcode
enMem
MemWrt
holds fixed
microcode instructions
holds user program written in macrocode instructions (e.g., MIPS, x86, etc.)

## Slide 17
MIPS32 ISA
- See Hennessy and Patterson, Appendix B for full description
Processor State
  - 32 32-bit GPRs, R0 always contains a 0
  - 16 double-precision, 32 single-precision FPRs
  - FP status register, used for FP compares & exceptions
  - PC, the program counter
  - Other special registers
Data types
  - 8-bit byte, 16-bit half word
  - 32-bit word for integers
  - 32-bit word for single precision floating point
  - 64-bit word for double precision floating point
Load/Store style instruction set
  - data addressing modes: immediate & indexed
  - branch addressing modes: PC relative & register indirect
  - byte addressable memory: big-endian mode
All instructions are 32 bits

## Slide 18
MIPS Instruction Formats
6 5 5 16
6 26
6 5 5 16
opcode rs rt immediate (rt)  (rs) op immediate
6 5 5 5 5 6
ALU
ALUi
6 5 5 16
Mem
0 rs rt rd 0 func (rd)  (rs) func (rt)
opcode rs rt displacement M[(rs) + displacement]
opcode rs offset BEQZ, BNEZ
opcode rs JR, JALR
opcode offset J, JAL

## Slide 19
A Bus-Based MIPS Datapath
Microinstruction: register to register transfer (17 control signals)
MA  PC means RegSel = PC; enReg=yes; ldMA= yes
B  Reg[rt] means RegSel = rt; enReg=yes; ldB = yes
enMem
MA
addr
data
ldMA
Memory
busy
MemWrt
Bus
32
zero?
A
B
OpSel
ldA
ldB
ALU
enALU
ALU
control
2
RegWrt
enReg
addr
data
rs
rt
rd
32(PC)
31(Link)
RegSel
32 GPRs
+ PC ...
32-bit Reg
3
rs
rt
rd
ExtSel
IR
Opcode
ldIR
Imm
Ext
enImm
2

## Slide 20
Memory Module
Assumption: Memory operates independently and is slow as compared to Reg-to-Reg transfers (multiple CPU clock cycles per access)
Enable
Write(1)/Read(0)
RAM
din
dout
we
addr
busy
bus

## Slide 21
Instruction Execution
Instruction fetch
Decode and register fetch
ALU operation
Memory operation (optional)
Write back to register file (optional)
  + computation of the next instruction address

## Slide 22
Microprogram Fragments
instr fetch: MA  PC # fetch current instr
      A  PC # next PC calculation
      IR  Memory
      PC  A + 4
      dispatch on Opcode # start microcode
ALU: A  Reg[rs]
      B  Reg[rt]
      Reg[rd]  func(A,B)
      do instruction fetch
ALUi: A  Reg[rs]
      B  Imm # sign extension
      Reg[rt]  Opcode(A,B)
      do instruction fetch

## Slide 23
Microprogram Fragments
LW: A  Reg[rs] # compute address
      B  Imm
      MA  A + B
      Reg[rt]  Memory # load from memory
      do instruction fetch
J: A  PC
      B  IR
      PC  JumpTarg(A,B) #JumpTarg(A,B) =
      do instruction fetch {A[31:28],B[25:0],00}
beqz: A  Reg[rs]
If zero?(A) then go to bz-taken
do instruction fetch
bz-taken: A  PC
      B  Imm << 2
      PC  A + B
      do instruction fetch

## Slide 24
MIPS Microcontroller
next state
PC (state)
Opcode
zero?
Busy (memory)
Control Signals (17)
s
s
6
Program ROM
addr
data
latching the inputs
may cause a
one-cycle delay
= 2(opcode+status+s) words
How big is “s”?
ROM size ?
Word size ?
= control+s bits

## Slide 25
State Op zero? busy Control points next-state
fetch0 * * * MA  PC fetch1
fetch1 * * yes .... fetch1
fetch1 * * no IR  Memory fetch2
fetch2 * * * A  PC fetch3
fetch3 * * * PC  A + 4 ?
ALU0 * * * A  Reg[rs] ALU1
ALU1 * * * B  Reg[rt] ALU2
ALU2 * * * Reg[rd]  func(A,B) fetch0
fetch3 ALU * * PC  A + 4 ALU0
Microprogram in the ROM

## Slide 26
State Op zero? busy Control points next-state
fetch0 * * * MA  PC fetch1
fetch1 * * yes .... fetch1
fetch1 * * no IR  Memory fetch2
fetch2 * * * A  PC fetch3
fetch3 ALU * * PC  A + 4 ALU0
fetch3 ALUi * * PC  A + 4 ALUi0
fetch3 LW * * PC  A + 4 LW0
fetch3 SW * * PC  A + 4 SW0
fetch3 J * * PC  A + 4 J0
fetch3 JAL * * PC  A + 4 JAL0
fetch3 JR * * PC  A + 4 JR0
fetch3 JALR * * PC  A + 4 JALR0
fetch3 beqz * * PC  A + 4 beqz0
...
ALU0 * * * A  Reg[rs] ALU1
ALU1 * * * B  Reg[rt] ALU2
ALU2 * * * Reg[rd]  func(A,B) fetch0
Microprogram in the ROM

## Slide 27
Microprogram in the ROM
State Op zero? busy Control points next-state
ALUi0 * * * A  Reg[rs] ALUi1
ALUi1 sExt * * B  sExt16(Imm) ALUi2
ALUi1 uExt * * B  uExt16(Imm) ALUi2
ALUi2 * * * Reg[rd] Op(A,B) fetch0
...
J0 * * * A  PC J1
J1 * * * B  IR J2
J2 * * * PC  JumpTarg(A,B) fetch0
...
beqz0 * * * A  Reg[rs] beqz1
beqz1 * yes * A  PC beqz2
beqz1 * no * .... fetch0
beqz2 * * * B  sExt16(Imm) beqz3
beqz3 * * * PC  A+B fetch0
...
JumpTarg(A,B) = {A[31:28],B[25:0],00}

## Slide 28
size = 2(w+s) x (c + s)
w = 6+2, c = 17, s = ?
no. of steps per opcode = 4 to 6 + fetch-sequence
no. of states = (4 steps per op-group ) x op-groups + common sequences
  = 4 x 8 + 10 states = 42 states  s = 6
Control ROM = 2(8+6) x 23 bits = 48 Kbytes
Control ROM
data
status & opcode
addr
next  PC
Control signals
 PC
/
w
/ s
/ c
Size of Control Store

## Slide 29
Reducing Size of Control Store
Control store must be fast, which is expensive
Reduce ROM height (= address bits)
    - reduce inputs by extra external logic
    - each input bit doubles the size of the control store
    - reduce states by grouping opcodes
    find common sequences of actions
    condense input status bits
    combine all exceptions into one, i.e., exception/no-exception
Reduce ROM width
    - restrict the next-state encoding-
    - next, dispatch on opcode, wait for memory, ...
    - encode control signals (vertical microcode)

## Slide 30
MIPS Microcontroller v2
uJumpType =
next | spin
| fetch | dispatch
| feqz | fnez
Control Signals (17)
Control ROM
address
data
+1
Opcode
ext
uPC (state)
jump
logic
zero
uPC
uPC+1
absolute
op-group
busy
uPCSrc
input encoding reduces ROM height

## Slide 31
Jump Logic
PCSrc = Case JumpTypes
  next  PC+1
  spin  if (busy) then PC else PC+1
  fetch  absolute
  dispatch  op-group
  feqz  if (zero) then absolute else PC+1
  fnez  if (zero) then PC+1 else absolute

## Slide 32
Instruction Fetch and ALU
State Control Points Next State
fetch0 MA  PC next
fetch1 IR  Memory spin
fetch2 A  PC next
fetch3 PC  A+4 dispatch
…
ALU0 A  Reg[rs] next
ALU1 B  Reg[rt] next
ALU2 Reg[rd]  func(A,B) fetch
…
ALUi0 A  Reg[rs] next
ALUi1 B  sExt16(Imm) next
ALUi2 Reg[rd]  Op(A,B) fetch

## Slide 33
Load and Store
State Control Points Next State
LW0 A  Reg[rs] next
LW1 B  sExt16(Imm) next
LW2 MA  A+B next
LW3 Reg[rt]  Memory spin
LW4 fetch
…
SW0 A  Reg[rs] next
SW1 B  sExt16(Imm) next
SW2 MA  A+B next
SW3 Memory  Reg[rt] spin
SW4 fetch

## Slide 34
Jumps
State Control Points Next State
J0 A  PC next
J1 B  IR next
J2 PC  JumpTarg(A,B) fetch
JR0 A  Reg[rs] next
JR1 PC  A fetch
JAL0 A  PC next
JAL1 Reg[31]  A next
JAL2 B  IR next
JAL3 PC  JumpTarg(A,B) fetch
JALR0 A  PC next
JALR1 B  Reg[rs] next
JALR2 Reg[31]  A next
JALR3 PC  B fetch

## Slide 35
Complex Instructions
ExtSel
A
B
RegWrt
enReg
enMem
MA
addr
addr
data
data
rs
rt
rd
32(PC)
31(Link)
RegSel
OpSel
ldA
ldB
ldMA
Memory
32 GPRs
+ PC ...
32-bit Reg
ALU
enALU
Bus
IR
busy
zero?
Opcode
ldIR
Imm
Ext
enImm
2
ALU
control
2
3
MemWrt
32
rs
rt
rd
rd M[(rs)] op (rt) Reg-Memory-src ALU op
M[(rd)]  (rs) op (rt) Reg-Memory-dst ALU op
M[(rd)]  M[(rs)] op M[(rt)] Mem-Mem ALU op

## Slide 36
Mem-Mem ALU Instruction
Mem-Mem ALU op
M[(rd)]  M[(rs)] op M[(rt)]
State Control Points Next State
  ALUMM0 MA  Reg[rs] next
  ALUMM1 A  Memory spin
  ALUMM2 MA  Reg[rt] next
  ALUMM3 B  Memory spin
  ALUMM4 MA  Reg[rd] next
  ALUMM5 Memory  func(A,B) spin
  ALUMM6 fetch
  Complex instructions usually do not require datapath modifications in a microprogrammed implementation, only extra space for the control program
  Implementing instructions without a hardwired controller is difficult without datapath modifications

## Slide 37
Performance
Microcode requires multiple cycles per instruction
  tC > max(treg-reg, tALU, t ROM)
Microcode requires multiple cycles per instruction
- Suppose 10 * t ROM < tRAM
- Compare against single-cycle hardwired implementation
- Good performance can be achieved even with CPI of 10
Microprogramming Advantages (1970’s)
- ROMs significantly faster than DRAMs
- For complex instruction sets, datapath and controller were simpler
- Adding instructions (e.g., floating-point) without datapath changes
- Fixing bugs in the controller is easy
- ISA compatibility across models is easy

## Slide 38
Decline of Microprogramming
Increasingly complex microcode
  - Complex instruction sets led to subroutine, call stacks in microcode
  Fixing bugs difficult with read-only nature of ROMs
Evolving Technology
  VLSI changed assumptions of ROMs vs RAMs, which became faster
  Microarchitectural innovations (pipelining, caches, buffers) make multi-cycle register-to-register execution unattractive
Evolving Software
  - Better compilers made complex instructions less important
  - Most complex instructions are rarely used
Transition to RISC
  Build fast instruction cache
  Use software subroutines, not hardware subroutines
  Use simple ISA to enable hardwired implementations

## Slide 39
Modern Microprogramming
Microprogramming is far from extinct
  Played crucial role in microprocessors of 1980’s (e.g., Intel 386, 486)
  Plays assisting role in modern microprocessors
Important role in early microprocessors (1980s)
    Example: Intel 386, 486
Assisting role in modern microprocessors
      Example: AMD Athlon, Intel Core 2 Duo, IBM Power PC
      Most instructions executed directly (hardwired control)
      Infrequently-used, complicated instructions invoke microcode engine
Assisting role in modern microprocessors
  Patchable microcode common for post-fabrication bug fixes
  - Example: Intel Pentiums load microcode patches at bootup

## Slide 40
Acknowledgements
    These slides contain material developed and copyright by
    Arvind (MIT)
    Krste Asanovic (MIT/UCB)
    Joel Emer (Intel/MIT)
    James Hoe (CMU)
    John Kubiatowicz (UCB)
    Alvin Lebeck (Duke)
    David Patterson (UCB)
    Daniel Sorin (Duke)