## Slide 1: ECE 252 / CPS 220 Advanced Computer Architecture I Reading Discussion 1
Benjamin Lee
Electrical and Computer Engineering
Duke University
www.duke.edu/~bcl15
www.duke.edu/~bcl15/class/class_ece252fall11.html

## Slide 2
ECE252 Administrivia
29 September – Homework #2 Due
  Use blackboard forum for questions
  Attend office hours with questions
  Email for separate meetings

## Slide 3
Classic Machines…
Technology and Architecture
  Stored program computer and new memory
  Computation bottlenecks and new transistors
Racing Moore’s Law
  Designs were outpaced by underlying technology
  Cray-1: Performance gain of 35% per year versus 60% in MOS scaling
  Cray-2: Performance gain of 13% per year versus 60% in MOS scaling
Rise of MOS Microprocessors
  Supercomputers used bipolar technologies with low volume
  Low volume implies less money for investment in bipolar technology
  Microprocessors used MOS technologies with high volume
  High volume implies more money for lithographic/device development

## Slide 4
Cramming more components…
Moore’s Law
  Number of transistors per chip double every year (2x / year)
  Corollary: Price per transistor decreases by a factor of two each year
  Corollary: Power and delay improve with scaling
  In practice, semiconductor technology improves (1.6x / year)
Forecasting
  Paper makes more than 25 predictions, all of which have come true
  Proliferation of computing into many areas (e.g., home, automobiles, portable communications, electronic wristwatches)
  Economics of market size and engineering costs and building large systems from standard components

## Slide 5
The 801 Minicomputer
Co-Design of Compilers and ISAs
  Philosophy of basing the ISA on what a compiler needs
  Influenced Berkeley RISC and Stanford MIPS projects
Case for Software Subroutines
  More responsive systems as interrupts occur at instruction boundaries and instructions are simpler, shorter
  Optimizing compilers can re-organize instructions for performance
  - “Wherever there is a system function that is expensive or slow in all its generality, but where software can recognize a frequently occurring degenerate case that function is moved from hardware to software, resulting in lower cost and improved performance”

## Slide 6
The Case for RISC
RISC for General-Purpose Processors
  VLSI technology allowed more functionality per chip, providing significant performance gains
  Pipelining is a key technology to improve instruction rates and RISC architectures are more amenable to pipelining
  Most complex instructions are un-used.
Debate
  Started a RISC versus CISC debate in the 1980s
  Debate died down in the 1990s as semiconductor technology provided sufficient on-chip resources to allow high-performance CISC implementations

## Slide 7
Instruction Sets and Beyond
Practical Rebuttal to RISC
  Technical elegance alone is insufficient in computer design
  Systems require upward compatibility and familiarity
  Designers benefit from well-defined, stable interface
Argument against All-or-None Approach
  Proposals for different approaches need not be segmented
  One side might easily adopt parts of a completely different proposal
  Example of windowed register file from Berkeley RISC that could be adopted by CISC processor if there were a need