## Slide 1: ECE 252 / CPS 220 Advanced Computer Architecture I Lecture 10 Instruction-Level Parallelism – Part 4
Benjamin Lee
Electrical and Computer Engineering
Duke University
www.duke.edu/~bcl15
www.duke.edu/~bcl15/class/class_ece252fall11.html

## Slide 2
ECE252 Administrivia
4 October – Homework #2 Due
  Use blackboard forum for questions
  Attend office hours with questions
  Email for separate meetings
4 October – Class Discussion
Roughly one reading per class. Do not wait until the day before!
  Srinivasan et al. “Optimizing pipelines for power and performance”
  Mahlke et al. “A comparison of full and partial predicated execution support for ILP processors”
  Palacharla et al. “Complexity-effective superscalar processors”
  Yeh et al. “Two-level adaptive training branch prediction”

## Slide 3
ECE252 Administrivia
6 October – Midterm Exam
  75 minutes, in-class
  Closed book, closed notes exam
  Performance metrics – performance, power, yield
  Technology – trends that changed architectural design
  History – Instruction sets (accumulator, stack, index, general-purpose)
  CISC – microprogramming, writing microprogram fragments
  Pipelining – Performance, hazards and ways to resolve them
  Instruction-level Parallelism – mechanisms to dynamically detect data dependences and to manage instruction flow (Scoreboard, Tomasulo, Physical Register File)
  Speculative Execution – exception handling, branch prediction
  Readings – High-level questions, not details

## Slide 4
Branch Prediction
Motivation
-- Branch penalties limit performance of deeply pipelined processors
-- Modern branch predictors have high accuracy (>95%) and can significantly reduce branch penalties
Hardware Support
-- Prediction structures: branch history tables, branch target buffer, etc.
-- Mispredict recovery mechanisms:
-- Separate instruction execution and instruction commit
-- Kill instructions following branch in pipeline
-- Restore architectural state to correct path of execution

## Slide 5
Static Branch Prediction
On average, probability a branch is taken is 60-70%.
But branch direction is a good predictor.
ISA can attach preferred direction semantics to branches (e.g., Motorola MC8810, bne0 prefers taken, beq0 prefers not taken).
ISA can allow choice of statically predicted direction (e.g., Intel IA-64). Can be 80% accurate.
JZ
JZ
backward
90%
forward
50%

## Slide 6
Dynamic Branch Prediction
Learn from past behavior
Temporal Correlation -- The way a branch resolves may be a good predictor of the way it will resolve at the next execution
Spatial Correlation -- Several branches may resolve in a highly correlated manner (preferred path of execution in the application)

## Slide 7
2-bit Branch Predictor
Use two-bit saturating counter.
Changes prediction after two consecutive mistakes.
- Temporal Correlation
- Branch can be taken (T), not-taken (N)
- 4 states (0, 1, 2, 3), each with corresponding prediction (T/N)
- Arcs correspond to resolved branch decision (T/N)

## Slide 8
Branch History Table (BHT)
BHT is an array of 2-bit branch predictors, indexed by branch PC
4K-entry branch history table, 80-90% accurate
0
0
Fetch PC
Branch?
Target PC
+
I-Cache
Opcode
offset
Instruction
k
BHT Index
2k-entry
BHT,
2 bits/entry
Taken/¬Taken?

## Slide 9
Two-Level Branch Prediction
Spatial Correlation: Pentium Pro uses the result from the last two branches
to select one of the four sets of BHT bits (~95% correct)
0
0
k
Fetch PC
Shift in
Taken/¬Taken
results of each branch
2-bit global branch history shift register
Taken/¬Taken?

## Slide 10
Branch Target Buffer (BTB) – v1
BHT only predicts branch direction (taken, not taken). Cannot redirect instruction flow until after branch target determined.
Store target with branch predictions.
During fetch: If (BP == taken) then nPC=target, else nPC=PC+4
Later: update BHT, BTB
IMEM
PC
Branch
Target
Buffer
(2k entries)
k
BPb
predicted
target
BP
target

## Slide 11
Branch Target Buffer (BTB) – v2
Keep both branch PC and target PC in the BTB
If match fails, PC+4 is fetched
Only taken branches and jumps held in BTB
I-Cache
PC
k
Valid
valid
Entry PC
=
match
predicted
target
target PC

## Slide 12
Mispredict Recovery
In-order execution
  No instruction following branch can commit before branch resolves
  Kill all instructions in pipeline behind mis-predicted branch
Out-of-order execution
  Multiple instructions following branch can complete before one branch resolves

## Slide 13
In-order Commit
  -- Instructions fetched, decoded in-order (entering the reorder buffer -- ROB)
  -- Instructions executed out-of-order
  -- Instructions commit in-order (write back to architectural state)
  -- Temporary storage needed in ROB to hold results before commit
Fetch
Decode
Execute
Commit
Reorder Buffer
In-order
In-order
Out-of-order
Kill
Kill
Kill
Exception?
Inject handler PC

## Slide 14
Branch Misprediction in Pipeline
  -- Can have multiple unresolved branches in reorder buffer -- ROB
  -- Can resolve branches out-of-order by killing all instructions in ROB that follow a mispredicted branch
Fetch
Decode
Execute
Commit
Reorder Buffer
Kill
Kill
Kill
Branch
Resolution
Inject correct PC
Branch
Prediction
PC
Complete

## Slide 15
Mispredict Recovery
  Take snapshot of register rename table at each predicted branch, recover earlier snapshot if branch mispredicted
t
v
t
v
t
v
Register File
Reorder
Buffer
Load
Unit
FU
FU
FU
Store
Unit
< t, result >
t1
t2
.
.
tn
Ins# use exec op p1 src1 p2 src2 pd dest data
Commit
Rename
Table
r1
t
v
r2
Rename
Snapshots
Ptr2 next to commit
Ptr1 next available
rollback next available

## Slide 16
Acknowledgements
    These slides contain material developed and copyright by
    Arvind (MIT)
    Krste Asanovic (MIT/UCB)
    Joel Emer (Intel/MIT)
    James Hoe (CMU)
    John Kubiatowicz (UCB)
    Alvin Lebeck (Duke)
    David Patterson (UCB)
    Daniel Sorin (Duke)