## Slide 1: ECE 252 / CPS 220 Advanced Computer Architecture I Lecture 17 Vectors
Benjamin Lee
Electrical and Computer Engineering
Duke University
www.duke.edu/~bcl15
www.duke.edu/~bcl15/class/class_ece252fall11.html

## Slide 2
ECE252 Administrivia
15 November – Homework #4 Due
Project Status
  Plan on having preliminary data or infrastructure
ECE 299 – Energy-Efficient Computer Systems
  www.duke.edu/~bcl15/class/class_ece299fall10.html
  Technology, architectures, systems, applications
  Seminar for Spring 2012.
  Class is paper reading, discussion, research project
  In Fall 2010, students read >35 research papers.
  In Spring 2012, read research papers.
  In Spring 2012, also considering textbook “The Datacenter as a Computer: An Introduction to the Design of Warehouse-scale Machines.”

## Slide 3
Last Time
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot

## Slide 4
Vector Processors

## Slide 5
Data-level Parallelism
Vectors effective for data-level parallelism (DLP)
  -- Vectors are most efficient way to exploit DLP
  -- Superscalar (e.g., DLP as instruction-level parallelism) is less efficient
  -- Multiprocessor (e.g., DLP as thread-level parallelism) is less efficient
Scientific Computing
  -- Weather forecasting, car-crash simulation, biological modeling
  -- Vector processors were invented for supercomputing, but fell out of favor after the advent of multiprocessors
Multimedia Computing
  -- Identical ops on streams or arrays of sound samples, pixels, video frames
  -- Vector processors were revived for multimedia computing

## Slide 6
Vector Processor History
Vectors widely used for supercomputing (1970s-1990s)
  -- Cray, CDC, Convex, TI, IBM
Transition away from vectors (1980s-1990s)
  -- Fitting a vector processor into a single chip was difficult
  -- Building supercomputers from commodity components was easier
Vectors are re-emerging as SIMD
  -- SIMD – single instruction multiple data
  -- SIMD provides short vectors in all ISAs
  -- Provides multimedia acceleration

## Slide 7
Parts of a Vector Processor
Scalar processor
  -- Scalar register file (e.g., 32 registers)
  -- Scalar functional units (arithmetic, load/store, etc…)
Vector register file
  -- Each register is an array of elements
  -- Example: 32 registers, each with 32 64-bit elements
  -- MVL – maximum vector length = max # of elements per register
Vector functional units
  -- Integer, floating-point, load/store, etc…
  -- Some datapaths (e.g., ALUs) shared by vector, scalar units

## Slide 8
Parts of a Vector Processor

## Slide 9
Vector Supercomputers
Cray-1, 1976
Scalar Unit
- Load/Store architecture
Vector Extension
- Vector registers
- Vector instructions
Implementation
- Hardwired control (no microcode)
- Pipelined functional units
- Interleaved memory system
- No data caches
- No virtual memory

## Slide 10
Cray-1 (1976)
Single Port
Memory
16 banks of 64-bit words
+
8-bit SECDED
80MW/sec data load/store
320MW/sec instruction
buffer refill
4 Instruction Buffers
64-bitx16
NIP
LIP
CIP
(A0)
( (Ah) + j k m )
64
T Regs
(A0)
( (Ah) + j k m )
64
B Regs
S0
S1
S2
S3
S4
S5
S6
S7
A0
A1
A2
A3
A4
A5
A6
A7
Si
Tjk
Ai
Bjk
FP Add
FP Mul
FP Recip
Int Add
Int Logic
Int Shift
Pop Cnt
Sj
Si
Sk
Addr Add
Addr Mul
Aj
Ai
Ak
V0
V1
V2
V3
V4
V5
V6
V7
Vk
Vj
Vi
V. Mask
V. Length
64 Element Vector Registers

## Slide 11
Vector Programming Model
+
+
+
+
+
+
[0]
[1]
[VLR-1]
Vector Arithmetic Instructions
ADDV v3, v1, v2
v3
v2
v1
Scalar Registers
r0
r15
Vector Registers
v0
v15
[0]
[1]
[2]
[VLRMAX-1]
VLR
Vector Length Register
v1
Vector Load and Store Instructions
LV v1, r1, r2
Base, r1
Stride, r2
Memory
Vector Register

## Slide 12
Vector ISA Benefits
Compact – single instruction defines N operations
  -- also fewer branches
Parallel – N operations are (data) parallel
  -- no dependencies between vector elements
  -- like VLIW, no complex hardware for dynamic scheduling
  -- scalable; additional functional units give additional performance
Expressive – memory ops describe access patterns
  -- vector memory ops exhibit continuous or regular access patterns
  -- vector memory ops can prefetch and/or effectively use memory banks
  -- amortize high latency for 1st element over large sequential pattern (bursts of data transfer…1st element incurs a long latency….subsequent elements are pipelined to produce a new element per cycle)

## Slide 13
Basic Vector Instructions
Suppose 64-element vectors
Instr Operands Operation Comment
VADD.VV V1, V2, V3 V1 = V2 + V3 vector + vector
VADD.SV V1, R0, V2 V1 = R0 + V2 scalar + vector
VMUL.VV V1, V2, V3 V1 = V2 * V3 vector x vector
VMUL.SV V1, R0, V2 V1 = R0 * V2 scalar x vector
VLD V1, R1 V1 = M[R1,…R1+63] load, stride=1
VLDS V1, R1, R2 V1 = M[R1,…R1+63*R2] load, stride=R2
VLDX V1, R1, V2 V1 = M[R1+V2(i), i=0 to 63] indexed gather
VST V1, R1 M[R1…R1+63] = V1 store, stride=1
VLDS V1, R1, R2 M[R1,…R1+63*R2] = V1 store, stride=R2
VLDX V1, R1, V2 M[R1+V2(i), i=0 to 63] = V1 indexed scatter

## Slide 14
Vector Code Example
# C code # Scalar Code # Vector Code
for (i=0 ; i<64 ; i++) LI R4, 64 LI VLR, 64
C[i] = A[i] + B[i]; loop: VLD V1, R1
L.D F0, 0 (R1) VLD V2, R2
L.D F2, 0 (R2) ADD.VV V3, V1, V2
ADD.D F4, F2, F0 VST V3, R3
S.D F4, 0 (R3)
DADDIU R1, 8
DADDIU R2, 8
DADDIU R3, 8
DSUBIU R4, 1
BNEZ R4, loop
-- Load immediate (LI) with length of vector (64)
-- Vector length register (VLR)

## Slide 15
Vector Length
Vector register holds a max number of elements
  -- MVL: Maximum vector length (e.g., 64)
  -- But application vectors may not match MVL
Vector length register
  -- VL: controls length of any vector operation (add, multiply, load, store)
  -- Example: vadd.vv with VL10 is equivalent to:
  for(i=0; i<10; i++) {V1[i] = V2[i] + V3[i]}
  -- Before vector instructions, VL is set to number less than or equal to MVL
How can we code applications where the vector length is not known until run-time?

## Slide 16
Strip Mining
Strip Mining
  -- Suppose application VL > MVL
  -- Generate loop that handles MVL elements per iteration
  -- Translate each loop iteration into a single vector instruction
Example: AX+Y
  -- First loop for (N mod MVL) elements. Remaining loops for MVL elements
  VL = (N mod MVL); # set VL to be a smaller vector
  for (i=0 ; i<VL ; i++) # 1st-loop translates into a single set
  Y[i] = A*X[i] + Y[i]; # of vector instructions
  low = (N mod MVL) # low – strips off beginning elements
  VL = MVL # set VL to be max vector length
  for (i=low ; i<N ; i++); # 2nd-loop translates into N/MVL sets
  Y[i] = A * X[i] + Y[i]; # of vector instructions

## Slide 17
Vector Instruction Execution
Use deep pipeline (fast clock) to execute operations for each vector element.
Simplify pipeline control because elements in vector are independent  no hazards.
V1
V2
V3
V3  V1 * V2
Six stage multiply pipeline

## Slide 18
Opt 1 – Chaining
Consider the following code with vector length of 32
  vmul.vv V1, V2, V3
  vadd.vv V4, V1, V5 # very long RAW hazard
Chaining
  -- V1 is not a single entity, but a vector of individual elements
  -- Pipeline forwarding can work for individual elements
Flexible Chaining
  -- Chain any vector to any other active vector operation
  -- Requires more read/write ports in the vector register file

## Slide 19
Opt 2 – Multiple Datapaths
ADDV C,A,B
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
Execution using one pipelined datapath
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
Execution using four pipelined datapaths
4 adders  4 elements / cycle
N/4 cycles
1 adder  1 element / cycle
N cycles

## Slide 20
Opt 2+: Multiple Lanes
  -- Vector elements interleaved across lanes
  -- Example: V[0, 4, 8, …] on Lane 1, V[1, 5, 9,…] on Lane 2, etc.
  -- Compute for multiple elements per cycle
  -- Example: Lane 1 computes on V[0] and V[4] in one cycle
  -- Modular, scalable design
  -- No inter-lane communication needed for most vector instructions

## Slide 21
Opt 3 – Conditional Execution
Suppose you want to vectorize this code:
  for (i=0 ; i<N ; i++) {
  if(A[i] != B[i]) {A[i] -= B[i]; } }
Solution: vector conditional execution
  -- Add vector flag registers, single-bit mask per vector element
  -- Use vector-compare to set the vector flag register
  -- Use vector flag register to control vector-sub
  -- Vector op executed only if corresponding flag element is set
  vld V1, Ra
  vld V2, Rb
  vcmp.neq.vv M0, V1, V2 # vector compare for mask
  vsub.vv V3, V2, V1, M0 # conditional vadd
  vst V3, Ra

## Slide 22
Vector Memory
Multiple, interleaved memory banks (16)
Bank busy time (e.g., 4 cycles) is time before bank ready to accept next request
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
+
Base
Stride
Vector Registers
Memory Banks
Address Generator

## Slide 23
Supercomputing to Multimedia
Support narrow data types
  -- Allow each vector registers to store 16-, 32-, or 64-bit elements
  -- Use a control register to indicate width of register elements
Support saturated and fixed-point arithmetic
  -- Minor modification to functional units
Support element permutations for vector reductions
  -- for(i=0 ; i<N ; i++) {S += A[i]}
  -- Rewrite as:
  for(i=0 ; i<N ; i+=VL) {S[0:VL-1]+=A[i:i+VL-1];} # S[…], A[…] are
  for(i=0 ; i<VL ; i++) {S+=[S[i];} # vectors of VL elements
  -- First loop trivially vectorizable
  -- Second loop vectorizable by splitting vector register S into two vector registers. Take a binary-tree approach to reduction

## Slide 24
SIMD in Superscalar Processors
SIMD extends conventional ISA
  -- SIMD – single instruction, multiple data
  -- MMX, SSE, SSE-2, SSE-3, 3D-Now, Altivec, VIS
Objective: Accelerate multimedia processing
  -- Define vectors of 16-, 32-bit elements in regular registers
  -- Apply SIMD arithmetic on these vectors
Advantages
  -- No vector register file, which would require additional area
  -- Simple extensions (new opcodes, modified datapath)

## Slide 25
SIMD Challenges
SIMD Vectors are short with fixed size
  -- Cannot capture data parallelism wider than 64 bits
  -- Recent shift from 64-bit to 128-bit vectors (SSE, Altivec)
SIMD does not support vector memory accesses
  -- Strided or indexed access require equivalent multi-instruction sequences
  -- With vector memory accesses, much lower benefits in performance and code density

## Slide 26
SIMD versus Vectors
  -- QCIF and CIF numbers are in clock cycles per frame
  -- All other numbers are in clock cycles per pixel
  -- MMX results assume no first-level cache misses
  -- Courtesy: Christos Kozyrakis, Stanford

## Slide 27
Intel Larrabee
  Vector Multiprocessor
  -- 2-way superscalar, 4-way multi-threaded, in-order cores with vectors
  -- Cores communicate on a wide ring bus
  -- L2 cache is partitioned among the cores
  -- Provides high aggregate bandwidth
  -- Allows data replication and sharing

## Slide 28
Larrabee x86 Core
-- separate scalar, vector units with separate registers
-- scalar unit: in-order x86 core
-- vector unit: 16 32-bit ops/clock
-- short execution pipelines
-- fast access to L1 cache
-- direct connection to L2 cache subset
-- instructions support prefetch into L1 and L2 caches

## Slide 29
Larrabee Vector Unit
Vector Instruction Set
-- 32 vector registers (512 bits each)
-- vector load/store with scatter/gather
-- 8 mask registers for conditional exec.
-- mask registers select lanes for an instruction
-- mask registers allow separate execution kernels in each lane
Vector Instruction Support
-- Fast read from L1 cache
-- Numeric type conversion and replication in memory path

## Slide 30
Vector Power Efficiency
Power and Parallelism
  -- Power(1-lane) = [capacitance] x [voltage]^2 x [frequency]
  -- If we double number of lanes, we double peak performance
  -- Then, if we halve frequency, we return to original peak performance.
  -- But, halving frequency allows us to halve voltage
  -- Power (2-lane) = [2 x capacitance] x [voltage/2]^2 x [frequency/2]
  -- Power (2-lane) = Power(1-lane)/4 @ same peak performance
Simpler Logic
  -- Replicate control logic for all lanes
  -- Avoid logic for multiple instruction issue or dynamic out-of-order execution
Clock Gating
  -- Turn-off clock when hardware is unused
  -- Vector of given length uses specific resources for specific # of cycles -- Conditional execution (masks) further exposes unused resources

## Slide 31
Summary
Vector Processors
  -- Express and exploit data-level parallelism (DLP)
SIMD Extensions
  -- Extensions for short vectors in superscalar (ILP) processors
  -- Provide some advantages of vector processing at less cost