## Slide 1: ECE 252 / CPS 220 Advanced Computer Architecture I Lecture 19 Summary
Benjamin Lee
Electrical and Computer Engineering
Duke University
www.duke.edu/~bcl15
www.duke.edu/~bcl15/class/class_ece252fall11.html

## Slide 2
ECE252 Administrivia
1 December 2011
Project Status
  Please submit project reports to Blackboard by midnight
Final Exam
  Wednesday, Dec 14, 2-5pm
  Closed book, closed notes exam
  Cumulative, with emphasis on latter half.
  6-7 Questions
  1/3 on earlier material, 2/3 on later material
  1/3 extended design questions
  2/3 short answer

## Slide 3
Architecture: Abstractions/Metrics
Computer architecture defines HW/SW interface
Evaluate architectures quantitatively

## Slide 4
Computer Architecture
Application
Physics
Gap too large to bridge in one step
Computer architecture is the design of abstraction layers,
which allow efficient implementations of computational applications on available technologies

## Slide 5
Abstraction Layers
Algorithm
Gates/Register-Transfer Level (RTL)
Application
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Microarchitecture
Devices
Programming Language
Circuits
Physics
Domain of early computer architecture
(‘50s-’80s)
Domain of recent computer architecture
(since ‘90s)

## Slide 6
In-order Datapath
(built, ECE152)
Chip Multiprocessors
(understand, experiment ECE252)
ECE 252 Executive Summary

## Slide 7
Performance Factors
Latency = (Instructions / Program) x (Cycles / Instruction) x (Seconds / Cycle)
Seconds / Cycle
  - Technology and architecture
  - Transistor scaling
  - Processor microarchitecture
Cycles / Instruction (CPI)
  - Architecture and systems
  - Processor microarchitecture
  - System balance (processor, memory, network, storage)
Instructions / Program
- Algorithm and applications
- Compiler transformations, optimizations
- Instruction set architecture

## Slide 8
Power and Energy
Definitions
- Energy (Joules) = a x C x V2
- Power (Watts) = a x C x V2 x f
Power Factors and Trends
- activity (a): function of application resource usage
- capacitance (C): function of design; scales with area
    - voltage (V): constrained by leakage, which increases as V falls
- frequency (f): varies with pipelining and transistor speeds
- Models in cycle-accurate simulators (e.g., Princeton Wattch)
Dynamic Voltage and Frequency Scaling (DVFS)
- P-states: move between operational modes with different V, f
    - Intel TurboBoost: increase V, f for short durations without violating thermal design point (TDP)

## Slide 9
Datapath: CISC versus RISC
Complex Instruction Set Computing
  - microprogramming
  - motivated by technology (slow instruction fetch)
Reduced Instruction Set Computing
  - hard-wired datapath
  - motivated by technology (caches, fast memory)
  - complex instructions rarely used

## Slide 10
CISC Microprograms
instr fetch: MA  PC # fetch current instr
      A  PC # next PC calculation
      IR  Memory
      PC  A + 4
      dispatch on Opcode # start microcode
ALU: A  Reg[rs]
      B  Reg[rt]
      Reg[rd]  func(A,B)
      do instruction fetch
ALUi: A  Reg[rs]
      B  Imm # sign extension
      Reg[rt]  Opcode(A,B)
      do instruction fetch

## Slide 11
CISC Bus-Based MIPS Datapath
Microinstruction: register to register transfer (17 control signals)
MA  PC means RegSel = PC; enReg=yes; ldMA= yes
B  Reg[rt] means RegSel = rt; enReg=yes; ldB = yes
enMem
MA
addr
data
ldMA
Memory
busy
MemWrt
Bus
32
zero?
A
B
OpSel
ldA
ldB
ALU
enALU
ALU
control
2
RegWrt
enReg
addr
data
rs
rt
rd
32(PC)
31(Link)
RegSel
32 GPRs
+ PC ...
32-bit Reg
3
rs
rt
rd
ExtSel
IR
Opcode
ldIR
Imm
Ext
enImm
2

## Slide 12
RISC Hard-wired MIPS Datapath
Figure A.17, Page A-29
IF/ID
ID/EX
EX/MEM
MEM/WB

## Slide 13
Visualizing the Pipeline
Figure A.2, Page A-8

## Slide 14
Hazards and Limits to Pipelining
Structural Hazards
  Hardware cannot support this combination of instructions.
  Solution: stall pipeline (interlocks)
Data Hazards
  Instruction depends on result of prior instruction still in pipeline
  Solution: forward data, stall pipeline
Control Hazards
  Instruction fetch depends on decision about control flow
  Example: compute branches early in pipeline, predict branches

## Slide 15
Tomasulo & Out-of-order
Out-of-order Execution
  Dynamically schedule instructions
  Execute instructions when dependences resolved
Tomasulo’s Algorithm
  Queue instructions until operands ready (reservation stations, ROB)
  Rename to eliminate write hazards (rename table, physical registers)
Precise Interrupts/Exceptions
  Instructions execute/complete out-of-order
  Instructions commit in-order via reorder buffer
  Check for exceptions when committing instruction

## Slide 16
Memory
DRAM – access dense array of slow memory with a command protocol
SRAM – access smaller array of fast memory on processor die
Virtual Memory – translate applications’ virtual addresses into physical addresses, providing better memory management and protection
Small,
Fast Memory
(RF, SRAM)
CPU
Big, Slow Memory
(DRAM)
A
B
holds frequently used data

## Slide 17
DRAM
-- Chip organized into 4-8 logical banks, which can be accessed in parallel
-- Access DRAM with activate , read/write, precharge commands
Row Address Decoder
Col.
1
Col. 2M
Row 1
Row 2N
Column Decoder & Sense Amplifiers
M
N
N+M
bit lines
word lines
Memory cell (one bit)
D
Data
Bank 1

## Slide 18
Caches
Caches exploit predictable patterns
Temporal Locality
Caches remember the contents of recently accessed locations
Spatial Locality
Caches fetch blocks of data nearby recently accessed locations

## Slide 19
Placement Policy
0 1 2 3 4 5 6 7
0 1 2 3
Set Number
Cache
Fully (2-way) Set Direct
Associative Associative Mapped
anywhere anywhere in only into
set 0 block 4
(12 mod 4) (12 mod 8)
0 1 2 3 4 5 6 7 8 9
1 1 1 1 1 1 1 1 1 1 0 1 2 3 4 5 6 7 8 9
2 2 2 2 2 2 2 2 2 2 0 1 2 3 4 5 6 7 8 9
3 3
0 1
Memory
Line Number
Line 12
can be placed

## Slide 20
Direct-Mapped Cache
Tag
Data Line
V
=
Line
Offset
Tag
Index
t
k
b
t
HIT
Data Word or Byte
2k
lines

## Slide 21
Average Memory Access Time
AMAT = [Hit Time] + [Miss Prob.] x [Miss Penalty]
  Miss Penalty equals AMAT of next cache/memory/storage level.
  AMAT is recursively defined
To improve performance
  Reduce the hit time (e.g., smaller cache)
  Reduce the miss rate (e.g., larger cache)
  Reduce the miss penalty (e.g., optimize the next level)
Simple design strategy
  Observe that hit time increases with cache size
  Design the largest possible cache with a hit time of 1-2 cycles.
  For example, design 8-32KB of cache in modern technology
  Design trade-offs are more complex with superscalar architectures and multi-ported memories

## Slide 22
Caches and Code
Restructuring code affects data access sequences
  Group data accesses together to improve spatial locality
  Re-order data accesses to improve temporal locality
Prevent data from entering the cache
      Useful for variables that are only accessed once
      Requires SW to communicate hints to HW.
      Example: “no-allocate” instruction hints
Kill data that will never be used again
      Streaming data provides spatial locality but not temporal locality
      If particular lines contain dead data, use them in replacement policy.
      Toward software-managed caches

## Slide 23
Caches and Code
What type of locality does this improve?
  for(i=0; i < N; i++) a[i] = b[i] * c[i];
  for(i=0; i < N; i++)
  d[i] = a[i] * c[i];
  for(i=0; i < N; i++) { a[i] = b[i] * c[i]; d[i] = a[i] * c[i];
  }

## Slide 24
Virtual Memory
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?

## Slide 25
Parallelism
Instruction-level Parallelism (ILP)
  - multiple instructions in-flight
  - hardware-scheduled: (1) pipelining, (2) out-of-order execution
  - software-scheduled: (3) VLIW
Data-level Parallelism (DLP)
  - multiple, identical operations on data arrrays/streams
  - (1) vector processors, (2) GPUs
  - (3) single-instruction, multiple-data (SIMD) extensions
Thread-level Parallelism (TLP)
  - multiple threads of control
  - if a thread stalls, issue instructions from other threads
  - (1) multi-threading, (2) multiprocessors

## Slide 26
VLIW and ILP (SW-managed)
Multiple operations packed into one instruction format
Instruction format is fixed, each slot supports particular instruction type
Constant operation latencies are specified (e.g., 1 cycle integer op)
Software schedules operations into instruction format, guaranteeing
  Parallelism within an instruction – no RAW checks between ops
  No data use before ready – no data interlocks/stalls
Two Integer Units,
Single Cycle Latency
Two Load/Store Units,
Three Cycle Latency
Two Floating-Point Units,
Four Cycle Latency
Int Op 2
Mem Op 1
Mem Op 2
FP Op 1
FP Op 2
Int Op 1

## Slide 27
Vectors and DLP

## Slide 28
Multithreading and TLP
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot

## Slide 29
Multiprocessors
Shared-memory Multiprocessors
  Provide a shared-memory abstraction
  Enables familiar and efficient programmer interface
P1
P2
P3
P4
Memory System

## Slide 30
Multiprocessors
Shared-memory Multiprocessors
  Provide a shared-memory abstraction
  Enables familiar and efficient programmer interface
Interconnection Network
P1
Cache
M1
Interface
P2
Cache
M2
Interface
P3
Cache
M3
Interface
P4
Cache
M4
Interface

## Slide 31
Multiprocessors
Shared-memory Multiprocessors
  Provide a shared-memory abstraction
  Enables familiar and efficient programmer interface
Interconnection Network
P1
Cache
M1
Interface
P2
Cache
M2
Interface
P3
Cache
M3
Interface
P4
Cache
M4
Interface

## Slide 32
Challenges in Shared Memory
Cache Coherence
“Common Sense”
P1-Read[X]  P1-Write[X]  P1-Read[X] Read returns X
P1-Write[X]  P2-Read[X] Read returns value written by P1
P1-Write[X]  P2-Write[X] Writes serialized
All P’s see writes in same order
Synchronization
Atomic read/write operations
Memory Consistency
What behavior should programmers expect from shared memory?
Provide a formal definition of memory behavior to programmer
Example: When will a written value be seen?
Example: P1-Write[X] <<10ps>> P2-Read[X]. What happens?

## Slide 33
Coherence Protocols
Implement protocol for every cache line.
Compare, contrast snoopy and directory protocols [[Stanford Dash]]

## Slide 34
Synchronization and Atomicity
Solution: Test-and-set instruction
  Add single instruction for load-test-store (t&s R1, lock)
  - Test-and-set atomically executes
    ld R1, lock; # load previous lock value
    st 1, lock; # store 1 to set/acquire
  If lock initially free (0), t&s acquires lock (sets to 1)
  If lock initially busy (1), t&s does not change it
  Instruction is un-interruptible/atomic by definition
  Inst-0 t&s R1, lock # atomically load, check, and set lock=1
  Inst-1 bnez R1 # if previous value of R1 not 0,
  …. acquire unsuccessful
  Inst-n stw R1, 0 # atomically release lock

## Slide 35
Sequential Consistency (SC)
Definition of Sequential Consistency
Formal definition of programmers’ expected view of memory
Each processor P sees its own loads/stores in program order
(2) Each processor P sees !P loads/stores in program order
(3) All processors see same global load/store ordering.
P and !P loads/stores may be interleaved into some order.
But all processors see the same interleaving/ordering.
Definition of Multiprocessor Ordering [Lamport]
Multi-processor ordering corresponds to some sequential interleaving of uni-processor orderings. Multiprocessor ordering should be indistinguishable from multi-programmed uni-processor

## Slide 36
For More
ECE 259 (Spring 2012)
  Advanced Computer Architecture II
  Parallel computer architecture design and evaluation
  Parallel programming, coherence, synchronization, consistency
ECE 299-01 (Spring 2012)
  Energy Efficient Computer Systems
  Technology, architecture, application strategies for energy efficiency
  Datacenter computing
ECE 254 (tbd)
  Fault-Tolerant and Testable Computer Systems
  Fault models, redundancy, recovery, testing
Computer architecture is HW/SW interface.
Consider classes on both sides of this interface.

## Slide 37
Looking Forward
Energy-efficiency
  Technology limitations motivate new architectures for efficiency
  Ex: specialization, heterogeneity, management
Technology
  Emerging technologies motivate new architectures for capability
  Ex: memory (phase change), networks (optical),
Reliability and Security
  Variations in fabrication, design process motivate new safeguards
  Ex: tunable structures, trusted bases
Multiprocessors
  Abundant transistors, performance goals motivate parallel computing
  Ex: parallel programming, coherence/consistency, management