## Slide 1: ECE 552 / CPS 550 Advanced Computer Architecture I Lecture 2 History, Instruction Set Architectures
Benjamin Lee
Electrical and Computer Engineering
Duke University
www.duke.edu/~bcl15
www.duke.edu/~bcl15/class/class_ece252fall12.html

## Slide 2
ECE 552 Administrivia
11 September – Homework #1 Due
Assignment on web page. Teams of 2-3.
Submit soft copies to Sakai.
Use Piazza for questions.
11 September – Class Discussion
Do not wait until the day before!
  Hill et al. “Classic machines: Technology, implementation, and economics”
  Moore. “Cramming more components onto integrated circuits”
  Radin. “The 801 minicomputer”
  Patterson et al. “The case for the reduced instruction set computer”
  Colwell et al. “Instruction sets and beyond: Computers, complexity, controversy”

## Slide 3
A Bit of History
Historical Narrative
- Helps understand why ideas arose
- Helps illustrate the design process
Technology Trends
- Future technologies may be as constrained as older ones
Learning from History
- Those who ignore history are doomed to repeat it
    - Every mistake made in mainframe design was also made in minicomputers, then microcomputers, where next?

## Slide 4
Charles Babbage
Charles Babbage (1791-1871)
- Lucasian Professor of Mathematics
- Cambridge University, 1827-1839
Contributions
- Difference Engine 1823
- Analytic Engine 1833
Approach
- mathematical tables (astronomy), nautical tables (navy)
    any continuous function can be approximated by polynomial
    mechanical gears and simple calculators

## Slide 5
Difference Engine
Karl Weierstrass
- Any continuous function can be approximated by a polynomial
- Any polynomial can be computed from difference tables
Example: All you need is an adder
f(n) = n2 + n + 41
d1(n) = f(n) - f(n-1) = 2n => f(n) = f(n-1) + d1(n)
d2(n) = d1(n) – d1(n-1) = 2 => d1(n) = d1(n-1) + d2(n)
n
d2(n)
d1(n)
f(n)
0
41
1
2
2
2
3
2
4
2
4
6
8
43
47
53
61

## Slide 6
Analytic Engine
Inspiration: Jacquard Looms
- Looms were controlled by punch cards
    - Cards with fixed, punched holes dictated weave pattern (program)
    - Same set of cards used with different color threads (numbers)
Definitions
- Store contains input, output variables
- Mill operates on variables
Operation
    An operation in the mill requires feeding two punched cards, producing a new punched card for store

## Slide 7
Harvard Mark I
History
- Howard Aiken – Professor of Physics, Harvard University
- Built in 1944 in IBM Endicott Laboratories
Technology
- Mechanical with some electro-magnetically controlled relays, gears
    750,000 components weigh 5 tons
    Synchronizing clock beats every 0.015 seconds (66Hz)
Performance
- 0.3 seconds for addition
    6 seconds for multiplication
    1 minute for a sine calculation - Broke down once a week

## Slide 8
ENIAC
History
- Electronic Numerical Integrator and Computer (ENIAC), 1943-45
- Eckert and Mauchly, University of Pennsylvania
Technology
- First electronic, operational, general-purpose analytic calculator
    30 tons, 72 square meters, 200KW
Performance
- Reads 120 cards per minute
    200 microsecond add, 6 millisecond division
    1000x faster than Mark I
    Not very reliable!
Application
- World War II ballistic calculations

## Slide 9
EDVAC
History
- Eckert, Mauchly, von Neumann, et al., 1944
- ENIAC instructions execute independently of calculated results
- Human intervention required to change instruction flow
- EDVAC addresses this problem
Technology
- First stored program computer
    Program manipulated as data
Instruction Sequencing
- Manual control: calculators
    External automatic control: Harvard Mark I (paper tape)
    Internal automatic control: EDVAC (read-write memory)
    Stored program computer: same storage for data and instructions

## Slide 10
Technology and Reliability
Early Technology
- ENIAC: 18,000 vacuum tubes, 20 10-digit numbers
- EDVAC: 4,000 vacuum tubes, 2,000 word storage
BINAC
- Two processors that checked each other for reliability
    Did not work because processors never agreed
Reliability Challenges
    Vacuum tubes, Williams tubes
    Charge storage on tube surface
Technology Solution
- Magnetic-core memory, 1954
- J. Forrester, MIT
- MIT Whirlwind, MTBF 20min, considered reliable

## Slide 11
Computing in the 1950s
Hardware was expensive
Storage and Memory Challenges
- Stores were small (1000 words), no resident system software
- Memory access time was 10-50x slower than processor cycle
- Instruction execution time dominated by memory access time
Computation Challenges
- Emphasize design of complex control circuits to execute an instruction
- Neglect time required to decode instruction
- Programmer’s view of machine inseparable from HW implementation

## Slide 12
Early Instruction Sets
Single Accumulator
- Carry-over from calculators, typically less than 2-dozen instructions
- Single operand (AC)
LOAD x AC  M[x]
STORE x M[x]  (AC)
ADD x AC  (AC) + M[x]
SUB x
SHIFT LEFT AC  2  (AC) SHIFT RIGHT
JUMP x PC  x
JGE x if (AC) ³ 0 then PC  x
LOAD ADR x AC  Extract address field (M[x])
STORE ADR x

## Slide 13
Single Accumulator Machine
LOOP LOAD N # AC  M[N]
    JGE DONE # if(AC>0), PC DONE
    ADD ONE # AC  AC + 1
    STORE N # M[N]  AC
F1 LOAD A # AC  M[A]
F2 ADD B # AC  (AC) + M[B]
F3 STORE C # M[C]  (AC)
    JUMP LOOP
DONE HLT
Ci Ai + Bi, 1  i  n
Notice M[N] is a counter, not an index.
How to modify the addresses A, B and C ?

## Slide 14
Self-Modifying Code
LOOP LOAD N # AC  M[N]
    JGE DONE # if (AC >= 0), PC  DONE
    ADD ONE # AC  AC + M[ONE]
    STORE N # M[N]  AC
F1 LOAD A # AC  M[A]
F2 ADD B # AC  AC + M[B]
F3 STORE C # M[C]  (AC)
    LOAD ADR F1 # AC  address field (M[F1])
    ADD ONE # AC  AC + M[ONE]
    STORE ADR F1 # changes address of A
    LOAD ADR F2
    ADD ONE
    STORE ADR F2 # changes address of B
    LOAD ADR F3
    ADD ONE
    STORE ADR F3 # changes address of C
    JUMP LOOP
DONE HLT
Ci Ai + Bi, 1  i  n
Each iteration requires:
total book-keeping
Inst fetch 17 14
Stores 5 4

## Slide 15
Index Registers
Specialized registers to simplify address calculations
- T. Kilburn, Manchester University, 1950s
- Instead of single AC register, use AC and IX registers
Modify Existing Instructions
- Load x, IX AC  M[x + (IX)]
- Add x, IX AC  (AC) + M[x + (IX)]
Add New Instructions
- Jzi x, IX if (IX)=0, then PC x, else (IX)(IX)+1
- Loadi x, IX IX  M[x] (truncated to fit IX)
Index registers have accumulator-like characteristics

## Slide 16
Using Index Registers
LOADi -n, IX # load n into IX
LOOP JZi DONE, IX # if(IX=0), DONE
    LOAD LASTA, IX # AC M[LASTA + (IX)]
    ADD LASTB, IX # note: LASTA is address
    STORE LASTC, IX # of last element in A
    JUMP LOOP
DONE HALT
Ci Ai + Bi, 1  i  n
Longer instructions (1-2 bits), index registers with ALU circuitry
Does not require self-modifying code, modify IX instead
Improved program efficiency (operations per iteration)
total book-keeping
Inst fetch 5 2
Stores 1 0

## Slide 17
Option 1: Increment index register by k
    AC  (IX) new instruction
    AC  (AC) + k
    IX  (AC) new instruction
Also, the AC must be saved and restored
Option 2: Manipulate index register directly
    INCi k, IX IX  (IX) + k
    STOREi x, IX M[x]  (IX) (extended to fit a word)
IX begins to resemble AC
    Several index registers, accumulators
    Motivates general-purpose registers (e.g., MIPS ISA R0-R31)
Operations on Index Registers

## Slide 18
Evolution of Addressing Modes
1. Single accumulator, absolute address
Load x AC  M[x]
2. Single accumulator, index registers
Load x, IX AC  M[x + (IX)]
3. Single accumulator, indirection
Load (x) AC  M[M[x]]
4. Multiple accumulators, index registers, indirection
Load Ri, IX, (x) Ri  M[M[x] + (IX)]
5. Indirection through registers
Load Ri, (Rj) Ri  M[M[(Rj)]]
6. The Works
Load Ri, Rj, (Rk) Rj = index, Rk = base address
Ri  M[Rj + (Rk)]

## Slide 19
Instruction Formats
Zero-address Formats
- Instructions have zero operands
- Operands on a stack
    add M[sp]  M[sp] + M[sp-1]
    load M[sp]  M[M[sp]]
- Stack can be registers or memory
- Top of stack usually cached in registers
One-address Formats
- Instructions have one operand
- Accumulator is always other implicit operand
C
B
A
SP
Register

## Slide 20
Instruction Formats (cont.)
Two-address Formats
- Destination is same as one of the operand sources
    Ri  (Ri) + (Rj) # (Reg x Reg) to Reg
    Ri  (Ri) + M[x] # (Reg x Mem) to Reg
- x can be specified directly or via register
- x address calculation could include indexing, indirection, etc.
Three-address Formats
- One destination and up to two operand sources
    Ri  (Rj) + (Rk) # (Reg x Reg) to Reg
    Ri  (Rj) + M[x] # (Reg x Reg) to Reg

## Slide 21
Data Formats
Data Sizes
- Bytes, Half-words, words, double words
Byte Addressing
- Location of most-, least- significant bits
Word Alignment
- Suppose memory is organized into 32-bit words (e.g., 4 bytes).
- Word aligned addresses begin only at 0, 4, 8, … bytes
Big Endian
Little Endian
MSB
MSB
LSB
LSB
0 1 2 3 4 5 6 7

## Slide 22
Software Developments
Numerical Libraries (up to 1955)
- floating-point operations
- transcendental functions
- matrix multiplication, equation solvers, etc.
High-level Languages(1955-1960)
- Fortran, 1956
- assemblers, loaders, linkers, compilers
Operating Systems (1955-1960)
- accounting programs to track usage and charges

## Slide 23
Compatibility
Early 1960s, IBM had 4 incompatible computers
- IBM 701, 650, 702, 1401
- Different instruction set architecture
- Different I/O system, secondary storage (magnetic taps, drums, disks)
- Different assemblers, compilers, libraries
- Different markets (e.g., business, scientific, real-time)
The need for compatibility motivated IBM 360.

## Slide 24
IBM 360: Design Principles
Amdahl, Blaauw and Brooks, “Architecture of the IBM System/360” 1964
1. Support growth and successor machines
2. Connect I/O devices with general methods
3. Emphasize total performance
- Evaluate answers per month rather than bits per microsecond
- Emphasize programmability
4. Eliminate manual intervention
  - Machine must be capable of supervising itself
5. Reduce down time
  - Build hardware fault checking and fault location support
6. Facilitate assembly
  - Redundant I/O devices, memories for fault tolerance
7. Support flexibility
  - Some problems required floating-point words > 36bits

## Slide 25
IBM 360: General Purpose Registers
Processor State
- 16 general-purpose, 32-bit registers
- may be used as index and base register
- register 0 has special properties
- 4 floating-point, 64-bit registers
    - a program status word (PSW) with program counter (PC), condition codes, control flags
Data Formats
  - 8-bit bytes: the IBM 360 is why bytes are 8-bits long today!
  - 16-bit half-words
  - 32-bit words
  - 64-bit double-words

## Slide 26
IBM 360: Initial Implementation
        Model 30 Model 70
    Storage 8K - 64 KB 256K - 512 KB
Datapath 8-bit 64-bit
Circuit Delay 30 nsec/level 5 nsec/level
Local Store Main Store Transistor Registers
Control Store 1 microsecond read Conventional circuits
IBM 360 instruction set architecture (ISA) completely hid underlying technological differences between models
Milestone: The first true ISA designed as portable hardware-software interface
- With minor modifications, ISA still survives today

## Slide 27
IBM, HotChips 2010
5.2 GHz in IBM 45nm CMOS technology
1.4 billion transistors in 512 sq-mm
64-bit virtual addressing
- original IBM360 was 24-bit
Quad-core design
Out-of-order, 3-way superscalar pipeline
Redundant datapaths
- every instruction performed in 2 parallel datapaths and results compared
L1 i-cache (64KB); L1 d-cache (128KB) d-cache
L2 cache (1.5MB), private, per-core
L3 cache (24MB), eDRAM
Scales to 96 cores in one machine
IBM z11: 47 Years Later

## Slide 28
Acknowledgements
    These slides contain material developed and copyright by
    Arvind (MIT)
    Krste Asanovic (MIT/UCB)
    Joel Emer (Intel/MIT)
    James Hoe (CMU)
    John Kubiatowicz (UCB)
    Alvin Lebeck (Duke)
    David Patterson (UCB)
    Daniel Sorin (Duke)