## Slide 1: ECE 552 / CPS 550 Advanced Computer Architecture I Lecture 17 Vectors
Benjamin Lee
Electrical and Computer Engineering
Duke University
www.duke.edu/~bcl15
www.duke.edu/~bcl15/class/class_ece252fall11.html

## Slide 2
ECE552 Administrivia
13 November – Homework #4 Due
Project Status
  Plan on having preliminary data or infrastructure
8 November – Class Discussion
Roughly one reading per class. Do not wait until the day before!
  Mudge, “Power: A first-class architectural design constraint”
  Lamport, “How to make a multiprocessor computer that correctly executes multiprocess programs”
  Lenoski et al. “The Stanford DASH Multiprocessor”
  Tullsen et al. “Simultaneous multithreading: Maximizing on-chip parallelism”

## Slide 3
Last Time
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Multiprocessing
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot

## Slide 4
Vectors and Data-level Parallelism

## Slide 5
Data-level Parallelism
Vectors effective for data-level parallelism (DLP)
  -- Vectors are most efficient way to exploit DLP
  -- Superscalar (e.g., DLP as instruction-level parallelism) is less efficient
  -- Multiprocessor (e.g., DLP as thread-level parallelism) is less efficient
Scientific Computing
  -- Weather forecasting, car-crash simulation, biological modeling
  -- Vector processors were invented for supercomputing, but fell out of favor after the advent of multiprocessors
Multimedia Computing
  -- Identical ops on streams or arrays of sound samples, pixels, video frames
  -- Vector processors were revived for multimedia computing

## Slide 6
Vector Processor History
Vectors widely used for supercomputing (1970s-1990s)
  -- Cray, CDC, Convex, TI, IBM
Transition away from vectors (1980s-1990s)
  -- Fitting a vector processor into a single chip was difficult
  -- Building supercomputers from commodity components was easier
Vectors are re-emerging as SIMD
  -- SIMD – single instruction multiple data
  -- SIMD provides short vectors in all ISAs
  -- Provides multimedia acceleration

## Slide 7
Parts of a Vector Processor
Scalar processor
  -- Scalar register file
  -- Example: 32 registers, each with 1 32-bit element
  -- Scalar functional units (arithmetic, load/store, etc…)
Vector register file
  -- Each register is an array of elements
  -- Example: 32 registers, each with 32 64-bit elements
  -- MVL – maximum vector length = max # of elements per register
Vector functional units
  -- Integer, floating-point, load/store, etc…
  -- Some datapaths (e.g., ALUs) shared by vector, scalar units

## Slide 8
Parts of a Vector Processor

## Slide 9
Vector Supercomputers
Cray-1, 1976
Scalar Unit
- Load/Store architecture
Vector Extension
- Vector registers
- Vector instructions
Implementation
- Hardwired control (no microcode)
- Pipelined functional units
- Interleaved memory system
- No data caches
- No virtual memory

## Slide 10
Vector Programming Model
+
+
+
+
+
+
[0]
[1]
[VLR-1]
Vector Arithmetic Instructions
ADDV v3, v1, v2
v3
v2
v1
Scalar Registers
r0
r15
Vector Registers
v0
v15
[0]
[1]
[2]
[VLRMAX-1]
VLR
Vector Length Register
v1
Vector Load and Store Instructions
LV v1, r1, r2
Base, r1
Stride, r2
Memory
Vector Register

## Slide 11
Vector ISA Benefits
Compact – single instruction defines N operations
  -- also fewer branches
Parallel – N operations are (data) parallel
  -- no dependencies between vector elements
  -- like VLIW, no complex hardware for dynamic scheduling
  -- scalable; additional functional units give additional performance
Expressive – memory ops describe access patterns
  -- vector memory ops exhibit continuous or regular access patterns
  -- vector memory ops can prefetch and/or effectively use memory banks
  -- amortize high latency for 1st element over large sequential pattern
  (bursts of data transfer…1st element incurs a long latency….subsequent elements are pipelined to produce a new element per cycle)

## Slide 12
Basic Vector Instructions
Suppose 64-element vectors
Instr Operands Operation Comment
VADD.VV V1, V2, V3 V1 = V2 + V3 vector + vector
VADD.SV V1, R0, V2 V1 = R0 + V2 scalar + vector
VMUL.VV V1, V2, V3 V1 = V2 * V3 vector x vector
VMUL.SV V1, R0, V2 V1 = R0 * V2 scalar x vector
VLD V1, R1 V1 = M[R1,…R1+63] load, stride=1
VLDS V1, R1, R2 V1 = M[R1,…R1+63*R2] load, stride=R2
VLDX V1, R1, V2 V1 = M[R1+V2(i), i=0 to 63] indexed gather
VST V1, R1 M[R1…R1+63] = V1 store, stride=1
VSTS V1, R1, R2 M[R1,…R1+63*R2] = V1 store, stride=R2
VSTX V1, R1, V2 M[R1+V2(i), i=0 to 63] = V1 indexed scatter

## Slide 13
Vector Code Example
# C code # Scalar Code # Vector Code
for (i=64 ; i>0 ; i--) LI R4, 64 LI VLR, 64
C[i] = A[i] + B[i]; loop: VLD V1, R1
L.D F0, 0 (R1) VLD V2, R2
L.D F2, 0 (R2) ADD.VV V3, V1, V2
ADD.D F4, F2, F0 VST V3, R3
S.D F4, 0 (R3)
DADDIU R1, 8
DADDIU R2, 8
DADDIU R3, 8
DSUBIU R4, 1
BNEZ R4, loop
-- Load immediate (LI) with length of vector (64)
-- Vector length register (VLR)

## Slide 14
Vector Length
Vector register holds a max number of elements
  -- MVL: Maximum vector length (e.g., 64)
  -- But application vector lengths may not match MVL
Vector length register
  -- VL: controls length of any vector operation (add, multiply, load, store)
  -- Example: vadd.vv with VL10 is equivalent to:
  for(i=0; i<10; i++) {V1[i] = V2[i] + V3[i]}
  -- Before sequence of vector instructions, VL set to number <= to MVL
How can we code applications where the vector length is not known until run-time?

## Slide 15
Strip Mining
Strip Mining
  -- Suppose application VL > MVL
  -- Generate loop that handles MVL elements per iteration
  -- Translate each loop iteration into a single vector instruction
Example: AX+Y
  -- First loop for (N mod MVL) elements. Remaining loops for MVL elements
  VL = (N mod MVL); # set VL to be a smaller vector
  for (i=0 ; i<VL ; i++) # 1st-loop translates into a single set
  Y[i] = A*X[i] + Y[i]; # of vector instructions
  low = (N mod MVL) # low – strips off beginning elements
  VL = MVL # set VL to be max vector length
  for (i=low ; i<N ; i++); # 2nd-loop translates into N/MVL sets
  Y[i] = A * X[i] + Y[i]; # of vector instructions

## Slide 16
Vector Instruction Execution
Use deep pipeline (fast clock) to execute operations for each vector element.
Simplify pipeline control because elements in vector are independent  no hazards.
V1
V2
V3
V3[i]  V1[i] * V2[i]
Six stage multiply pipeline

## Slide 17
Opt 1 – Chaining
Consider the following code with vector length of 32
  vmul.vv V1, V2, V3
  vadd.vv V4, V1, V5 # very long RAW hazard
Chaining
  -- V1 is not a single entity, but a vector of individual elements
  -- Pipeline forwarding can work for individual elements
Flexible Chaining
  -- Chain any vector to any other active vector operation
  -- Requires more read/write ports in the vector register file

## Slide 18
Opt 2 – Multiple Datapaths
ADDV C,A,B
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
Execution using one pipelined datapath
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
Execution using four pipelined datapaths
4 adders  4 elements / cycle
N/4 cycles
1 adder  1 element / cycle
N cycles

## Slide 19
Opt 2+: Multiple Lanes
  -- Vector elements interleaved across lanes
  -- Example: V[0, 4, 8, …] on Lane 1, V[1, 5, 9,…] on Lane 2, etc.
  -- Compute for multiple elements per cycle
  -- Example: Lane 1 computes on V[0] and V[4] in one cycle
  -- Modular, scalable design
  -- No inter-lane communication needed for most vector instructions

## Slide 20
Opt 3 – Conditional Execution
Suppose you want to vectorize this code:
  for (i=0 ; i<N ; i++) {
  if(A[i] != B[i]) {A[i] -= B[i]; } }
Solution: vector conditional execution
  -- Add vector flag registers, single-bit mask per vector element
  -- Use vector-compare to set the vector flag register
  -- Use vector flag register to control vector-sub
  -- Vector op executed only if corresponding flag element is set
  vld V1, Ra
  vld V2, Rb
  vcmp.neq.vv M0, V1, V2 # vector compare for mask
  vsub.vv V3, V2, V1, M0 # conditional vadd
  vst V3, Ra

## Slide 21
Vector Memory
Multiple, interleaved memory banks (e.g., 16)
Provides memory-level parallelism when filling vector registers
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
+
Base
Stride
Vector Registers
Memory Banks
Address Generator

## Slide 22
Supercomputing to Multimedia
Support narrow data types
  -- Allow each vector register to store 16-, 32-, or 64-bit elements
  -- Use a control register to indicate width of register elements
Support fixed-point arithmetic
  -- Minor modification to functional units
Support element permutations for vector reductions
  -- for(i=0 ; i<N ; i++) {S += A[i]}
  -- Rewrite as:
  for(i=0 ; i<N ; i+=VL) {S[0:VL-1]+=A[i:i+VL-1];} # S[…], A[…] are
  for(i=0 ; i<VL ; i++) {S+=[S[i];} # vectors of VL elements
  -- First loop trivially vectorizable
  -- Second loop vectorizable by splitting vector register S into two vector registers. Take a binary-tree approach to reduction

## Slide 23
SIMD in Superscalar Processors
SIMD extends conventional ISA
  -- SIMD – single instruction, multiple data
  -- MMX, SSE, SSE-2, SSE-3, 3D-Now, Altivec, VIS
Objective: Accelerate multimedia processing
  -- Define vectors of 16-, 32-bit elements in regular registers
  -- A logical vector register may span multiple physical registers
  -- Apply SIMD arithmetic on these vectors
Advantages
  -- No vector register file, which would require additional area
  -- Simple extensions (new opcodes, modified datapath)

## Slide 24
SIMD Challenges
SIMD vectors are short with fixed size
  -- Cannot capture data parallelism wider than 64 bits
  -- Recent shift from 64-bit to 128-bit vectors (SSE, Altivec)
SIMD does not support vector memory accesses
  -- Strided or indexed access require equivalent multi-instruction sequences
  -- Without vector memory accesses, much lower benefits in performance and code density

## Slide 25
SIMD versus Vectors
  -- QCIF and CIF numbers are in clock cycles per frame
  -- All other numbers are in clock cycles per pixel
  -- MMX results assume no first-level cache misses
  -- Courtesy: Christos Kozyrakis, Stanford

## Slide 26
Intel Larrabee
  Vector Multiprocessor
  -- 2-way superscalar, 4-way multi-threaded, in-order cores with vectors
  -- Cores communicate on a wide ring bus
  -- L2 cache is partitioned among the cores
  -- Provides high aggregate bandwidth
  -- Allows data replication and sharing

## Slide 27
Larrabee x86 Core
-- separate scalar, vector units with separate registers
-- scalar unit: in-order x86 core
-- vector unit: 16 32-bit ops/clock
-- short execution pipelines
-- fast access to L1 cache
-- direct connection to L2 cache subset
-- instructions support prefetch into L1 and L2 caches

## Slide 28
Larrabee Vector Unit
Vector Instruction Set
-- 32 vector registers (512 bits each)
-- vector load/store with scatter/gather
-- 8 mask registers for conditional exec.
-- mask registers select lanes for an instruction
-- mask registers allow separate execution kernels in each lane
Vector Instruction Support
-- Fast read from L1 cache
-- Numeric type conversion and replication in memory path

## Slide 29
Vector Power Efficiency
Power and Parallelism
  -- Power(1-lane) = [capacitance] x [voltage]^2 x [frequency]
  -- If we double number of lanes, we double peak performance
  -- Then, if we halve frequency, we return to original peak performance.
  -- But, halving frequency allows us to halve voltage
  -- Power (2-lane) = [2 x capacitance] x [voltage/2]^2 x [frequency/2]
  -- Power (2-lane) = Power(1-lane)/4 @ same peak performance
Simpler Logic
  -- Replicate control logic for all lanes
  -- Avoid logic for multiple instruction issue or dynamic out-of-order execution
Clock Gating
  -- Turn-off clock when hardware is unused
  -- Vector of given length uses specific resources for specific # of cycles -- Conditional execution (masks) further exposes unused resources

## Slide 30
Summary
Vector Processors
  -- Express and exploit data-level parallelism (DLP)
SIMD Extensions
  -- Extensions for short vectors in superscalar (ILP) processors
  -- Provide some advantages of vector processing at less cost